## Slide 1: Battery Management and Communication System
10s1p Li-ion instrumentation & control BQ76930 monitoring & STM32 firmware Operator dashboard NVIDIA Jetson AI expansion path

## Slide 2: Concept and Application of the Design
Split-domain architecture for safety Power Domain: Battery, sensing, cooling, protection Host Domain: STM32 control and desktop UI
  Split-domain architecture for safety
  Power Domain: Battery, sensing, cooling, protection
  Host Domain: STM32 control and desktop UI
What We Designed
  10s1p Li-ion monitoring Current & thermal sensing Active cooling & balancing Operator dashboard
Technical Principles
  BQ76930 cell supervision 20mΩ shunt & 10K NTC sensing PWM fan control USB CDC telemetry
Intended Applications
  Lab battery characterization
  Embedded controls experiments
  AI battery health estimation on Jetson
Relevant EE Subjects
  Power electronics & embedded systems
  PCB design & controls
  Hardware-software co-design
Why the Architecture Matters
  Improves observability
  Reduces fault propagation risk
  Enables independent testing during bring-up

## Slide 3: Technical Design Objectives
Translating project requirements into explicit numerical targets from the design report and firmware code.
Battery Coverage
  Monitor 10 cell voltages, 10 NTCs, pack current, and fan telemetry.
  Implemented coverage
Pack Electrical Target
  Support Molicel P42A pack (151.2 Wh nominal) with cell-level visibility.
  Pack specification
Current Resolution
  BQ76930 coulomb-counter + 20mΩ shunt for pack current estimation.
  Implemented conversion
Safety Response Window
  Fast thermal/overcurrent monitoring; slower 1-10s balancing.
  Firmware architecture target
Cooling Control
  0-100% duty, 2°C hysteresis, 4-sample RPM avg, 2s stall detection.
  Bench-implemented
Host Interface
  USB CDC telemetry, QWebChannel command delivery, 50ms polling.
  Integrated path

## Slide 4: Final High-Level Design
System partitioned into battery unit, control electronics, and operator station Isolates high-energy pack from USB host interface
  System partitioned into battery unit, control electronics, and operator station
  Isolates high-energy pack from USB host interface
Battery Domain
Control Domain
Host Domain

## Slide 5: Final Low-Level Design: Electrical Implementation
Core low-level implementation across three main schematic pages.

## Slide 6: Final Low-Level Design: Program Flow-Charts
Implementation flow logic synthesized directly from firmware and dashboard operations.
Firmware Runtime Flow
1. Boot and bring-up
2. BMS interface detection
3. Sensor acquisition
4. Control, protection, and telemetry
Desktop Dashboard Flow
1. Launcher startup
2. Serial connection layer
3. Parsing and frame assembly
4. State normalization and GUI update

## Slide 7: Technical Challenges
Key integration challenges across sensing, firmware, comms, and packaging.
High-impedance thermistor readings were noisy
  Problem: Noisy high-impedance NTC values at fast ADCs.
Problem:
  Solution: Increased sampling time, used Beta-model math.
Solution:
  Workaround: Next Step: Full reference thermometer calibration.
Workaround:
PWM fan control required missing HAL timer pieces
  Problem: Missing HAL TIM drivers for PWM.
Problem:
  Solution: Added TIM drivers, tuned to 1 kHz PWM & 2°C hysteresis.
Solution:
  Workaround: RPM falls back to duty cycle on timeout.
Workaround:
Mixed serial formats broke clean frame reconstruction
  Problem: Mixed serial formats caused incomplete reads.
Problem:
  Solution: Regex parser, frame assembly, 0.3s timeout.
Solution:
  Workaround: Fallback: GUI simulation mode.
Workaround:
Compact enclosure packaging fought airflow and fit
  Problem: Compact footprint impacted tolerances & airflow.
Problem:
  Solution: Iterative CAD revisions for fit & airflow.
Solution:
  Workaround: Next Step: Production-ready harness & enclosure refinement.
Workaround:

## Slide 8: Major Components of the Design and Implementation
Primary implementation ownership per subsystem.
Battery Pack and Harness
  10s1p cell holder Enclosure fit-up Harness routing
BMS Hardware Stack
  BMS schematic/layout BQ76930 monitoring Protection interfaces
Embedded Control Firmware
  STM32F303RC bring-up ADC & sensing integration Fan & USB CDC control
Operator Dashboard
  PyQt6 launcher & bridge Command-surface GUI Jetson data path

## Slide 9: Who Contributed to What
Subsystem leadership across the team.
Dashboard and System Integration
  Dashboard and GUI design/implementation
  CAD and enclosure refinement
  Firmware integration and telemetry path work
  NVIDIA Jetson AI model pipeline direction
E-Load and Bench Validation
  E-Load development
  Testing and debugging support
  NVIDIA Jetson AI model contribution
  Battery charger and pack/enclosure harness setup
PCB and Validation Hardware
  BMS layout and PCB design
  E-Load validation
  BMS validation
  Battery charger and battery-cell harness engineering
Architecture and Schematic Direction
  Overall planning and system planning
  BMS schematic development
  Emulation board design
  Firmware assistance and architecture support

## Slide 10: Design Considerations
System shaped by schedule, thermal, packaging limits Uses robust, reliable communication standards
  System shaped by schedule, thermal, packaging limits
  Uses robust, reliable communication standards
Time and Integration Risk
  Tolerant serial framing Simulation mode Staged bring-up
Power, Thermal, and Safety Tradeoffs
  1 kHz PWM fan path Breakpoint auto-curve 2°C hysteresis Clear fault observability
Size, Weight, and Cost
  Compact enclosure with optimized airflow Reused STM32Cube/HAL & USB CDC Iterative 3D-printed revisions
Industry Standards and Interfaces Used
USB 2.0 CDC
I2C
ADC + NTC sensing
PWM + Tach capture
JSON / tokenized telemetry
QWebChannel

## Slide 11: Test Report
Validated behaviors based directly on repo documentation and implementation.
Test Item
Original Objective
Observed / Implemented Result
Status
  Cell and thermal visibility
  Show all 10 cells and 10 thermistor channels
  10 cell voltages plus thermistor mapping to the GUI are implemented
  Met
  USB host link
  Reliable host communication at 115200 baud
  USB CDC plus GUI serial connect flow defaults to 115200
  Met
  Fan control loop
  Auto/manual cooling with measurable RPM
  1 kHz PWM, 0-100% duty, 2 deg C hysteresis, 2 s RPM timeout, 4-sample average
  Met
  Current sensing
  Convert BQ current registers into pack current
  20 mOhm shunt conversion implemented at 0.422 mA/LSB
  Met
  Parser resilience
  Handle mixed telemetry formats without dropping frames
  Regex/token parser, JSON handling, and 0.30 s multiline finalize path are implemented
  Met
  Calibration completeness
  Close the loop with calibrated live hardware data
  Integration and calibration are identified next steps in the repo
  Partial
Validation Strategy
  Firmware checks Serial reconstruction tests GUI verification Staged bench testing
How Close to Spec?
  Implemented: Comms, telemetry, fan control, monitoring. Remaining gap: Calibration & live scale testing.
Key Quantitative Anchors
  10 cells, 10 NTCs 115200 baud, 1 kHz PWM 2°C hysteresis, 0.422 mA/LSB 2s CMD timeout, 50ms fallback

## Slide 12: Demo Video Placeholder
Reserved space for the recorded demo clip.
Insert final demo video here
  Sequence: Connect USB, stream telemetry, toggle fan, show status, demo interaction.
Scene 1
Scene 2
Scene 3
Scene 4

## Slide 13: Summary
  Delivered cross-domain engineering system with a path toward AI analytics.
What Was Achieved
  BQ76930 sensing & STM32 control USB telemetry & premium dashboard Validated architecture
What Is Strongest
  Cell visibility & current measurement Thermal control Parser robustness & GUI usability
What Comes Next
  Final calibration & closer charger validation Fault handling & trending Jetson-based state estimation
Closing Takeaway
  A modular, safe, expandable battery platform ready for analytics and validation.
  Sources used in this deck: final report, weekly reports, firmware plans, dashboard source, schematic PDFs, and project assets from the EE175 workspace.