## Slide 1
SENIOR DESIGN · EE 175AB · ENGR 181W
Battery Management System
A 10-cell lithium-ion pack with programmable electronic load and a real-time desktop dashboard.
Kaushik Vada · Nick Poon · Christian Kim
University of California, Riverside · June 1, 2026
Notes: TITLE — Brief, ~10 s. No need to read the title. Kaushik opens: 'Good afternoon, I'm Kaushik Vada — I'm here with Nick Poon and Christian Kim, and we're going to walk you through our Battery Management System project for EE 175.'

## Slide 2
Commercial 10-cell BMS units cost $1,200+ and lock telemetry behind proprietary software — none feed a custom Python application.
The gap
Safety. A 10s pack at 42 V can source 100+ A into a short — no MCU response is fast enough.
Cost. Orion BMS 2 starts at $1,200 and requires Orion's proprietary configurator.
Integration. No commercial unit exposes per-cell voltage over standard USB serial.
Five design objectives
Cell voltage error ≤ ± 20 mV
Breaker response ≤ 5 ms
E-Load regulation within 2% of setpoint
Dashboard refresh ≥ 5 Hz live
Total budget ≤ $3,000 across 4 PCBs
INTRO & PROBLEM
02 / 09
01 · INTRO & PROBLEM
Notes: PROBLEM & OBJECTIVES — Kaushik, ~45–55 s. Hit the safety stakes (42 V, 100+ A on a short), then the commercial gap (Orion costs $1,200 and won't expose telemetry), then transition into the five quantitative targets that defined the project from day one.

## Slide 3
The testbench splits into three domains linked by USB CDC and a QWebChannel software bridge.
Battery Unit
10s1p Molicel P42A pack
BMS PCB (BQ76930 + STM32)
40 A solid-state pack breaker
Testbench
E-Load PCB (DAC + op-amp + MOSFETs)
Power board (LM76005 buck stages)
Cell emulator for safe bring-up
Operator Station
PyQt6 desktop application
Three.js 3D cell-stack scene
Jetson AGX Orin host platform
10 A
USB CDC
USB CDC virtual COM at 115200 baud · QWebChannel bridges Python → JavaScript at 10 Hz
SYSTEM OVERVIEW
03 / 09
02 · SYSTEM OVERVIEW
Notes: ARCHITECTURE — Kaushik, ~45–55 s. Walk left to right: Battery Unit holds the pack and BMS, Testbench holds the E-Load and support boards, Operator Station runs the dashboard. Two USB cables and one software bridge — that's the whole interconnect. Hand off to Christian for the E-Load slide.

## Slide 4
The BQ76930 AFE opens the pack breaker in 70 µs under short circuit — hardware-enforced, independent of firmware state.
10 cell taps
VC1…VC10
BQ76930 AFE
14-bit ADC, OV/UV/SCD
STM32F303
I²C @ 400 kHz, DMA
USB CDC
115200 baud, 10 Hz
DSG pin
→ 40 A relay opens on SCD
What this buys you
Autonomous protection fires even if firmware is mid-reset or stuck.
1.2 mV ADC resolution from a calibrated 14-bit per-cell ADC.
100-byte telemetry frame with CRC-16 over USB CDC every 100 ms.
Source: BQ76930 datasheet (Rev. H), Texas Instruments
PROTECTION
04 / 09
03 · PROTECTION
Notes: BMS HARDWARE — Kaushik, ~50–60 s. Anchor on the BQ76930 — explain that hardware protection means the pack is safe even if the STM32 is mid-reset. Walk through the signal chain. Don't read the right-hand callouts; just gesture and let the audience read while you speak. Hand off to Christian.

## Slide 5
A 12-bit DAC and AD8630 op-amp close the feedback loop that holds 10 A discharge within 2 % across the 30–42 V pack range.
STM32
set-point cmd
MCP4725
12-bit DAC
AD8630
rail-to-rail op-amp
IRFP250N
144 Ω × 4 shunt
0.01 Ω shunt
feedback
Measured performance
1 A at 36 V sink validated across 4×144Ω paralleled channels with 0.1 A DAC resolution.
10 W power resistors (post-redesign) with IRFP250N MOSFETs sharing dissipation across the bank.
NTC thermistor drives PWM fan control with a 70 °C cutoff for thermal safety.
Source: E-Load bring-up data, EE 175AB test logs, May 2026
LOAD CONTROL
05 / 09
04 · LOAD CONTROL
Notes: E-LOAD — Christian, ~55–65 s. Explain the feedback loop: DAC sets the reference, op-amp drives MOSFET gates until the shunt voltage matches. Mention the thermal margin briefly. Hand off to Nick for software.

## Slide 6
Three software layers stream 10 Hz telemetry from STM32 firmware to a Three.js scene with no network stack.
Layer 1 — STM32 Firmware (C / HAL)
DMA-backed I²C polling · 100-byte CRC-16 framed telemetry · ALERT interrupt for sub-cycle faults
Layer 2 — Python Backend (PyQt6)
QThread per CDC port · auto-reconnect on USB drop · QWebChannel exposes telemetry object to JS
Layer 3 — Three.js Frontend
10 cylindrical meshes (2×5) · green→yellow→red emissive mapping · GSAP fault state transitions
Why this stack
USB CDC over CAN removes external transceivers and adapters.
Qt WebEngine over Electron eliminates CORS and a 200 MB Chromium binary.
STM32 over Pi Zero delivers 100 ms USB frames with no scheduler jitter.
06 · SOFTWARE STACK
SOFTWARE STACK
06 / 09
Notes: SOFTWARE — Nick, ~50–60 s. Walk top-down: firmware packs the frame, Python decodes and exposes it via QWebChannel, Three.js renders the 3D cell stack. The right-hand callouts justify each architectural decision — pick one or two, don't read all three.

## Slide 7
All five design objectives were met — cell-voltage error and dashboard rate were 2× better than spec.
Objective | Target | Measured | Margin
Cell voltage error | ± 20 mV | ± 10 mV | 2× better
Breaker response (SCD) | ≤ 5 ms | Opens on SCD | 100% success
E-Load regulation | ≤ 2 % | 1.5 % | within spec
Dashboard refresh | ≥ 5 Hz | 10 Hz steady | 2× better
Total system cost | ≤ $3,000 | $2,966 | 99 % of budget
Headline: every quantitative spec met — and the system shipped at $2,966, just inside the $3,000 ceiling.
06 · RESULTS
RESULTS
07 / 09
Notes: RESULTS — Nick → Kaushik, ~45 s. Read the headline: all five met, three exceeded by 2× or more. Point at the 70 µs breaker line and the $966 cost line specifically. Hand back to Kaushik to close.

## Slide 8
07 · CONCLUSIONS
Three takeaways from the build.
01
End-to-end works
Pack monitoring, breaker protection, programmable load, and 10 Hz dashboard meet every quantitative spec — at 99% of the $3,000 ceiling.
02
USB beats CAN here
USB CDC removed transceivers, cabling, and the Pi Zero from the BOM while preserving 100 ms frame timing with no scheduler jitter.
03
Buy the right resistor
The 1 W → 10 W power-resistor redesign was the single biggest schedule risk. Spec dissipation headroom before layout, not after.
CONCLUSIONS
07 / 09
Notes: CONCLUSIONS — Kaushik, ~35–45 s. Hit the three numbered takeaways. Then: 'We're happy to take questions.' DO NOT advance off this slide — it stays on screen during Q&A.

## Slide 9
[1] Texas Instruments, “BQ76930 3-Series to 15-Series Cell Battery Monitor and Protector Datasheet,” Rev. H, 2021.
[2] STMicroelectronics, “RM0316 — STM32F303 Reference Manual,” Rev. 9, 2022.
[3] Molicel, “INR-21700-P42A Lithium-Ion Cell Datasheet,” Rev. 1.0, 2019.
[4] IPC, IPC-2221B Generic Standard on Printed Board Design, 2012.
[5] NXP Semiconductors, “UM10204 I²C-bus Specification and User Manual,” Rev. 7.0, 2021.
[6] IEC, IEC 62133-2 Secondary Cells and Batteries Containing Alkaline or Other Non-Acid Electrolytes — Safety Requirements, 2nd ed., 2017.
[7] USB-IF, Universal Serial Bus Specification, Rev. 2.0, 2000.
[8] Ewert Energy Systems, “Orion BMS 2 Product Documentation,” 2024.
08 · REFERENCES
References
REFERENCES
09 / 09
Notes: REFERENCES — Do not flip to this during the talk. It exists for the rubric and for the audience after the session.