## Slide 1
EE 175AB Senior Design · ENGR 181W Technical Communication
Battery Management System
A 10-cell lithium-ion pack with a custom programmable
electronic load and a PyQt6 desktop dashboard.
Kaushik Vada · Nicholas Poon · Christian Kim
University of California, Riverside · Department of Electrical Engineering · June 1, 2026
Project team also includes Connor Stewart (architecture & BMS schematic). Advised by Dr. Roman Chomko.
Notes: [Kaushik, 10s] Welcome — we're presenting the Battery Management System we built for EE 175AB. It's a 10-cell lithium-ion pack with a programmable electronic load and a PyQt6 desktop dashboard. I'll cover the problem, Nick will walk through hardware, Christian will cover the E-Load and our validation, and I'll close with results and future work. Connor Stewart was our fourth team member but is not presenting today.

## Slide 2
Kaushik · Problem & objectives
Battery Management System · EE 175AB / ENGR 181W 2 / 9
Off-the-shelf BMS units cost $800–$1,680 and lock telemetry behind
proprietary software — none expose per-cell data to a custom application.
Cost
Orion BMS 2 sits at $820–$1,680 and requires its proprietary configurator.
Visibility
Commercial units don't expose per-cell voltage over a standard USB serial port.
Safety
A 10s pack at 42 V stores 151 Wh — fault response has to be hardware-enforced, not firmware-timed.
Design objectives
Cell voltage error
≤ ± 20 mV
Pack current error
≤ ± 10 mA
E-Load regulation
controlled sink at 36 V
Telemetry link
USB CDC @ 115200 baud
Fan control
0–100 % PWM, auto + manual
Pack budget
≤ $3,000 across 3 PCBs
Sources: Ewert Energy Systems, Orion BMS 2 product documentation (2024); EE 175AB Final Report §2.1, §3.5.
Notes: [Kaushik, 75s] The problem we set out to solve: commercial BMS units like the Orion BMS 2 start around $820 and lock all telemetry behind proprietary software — there's no way to stream per-cell voltage into a custom Python application. That matters because a 10-cell lithium pack at 42 volts stores 151 watt-hours; fault response has to be hardware-enforced, not firmware-timed. So we set six design objectives: cell voltage accuracy within ±20 mV, pack current within ±10 mA, a controllable E-Load sinking current at 36 V, USB CDC telemetry at 115200 baud, PWM fan control, and a total project budget under three thousand dollars.

## Slide 3
Nick · System architecture
Battery Management System · EE 175AB / ENGR 181W 3 / 9
Three subsystems, three custom PCBs, one USB CDC bridge to the dashboard.
Battery Unit
Nick · Connor
10s1p Molicel P42A pack
10-cell, 36 V nominal, 42 V full
Custom BMS PCB
BQ76930 AFE + STM32F303RCT6
Two-stage main breaker (relay)
Active-cooling enclosure (2× fans)
Testbench Ecosystem
Christian · Nick · Connor
Custom E-Load PCB
12-bit DAC + AD8630 + MOSFETs
36 V / 1 A controllable sink
Cell Emulator PCB
Voltage dividers + NTC pots
Bring-up without live cells
Operator Station
Kaushik · Christian · Nick
PyQt6 desktop application
QWebChannel → Qt WebEngine UI
Three.js 3D cell stack
BMS, E-Load, telemetry tabs
Cross-platform: Windows + macOS
Runs entirely on the host laptop
Data path
Battery Unit — SYSBUS+/− DC bus → E-Load XT60 · Both STM32s — USB CDC virtual COM @ 115200 baud → Operator Station
Source: EE 175AB Final Report §5.1 System Architecture, §5.2 Hardware Architecture.
Notes: [Nick, 45s] The system splits into three subsystems, each backed by a custom PCB. Connor and I built the Battery Unit — the 10-cell Molicel pack, BMS board, and breaker. Christian led the E-Load, and Connor built the Cell Emulator so we could bring everything up without live cells. Kaushik wrote the operator dashboard. Power flows from the pack out the SYSBUS terminals to the E-Load, and both STM32s talk to the host laptop over standard USB CDC at 115200 baud — no custom drivers needed.

## Slide 4
Nick · BMS hardware
Battery Management System · EE 175AB / ENGR 181W 4 / 9
BQ76930 AFE handles cell sensing and fault flagging; an electromechanical
relay isolates the pack under fault — independent of firmware state.
10 cell taps
VC1 … VC10
BQ76930 AFE
14-bit ADC · OV/UV/OC/SCD
STM32F303RC
I²C @ 400 kHz · DMA
USB CDC
115200 baud · 10 Hz
Breaker
DSG output → electromechanical relay opens the SYSBUS path on OV / UV / OC / SCD faults. MOSFET-based breaker was swapped for a mechanical relay during bring-up after surplus FETs showed depletion-mode behavior (Test 3, iter. 3).
What this buys us
Hardware-enforced safety
BQ76930 raises ALERT and drives DSG low even if firmware is mid-reset — the relay opens unconditionally.
Per-cell visibility
All 10 cell voltages and 10 thermistor channels stream live to the dashboard; measured ±10 mV.
Always-on diagnostics
GND-ALWAYS-ON keeps the MCU and USB alive in a fault state for diagnosis and fan control.
Sources: Texas Instruments, BQ76930 datasheet Rev. G; EE 175AB Final Report §5.2.1, §8.2.12, §11.3.
Notes: [Nick, 60s] The BMS board centers on the BQ76930 analog front-end, which monitors all ten cells and runs the protection thresholds in hardware. The STM32 talks to it over I²C and streams structured frames out USB CDC at 10 Hz. Originally we used back-to-back MOSFETs for the main breaker, but the surplus parts we got behaved in depletion mode instead of enhancement mode, so we swapped the breaker for an electromechanical relay sourced from the makerspace. That's a tradeoff — we lost directional charge/discharge control, but the relay is unconditionally reliable. The GND-ALWAYS-ON topology is important: even when the breaker opens, the MCU and USB stay alive, so we can still cool the pack and diagnose what tripped.

## Slide 5
Christian · E-Load subsystem
Battery Management System · EE 175AB / ENGR 181W 5 / 9
12-bit DAC and an AD8630 op-amp close a feedback loop that sinks
controlled current at 36 V — derated to 1 A after a full redesign.
STM32F303
I²C set-point
MCP4725 DAC
12-bit, I²C
AD8630 op-amp
rail-to-rail
2× IRFP250N
MOSFET sink
4× 144 Ω shunt
current feedback
feedback to op-amp
Why the spec changed
Initial bring-up triggered a visible arc at the XT60 and destroyed the TVS diode. The original 0.5 W resistor bank was inadequate for the target current. Nick redesigned the load bank with 10 W-rated parts, and the target was lowered from 5 A to 1 A at 36 V (Test 6, iter. 2).
Measured performance
1 A at 36 V
Sustained controlled-current sink, no thermal shutdown, no component failure.
Linear DAC mapping
Current scales linearly with the DAC code from 0 to full scale.
Thermal control
NTC + open-loop PWM fan ramps from 20 % at 25 °C to 100 % at 45 °C.
Sources: EE 175AB Final Report §5.2.2, §8.1.13, §11.6 (E-Load redesign + current-sink validation).
Notes: [Christian, 60s] The E-Load is a closed-loop current sink. The STM32 sets a DAC code, the MCP4725 outputs a reference voltage, the AD8630 op-amp drives the gates of two paralleled MOSFETs, and the voltage across four paralleled 144-ohm shunts is fed back to close the loop. The first iteration was painful — when we applied the load, the XT60 arced and the TVS diode sacrificed itself. The 0.5-watt resistor bank we'd specified was wildly under-rated. Nick completely redesigned the load bank using 10-watt resistors and we lowered the target from 5 amps to 1 amp at 36 volts. After the redesign we got clean linear DAC-to-current behavior and the thermistor-driven fan keeps the MOSFETs in the safe range.

## Slide 6
Kaushik · Software stack
Battery Management System · EE 175AB / ENGR 181W 6 / 9
Three software layers stream live telemetry from STM32 firmware to a
Three.js scene — no HTTP, no network, all on the operator's laptop.
1
STM32 firmware (C / HAL)
I²C polling of BQ76930 over DMA · 100-byte CRC-bounded telemetry frames · USB CDC at 115200 baud · ALERT IRQ for sub-cycle faults.
2
Python backend (PyQt6)
PySerial worker per virtual COM port · auto-reconnect on USB drop · telemetry parser builds full snapshots before forwarding · QWebChannel bridges Python → JavaScript.
3
Qt WebEngine frontend
Local HTML / JS hosted in WebEngine · BMS tab (10-cell grid + Three.js), E-Load tab (DAC slider + Three.js), shared Three.js + GSAP layer for transitions.
Why this stack
USB CDC over CAN
No external transceivers or proprietary adapters; readable from any serial terminal.
PyQt6 over Electron
WebEngine gives us Three.js and GSAP without shipping Chromium and a network stack.
STM32 on both boards
Single toolchain, shared peripheral setup, drop-in replacement on either board.
Source: EE 175AB Final Report §5.3 Software Architecture, §5.4 Rationale and Alternatives.
Notes: [Kaushik, 60s] The software splits into three layers. At the bottom, the STM32 firmware polls the BQ76930 over I²C, packages telemetry into CRC-bounded frames, and pushes them out USB CDC. In the middle, a PyQt6 backend reads the serial port, parses the frames into full snapshots, and exposes them to JavaScript via QWebChannel. At the top, Qt WebEngine hosts the actual UI as local HTML and JavaScript — three tabs for BMS, E-Load, and shared Three.js views. The reason this stack works is that everything runs on one machine with no network roundtrip. QWebChannel gives JavaScript direct access to live hardware data without a server, and using USB CDC means any standard serial terminal can read the same frames for debugging.

## Slide 7
Christian · Validation & results
Battery Management System · EE 175AB / ENGR 181W 7 / 9
Nine test cases run, all passed — the BMS powered an NVIDIA Jetson
Orin Nano running a 1.3 B-parameter AI model end to end.
Test | What we validated | Iter. | Outcome
1 — I²C bring-up | BQ76930 detection · register init · CRC fallback | 3 | Pass after SHIP-mode + USB ESD fixes
2 — Cell telemetry | All 10 cell voltages + 10 thermistors | 2 | Pass after harness direct-solder
3 — Breaker logic | DSG / CHG response · fault trip | 3 | Pass after MOSFET → relay swap
4 — Fan control | Auto + manual PWM · 25 °C → 45 °C ramp | 2 | Pass after tachometer deprecated
5 — USB host link | CDC enumeration on Windows + macOS | 3 | Pass after enumeration + ESD fix
6 — E-Load sink | Linear DAC → current at 36 V / 1 A | 2 | Pass after full load redesign
7 — Thermistor | End-to-end thermal tracking | 1 | Pass first iteration
8 — Cell balancing | Live AA pack · 200 mV drop in 10 min | 2 | Pass after harness rework
9 — Jetson Orin Nano | Boot + run 1.3 B parameter AI inference | 1 | Pass first iteration
± 10 mV
measured cell
voltage accuracy
$2,966
total project cost
across 3 PCBs
1.3 B
param AI model running
on BMS-powered Jetson
Source: EE 175AB Final Report §11 Test Report (Tests 1–9); §3.5 Budget & Cost.
Notes: [Christian, 75s] We ran nine test cases against the full system. Most of them passed in two or three iterations because of the bring-up issues — Test 1 needed a SHIP-mode wakeup pulse and a USB ESD diode workaround before the BQ76930 would respond. Test 3, the breaker, took three iterations and ended in the MOSFET-to-relay swap. Test 6, the E-Load, is the redesign we just walked through. The standout result is Test 9: we powered an NVIDIA Jetson Orin Nano directly off the SYSBUS terminals and ran a 1.3-billion parameter AI inference workload through it with no faults triggered. That's the headline — the pack and the BMS are stable enough to power a real compute load, not just bench equipment. End to end, ±10 mV cell accuracy, $2,966 in total project cost.

## Slide 8
Battery Management System · EE 175AB / ENGR 181W 8 / 9
Conclusion
Future work
1
Full-stack senior design works.
Custom PCBs, custom firmware, custom desktop app — all integrated, all observable from one dashboard.
2
Safety is hardware-enforced.
BQ76930 + electromechanical relay isolate the pack on fault regardless of firmware state; GND-ALWAYS-ON keeps diagnostics alive.
3
Real compute workload validated.
The pack powered an NVIDIA Jetson Orin Nano running a 1.3 B-parameter AI model end-to-end without tripping protection.
BMS
Integrate the relay onto the PCB · USB isolation between BMS and E-Load · backup over-temperature comparator · charger harness redesign.
E-Load
Scale beyond 1 A · proper op-amp feedback filtering · correct shunt selection · constant-power and constant-resistance modes.
Dashboard
Hardware-in-the-loop replay mode from stored telemetry · bidirectional USB hot-plug · LCD module for headless monitoring.
Notes: [Kaushik, 45s] To wrap up: we built a complete senior-design BMS with custom hardware, custom firmware, and a custom desktop dashboard, and we got all three layers to talk to each other reliably. Safety is hardware-enforced — the BQ76930 and the relay can isolate the pack without any firmware involvement. And we proved the system is solid enough to power a real compute workload: an NVIDIA Jetson Orin Nano running a 1.3 billion parameter AI model. Future work is straightforward: redesign the breaker as an integrated relay on the board, scale the E-Load past one amp, and add a hardware-in-the-loop replay mode to the dashboard. Thank you — we'd be glad to take questions.

## Slide 9
Team · Acknowledgments & references
Battery Management System · EE 175AB / ENGR 181W 9 / 9
Acknowledgments
Key references
Dr. Roman Chomko
EE 175A/B faculty advisor — architecture review, documentation rigor, design oversight across both quarters.
Mehrnoosh Ayazi
Lab session support and weekly bring-up guidance through the rework phases.
Manglai Zhou
Makerspace access, lithium-cell storage, and the relay that replaced the failed breaker MOSFETs.
Connor Stewart
Fourth team member — overall hardware architecture, BMS schematic logic, Cell Emulator PCB.
[1] Texas Instruments, BQ769x0 3-Series to 15-Series Cell Battery Monitor Family, Datasheet SLUSBK2G, Rev. G, May 2016.
[2] STMicroelectronics, RM0316 — STM32F303xB/C/D/E Reference Manual, Rev. 10, 2020.
[3] Analog Devices, AD8628/AD8629/AD8630 Zero-Drift Op-Amp Datasheet, Rev. K, 2023.
[4] Microchip Technology, MCP4725 12-Bit DAC with EEPROM, Datasheet DS20002039F, 2023.
[5] Molicel, INR-21700-P42A Lithium-Ion Cell Datasheet, Rev. 1.0, 2019.
[6] IPC, IPC-2221B Generic Standard on Printed Board Design, 2012.
[7] NXP Semiconductors, UM10204 I²C-Bus Specification, Rev. 7.0, 2021.
[8] USB-IF, Universal Serial Bus Specification, Rev. 2.0, 2000.
[9] Ewert Energy Systems, Orion BMS 2 Product Documentation, 2024.
Contact: vvada002@ucr.edu · npoon010@ucr.edu · ckim331@ucr.edu · cstew032@ucr.edu
Notes: [Team, 15s buffer] Thanks again to Dr. Chomko, Mehrnoosh Ayazi, and Manglai Zhou for support throughout the project, and to Connor Stewart, our fourth team member. Full references and design files are linked in the report.