## Slide 1
Assignment: Caches
Instructor: Elaheh Sadredini
elaheh@cs.ucr.edu
University of California, Riverside

## Slide 2: Grading (total 4 points)
Question 1: 1 point
  Part B: 0.4 points, Part C: 0.4 points
Question 2: 1.2 point
  Each part 0.4 point
Question 3: 1.4 point
  Part A, B, C each 0.4 point, Part D 0.2 point
Question 4: 0.6 point
  Each part 0.2 point

## Slide 3: Review: What goes into and out from a cache?
Processor
Memory
Cache

## Slide 4: What goes into and out from a cache?
Processor
Memory
Address
Data In
Data Out
Address
Data Out
Data In
Cache
Tag
Data
Tag
Data
Tag
Data
Tag
Data
=

## Slide 5: What goes into and out from a cache?
Processor
Memory
Address
Data In
Data Out
Address
Data Out
Data In
Cache
Tag
Data
Tag
Data
Tag
Data
Tag
Data
=
lw
Hit
Load – hit in cache

## Slide 6: What goes into and out from a cache?
Processor
Memory
Address
Data In
Data Out
Address
Data Out
Data In
Cache
Tag
Data
Tag
Data
Tag
Data
Tag
Data
=
lw
Miss
Load – miss in cache

## Slide 7: Question 1: Diagram of the Caches
Draw a diagram of the following caches (note: answer for part A is provided. Follow the same structure for part B and C)
Direct-mapped, cache capacity = 64 cache line, cache line size = 8-byte, word size = 4-byte, write strategy: write through
Fully-associative, cache capacity = 256 cache line, cache line size = 16-byte, word size = 4-byte, write strategy: write back
4-way set-associative, cache capacity = 4096 cache line, cache line size = 64-byte, word size = 4-byte, write strategy: write back
Tag
Data
V
Data
Tag
Data
V
Data
Tag
Data
V
Data
64

## Slide 8: Answer

## Slide 9: Question 2: How are the bits used for addressing?
Determine which bits in a 32-bit address are used for selecting the byte (B), selecting the word (W), indexing the cache (I), and the cache tag (T), for each of the following caches:
Direct-mapped, cache capacity = 64 cache line, cache line size = 8-byte, word size = 4-byte
Fully-associative, cache capacity = 256 cache line, cache line size = 16-byte, word size = 4-byte
4-way set-associative, cache capacity = 4096 cache line, cache line size = 64-byte, word size = 4-byte
Note: cache capacity represents the maximum number of cache blocks (or cache lines) that can fit in the cache

## Slide 10: Answer

## Slide 11: Question 3: How much overhead for the caches?
Calculate the number of bits used for actual data and overhead (i.e., tag, valid bit, dirty bit) for each of the following caches
Direct-mapped, cache capacity = 64 cache line, cache line size = 8-byte, word size = 4-byte, write strategy: write through
Fully-associative, cache capacity = 256 cache line, cache line size = 16-byte, word size = 4-byte, write strategy: write back
4-way set-associative, cache capacity = 4096 cache line, cache line size = 64-byte, word size = 4-byte, write strategy: write back
D. How the cache line size affect the overhead?

## Slide 12: Answer

## Slide 13: Question 4: Average Memory Access Time
Consider the processor (on right) with two-level cache hierarchy. Suppose that 65% of benchmark A’s instructions are accessed from the L1 cache, whereas the rest come from the L2 cache.
What is the average access time for memory instructions in the benchmark
If we change the L1 cache to be 4-way set associative we increase its flexibility and find that 85% of the instructions are now accessed from the L1. What is the average access time for memory instructions in the benchmark now?
What is the speedup for changing the L1?
c
L1
L2
DRAM
Direct Mapped
Size: 64 kB
Latency: 1 cycle
8-way assoc.
Size: 256 kB
Latency: 5 cycles

## Slide 14: Answer