## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Boolean Functions

## Slide 4: Levels of Abstraction for Computer System
Application S/W
Operating System
Instruction set Architecture (ISA)
Microarchitecture (ALU,controllers ,cache…
Programs
Programs
(drivers,…)
Logic (adders,memories,…)
Gates, digital circuits
Analog Circuits
Devices (transistors, diodes, . . .)
Physics (Electrons)
Assembly language
L1
L2
L3
L4
L8
L9
L10
L1, L2 - application programmers levels
L3, L2,L4 – system programmers levels
Programs
S/W
H/W
H/W
L5
L6
L7

## Slide 5: Boolean Algebra Theorems
X+0=X | X·1=X | Identities
X+1=1 | X·0= 0 | 
X+X=X | X·X=X | Idempotency
~(~X)=X |  | Involution
X+~X=1 |  | Complements
X+Y= Y+X | X·Y= Y·X | Commutativity
(X+Y)+Z=X+(Y+Z) | (X·Y) ·Z=X·(Y·Z) | Associativity
X·Y+X·Z=X·(Y+Z) | (X+Y)·(X+Z)=X+Y·Z | Distributivity
X+X·Y=X | X·(X+Y)=X | Covering
X·Y+X·~Y=X | (X+Y)(X+~Y)=X | Combining
X·Y+~X·Z+Y·Z=X·Y+~X·Z | (X+Y)·(~X+Z)·(Y+Z)=(X+Y)(~X+Z) | 

## Slide 6: Boolean Algebra Theorems
X+X+. . . +X =X | Generalized Idempotency
X·X· . . . ·X =X | 
X1 +X2 + . . .+Xn = ~X1·~X2· . . . ·~Xn | DeMorgan’s Theorem
X1·X2· . . . ·Xn = ~X1 +~X2 + . . .+~Xn | 
f (X1,X2 …Xn, +,,) = f(X1,X2 …Xn, ,+) | Generalized DeMorgan’s Theorem

## Slide 7: Representation of Boolean Functions
f(x1,x2, . . .xn)
xi = {0,1}; X = {x1,x2 . . .xn}  Bn
f(X) : Bn  B; B={0,1}
x1,x2 . . . are variables
x1, x1, x2, x2 , . . . are literals
each vertex of Bn is mapped to 0 or 1
the onset of f is {x|f(x)=1} =f 1
the offset of f is {x|f(x)=0} =f 0
if f 1 = Bn, f is the tautology, i.e. f  1
if f 0 = Bn (f 1 = ), f is not satisfiable
if f(x) = g(x) for all x Bn, then f and g are equivalent
Write simply f instead of f 1

## Slide 8: Truth Tables (1)
The truth table for n-variable function f(x1, x2, . . . xn) is a table of its values at each of 2n vertices of Bn.
  There are 2n vertices in input space Bn (2n rows in the truth table).There are 2^2^n distinct logic functions. Each subset of vertices is a distinct logic function: f  Bn Intractable for large n, but canonical (sole).
Canonical means if two functions are the same, canonical representation of each one is isomorphic.
x1x2 . . . xn | f(x1,x2, . . . xn)
0 0 . . . 0 0 | 0
0 0 . . . 0 1 | 1
. . . | . . .
1 1 . . . 1 1 | 1

## Slide 9: Truth Tables (2)
y = f(x1,x2,x3) = x3 (2-cube)
x1
x3
000
x2
001
010
011
100
110
111
101
x1x2 x3 | f(x1,x2,x3)
0 0 0 | 0
0 0 1 | 1
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 0
1 1 1 | 1

## Slide 10: Algebraic Representation of Logic Function
A product term: a single literal or a logical product (conjunction) of two or more literals
A sum-of-product (SOP): a logical sum of product terms (disjunction)
A sum term: a single literal or a logical sum of two or more literals
A product-of-sums (POS): a logical product of sum terms
A normal term: no variable appears more than once
A minterm: normal product term with n literals (n-variable function)
A maxterm: normal sum term with n literals.

## Slide 11: Logical Expressions. Shannon’s Expansion
Lemma:
Any boolean function f(x1,x2,…xn) can be represented thus: f(x1,x2,…xn) = ~xi·f(x1,x2,…0,…xn)+ xi·f(x1,x2…1,…xn).
Proof: substitution
  Let xi =0, then f = f(x1,x2…0,…xn).
  Let xi=1, then f = f(x1,x2…1,…xn)
The decomposition f by all variables in series:
The decomposition by x1: f(x1,x2,…xn) = ~x1·f(0,x2,…xn)+x1·f(1,x2,…xn).
The decomposition by x1, x2: f(x1,x2,…xn)=~x1·~x2 ·f(0,0,x3…xn) + ~x1·x2·f(0,1,x3,…xn) + +x1·~x2·f(1,0,x3,…xn) + x1·x2·f(1,1,x3,…xn).
The decomposition by all variables:
f(x1,x2,…xn)=~x1·~x2…~xn· f(0,0,…0) + ~x1·~x2 …~xn-1 xn
·f(0,0,…1) +~ x1·~x2…xn-1~xn· f(0,0,…1,0) +… + x1·x2 …xn·f(1,1,…1).
Only minterms are remained in formulation.

## Slide 12: Canonical Forms of Representation Functions (DNF and CNF)
Canonical Sum of Products: sum of the minterms corresponding to 1-values of function.
f(x1,x2, . . .xn) =  (1  2…  n) x11 x2 2…xn n,
  where (1  2…  n)f1 xii =~xi, if i =0; xii =xi, if i =1;
Canonical Product of Sums: product of the maxterm corresponding to
  0-values of function.
  f = (1, 2,. . . n) f1 x11 x22 . . . Xnn =
  = (1, 2,. . . n)  f1 (x1~1+ x2 ~2 + . . . + xn ~n) 
  f =  (1, 2,. .. n)  f0 (x1~1+ x2 ~2 + . . . + xn ~n)
Canonical forms are unique.

## Slide 13: Cubical Representation (n-Cube)
B0
f(x1) B1
f(x1,x2) B2
f(x1,x2,x3 ) B3
x1
x1
x3
000
x2
001
010
011
100
110
111
101
x1

## Slide 14: n-Cube (2)
f(x1,x2,x3,x4)
B4
K-cube is the corresponding
product of n-k literals
0000
0001
0011
0100
0110
0110
0101
0111
1011
1100
1110
1100
1101
1000
x2
x3
x4
x1=0
x1=1
x3
x1
x2
x4
0000
1000
0010
1010
0011
1011
1001
0100
0110
1100
1110
0111
1111
1101
0101
0111

## Slide 15: Cubes
A subcube is a set of exactly 2m adjacent vertices of a cube Bn.
The product of literals is a cube.
If product of literals C  f , C is a subcube, then C is implicant of f.
If C has m literals, then cube |C| has 2n-m vertices.1-cube covers two vertices of Bn and has n-1 literals. 0-cube (vertex) is minterm of f (has n literals).

## Slide 16: Example
x1x2 x3 | f(x1,x2,x3)
0 0 0 | 1
0 0 1 | 1
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 0
1 1 1 | 1
Canonical sum:
y= K0+ K1 + K3 + K5 + K7=
= x1·x2·x3 +x1·x2·x3 + x1·x2·x3 + x1·x2·x3 + x1·x2·x3
Canonical product:
y= D2·D4·D6=
= (x1 + x2 + x3)·(x1 + x2 + x3)·(x1+ x2+ x3)
Ki is minterm
Dj is maxterm

## Slide 17: Representation of Boolean Functions in Polynomial Form
Theorem: Any Boolean function can be represented by the polynomial form:
Proof:
  Get SOP (canonical form)
  Substitute xi for 1 xi
  Instead of “+”, put “”
  Perform equivalence conversions.
Example:
y=x1· x2· x3 + x1· x2· x3+ x1· x2·x3 + x1·x2·x3+x1·x2·x3 =
=(1x1)(1x2)(1x3)  (1x1)(1x2)x3  (1x1)x2x3 x1(1x2)x3 x1x2x3
=1x1x2x1x2x1x3  x2x3  x1x2x3

## Slide 18: Representation of Boolean Functions in Polynomial Form (2)
The coefficients of function polynomial decomposition:
  f(0,0,0) = 1 = a0  a0=1;
  f(0,0,1) = 1 = a0a3 = 1  a3  a3=0;
  f(0,1,0) = 0 = a0a2 =1 a2  a2=1;
  f(0,1,1) = 1 = a0 a2  a3 a23= 110a23  a23=1;
  f(1,0,0) = 0 = a0a1=1a1 a1=1;
  f(1,0,1) = 1 = a0a1a3a13=110a13 a13=1;
  f(1,1,0) = 0 = a0a1a2a12=111a12 a12=1;
  f(1,1,1) = 1 = a0a1 a2a3  a12a13a23a123=
  =1 1 1 0 1 1 1 a123 a123=1
From here:
  y = 1 x1 x2 x1x2 x1x3 x2x3  x1x2x3

## Slide 19: Functional Completeness
Post defined five classes of Boolean functions:
  “0”-preserving (or “False”-preserving) – Class 1 (C1)
f(0,0,…0) = 0. Example: Conjunction, Disjunction, etc.
  “1”-preserving (or “Тrue”-preserving) – Class 2 (C2)
f(1,1,…1) =1. Example: Conjunction, Disjunction, etc.
  Linear functions (or counting) - Class 3 (C3)
  f(x1,x2, . . .xn) = a0  a1x1 a2x2 . . .  anxn
Example: y = x1  x2
  Monotonous – Class 4 (C4)
The value of function does not decrease when the value of variable increases:
  Let (1 2… n)<(1,2…n), where i, j (0,1),
  then f(12… n)  f(12…n)
Example: Conjunction, Disjunction, etc.

## Slide 20: Functional Completeness (2)
x1 x2 x3 | f(x1,x2,x3)
0 0 0 | 1
0 0 1 | 1
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 0
1 1 1 | 0
Self-dual – Class 5 (C5) A function f(x1,x2…xn) is self-dual if its reading from top to bottom is the same as the complement of reading it from bottom to top (in the standard ordering of values for arguments). Example:
That is, a self-dual function obeys the
following condition: for every pair of
opposite values of arguments takes
opposite value.
In other words, for any (1,2, ... n)
f(1, 2,… n) = f(1, 2,… n)

## Slide 21: Functional Completeness (3)
These five classes have the following common property:
Applying operations of superposition and substitution within some class, we can obtain the functions that belong to the same class. These five classes are closed.
Theorem (Post's Functional Completeness Theorem):
A set N of Boolean functions is functionally complete if and only if for each of the five defined classes, there is a member of N which does not belong to that class.

## Slide 22: Functional Completeness (4)
It is necessary and sufficient:
  N should contain at least one non “0”-preserving function (NC1).
  N should contain at least one non “1”-preserving function (NC2).
  N should contain at least one non linear function (NC3).
  N should contain at least one non monotonous function (NC4).
  N should contain at least one non self-dual function (NC5)

## Slide 23: Examples of Bases
Basis: AND, OR, NOT
  Minimal bases:
  NAND
  NOR
  AND, XOR, Const.”1”
  Implication, NOT
  Implication, OR, const 0 (basis of Hilbert)
  Minimal basis contains maximum from 3 up 5 functions.

## Slide 24: Two-Variables Functions
00 | 01 | 10 | 11 | Formula | Function | C1 | C2 | C3 | C4 | C5
0 | 0 | 0 | 0 | y= 0 | Const.”0” | x |  | x | x | 
0 | 0 | 0 | 1 | y = x1x2 | AND | x | x |  | x | 
0 | 0 | 1 | 0 | y = x1 ~x2 | x1>x2 | x |  |  |  | 
0 | 0 | 1 | 1 | y = x1 | Variable x1 | x | x | x | x | x
0 | 1 | 0 | 0 | y = ~x1x2 | x1 <x2 | x |  |  |  | 
0 | 1 | 0 | 1 | y = x2 | Variable x2 | x | x | x |  | x
0 | 1 | 1 | 0 | y = x1  x2 | XOR | x |  | x |  | 
0 | 1 | 1 | 1 | y = x1 + x2 | OR | x | x |  | x | 
1 | 0 | 0 | 0 | y = x1 + x2 | NOR |  |  |  |  | 
1 | 0 | 0 | 1 | y =1 x1  x2 | XNOR |  | x | x |  | 
1 | 0 | 1 | 0 | y = x2 | NOT x2 |  |  | x |  | x
1 | 0 | 1 | 1 | y = x1 + ~x2 | Implication x2x1 |  | x |  |  | 
1 | 1 | 0 | 0 | y = x1 | NOT x1 |  |  | x |  | x
1 | 1 | 0 | 1 | y = ~x1 + x2 | Implication x1 x2 |  | x |  |  | 
1 | 1 | 1 | 0 | y = x1x2 | NAND |  |  |  |  | 
1 | 1 | 1 | 1 | y=1 | Const.”1” |  | x | x | x | 

## Slide 25: Binary Decision Diagrams
A Binary Decision Diagram (BDD) is a directed acyclic graph
  Graph: set of vertices connected by edges
  Directed: edges having direction
  Acyclic: no path in the graph can lead to a cycle
The size of a BDD is as big as the truth table:
  1 leaf per row
  Often abbreviated as DAG
  Many logic functions can be represented compactly - usually better than SOP’s.
Each vertex represents a decision on a variable
The value of the function is found at the leaves
Each path from root to leaf corresponds to a row in the truth table.

## Slide 26: Binary Decision Diagrams
f(x1, x2, x3) = ~x1~x2 + ~x1x2~x3 + x1x2~x3
0
1
1
0
0
1
0
1
0
1
0
1
x1
x2
x2
x3
x3
f(x1,x2,x3)
Root node
~(x2x3)
x2 ~x3
~x3
~x3
x3
x3
1
1
0
1
0
0
1
0
0
1
x1 x2 x3 | f(x1x2x3)
0 0 0 | 1
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 0

## Slide 27: ROBDDs – Reduced Ordered BDDs
Size of BDD critically dependent on variable ordering
ROBDD:
  Directed acyclic graph (DAG)
  One root node, two terminals 0, 1
  Each node, two children, and a variable
  Shannon co-factoring tree, except reduced and ordered (ROBDD)
  Reduced:
    Any node with two identical children is removed
    Two nodes with isomorphic BDD’s are merged
  Ordered:
    Co-factoring variables (splitting variables) always follow the same order along all paths.

## Slide 28: Transformation from BDD to ROBDD
1
x1
x2
x2
x3
f(x1,x2,x3)
~x2 + ~x3
x2 ~x3
~x3
~x3
x3
0
1
x1
x2
x2
f(x1,x2,x3)
~(x2x3)
x2 ~x3
~x3
0
x3
x 3
x3
f(x1, x2,x3) = ~x1~x2 + ~x1x2~x3 + x1x2~x3

## Slide 29: Reordering Variables
Root node
1
0
1
0
0
0
1
0
1
0
1
0
x2
x1
x1
x3
x3
f(x1,x2,x3)
~x1
~x3
x3
x3
1
1
0
1
1
0
1
0
0
1
x3
~x3
~x3
x2 x1 x3 | f(x1x2x3)
0 0 0 | 1
0 0 1 | 1
0 1 0 | 0
0 1 1 | 0
1 0 0 | 1
1 0 1 | 0
1 1 0 | 1
1 1 1 | 0

## Slide 30: Reordering Variables
x3
x2
x1
x3
f(x1,x2,x3)
~x3
~x1
~x3
x2
x1
x1
x3
x3
f(x1,x2,x3)
~x1x3
~x3
x3
~x3
0
1
1
0
Y=x2?(x3?0:1):(x1?0:1) (C) y = ~x1·~x2 + x2·~x3

## Slide 31: Examples
a
c
c
b
0
1
a
b
c
c
1
b
0
Ordered Not ordered
order – a,c,b

## Slide 32: ROBDDs
ROBDDs are canonical for a given variable order
ROBDD are more compact than other canonical forms
ROBDD size depends on the variable order
F=x1x2x3x4
x1
x2
x2
x3
x3
x4
x4
1
0

## Slide 33: Shannon Cofactors
f(x1,x2, . . . xn) = ~xif~xi(x1,x2 . . .xi-1, xi+1 . . .xn) + xi fxi (x1,x2 . . .xi-1, xi+1 …xn)
f~xi,fxi - cofactors of f by literals ~xi and xi.
Cofactor (fx): the function that is obtained when substituting 1 for x in f.
BDD is a compressed Shannon co-factoring tree:
  f = v·fv + ~v·f~v
  Leafs are constants “0” and “1”
  Each node is written as a triple: f = (v,g,h) where g=fv , h=f~v. v is a top variable of f.
  This triple is read as: f = if v then g else h = ite (v,g,h) = v·g+~v·h.
  a multiplexer can be put into compliance to each node.

## Slide 34: Cofactors
MUX
f
v
h
g
0
1
v
h
g
0
1
x
x
a
b
c
0
1
0
1
f = ~vh+vg
f=0 f=1
f=x
f=(a+b)c
f=c
f=bc

## Slide 35: Example
a b c d | y
0 0 0 0 | 0
0 0 0 1 | 0
0 0 1 0 | 1
0 0 1 1 | 1
0 1 0 0 | 0
0 1 0 1 | 1
0 1 1 0 | 1
0 1 1 1 | 1
a b c d | y
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 0
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
Y = f(a,b,c,d)

## Slide 36: Example
b
c
a
b
b
c
c
d
1
0
c+bd
c+d
d
a
c
d
b
1
0
b
bd
c+bd
f=ab+~ac+b~cd
Two different orderings, the same function

## Slide 37: Advantages of ROBDDs
Canonical form representation for Boolean functions (for a given order of variables)
Substantially more compact than CNF or DNF
Efficient manipulation of BDD’s
Easy to solve some important problems:
  Tautology checking: just check if BDD is identical to function
  Identity checking
  Satisfiability: look for a path from root to leaf
  Use small memory area

## Slide 38: Summary
BDDs
  Very efficient data structure
  Efficient manipulation routines
  A few important functions don’t come out well
  Variable order can have high impact on size
Application in many areas of CAD:
  Hardware verification
  Logic synthesis