## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Synthesis of Synchronous FSM

## Slide 4: Structural Synthesis of FSM
Abstract FSM is the model of algorithm of some transformation of information. Structural FSM is the model of device, that performs this transformation.
FSM
(k state-
variables)
m inputs
n outputs
Abstract
FSM
X
Y

## Slide 5: Clocked Synchronous FSM Structure (Mealy Machine)
General structure of a clocked synchronous FSM.
The state memory – is a set of flip-flops that store a current state of FSM.
The next state logic determines the next state of FSM:
St+1 = (St, Xt ).
The output logic determines the output function of FSM:
Yt =  (St , Xt).
Yt
Xt
State Memory
Output Logic
St
St+1
Clock
Excitation functions
Next State
Logic

## Slide 6: Clocked Synchronous FSM Structure (Moore Machine)
Xt
Next State
Logic
State Memory
Output Logic
St
St+1
Clock
Yt
St+1 = (St, Xt ); Yt =  (St)
Xt
Next State
Logic
State Memory
St
St+1
Clock
Yt
St+1 = (St, Xt ); Yt = St
Output coded
state assignment

## Slide 7: Mealy FSM with Pipelined Output
Outputs during one clock period depend on the state and input during the previous clock period.
Output Pipeline Register
Xt
Next State
Logic
State Register
Output Logic
St
St+1
Clock
Yt-1
Yt

## Slide 8: Classification of Flip-flops and Latches
Flip-flops and latches serve for storing one bit of information. It is the elementary Moore FSM, having two states.
Classification:
According to logic functionality
  RS, D, T, JK , etc
  Combined flip-flops
  Flip-flops with complex input logic.
According to the way of information writing
  Asynchronous (non-clocked)
  Synchronous (clocked) flip-flops.
Synchronous
  Level-sensitive (latches)
  Edge-triggered (flip-flops)
  Master/Slave (flip-flops):
Master-slave (two-stage flip-flops) and one-stage flip-flops (six-gate design).

## Slide 9: Classification of Flip-flops and Latches
Latches: asynchronous and level sensitive
  If input signal is changed, the state of flip-flop can change (asynchronous)
  Level sensitive latches change state only at the presence/absence of clock.
  Flip-flops:
  In one-stage flip-flop, switching occurs as soon as occur front of clock
  In a two-stage over two cycles. Use two latches: master and slave.
Master forms the next state, then next state is copied to slave.
Logic functioning of flip-flops is described by means transition tables (truth tables), characteristic equations, Karnaugh maps, state diagrams (STG), “dictionaries” – matrixes of transition functions.

## Slide 10: Asynchronous RS-latch
RS latch is a building block for other types of latches and flip-flops.
R – Reset (Clear), S – Set (Preset)
S
R
S
R
Q
Q
Q
Q
S
R
R
S

## Slide 11: Truth Table of RS-Latch
R | S | Q | Q*
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | -
1 | 1 | 1 | -
R | S | Q*
0 | 0 | Q
0 | 1 | 1
1 | 0 | 0
1 | 1 | -
Characteristic equation of RS-latch
Q* = S + ~RQ
11
R
SQ
00
01
11
10
0
1
1
1
1
-
-
Q*

## Slide 12: RS-Latch
The matrix of excitation functions “-” - don’t care
Transition | R | S
0  0 | - | 0
0  1 | 0 | 1
1  0 | 1 | 0
1  1 | 0 | -
01
0
1
10
-0
0-

## Slide 13: Circuits of Asynchronous RS Latches
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Qlast | Qlast
S | R | Q | Q
0 | 0 | Qlast | Qlast
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
S
R
Q
Q
S
R
Q
Q

## Slide 14: Metastability
Metastability is inherent in any bi-stable system
Black line – static transfer characteristic of upper inverter, white line – lower. Theoretically in metastable state, the circuit can stay unrestrictedly long.
Stable
Stable
Vin2=Vout1
Vin2=Vout1
Vout1
Vout2
Vin1=Vout2
Vout=T(Vin) – transfer function
Vin1
Vin2
Vout1
Vout2
Metastable state

## Slide 15: Timing Diagram of RS Latch
If S and R change simultaneously from zero to one, then the next state is not predictable, and oscillation may rise in the outputs or metastable states can occur. Instability may occur in case that the negative pulse, given to the inputsS or R, is too short.
When both input signals S andR are equal to zero, both Q иQ equal one.
S
Q
Q
R

## Slide 16: Description by Verilog of RS Latch with Inverse Inputs
'timescale 1 ns/1 ps
module RS_Latch(Q, R_L, S_L);
input R_L, S_L;
output Q;
reg Q;
always @(R_L or S_L)
begin
if ((R_L==0) && (S_L==0))
$display (“RS – indeterminate state”);
if ((R_L==0) && (S_L==1)
Q <= #13 0;
else if ((R_L==1) && (S_L ==0));
Q<= #17 1;
end
endmodule
‘timescale directive has been used to set up the simulator both a default time unit (1 ns) and a precision of 100 ps.

## Slide 17: Circuit of Synchronous RS Latch
RS-latch with enable input:
S and R only have effect when Clock=1.
S
R
Q
Q
C
S
R
Clock
Q
Q

## Slide 18: Synchronous RS Latch
SR
CQ
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
1
1
Characteristic equation:
Q* = SC +RQ + CQ
Truth table
S | R | C | Q* | Q*
0 | 0 | 1 | Qlast | Qlast
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
x | x | 0 | Qlast | Qlast

## Slide 19: D Flip-Flop
D flip-flop has one information input. Its state repeats input signal, but with delay, defined by clock. D flip-flop is mainly synchronous.
D | Q | Q*
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
Transition | D
0  0 | 0
0 1 | 1
1 0 | 0
1 1 | 1
Characteristic equation
of D flip-flop: Q* = D
1
0
0
1
0
1

## Slide 20: Designing D Latch Based on RS Latch
D | Q | Q* | R | S
0 | 0 | 0 | - | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | -
S
R
Q
Q
C
D
Clock
R = D S = D

## Slide 21: D Latch
module d_latch(data, clk, q);
input data, clk;
output q;
reg q;
always @( clk or data)
begin
if (clk)
q<=data;
end
endmodule // d_latch
D
Clock
Variant of circuit with minimum number of gates.
Q

## Slide 22: Timing Diagram of D Latch
There is a (shaded) window of time around the falling edge of Clock
when D input must not change. That interval begins at time tsetup and ends at time thold afterward.
Tsetup – setup time, thold – hold time.
thold
tsetup
Q
D
Clock

## Slide 23: D Latch
D | C | Qt | Qt+1
x | 0 | 0 | 0
x | 0 | 1 | 1
0 | 1 | x | 0
1 | 1 | x | 1
D
CQ
00
01
11
10
0
1
1
1
1
1
1-hazard
D
C
This latch is unreliable as its circuit has static hazard at changing the state of inputs from 111 to 101.
Q*=~CQ+CD

## Slide 24: D Latch (2)
Reliable latch
C
D
C
Q
D latch in SystemVerilog
module latch(input logic clk,
input logic data,
output logic q);
always_latch
if (clk) q <= data;
endmodule
SystemVerilog can generate
a warning if the always_latch block doesn’t imply a latch
To design a circuit, free from hazards, add DQ implicant.
Q* = D·C + C·Q +D·Q

## Slide 25: D Latch Using Multiplexer
Q* = D·C + C·Q
0
1
Q
D
Clock
0
1
Q
D
Clock
Q* = D·C + C·Q
Positive level sensitive latch
Negative level sensitive latch

## Slide 26: Edge-Triggered D Flip-Flops
D flip-flop has asynchronous inputs R(clear) and S (preset) that may be used to force the flip-flop to a particular state independent of the clock and D inputs
R | S | D | C | Q* | Mode
0 | 1 | X | x | 0 | Reset
1 | 0 | X | x | 1 | Set
0 | 0 | X | x | - | Not allowed
1 | 1 | 0 |  | 0 | Writing 0
1 | 1 | 1 |  | 1 | Writing 1
Clock
D
C
S
R
D
Q
D flip-flop (IC 74LS74)

## Slide 27: Edge-Triggered D Flip-Flop Circuit
Q
S
C
R
D
Q

## Slide 28: Verilog Description of D Flip-Flop
module dff_async (reset, set, data, clk, q);
input clk, reset, set, data;
output reg q;
always @(posedge clk, negedge reset, negedge set)
begin
if (reset ==1’b0)
q<=1’b0; // reset is preferred
else if (set==1’b0)
q<=1’b1;
else q<=data;
end
endmodule // dff_async

## Slide 29: D Flip-Flop in System Verilog
module D_ff_r(input logic clk,
input logic data,reset,set, output logic q);
always_ff @(posedge clk or negedge reset
or posedge set)
if( !reset) q<=0;
else if (set) q<=1;
else
q <= data;
endmodule

## Slide 30: Set-up and Hold Times
Set-up time
  Time during which data must be stable before the clock comes
Hold time
  Time during which data must be stable after the clock comes

## Slide 31: Timing Diagrams of D Flip-Flop
During time interval (tsetup , thold - shaded) – signal in the input D must not change. Else metastable states can occur.
From metastable state flip-flop can return on its own state
  After probabilistic delay
  By applying another triggering clock edge with a D-input that meets the setup- and hold- time requirements
t setup
D
CLK
t hold
Q
tpLH
tpHL

## Slide 32: Edge-Triggered D Flip-flop with Enable Input
A commonly desired function D-flip-flops is the ability to hold the last value stored rather than load a new value. This is accomplished by adding an enable input.
D
EN
CLK
R
R | D | EN | CLK | Q*
1 | x | 0 |  | Last Q
1 | 0 | 1 |  | 0
1 | 1 | 1 |  | 1
1 | x | x | 0 | Last Q
1 | x | x | 1 | Last Q
0 | x | x | x | 0

## Slide 33: Verilog Description
D
CLK
Reset
D
C
Q
Q
EN
module dff_clk_en(data, clk, reset, en, q);
input data, en, reset, clk;
output reg q;
always @( posedge clk or negedge reset)
if (! reset)
q<=1’b0;
else if (en)
q<=data;
endmodule
0
1

## Slide 34: Т Flip-Flop (1)
T flip-flop (toggle) has one information input like D flip-flop.
Characteristic equation of Т flip-flop
Q* = ~T·Q + T·~Q = TQ
0
1
1
0
0
1
T | Q | Q*
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Transition | T
0  0 | 0
0  1 | 1
1  0 | 1
1  1 | 0

## Slide 35: Т Flip-Flop (2)
Designing T flip-flop based on RS latch
R = T·Q S = T· ~Q
Not operating circuit.
While there is positive level of
clock in the input C and T=1,
the circuit falls into generation mode.
C
S
C
R
T
T | Q | Q* | R | S
0 | 0 | 0 | - | 0
0 | 1 | 1 | 0 | -
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0

## Slide 36: Master/Slave T Flip-Flop
Violation between storing old information and writing new are decided by inserting the second flip-flop.
In fact double stage flip-flop consists of two serial connected latches: Мaster and Slave.
T flip-flop with inverter
Q
T
Clock
T
C
S
C
R
S
C
R
T
C
M
S

## Slide 37: Master/Slave RS and D Flip-Flops
Flip-flop changes its output only at the falling edge of a signal C New output value depend on input values not just at the falling edge but during the entire interval in which C=1.
Q
~Q
S
R
C
S
C
R
S
C
R
M
S
Q
D
C
D
C
D
C
M
S

## Slide 38: Master/Slave D Flip-Flop (Using MUXs)
D
Clock
Q
D
C
0
1
D
Clock
0
1
Q
Master
Slave
Negative edge triggered D flip-flop

## Slide 39: Transmission Gate
En
En
A
B
A
B
En
En
D
Q
CLK
CLK
CLK
D-Latch using MUXs

## Slide 40: 2:1 Mux Description
module mux2_1(in0, in1,s, y);
input in0,in1,s;
output y;
reg y;
always @(in0,in1,s,)
if(s==1)y=in1;
else y=in0;
endmodule
always @(in0,in1,s,)
begin
if (s==1 ) y=in1;
end
always @(in0,in1,)
begin
y=in0;
if (s==1) y=in1;
end
In this example, instead of the multiplexer, a level-controlled latch will be obtained.
y = s·in1 + ~s·y.
In both cases a description of the multiplexer 2: 1 will be obtained

## Slide 41: Master- Slave D FF
D
CLK
QM
QS

## Slide 42: Verilog Description of T Flip-flop Positive Edge Triggered with QN Output
module tff_qn(t, clk, reset, en, q,qn);
input t, reset, clk;
output q,qn;
reg q,qn;
always @( posedge clk or negedge reset)
if (! reset)
q<=1’b0;
else
q<=q^t;
always @(q) qn<=!q;
endmodule

## Slide 43: JK Flip-Flop
Q
Q
J
C
K
J
C
K
0
1
-1
0-
-0
1-
J | K | Q | Q*
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 44: JK Flip-Flop (2)
J
KQ
00
01
11
10
0
1
1
1
1
1
Characteristic equation of JK flip-flop
Q* = JQ +KQ
The matrix of excitation functions
Transition | J | K
0  0 | 0 | -
0  1 | 1 | -
1  0 | - | 1
1  1 | - | 0

## Slide 45: Master/Slave JK Flip-Flop
R =KQ; S = J~Q
S
C
R
S
C
R
Clock
J
K
Q
~Q
J | K | Q | Q* | R S
0 | 0 | 0 | 0 | - 0
0 | 0 | 1 | 1 | 0 -
0 | 1 | 0 | 0 | - 0
0 | 1 | 1 | 0 | 1 0
1 | 0 | 0 | 1 | 0 1
1 | 0 | 1 | 1 | 0 -
1 | 1 | 0 | 1 | 0 1
1 | 1 | 1 | 0 | 1 0

## Slide 46: Edge-Triggered JK Flip-Flop
Design JK flip-flop based on edge-triggered D flip-flop.
Define the excitation function of base D flip-flop by the table.
Dt = Qt+1 = JQ  KQ
0
1
J
K
Clk
D
C
Q
J | K | Q | Q* | D
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 47: JK Flip-Flop with Inverse Asynchronous Reset in Verilog
module jk_ff (j, k, clk, reset, q);
input (j, k, clk, reset);
output reg q;
always @ (posedge clk or negedge reset)
begin
if (!reset)
q <= 1’b0;
else case ({j, k})
2’b00: q <=q;
2’b01: q <= 1’b0;
2’b10: q <=1’b1;
2’b11: q <= ~ q;
default: q <= 1’b0;
endcase
end
endmodule // jk_ff

## Slide 48: Designing Other Flip-Flops Based on JK Flip-Flop
Q
Q
J
C
K
S
C
R
If J∙K1, then JK flip-flop is turned into RS flip-flop.
Q
Q
D
J
C
K
Q
Q
J
C
K
T
“1”
Q
Q
J
C
K
C
T
D flip-flop
T flip-flop (edge-triggered)
T flip-flop (clocked)
RS flip-flop

## Slide 49: Summary of Latch and Flip-Flop Characteristic Equations
Device Type | Characteristic Equation
SR latch | Q*=S +RQ
Gated SR latch | Q* = SC +RQ + CQ
D latch | Q* = D
Master/Slave SR flip-flop | Q* = S +RQ
Edge-triggered D flip-flop | Q* = D
Master/Slave JK flip-flop | Q* = JQ +KQ
Edge triggered JK flip-flop | Q* = JQ +KQ
T flip-flop (edge triggered) | Q* =Q
T flip-flop (clocked) | Q* = TQ +TQ
D flip-flop with enable | Q* = EnD +EnQ

## Slide 50: Asynchronous and Synchronous Reset
Asynch. reset
Synchronous reset vs. asynchronous
In many cases synchronous reset more preferable
 | sync. | async.
area | larger | smaller
reset speed | slower | faster
skew effects | robust | vulnerable
meta-stability | no | yes
power consumption | more | less
D
Q
clk
D
Q
clk
0
1
reset
0
Synch. reset
D
clk
clk
D

## Slide 51: Synchronous Reset
rst_n | D | clk | Q*
0 | x |  | 0
1 | 0 |  | 0
1 | 1 |  | 1
x | x | 0 | Last Q
x | x | 1 | Last Q
D
Q
rst_n
D
clk
D
Q
rst_n
D
clk
En
0
1

## Slide 52: Rising Edge D Flip-Flop with Synchronous Reset in Verilog
module dff_synch_rst (data, clk, reset_n, q);
input data, clk, rst_n, q;
output q;
reg q;
always @(posedge clk)
begin
if (!rst_n)
q<=1’b0;
else q<=data;
endmodule

## Slide 53: Scan D Flip-Flop
An important flip-flop function - scan capability.
To drive the flip-flop’s D-input with an alternate source of data during device testing
All flip-flops are put into testing mode
Load test pattern
All flip-flops are put into normal mode
After one or more clock ticks flip-flops are put back into test mode
Test results are scanned out.

## Slide 54: Scan D Flip-Flop (2)
D
TE
TI
Clk
Q
Q
TE | TI | D | Clk | Q
0 | x | 0 |  | 0
0 | x | 1 |  | 1
1 | 0 | x |  | 0
1 | 1 | x |  | 1
x | x | x | 0 | Last Q
x | x | x | 1 | Last Q

## Slide 55: Scan D Flip-Flop (3)
0
1
TE
D
TI
Clk
D
C
D
C
Clk
TI
TE
D
Q
Q

## Slide 56: Scanning Chain
Тhe signal of global TE input is held during n clock ticks.
n-bit vector (n=4) is loaded in n flip-flops through global input TI.
Then TE signal is negated and the circuit functions during one or more clock ticks.
New state of the circuit can be read during n clock ticks at condition that TE=1.
TO
D
TE
TI
Clk
Q
Q
D
TE
TI
Clk
Q
Q
D
Q
Q
D
TE
TI
Clk
Q
Q










ТI
Clk
TE
Тesting of the circuit
TE
TI

## Slide 57: Double-Edge-Triggered Flip-Flops
Double-edge-triggered (DET) flip-flop can receive input
signal at two levels of the clock.
0
1
D
Clock
D
C
D
C
Set
Reset
Q
D flip-flop based on two single-edge-triggered flip-flops

## Slide 58: Double-Edge-Triggered D Flip-Flop Using MUXs
0
1
D
Clock
0
1
Q
0
1

## Slide 59: Double-Edge-Triggered Flip-Flop
DET D flip-flop with asynchronous reset(preferred) and set inputs
Truth Table
D
C
PRE
CLR
CLR(R) | Preset (S) | C | D | Q* | mode
0 | 0 |  | 0 | 0 | “0” writing
0 | 0 |  | 1 | 1 | “1” writing
0 | 0 |  | 0 | 0 | “0” writing
0 | 0 |  | 1 | 1 | “1” writing
0 | 0 | 0 | x | Qlast | Hold
0 | 0 | 1 | x | Qlast | Hold
1 | x | x | x | 0 | Asynch. reset
0 | 1 | x | x | 0 | Asynch. set

## Slide 60: Double-Edge-Triggered Flip-Flop
DET D flip-flop with synchronous reset and set (preferred) inputs
D
C
S
R
CLR | Preset | C | D | Q* | mode
0 | 0 |  | 0 | 0 | “0” writing
0 | 0 |  | 1 | 1 | “1” writing
0 | 0 |  | 0 | 0 | “0” writing
0 | 0 |  | 1 | 1 | “1” writing
0 | 0 | 0 | x | Qlast | Hold
0 | 0 | 1 | x | Qlast | Hold
x | 1 |  | x | 1 | Synch. set
x | 1 |  | x | 1 | Synch. set
1 | 0 |  | x | 0 | Synch.reset
1 | 0 |  | x | 0 | Synch.reset

## Slide 61: Sequence of Structural Synthesis of FSM
Task of structural synthesis of FSM is designing FSM circuit according to its representation.
Sequence of structural synthesis:
Determine the number of state variable
Coding of input and output signals of FSM;
State assignment
Definition of excitation functions of flip-flops
Definition of output functions
Minimization of boolean functions
Designing of logic circuit.

## Slide 62: Coding of Input and Output Signals of FSM
Given abstract FSM A = {X, Y, S, , }
Determine the number of inputs and outputs of FSM.
The number of inputs m depend on M=|X| [log 2 M]  m M
Each symbol (letter) of input alphabet is put in accordance with a set of zeros and ones of input signals of FSM x1,x2...xm.
Number of output signals of FSM n depend on N=|Y| [log 2 N]  n N
Each letter of output alphabet is put in accordance with a set of zeros and ones of output signals of FSM y1, y2 ... yn.
All the letters of input (output) alphabet are coded by different codes.

## Slide 63: FSM States Assignment
State assignment significantly influences on the complexity of FSM.
Goals:
  Assign a unique code to each state to produce a minimal binary logic level implementation.
  The complexity of excitation functions depend on type of flip-flop.
  The state variables is defined from the following ratio: [log2K]  k  K , where K=|S| – number of internal states of FSM.
  Each state of FSM is put in accordance with k-bit set of zeros and ones so that none of two states has equal code. This procedure is called states assignment of FSM.
  The simplest methods of coding: binary and unary.

## Slide 64: State Assignment
At binary coding the number of flip-flops is taken minimum k=[log2 К].
May use the first K binary integers in binary counting order (this does not always lead to simplest excitation equations).
At unary coding (“1 from К”) the number of flip-flops is taken maximum (k=K): “one–hot” assignment.
At this assignment the combinational circuit is minimal.
This structure is similar to shift register. Disadvantage: require many flip-flops.
If k internal variables is used and the FSM has K states, the number of variants of state assignment is defined by 2k!/ ((2k - К)!k!).
In order to find the best variant of assignment, it is necessary to try all the variants of assignment. Though it is huge work.

## Slide 65: State Assignment (Total Approach)
Initial state S0 – 00…00 or 11…11.
Minimize the number of state variables that change on each transition.
Maximize the number of state variables that don’t change in a group of related states.
If there are unused states (K<2k) then choose the most convenient state variables combinations.
The set of state variables decompose into individual bits or fields where each bit or field has a well-defined meanings with respect to the input effects or output behavior.
Consider more than the minimum number of state variables.

## Slide 66: Excitation and Output Functions Definition
Use coded transition and output table.
Excitation functions is defined for each type of flip-flop in accordance with its matrix of excitation functions.
Current and next state codes are compared. The values of functions is determined on each transition and written in the excitation table.
D flip-flop has the simplest characteristic equation D=Q*.Comparison is not needed.
Unused states:
Minimal cost:
  Next state entries can be marked as “don’t cares”. This simplifies the excitation and output logic.
Minimal risk.
  Next state entries can be market as “0” (if initial state 00…00)

## Slide 67: Design of FSM. Example 1
Synthesize of sequence detector circuit for 001 or 101 sequences.
Construct STG of detector
S0
S1
S3
S2
S4
0/0
1/0
1/0
0/0
1/1
0/0
1/1
1/0
0/0
0/0

## Slide 68: State Minimization (Method of Successive Partitions)
X S | 0 | 1 | 
S0 S1 S2 S3 S4 | S1,0 S2,0 S2,0 S4,0 S2,0 | S3,0 S3,0 S3,1 S3,0 S3,1 | A1 A1 B1 A1 B1
X S | 0 | 1 | 
S0 S1 S3 | A1 B1 B1 | A1 A1 A1 | A2 B2 B2
S2 S4 | B1 B1 | A1 A1 | C2 C2
S X | 0 | 1 | 
S0 |  |  | A3
S1 S3 | C2 C2 | B2 B2 | B3 B3
S2 S4 | C2 C2 | B2 B2 | C3 C3
P1={A1,B1}; A1={S0,S1,S3}; B1={S2,S4}
P2={A2,B2,C2};
A2 =S0; B2={S1,S3}; C2={S2,S4}
PO
P2 = P3 = PFin
S1S3=S13
S2  S4=S24
P2

## Slide 69: State Minimized Sequence Detector for 001 or 101
S0
S13
S24
x/0
1/0
0/0
1/1
0/0
X S | 0 | 1
S0 | S13,0 | S13,0
S13 | S24,0 | S13,0
S24 | S24,0 | S13,1

## Slide 70: Synthesis Using D Flip-Flops
State Assignment:
The simplest next-state logic:
States which have the same next state for a given input should have unit-distant assignment.
The simplest output logic:
States which have the same output for a given input should have unit-distant assignment.

## Slide 71: Synthesis Using D Flip-Flops
The number of flip-flops is taken minimum: k = [log23] =2
State assignment
State | q1q2
S0 | 0 0
S1 | 0 1
S2 | 1 1

## Slide 72: Determine Excitation Functions
q1q2
X
0
1
00
01
11
01
01
11
01
11
01
q1q2
X
0
1
00
01
11
1
1
10


d2
1
1
1
1
d1=q2x;
d2 = 1;
y = q1x
d1
q1q2
X
0
1
00
01
11
1
1
10


0-0 0
0-1 1
1-0 0
1-1 1
d
q1q2
X
0
1
00
01
11
10


y
1

## Slide 73: The circuit of FSM
D
C
R
d1
q1
D
C
d2
q2
“1”
R
x
Clock
Reset
y

## Slide 74: An Example 2 of Synthesis (Linear Adder)
Consider the design of linear adder.
S1
S0
S2
S3
S4
0/-
1/-
0/0
1/1
0/1
1/0
0/-
1/-
0/0
1/1
Design a circuit using D flip-flops.
Assume k= log2K= 3. State assignment:
S0 – 000; S3 – 011;
S1 – 001; S4 – 100;
S2 – 010;
000
001
010
011
111

## Slide 75: State Assignment
State | Simplest q1q2q3 | Decomposed q1q2q3 | One-hot q1q2q3q4q5 | Almost One-hot q1q2q3q4 | Gray encoding | Johnson’s encoding
S0 | 000 | 000 | 10000 | 0000 | 000 | 000
S1 | 001 | 001 | 01000 | 1000 | 001 | 100
S2 | 010 | 010 | 00100 | 0100 | 010 | 110
S3 | 011 | 100 | 00010 | 0010 | 011 | 111
S4 | 100 | 101 | 00001 | 0001 | 111 | 011

## Slide 76: Structural Table of Transitions
Present State |  | X | Next State |  | Y | D1 | D2 | D3
S0 | 000 | 0 | S1 | 001 | - |  |  | 1
 |  | 1 | S2 | 010 | - |  | 1 | 
S1 | 001 | 0 | S0 | 000 | 0 |  |  | 
 |  | 1 | S0 | 000 | 1 |  |  | 
S2 | 010 | 0 | S1 | 001 | 1 |  |  | 1
 |  | 1 | S3 | 011 | 0 |  | 1 | 1
S3 | 011 | 0 | S2 | 010 | - |  | 1 | 
 |  | 1 | S4 | 100 | - | 1 |  | 
S4 | 100 | 0 | S3 | 011 | 0 |  | 1 | 1
 |  | 1 | S3 | 011 | 1 |  | 1 | 1

## Slide 77: Structural Table of Transitions
Present State |  | X | Next State |  | Y | D1 | D2 | D3
S0 | 000 | 0 | S1 | 001 | - |  |  | 1
 |  | 1 | S2 | 010 | - |  | 1 | 
S1 | 001 | 0 | S0 | 000 | 0 |  |  | 
 |  | 1 | S0 | 000 | 1 |  |  | 
S2 | 010 | 0 | S1 | 001 | 1 |  |  | 1
 |  | 1 | S3 | 011 | 0 |  | 1 | 1
S3 | 011 | 0 | S2 | 010 | - |  | 1 | 
 |  | 1 | S4 | 111 | - | 1 | 1 | 1
S4 | 111 | 0 | S3 | 011 | 0 |  | 1 | 1
 |  | 1 | S3 | 011 | 1 |  | 1 | 1
Next State Functions

## Slide 78: Excitation Functions
1
-
-
-
-
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
D1
1
1
-
-
-
-
1
1
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
D2
1
1
1
-
-
-
-
1
1
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
D3
-
-
1
1
-
-
-
-
-
-
1
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
y
1

## Slide 79: Excitation Functions
1
-
-
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
D1
1
1
-
-
-
-
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
D2
1
1
1
-
-
-
-
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
D3
-
-
1
1
-
-
-
1
-
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
y
1
-
-
1
1
1
1
1
1
D1=q1q2q3x; D2 =q3x+q2q3; D3 =q1+q3x+q2x; y=q2q3+q1q3x;

## Slide 80: Excitation and Output Functions of FSM
D1 = q2q3x;
D2 = q2q3 x +q3 x +q1;
D3 = q3 x + q2x + q1;
y = q2 x + q2x;
Design a circuit using IC 74LS74 D flip-flops and NAND gates

## Slide 81: The Circuit of Linear Adder
1
2
x
3
4
5
7
8
q1
q2
q3
5
7
1
8
2
7
5
5
8
4
4
2
8
Clock
Reset
y
5
2
1
6
D
D
D
D
6
R
R
R
2

## Slide 82: FSM Description by Verilog Description of Linear Adder
module linear_adder(data_in, data_out, reset, clock);
input data_in, reset, clock;
output data_out;
reg data_out;
reg [2:0] pres_state, next_state;
parameter S0 = 3’d0, S1= 3’d1, S2= 3’d2, S3 = 3’d3,
S4= 3’d4;
// FSM register
always @(posedge clock or negedge reset)
begin:statereg
if(!reset) //asynchronous reset
pres_state< = S0;
else pres_state <= next_state;
end //statereg

## Slide 83: Description of Linear Adder (2)
// Next state logic
always @(pres_state, data_in)
begin: fsm
case (pres_state)
S0: case (data_in)
1’b0: next_state = S1;
1’b1: next_state = S2;
endcase
S1: next_state = S0;
S2: case(data_in)
1’b0: next_state = S0;
1’b1: next_state = S3;
endcase

## Slide 84: Description of Linear Adder (3)
S3: case (data_in)
1’b0: next_state = S2;
1’b1: next_state = S4;
endcase
S4: next_state = S3;
default: next_state = S0;
endcase
end //fsm
//Mealy output definition
always @(data_in, pres_state)
begin:outputs
casex (pres_state)
S0: data_out =1’bx;

## Slide 85: Description of Linear Adder (4)
S1: if(data_in)
data_out= 1’b1;
else data_out = 1’b0;
S2: if (data_in)
data_out = 1’b0;
else data_out = 1’b1;
S3: data_out =1’bx; S4: if(data_in)
data_out= 1’b1;
else data_out = 1’b0;
default: data_out = 1’b0;
endcase
end //outputs
endmodule

## Slide 86: Test Bench
module line_adder_stimulus;
wire data_out;
reg data_in, clock, reset;
linear_adder line(data_in, data_out, reset, clock);
initial begin
data_in=1;
reset =0;
clock = 0;
#12 reset=1;
#60 data_in=0;
# 45 data_in=1;
# 50 data_in=0;

## Slide 87: Test Bench (2)
#15 data_in = 1;
#50 $stop;
end
always #5 clock = ~clock; //clock generation
endmodule
Other example of clock generation within a test bench
`timescale 1ns/1ps
module clkgen(clk);
output clk;
reg clk;
initial begin
clk=1;
end
always begin
#6 clk=0; //6 ns high
#4 clk=1; end //4 ns low
endmodule

## Slide 88: FSM Description by Verilog Example 3
Design clocked synchronous FSM with two inputs X1 and X2 and one output Y. The output signal must be equal to 1, if the number of ones, that enter X1 and X2 inputs since launching, is divisible by 3. In other cases the signal in the output must be equal to 0.
Design STG.

## Slide 89: STG of FSM
00
S0/1
S1/0
S2/0
01
10
01
10
00
00
11
11
11
01
10
X = {00,01,10,11}; Y ={0,1}; S = {S0,S1,S2}.
Designate states as follows: st0, st1, st2;
input signals – data; output signal – q.
pres_state – current state; next_state – next state.
A
x1
x2
y

## Slide 90: FSM Description by Verilog Example 3
module moore_countmod3 (data, clock, reset, q);
input reset, clock;
input [1:0] data;
output reg q;
reg[1:0] pres_state, next_state;
parameter st0 = 2’b00, st1 = 2’b01, st2 = 2’b10;
//FSM register
always @(posedge clock, negedge reset)
begin:statereg
if(!reset) //asynchronous reset
pres_state <= st0;
else pres_state <= next_state;
end //statereg

## Slide 91: FSM Description by Verilog Example 3 (2)
//FSM next state logic
always @(pres_state or data)
begin: fsm
case (pres_state)
st0: case (data)
2’b00: next_state = st0;
2’b11: next_state = st2;
default: next_state = st1;
endcase
st1: case (data)
2’b00: next_state = st1;
2’b11: next_state = st0;
default: next_state = st2;
endcase
st2: case (data)
2’b00: next_state = st2;
2’b11: next_state = st1;
default: next_state = st0;
endcase
default: next_state= st0;
endcase
end //fsm
//Moore output definition
always @(pres_state)
begin: outputs
if (pres_state==st0)
q = 1’b1;
else q= 1’b0;
end //outputs
endmodule

## Slide 92: SystemVerilog (FSM) Example 3
module Moore_cntmod3( input logic clk, input logic reset,
input logic [1:0] data,
output logic q);
typedef enum logic [1:0] {s0, s1, s2} statetype;
statetype [1:0] state, nextstate;
// state register
always_ff @(posedge clk, posedge reset)
if (reset) state <= s0;
else state <= nextstate;

## Slide 93: SystemVerilog (FSM) Example 3 (2)
// next state logic
always_comb
case (state)
s0: case (data)
2’b00: nextstate = s0;
2’b11: nextstate = s2;
default: nextstate = s1;
endcase
s1: case (data)
2’b00: nextstate = s1;
2’b11: nextstate = s0;
default: nextstate = s2;
endcase
s2: case (data)
2’b00: nextstate = s2;
2’b11: nextstate = s1;
default: nextstate = s0;
endcase
default: nextstate= s0;
endcase //output logic
assign q = (state==s0);
endmodule

## Slide 94: Data Types
SystemVerilog introduces the logic type (synonym a reg ).
Advantages:
Logic avoids misleading users about whether it is actually a flip-flop.
SystemVerilog relaxes the rules on assign statements and hierarchical port instantiation
Logic can be used outside always blocks where a wire traditionally would have been required. Nearly all SystemVerilog signals can be logic.
The typedef statement defines statetype to be a two-bit logic value with three possibilities: s0, s1, or s2.
State and nextstate are statetype signals.
The enumerated encodings default to numerical order:s0 = 00, s1 = 01, and s2 = 10. The encodings can be explicitly set by the user
Synthesis tool views them as suggestions, not requirements.

## Slide 95: State Encoding Techniques
Select the desired encoding technique with FSM Encoding Algorithm (FSM_ENCODING). For example XST.
Auto State Encoding
In automatic mode, XST tries to select the best suited encoding method for a given FSM.
One Hot Encoding
One-Hot State Encoding is the default encoding scheme.
  The state register is implemented with one flip-flop for each state.
  In a given clock cycle - one and only one bit of the state register is asserted.
  Only two bits toggle during a transition between two states.
  One-Hot State Encoding is usually a good choice for optimizing speed or reducing power dissipation.

## Slide 96: State Encoding
Gray State Encoding:
  Only one bit switches between two consecutive states.
  It is appropriate for controllers exhibiting long paths without branching.
  Minimizes hazards and glitches.
  Good results can be obtained when implementing the state register with T flip-flops.
  Can be used to minimize power dissipation.
Compact State Encoding
  Compact State Encoding consists of minimizing the number of bits in the state variables and flip-flops.
  This technique is based on hypercube immersion.
  Compact State Encoding is appropriate when trying to optimize area.

## Slide 97: State Encoding
Johnson State Encoding
  Like Gray State Encoding, Johnson State Encoding is beneficial when using state machines containing long paths with no branching.
  Only one bit switches between two consecutive states.
Sequential State Encoding
  Sequential State Encoding consists of identifying long paths and applying successive radix two codes to the states on these paths. Next state equations are minimized.
Speed1 State Encoding
  Speed1 State Encoding is oriented for speed optimization. The number of bits for a state register depends on the specific FSM, but is generally greater than the number of FSM states.

## Slide 98: Example
x1: 0110111000110
x2: 1110101000111
y: 0000100001110
Y: 000001
FSM
x1
x2
y
01/0
10/0
00/0
11/0
00/0
11/0
00/0
11/0
S0
S1
S2
S3
00/1
11/1
01/0, 10/0
01/0
10/0
01/0
10/0
If these sequences coincide on four consecutive clock cycles, y = 1. In all other cases, y = 0.
The function FSM is comparison of the input sequences of zeros and ones arriving at inputs.

## Slide 99: Verilog Description of Mealy FSM
module Mealy_fsm(x1,x2,y,clk,reset);
input x1,x2,clk,reset;
output reg y;
reg [1:0] state, next_state;
parameter S0=2'b00, S1=2'b01, S2=2'b10, S3=2'b11;
//register
always @(posedge clk, negedge reset)
if (!reset) //asynchronous reset
state<=S0;
else state<=next_state;
//next state logic
always @(state, x1, x2)

## Slide 100: Verilog Description of Mealy FSM
case (state)
S0:next_state=(x1==x2)? S1:S0;
S1:next_state=(x1==x2)? S2:S0;
S2:next_state=(x1==x2)? S3:S0;
S3:next_state=(x1==x2)? S3:S0;
default: next_state=S0;
endcase
//output logic
always @(state, x1, x2)
if ((state==S3)&&(x1==x2)) y=1;
else y=0;
endmodule

## Slide 101: SystemVerilog Description of Mealy FSM
module Mealy_fsm(input logic clk, input logic reset, input logic x1,x2, output logic y);
typedef enum logic [1:0] {s0, s1,s2, s3} statetype;
statetype [1:0] state, nextstate;
// state register
always_ff @(posedge clk, negedge reset)
if (!reset) //asynchronous reset
state<=S0;
else
state<=next_state;

## Slide 102: SystemVerilog Description of Mealy FSM (cntd)
//next state logic
always_comb
case (state)
s0: next_state=(x1==x2)? s1:s0;
s1:next_state=(x1==x2)? s2:s0;
s2:next_state=(x1==x2)? s3:s0;
s3:next_state=(x1==x2)? s3:s0;
default: next_state=s0;
endcase
//output logic
always_comb
if ((state==S3)&&(x1==x2)) y=1;
else y=0;
endmodule

## Slide 103: Design of FSM as an Arbiter Circuit
Arbiter
Device1
Device 2
Device 3
Shared Resource
r1
g1
r2
g2
g3
r3
X={r1,r2,r3} Y={g1,g2,g3}
The purpose of machine: to control access by
various devices to a shared resource

## Slide 104: State Diagram for the Arbiter
S0/-
S1/g1
S2/g2
S3/g3
r1 r2r3
r1
r1
r1
r1r2
r2
r2
r1r2r3
r3
r3
clk=0;
….
Always
begin
#1 clk=~clk;
#2 clk=~clk;
end

## Slide 105: Verilog Code for Arbiter
module arbiter (input[1:3] r, input reset, clk,
output wire[1:3] g); reg[1:0] state, next_state;
parameter s0 =2’b00, s1=2’b01,s2=2’b10, s3=2’b11;
//state register
always @(posedge clk)
if (reset==0) state<=s0; else state<=next_state;
//next state logic
always@(state,r)
case(state)
s0: casex (r)
3’b000:next_state=s0;
3’b1xx: next_state=s1;
3’b01x: next_state=s2;
3’b001: next_state=s3;
default: next_state=s0;
endcase
s1: if(r[1]) next_state=s1;
else next_state =s0;
s2: if(r[2]) next_state=s2;
else next_state =s0;
s3: if(r[3]) next_state=s3;
else next_state =s0;
default: next_state=s0;
endcase
//output logic
assign g[1]=(state==s1);
assign g[2]=(state==s2);
assign g[3]=(state==s3);
endmodule

## Slide 106: Binary to BCD Conversion
 |  | BCD2 | BCD1 | BCD0 | Binary digit
 |  |  |  |  | 1010 1101
Bit7 | No correction |  |  | 1 | 010 1101
Bit6 | No correction |  |  | 10 | 10 1101
Bit5 | Correction |  |  | +101 11 1000 | 0 1101
Bit4 | No correction |  | 1 | 0000 | 1101
Bit3 | No correction |  | 10 | 0001 | 101
Bit2 | No correction |  | 100 | 0011 | 01
Bit1 | Correction |  | +1000 11 1011 | +0110 11 1001 | 1
Bit0 |  | 1 | 0111 | 0011 | 173
111111110010_0101_0101; D=( . . .(an-12+an-2) 2+an-3) 2+ . . .+a1) 2 +a0; Di = 2Di-1 +ai ; 1001+1 1_0000

## Slide 107: Binary to BCD Conversion
1. Assign value 0 to the result and then on every iteration:
2. Analyse if a correction of next digits of a decimal number is required. If the next digit di > 4, then add 3 to that digit.
3. Shift decimal number to the left (multiply the result by 2), the most significant bit of the binary number becomes the less significant bit of the intermediate result as the original number and the result are on the same shift chain.
4. Repeat steps 3 and 4 until all the digits are available.

## Slide 108: The Structure of Unit
RB
CMP
4
CMP
BCD0
BCD1
BCD2
x3
x2
>4
>4
3
3
0
1
0
1
BCD1_next
BCD0_next
Sum0
Sum1
4
Cnt
x2
x3
Binary
FSM
Start
Cnt==0
Done
y1
y1
y1
y2
y3
y3
y3
y2
y3
y3
y3

## Slide 109: Flow-Chart of Algorithm
Begin
Cnt=8; RB=B; BCD0=0; BCD1=0; BCD2=0; Done=0;
Yes
No
BCD0 =BCD0_next;
BCD1=BCD1_next;
Cnt==0?
No
Yes
Done=1
Start==1?
start==1?
Yes
End
S0
S1
S2
S3
S0
y1
y2
y3
No
Shift left RB,BCD0,BCD1,BCD2
Cnt=Cnt-1
Start==1?
y1
S3
y3
Graph of FSM

## Slide 110: FSM Analysis
The goal of FSM analysis is to determine the next state and output functions so that the behavior of circuit can be predicted.
Stages of analysis:
Determine the next state  and output  functions
Use that functions to construct state/output table
Draw a state diagram (optional)
Next state functions are determined using characteristic equations of flip-flops.

## Slide 111: Example 1
Determine next state and output functions
Characteristic equation of T flip-flop: q* = q T
Excitation functions: t1 = x; t2 = q1·x;
q1* = q1 x;
q2* = q1·x·q2 + q1 ·x ·q2;
y = x·q1·q2; Mealy FSM output equation
Next state equations
x
y
t1
t2
J
J
K
K
q1
q2
Clock
Reset

## Slide 112: Example 1 (2)
Construct transition/output table
State transition graph
Assign state names to each state
00 – S0, 01 – S1, 10 – S2, 11 – S3
S0
S1
S2
S3
0/0
1/0
0/0
1/0
0/0
1/0
0/0
1/1
X S | 0 | 1
00 | 00/0 | 10/0
10 | 10/0 | 01/0
01 | 01/0 | 11/0
11 | 11/0 | 00/1

## Slide 113: Example 2
clk
reset
D
C
R
S
“1”
D
C
S
“1”
D
C
R
S
“1”
q2
~x
~q2
~q1
x
~q1
q2
q1
q3
x
~q2
q3
~q1
~x
q1
x
q1
~q1
~q2
q2
q3
~q3
y
~q1
q3
d1
d2
d3
R
x

## Slide 114: Example 2 (2)
Characteristic equation of D flip-flop: q* = d
Determine next state and output functions
d1 =q2~x+~q1~q2x
d2 =~q2q3+q1q3x+~q1q2~x
d3 =~q1~x+~q2q3+q1x
q1*=d1; q2*=d2; q3*=d3;
Y=~q1q3 Moore FSM output function
Excitation functions

## Slide 115: Example 2 (3)
Construct transition/output table
Assign state names to each state
000 – A, 001 – B, 100 – C, 011 – D, 010 – E, 111 – F
X q1q2q3 | 0 | 1 | Output
000 | 001 | 100 | 0
001 | 011 | 111 | 1
100 | 000 | 001 | 0
011 | 111 | 010 | 1
010 | 111 | 010 | 0
111 | 100 | 011 | 0

## Slide 116: Example 2 (3)
X q1q2q3 | 0 | 1 | Output
A | B | C | 0
B | D | F | 1
C | A | B | 0
D | F | E | 1
E | F | E | 0
F | C | D | 0

## Slide 117: Timing Parameters
TCOMB - time, required for the flip-flop changes to propagate through combinational logic elements (flip-flop) excitation logic.
The condition for proper circuit operation:
TCLK >= TCLK-Q + TCOMB + TSETUP
TCLK – TCLK-Q – TCOMB >= TSETUP
Setup-time margin
TCLK – TCLK-Q(max) – TCOMB(max) - TSETUP >=0; TSETUP_SLACK
Hold-time margin
TCLK-Q(min) + TCOMB(min) >=THOLD
TCLK-Q(min) + TCOMB(min) – THOLD >=0; THOLD_SLACK
Critical path delay – propagation delay through the longest path.
For proper operation
TCLK-Qmin+ TCOMB(MIN) – THOLD – TSKEW(MAX) > 0