## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Problems of Synchronous Design

## Slide 4: Timing Diagram of D Flip-Flop
TCCQ
Q
Q
CLK
D
CLK
Tsetup
CLK
d
Q
Thold
TPDQ
Decision
window
TCCQ – Contamination delay (reaction minimal time)
TPDQ – Propagation delay or maximal reaction time
Thold <= TCCQ

## Slide 5: Synchronous System
R1
R2
CLK
Comb. Logic (CL)
Q1
TH
TL
TCLK
Tpd
TCLK-Q
CLK
D2
TCCQ
Q1
Q2
D2
Timing Diagram of the Path Between Registers
TPD – propagation delay through combinational logic (Tcomb_max)

## Slide 6: Maximum Delay for Setup Time Constraint
TCLK >= T CLK-Q + Tpd +TSETUP
Tpd<= TCLK – (TCLK-Q + TSETUP)
Setup time constraint
limits the maximum delay through combinational logic
Setup Slack
Q1
TH
TL
TCLK
Tpd
TCLK-Q
TSETUP
CLK
D2
CL
>
>
Q1
Q2
D2
R1
R2

## Slide 7: Minimum Delay for Hold Time Constraint
T HOLD < =TCC_Q+TCD
TCOMB_MIN >= T HOLD - TCC_Q
Hold time constraint limits the minimum delay through combinational logic
THOLD SLACK
THOLD
Q1
TH
TL
TCLK
Tcd
TCCQ
CLK
D2
TCCQ – contamination
delay clock – to-Q
Tcd – contamination delay through CL

## Slide 8: Timing Diagram
flip-flop outputs (Q1)
TH
TL
TCLK
TCOMB
TCLK-Q
TSETUP
THOLD
Setup time margin
Setup Slack
CLK
Combin. outputs
Flip-flops
Inputs (D2)
Window decision
TCCQ

## Slide 9: Example: Setup and Hold Time Constraints
а
CLK-Q
c
b
D-CLK
d
CL1 (min)
D
CL2 (max)
D
Q
Q
ab
cd
CLK
CL1 – combinational
circuit with minimal delay
CL2 – combinational
circuit with maximal delay

## Slide 10: Maximum Delay for Setup Time Constraint
Setup Slack
а
TH
TL
TCLK
Tab
TCLK-Q
TSETUP
CLK
b
TCLK >= T CLK-Q + TCOMB_MAX +TSETUP
TCOMB_MAX= Tab=TPD
Tcomb_max<= TCLK – (TCLK-Q + TSETUP)

## Slide 11: Minimum Delay for Hold Time Constraint
THOLD SLACK
THOLD
c
TH
TL
TCLK
Tccd
TCCQ
CLK
d
T HOLD < =TCC_Q+Tccd
TCOMB_MIN >= T HOLD - TCC_Q
TCOMB_MIN = Tcd

## Slide 12: Setup and Hold Time for Ideal Clock
Setup – the time before a clock edge before which the data should be stable on the D pin of a flip-flop.
Hold – time after a clock edge for which the data should be held stable.
Setup slack = data setup requierement – last arriving signal
Hold slack = earliest arriving signal - data stability requirement
Hold Slack
Setup Slack
Setup
Hold
Tmin
Tmax

## Slide 13: Example
Clock-to-Q contamination delay | TCCQ | 30ps
Propagation delay | T CLK-Q | 80ps
Setup time Tsetup | Tsetup | 50ps
Hold time | Тhold | 60ps
Logic gates contamination delay | Тccd | 25ps
Logic gate propagation delay | Tpd | 40ps

## Slide 14: Timing Analysis

## Slide 15: Timing Analysis
Critical path: B=1; C=0; D=0; A rises from 0 to 1 (01), triggering n1 to rise(01) ,X′ to rise, and Y′ to fall (10).
This path involves three gate delays.
Tclk ≥tpcq +3tpd +tsetup = 80+3×40+50 = 250ps
The maximum clock frequency is fc =1/Tc =4 GHz.
FIixing Hold Time Violations
A short path occurs when A=0 and C rises (01), causing X′ to rise (01).
For the short path, we assume that each gate switches after only a contamination delay.
This path involves only one gate delay. Thold< =Tccq+Tccd
tccq +tcd =30+ 25=55 ps. 60ps>55ps
X′ must remain stable for 60 ps after the rising edge of CLK .
The circuit has a hold time violation and may behave erratically at any clock frequency.

## Slide 16: Fixing Hold Time Violations
The short paths are slowed by the contamination delay of the buffer.
Now X′ will not change until tccq +2tcd =30+2×25=80 ps. This is after the 60 ps hold time has elapsed, so the circuit now operates correctly.

## Slide 17: Clock Skew
Clock skew – a difference between arrival times of the clock at different devices.
If Tskew > Tclk second register will not be able to store new data
correct
incorrect
IN
Clock
Q1
Q2
Clock D
tskew
IN
Clock
Q2
FF1
FF2
D
Q1
D
Q
ClockD

## Slide 18: Clock Skew
CLK1
CLK2
CLK
TSKEW
R1 receives the latest skewed clock and R2 receives the earliest
skewed clock.
There is a little time for data to propagate
between registers.
CL
>
>
Q1
Q2
D2
CLK1
CLK2
R1
R2

## Slide 19: Timing Diagram with Clock Skew
Setup Slack
Q1
TCLK
Tpd
TPCQ
TSETUP
CLK2
D2
CLK1
TSKEW
TCLK ≥ TPCQ + TPD+ TSETUP + TSKEW
TPD <=TCLK – (TPD + TSETUP + TSKEW)
Setup Constraints
Tpcq – propagation delay CLK to Q
The data propagates through the register and CL and must setup before R2 samples it.

## Slide 20: Timing Diagram with Clock Skew
Hold Constraints
THOLD
Q1
Tcd
TCCQ
D2
TCLK
CLK2
CLK1
In the worst case, R1 receives an early skewed clock, CLK1, and R2 receives a late skewed clock, CLK2.
TCCQ +TCD >= THOLD +TSKEW
TCD <= THOLD + TSKEW − TCCQ

## Slide 21: Setup and Hold Violations
Hold Slack
Setup Slack
Setup
Hold
Tmin
Tmax
Setup Violation
Hold Violation
Latest required time
Earliest required time

## Slide 22: Cycle Time – Critical Path Delay
Cycle time(T) cannot be smaller than longest path delay (Tmax)
Tmax + Tsetup + Tskew +T clk-to-Q  T
T
Data
Critical path – 4 logic levels
Clock

## Slide 23: A Clock-signal Path Leading to Skew
Clock
D
D
D
D
D

## Slide 24: Clock Signal Routing to Minimize Skew (Clock Tree)
D
D
D
D
D
Clock

## Slide 25: Asynchronous Inputs
Digital systems of all types unavoidably must deal with asynchronous input signals that are not synchronized with the system clock.
D flip-flop samples an asynchronous input IN_async at each tick of CLK and produces IN_sync, that is valid during the next clock period.
Combina-tional
Logic
CLK
IN_async
IN_sync
Reg
Simple Synchronizer
Outputs
D

## Slide 26: A Single Simple Synchronizer
If an input signal is missed at one clock tick, it can always be detected at the next one.
Clock
Asyncin
Syncin

## Slide 27: Timing Parameters for Metastability Analysis
TSETUP
Tpd
TCLK
Decision
window
stable
CLK
D
Q
stable
Metastable
Ts Th
Tr
Decision
window
unstable
Normal flip-flop operation
Metastable behavior
THOLD
Tres = TCLK - TCOMB - TSETUP

## Slide 28: Two Synchronizers for the Same Asynchronous Input
Two flip-flops will not see the clock and input signals at precisely the same time.
When asynchronous input transitions occur near the clock edge, there is a small window of time during which one flip-flop may sample the input as 1, and the other – as 0.
SYNC1
Synchronous
System
Asyncin
Clock
D
D
SYNC2

## Slide 29: Synchronizer Failure and Metastability
There are two ways to get a flip-flop out of the metastable state:
Use the faster flip-flops with short setup time
Wait ”long enough”, so the flip-flop comes out of metastability on its own
Metastability resolution time Тres
Tres = TCLK-Q if input is changed out of “decision window” (aperture) time.
Tres=Tclk –Tcomb – Tsetup
To minimize Тres for a given clock period, it is necessary to minimize Tcomb and Tsetup.

## Slide 30: Reliable Synchronizer Design
If the clock period is greater than Tres+Tsetup FF2 SYNCIN becomes a synchronized copy of the asynchronous input ASYNCIN on the next clock tick without ever becoming metastable itself. Tres(max)=tclk
D Q
D Q
Synchronous
System
ASYNCIN
CLOCK
META
SYNCIN
FF1
FF2
Tcomb=0
TASYNCIN > Clock period

## Slide 31: Description of Synchronizer
Verilog
module Synchronizer_dual (clk,Asyncin, Syncin);
input clk,Asyncin;
output Syncin;
reg meta,b;
always@(posedge clk)
begin
meta<=Asyncin;
b<=meta;
end
assign Syncin=b;
endmodule
System Verilog
module synchronizer( input logic asyncin, input logic clk, output logic syncin ); logic meta,b; always_ff @(posedge clk) begin b<=meta; meta<=asyncin; end
assign syncin=b;
endmodule

## Slide 32: Multiple-Cycle Synchronizer with Deskewing
D
C
D
C
Divide-by-N
counter
D
C
Synchronous System
AsyncIN
Meta
SyncIN
Deskewed SyncIN
Clock
CLOCKN
Tres=(n·TCLK) –TSETUP
n=2 , n=3 - reliable