## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Asynchronous FSM. Self-Timed Circuits

## Slide 4: FSM Models
FSM and environment are timed by an external clock
State variables are stored in flip-flops
State variables change simultaneously
External
environment
FSM
X
Y
Synchronous model
Clock
Environment – datapath logic, other FSM, etc.

## Slide 5: FSM Models (2)
FSM changes it state only if input variables change (Feedback Sequential Circuit)
State variables are stored in gate delays
State variables change at any time
FSM
External
environment
X
Y
Asynchronous model

## Slide 6: FSM Models (3)
a – environment prepared inputs for FSM
b – transition processes were finished and FSM prepared output signals.
This model is the variant of asynchronous model
Req/Ack handshakes
This model is used in interfaces
a b | 
0 1 | FSM prepared outputs
1 1 | environment reacted and prepared outputs
1 0 | FSM read inputs and go to phase of work
0 0 | Environment take off Its outputs
FSM
Environment
b
Y
a
X

## Slide 7: Fundamental Asynchronous FSM
Restrictions of Asynchronous FSM
All states of primary table states must be stable.
Excitation logic must be hazard free.
Only one input signal can be changed at a time (changes of input signals must be limited by unit-distant combinations).
Propagation delay through the excitation logic and feedback path must be satisfied the following:
  The maximum delay must be less than the time between successive input change
  The minimum must be greater than maximum timing skew through the input logic (the time between input change must be greater than the time required to reach a steady state).
Anti-race state assignment must be provided.

## Slide 8: Asynchronous FSM
These conditions are sufficient but may not be necessary
1,3,4 items – restrictions on external environment
2,4,5 must be satisfied during synthesis
Next State
Logic
Output Logic
Feedback loop
Outputs
Inputs
Mealy machine only

## Slide 9: Asynchronous Counter (Example)
The first requirement
Transition graph of modulo-4 counter
0
1
2
3
0
0
0
1
1
1
1
0

## Slide 10: Transition Graph of Asynchronous Counter
0
0
0
0
0
0’
1’
2
1
2’
3’
3
1
1
0
0
1
1
1
0
000
001
010
011
100
101
110
111
1
1
1

## Slide 11: Races of Memory Elements
Races occur when at transition of FSM from one state to another several state variables (latches) change.
1
1
1
1
Invalid state
0
0`
1`
2
1
2`
3`
3
0
0
0
0
1
1
0
0
1
1
0
000
001
010
011
100
101
110
111
t2<t3
Invalid state
t2>t3
0
0
0

## Slide 12: Anti-Race Assignment
The fifth requirement
Critical race: if FSM does not occur in required state.
Non-critical race: despite races, FSM occurs in required state.
Present state 101, input changes from 1 to 0, next state must be 110.
Assume that t2>t3: 101100 (invalid stable state)
If t2=t3 : 101110 (required stable state)
If t2<t3:101111 (unstable not-provided state – behavior unpredictable)
It is an example of critical races.
To prevent races it is essential that states connected to transitions, have Hamming distance equal to one (unit-distance assignment).

## Slide 13: Anti-Race Assignment –Gray Code (2)
0
0
0
0
0
0’
1’
2
1
2’
3’
3
1
1
0
0
1
1
1
0
000
001
011
010
110
111
101
100
1
1
1

## Slide 14: Anti-Race Assignment (3)
Unit distance assignment for FSM with k state variables is possible if FSM is mapped onto k-hypercube.
To get race-free assignment it is necessary that the FSM state diagram would not have the cycles of odd length.
Else dummy states must be included in state diagram.
Si
Sk
Sm
00
01
11
Si
Sk
Sm
Si’
00
01
11
10

## Slide 15: Essential (or Functional) Hazards
The third requirement
There are two type of hazards in combinational circuits: essential and logical. Logical hazards depend on gate delays. Essential hazards do not depend on gate delays. They occur since input signals come not simultaneously
Definition:
The set A belongs to subcube which is generated by sets A1,A2… Am , if and only if all variables xi whose values coincide on all sets A1, A2, … Am have such values in set A.
Writing: A(A1, A2, … Am)
Example: A1=1001, A2=0001, A3=0000, A4=0110, A=1000.
By definition:
A(A1,A2,A3 ), A(A1, A3), A(A1,A4), but A (A1, A2)

## Slide 16: Essential (or Functional) Hazards (2)
Static essential hazards
Given function f. Two sets of input variables A and C have static essential hazard if:
f(A) = f(C);
There are at least two sets B and C such that B(A,C)and f(B)  f(A).
Dynamic essential hazards
Two sets of input variables A and D have dynamic essential hazard if:
f(A)  f(D);
At least two sets B and C exist that B(A,D) and C(B,D)
f(B) = f(D) and f(C) = f(A):
Essential hazards are inherent for any logic function and do not depend on implementation of function.

## Slide 17: Example
fmin = ~x1x3 + x2;
Inputs change from A to C
if 000  001  101, f changes
0  1  0
The function has static essential hazard
Inputs change from A to D
If 000  001 101  111, f changes
0  1  0  1
The function has dynamic essential hazard.
Changes of input signals must be limited by unit-distant combinations.
 | x1 x2 x3 | f
A | 0 0 0 | 0
B | 0 0 1 | 1
 | 0 1 0 | 1
 | 0 1 1 | 1
 | 1 0 0 | 0
C | 1 0 1 | 0
 | 1 1 0 | 1
D | 1 1 1 | 1

## Slide 18: Logical (Timing) Hazards
The second requirement
Logical hazards occur on account delays in wires and logical gates.
Example:
f 0 – 1 – 0
x
10
01
If wire delay < inverter delay

## Slide 19: Logical (Timing) Hazards (2)
Definition 1:
Combinational circuit has logical static hazard by changing input set from A to B if:
  f(A) = f(B)
  There aren’t essential static hazards between sets A and B in the output circuit may occur single hazard 01 0 or 1  0 1.
Definition 2:
Combinational circuit has logical dynamic hazard by changing input set from A to B if:
  f(A)  f(B)
  There aren’t essential dynamic hazards between sets A and B in the output circuit may occur multiple hazards 01 0  1 or 1  0 1 0.

## Slide 20: Static Hazard: Example 1
Each gate has delay (marked as 1, 2, 3).
Let input set (collection) be 010. Output signal is 1.
At changing input set from 010 to 011 short-time signal (glitch) equal to 0 occurs at the output if 1<2.
It is static -1 hazard.
Y = x1x3 + x2 x3
x1 1
x3 1
x2 1
x3 0
1 0 1
y
1
2
3
1 0
01

## Slide 21: Finding Static Hazard Using Karnaugh Maps
The way to eliminate the hazard:
Include extra product terms (AND gates) to cover the hazardous input pairs.
Add consensus term x1x2. Then y = x1x3 + x2x3 +x1x2.
Karnaugh map for given function y = x1x3 + x2 x3
x1
x2x3
00
01
11
10
1
1
1
1
0
1

## Slide 22: Example 1
Static hazard-free circuit
1
0
x1
x3
x2
y

## Slide 23: Example 2
f= (x2+x3)(x1 +x3)
0
0
f 0  1  0
x1
x3
x2
x3
4
5
0
0
0
1
0
1
1
1
1
1
2
3
4
5
6
x3
x2
x1
00
01
11
10
0
1
x1
x2x3
f
1
1
1
1
f= (x2+x3)(x1 +x3) (x1+x2).
x1
x3
x2
x3
f

## Slide 24: Example 3
1 |  |  | 1
1 | 1 |  | 
1 | 1 | 1 | 1
 |  | 1 | 1
cd 00 01 11 10
ab
00
01
11
10
D3
1 |  |  | 1
1 | 1 |  | 
1 | 1 | 1 | 1
 |  | 1 | 1
cd 00 01 11 10
ab
00
01
11
10
D3
Y = a b d + b c + a c
a
b
c
d
d
a
b
c
Y = a b d + b c + a c +
+ a c d + ab +b c d
Hazard-free SOP

## Slide 25: Dynamic Hazards





y
x1
x2
x3
x4
x5
01110 11110
1  0,  0 1,
If  changes faster than , there is static hazard on  output: 1  0  1.
If  change only after  has static hazard, 1010 can occur on output y.

## Slide 26: Feedback Sequential Circuits
Asynchronous FSM - circuits with feedback.
In the scheme with n loops feedback there are n binary state variables and 2n states. All latches and flip-flops are circuits with feedback.
Each of them has at least one feedback loop, which provides storage of zero or one. Feedback loops are memory elements. Any circuit with a feedback loop is of type RS or D latch.

## Slide 27: General Structure of a Latch
Characteristic equation of RS-latch: Q* = S + RQ.
Characteristic equation of D-latch: Q* = CD + CQ.
Excitation
Logic


Q*
Q
Q
Feedback loop
Control
Inputs

## Slide 28: RS Latch, D Latch
Q
S
R
D
Q
C
0
10
01
10
10
0
1
1
2
Unreliable D Latch
RS Latch

## Slide 29: Hazard-Free D-Latch
D
Q
C
D
00
01
11
10
0
1
D
CQ
Q*
1
1
1
C
1
Q

## Slide 30: Anti-Race State Assignment
The unit-distance assignment is not possible since graph contains cycles of odd length.
Example: given transition graph
11
10
11
01
01
10
00
11
01
11
00
00
00
10
S1/1
S0/0
S3/1
S4/0
S2/0

## Slide 31: Anti-Race State Assignment (2)
To remove odd length cycles, include extra state into transitions S2 S0 and S4 S0.
10
11
10
11
01
01
00
11
01
11
00
00
00
10
00
S1/1
S0’/0
S0’’/0
S2/0
S3/1
S4/0

## Slide 32: Flow-Table
Stable states have been marked
Present State | Code | Next State |  |  |  | 
 |  | Inputs |  |  |  | Output
 |  | 00 | 01 | 10 | 11 | 
S0` | 0 0 0 | 000 | 010 | 100 | - | 0
S0`` | 0 0 1 | 000 | - | - | - | 
S1 | 0 1 0 | - | 010 | - | 011 | 1
S2 | 0 1 1 | 001 | - | 011 | 011 | 0
S3 | 1 0 0 | 100 | - | 100 | 101 | 0
S4 | 1 0 1 | 001 | 101 | - | 101 | 1

## Slide 33: “One-Hot” State Assignment
This method use one state variable for each state
S1/1
S2/0
10
11
01
01
S0/0
10
00
S3/1
S4/0
11
01
11
00
00
10
11
11
S12
00
S20
01
S01
10
S03
11
S34
S40
00
00
 | q0 q1 q2 q3 q4
S4 S3 S2 S1 S0 | 0 0 0 0 1 0 0 0 1 0 0 0 1 0 0 0 1 0 0 0 1 0 0 0 0
S40 S34 S20 S12 S03 S01 | 1 0 0 0 1 0 0 0 1 1 1 0 1 0 0 0 1 1 0 0 1 0 0 1 0 1 1 0 0 0

## Slide 34: “One-Hot” State Assignment
Intermediate states are represented by all zeroes except for ones corresponding two state variables associated with terminal states.
Two state variables switch at any transition.

## Slide 35: Flow Table for “One-Hot” Assignment
Present state | Code q0q1q2q3q4 | Inputs |  |  |  | Output
 |  | 00 | 01 | 10 | 11 | 
S0 | 1 0 0 0 0 | 10000 | 11000 | 10010 | - | 0
S01 | 1 1 0 0 0 | - | 01000 | - | - | 0
S03 | 1 0 0 1 0 | - | - | 00010 | - | 0
S1 | 0 1 0 0 0 | - | 01000 | - | 01100 | 1
S12 | 0 1 1 0 0 | - | - | - | 00100 | 1
S2 | 0 0 1 0 0 | 10100 | - | 00100 | 00100 | 0
S20 | 1 0 1 0 0 | 10000 | - | - | - | 0
S3 | 0 0 0 1 0 | 00010 | - | 00010 | 00011 | 0
S34 | 0 0 0 1 1 | - | - | - | 00001 | 0
S4 | 0 0 0 0 1 | 10001 | 00001 | - | 00001 | 1
S40 | 1 0 0 0 1 | 10000 | - | - | - | 1

## Slide 36: Steps of Desing a Feedback Sequential Circuit
Devise a state diagram for an FSM that implemented the required functional behavior
Derive the flow table and reduce the number of states if possible
Perform the state assignment and derive the excitation table
Obtain the next-state and output expressions
Construct a circuit that implements these expressions

## Slide 37: Example: Asynchronous T Flip-Flop Design
Transformation of a graph of T flip-flop to a new graph with stable states
S0/0
S1/1
0
0
1
1
0
0
S0/0
S1/1
S0`/0
1
0
S1`/1
1
1
1
0

## Slide 38: Asynchronous T Flip-Flop Design
Primitive flow table
Race-free assignment
Designing of T flip-flop based on two RS-latches
Stable states have been marked
Pres. T state | 0 | 1 | Output
S0 | S0 | S0` | 0
S0` | S1 | S0` | 0
S1 | S1 | S1` | 1
S1` | S0 | S1` | 1
State | q1q2
S0 | 0 0
S0` | 1 0
S1 | 1 1
S1` | 0 1

## Slide 39: Excitation Functions Definition
Trans. | R S
00 | - 0
01 | 0 1
10 | 1 0
11 | 0 -
T
q1q2
00
01
11
10
0
1
00
00
11
11
10
01
01
10
T
q1q2
00
01
11
10
0
1
0
0
-
1
0
-
-
0
S2
S1
T
q1q2
00
01
11
10
0
1
0
0
-
-
1
0
0
-
R1
T
q1q2
00
01
11
10
0
1
-
-
0
0
0
-
1
0
T
q1q2
00
01
11
10
0
1
-
1
0
0
-
0
0
-
R2
State Table
Excitation Functions

## Slide 40: Asynchronous T Flip-Flop Circuit
R1 = Tq2; S1 = Tq2;
R2 = Tq1; S2 = Tq1;
q2
q2
q1
q1
T
S1
R1
S2
R2
This circuit is very reminiscent master/slave scheme - t6

## Slide 41: Asynchronous T Flip-Flop Circuit (2)
q1* = ~Tq1 + T~q2 + q1~q2; q2* = ~Tq1+Tq2 + q1q2;
q1* = ~Tq1 + T~q2+q1~q2 =~T q1 T ~q2 q1 q2;
q2* = ~Tq1 + Tq2 + q1q2 =~Tq1 Tq2  q1q2 ;
T
q1q2
00
01
11
10
0
1
0
0
1
1
1
0
0
1
q1*
T
q1q2
00
01
11
10
0
1
0
0
1
1
0
1
1
0
q2*

## Slide 42: Asynchronous T Flip-Flop Circuit (3)
T
q1*
q2*
q1
q2
q1
This circuit is faster than the previous one - t 3

## Slide 43: Asynchronous 3-state Counter Synthesis
0
0
0
0
0’
1’
2
1
2’
1
1
0
0
1
1
000
001
011
010
110
100
1
1
0

## Slide 44: Primitive Flow Table
S X | 0 | 1
000 | 000 | 001
001 | 011 | 001
011 | 011 | 010
010 | 110 | 010
110 | 110 | 100
100 | 000 | 100

## Slide 45: Excitation Functions
x
x
1
1
-
-
1
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
q1*
1
q1
q2
1
1
-
-
-
q3x 00 01 11 10
q1q2
00
01
11
10
q2*
q2
q1
1
1
1
1
-

## Slide 46: Excitation Functions
1
-
-
-
q1q2
00
01
11
10
q2
1
1
1
-
q1
q1* =q2q3x+q1q2+q1x
q2* = q1q2+q2x+q3x
q3* = q1q2x+q2q3+q3x
Static hazards are removed
Next state functions q1*,q2* ,q3*.
q3x 00 01 11 10
q3*
x

## Slide 47: Counter Circuit
X
q1*
q1
q2*
q2*
q3*
q3*
q2
~q3
~X
q1
q2
q1
X
~q1
q2
q2
~X
~X
~X
q3
~q1
~q2
X
~q2
q3

## Slide 48: Analysis of Asynchronous FSM
Example 1.The analysis of designed circuit (asynchronous T flip-flop circuit)
The next state function for given circuit is the following:
q1* = q1~q2 + T~q2+~Tq1
q2*=q1q2+Tq2+~Tq1
These can be represented on Karnaugh maps
Аs expected, there are no hazards in Karnaugh maps for q1* and q2*.
T
q1q2
00
01
11
10
0
1
0
0
1
1
1
0
0
1
q1*
T
q1q2
00
01
11
10
0
1
0
0
1
1
0
1
1
0
q2*

## Slide 49: Analysis of Asynchronous FSM (2)
Combining Karnaugh maps gives the following map:
This is flow-table for asynchronous T flip-flop
T
q1q2
00
01
11
10
0
1
00
00
11
11
10
01
01
10
q1*q2*

## Slide 50: Analysis of Asynchronous FSM (3)
Example 2
q
p
Y1
Y2
y1
y2
Z

## Slide 51: Analysis of Asynchronous FSM (3)
Y1 =y1p + p q y2; Y2 = y2 p + y1 p q;
p
q
pq 00 01 11 10
y1y2
00
01
11
10
Y1
1
1
1
1
y1
y2
1
q
pq 00 01 11 10
y1y2
00
01
11
10
Y2
1
1
1
1
y1
y2
p
1
Rows are state variable combinations, columns are input combinations

## Slide 52: Analysis of Asynchronous FSM (3)
Combine maps. Y-map
q
A – 00, B – 01, C – 10, D -11 (transient state)
A/0
0001
B/0
10
1011
0001
C/1
11
1011
0001
pq 00 01 11 10
y1y2
00
01
11
10
Y1Y2
10
10
11
11
y1
y2
00
00
00
00
00
00
00
00
01
10
01
01
p

## Slide 53: State Adjacency Diagram
The adjacency diagram is a simplified state diagram that omits self-loops and does not show the directions of transitions.
Two states are adjacent if there is an arc between them in the state adjacency diagram.
11
10
11
01
01
10
00
11
01
11
00
00
00
10
S1/1
S0/0
S3/1
S4/0
S2/0
Given graph
S1
S0
S3
S4
S2
Adjacency diagram

## Slide 54: Anti-Race Assignment
S0
S1
S2
S3
S0
Race-free assignment using 3-cube.
Each state in original state diagram is represented by two equivalent states
S1
S2
S3
S0
S21
S31
S11
S01
000
100
111
010
011
110
001
101
The worst possible adjacency diagram for four states

## Slide 55: Other Variants of Assignment
S0
S1
S2
S3
000
100
101
111
011
001
110
010
S0
S0
S1
S1
S3
S2
S2
000
100
101
111
011
010
001
110
S3

## Slide 56: Comparison on Synchronous and Asynchronous FSM
Synchronous:
  Circuits that use a clock to separate consecutive system states from one another.
Asynchronous:
  Circuits that define states in terms of input values and internal actions
  Avoid clock distribution problems
  Consume power only when needed
  Global synchrony does not exist
Synchronous:
  May be used abstract model FSM for synthesis
  Simplicity for synthesis
Asynchronous:
  Impossible use abstract model FSM for synthesis
  Asynchronous design is often unavoidable. Asynchronous interfaces, arbiters, etc.

## Slide 57: Pipeline
Pipelining – popular design technology which is often used to accelerate the operation of processor equipment.
Example: consider a circuit for computing log2|a+b|. а and b signals represent numbers’ flow.

log
a
b
clk
clk
clk
output
Tmin= tclk-to-Q + tpd,logic + tsetup + tskew + tjitter
Tpd, logic – signal propagation delay through adder, circuits that define module and logarithm. This delay is more than the one of the registers.

## Slide 58: Pipeline (2)
Assume that all logic blocks have equal propagation delay. In this case each block will be active only one third cycle.
Application of pipeline processing will increase throughout the device.
Synchronous pipeline

log
a
b
clk
clk
clk
output
clk
clk

## Slide 59: An Example of Pipelining
Tmin.pipe = tclock-to-q +max(tpd,add, tpd,mod, tpd,log)
S=Twithout pipe /Tpipe=NK/(N+K-1)
S (speed-up, N – number of entries, K – number of pipeline stages.)
Beginning from cycle 3, result gives out in each cycle.
Cycle | Sum | Module | Logarithm
1 | a1+b1 |  | 
2 | a2+b2 | ¦a1+b1¦ | 
3 | a3+b3 | ¦a2+b2¦ | log¦a1+b1¦
4 | a4+b4 | ¦a3+b3¦ | log¦a2+b2¦
5 | a5+b5 | ¦a4+b4¦ | log¦a3+b3¦
6 | a6+b6 | ¦a5+b5¦ | log¦a4+b4¦

## Slide 60: Example
Y = (a + b) + (c + d)
+
+
+
a
b
c
d
y
ra
ry
rb
rc
rd
Tmin= TCLK-Q + 2*TCOMB, MAX + TSETUP + TSKEW + TJITTER+TT

## Slide 61: Pipelined Addition
+
+
a
b
d
+
c
y
Tmin= TCLK-Q + TCOMB, MAX + TSETUP + TSKEW + TJITTER+TT.

## Slide 62: Description of Pipeline in Verilog
module pipelined_adder (a,b,c,d,clk,y_reg);
parameter n=16;
input [n-1:0] a,b,c,d;
input clk;
output reg[n+1:0] y_reg;
reg[n-1:0] ra, rb, rc, rd;
reg[n:0] pab, pcd;
wire[n:0] sum1,sum2;
wire[n+1:0] sum3;
always @(posedge clk)
begin ra<=a; rb<=b; rc<= c; rd<=d; end
assign sum1=ra+rb;
assign sum2=rc+rd;
always @(posedge clk)
begin
pab<=sum1;
pcd<=sum2;
end
assign sum3=pab+pcd;
always @(posedge clk)
y_reg<= sum3;
endmodule

## Slide 63: Synchronous Pipeline
Rhythm of all events is given by a clock generator
Implicit (global) synchronization:
Clock period T > Max (tpd1, tpd2, tpd3) + tpdreg
R1
R2
R3
R4
CL
CL
CL
CL
CL1
CL2
CL3
CLK

## Slide 64: Asynchronous Pipeline (Self-Timed)
Explicit (local) synchronization:
Req/Ack handshakes.
Generation completion signals “Request/Acknowledgement”
Handshaking protocol
R1
R2
R3
R4
CL
Req
Ack
CL1
CL2
CL3
Req
Ack
Ack
Req
Req
Ack

## Slide 65: 2-Phase Protocol
Sender
Receiver
Request
Acknowledgment
Data
Sender action
Receiver action
Ack
1
1
2
3
1
Data
Req
Cycle 1
Cycle 2

## Slide 66: 2-Phase Protocol (2)
Sender puts data on the bus (1) and generates event (Req (2) changes polarity).
Getting the request, receiver accepts data (if possible) and forms Ack (3).
If the receiver is busy, Ack is not formed and the sender is blocked until the receiver is free.
As soon as Ack is generated, the sender gives out next data word.
C-element of Muller generates completion signal.

## Slide 67: Completion Detection: Muller’s C-element
A
C
B
F
Output of C-element is a copy of its inputs if they are identical.
If the given condition is not met, output does not change.
A
B
F
S
R
A B | Fn+1
0 0 0 1 0 1 1 | 0 Fn Fn 1

## Slide 68: Implementation of 2-Phase Protocol Using Muller’s C-element
Sender
Receiver
Data
C
Ack
F
Req
DataReady
DataAccepted
Advantages: simplicity and speed Disadvantages: transitions which initialize events can occur in any direction (01, 10).

## Slide 69: 4-Phase Handshake Protocol
This protocol is also known as RTZ (Return-To-Zero).
Difference: before the beginning of the next cycle, all signals return to the initial state.
Req
2
4
3
1
Data
Ack
5
6
Sender’s action
Receiver’s action

## Slide 70: 4-Phase Handshake Protocol (2)
In the beginning of cycle Req = Ack =0.
As soon as a new data word (1) occurs, Req signal passes into higher level (2) - Req .
When the receiver is ready, it will receive data (Ack (3)).
Then Req (4) and Ack (5) signals pass into lower level.
Only after that the sender is allowed to put new data on the bus.
DataReady and DataAccepted signals must be impulse.
Disadvantages - complexity and lower speed.
Advantages – reliability.

## Slide 71: Implementation of 4-phase Protocol Using C-elements
Sender
Receiver
Data
C
Ack
F
Req
DataReady
DataAccepted
C
S

## Slide 72: Example: Memory Read Cycle
Transition signaling, 2-phase
Valid address
Address
Valid data
Data
Addr
Data
Addr
Data

## Slide 73: Example: Memory Read Cycle (2)
Transition signaling, 4-phase
Valid address
Address
Valid data
Data
Data
Addr
Addr
Data

## Slide 74: Self-Timed Pipelined Datapath
R1
R2
R3
R4
CL1
CL2
CL3
Input
HS
HS
HS
Start
Done
Req
Req
Start
Done
Start
Done
Ack
Ack
Ack
Ack
Req
Req
Output

## Slide 75: Self-Timed Pipelined Datapath (2)
Output
R1
R2
R3
R4
CL1
CL2
CL3
C
C
C
C
C
C
C
Input
Req1
Ack1
En1
Start1
Done1
En2
Start2
Done2
En3
Start3
Done3
En4
Ackout
Req2
Ack2
Req3
Req4
All Req, Ack signals turn to 0 (zero activity of the circuit).
All Start signals have low level.
Req1 En1 - input data are stored in R1.
Start 1 - CL1 launches. (Ack1 Req1 ).
After completion of computing CL1 puts data on the bus (Done), Req2Ack2Start1 (CL1 block is ready for new data processing).

## Slide 76: Diagram of Transition for 1-st Cascade
Reqi
Ack1
Req1
Ack1
Start
Ack2
Start
Ack2
Req2
Req2
C-element 1
C-element 2
Nodes – events, arrows – dependencies.
dashed arrows - next cascade