## Slide 1: Static Timing Analysis
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2
CONFIDENTIAL INFORMATION
The information contained in this presentation is the confidential and proprietary information of Synopsys. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Synopsys without prior written authorization.
IMPORTANT NOTICE
In the event information in this presentation reflects Synopsys’ future plans, such plans are as of the date of this presentation and are subject to change. Synopsys is not obligated to update this presentation or develop the products with the features and functionality discussed in this presentation. Additionally, Synopsys’ services and products may only be offered and purchased pursuant to an authorized quote and purchase order or a mutually agreed upon written contract with Synopsys.

## Slide 3: Course Overview
STA Concepts
  1 lecture
Delay Modeling
  1 lecture
Interconnect Parasitics
  1 lecture
Delay Calculation
  1 lecture
Configuring the STA Environment
  1 lecture
Timing Checks
  1 lecture
Crosstalk and Noise
  1 lecture

## Slide 4
Crosstalk and Noise

## Slide 5: Crosstalk
Cc4
Cc3
Cc1
Cc2
Cc5
N1
N2
N3
1
0
Gitch

## Slide 6: Crosstalk Definition
Mechanisms that cause crosstalk
Mutual capacitance
Mutual inductance
Mutual Capacitance, Cm Mutual Inductance, Lm
Cm
Aggressor
Victim
Lm
Aggressor
Victim
Notes: 6
IDESA - IC Design Skills for Advanced DSM Technologies
Crosstalk is the most common SI problem. The crosstalk is electrical interaction between two long nets. The causes of the crosstalk are: long parallel nets, coupling capacitance or inductance and high frequency switching. If signals in two neighboring parallel nets change in the same direction, then speed-up occurs, and if in the opposite direction, slow-down occurs. Coupling not only changes the delay on a wire but can also induce coupling noise. The concept of crosstalk requires to define a “victim” and “aggressor” net.
Mutual capacitance is one of the two mechanisms that cause crosstalk
Mutual capacitance is the coupling of two conductors via the electric field. Mutual capacitance will inject a current onto the victim line proportional to the rate of change of voltage on the driven line. Since the induced noise is proportional to the rate of change, mutual capacitance becomes very significant in high-speed digital applications.
Mutual inductance is another mechanism that causes crosstalk.
Mutual inductance induces current from a driven line onto a quiet line by means of the magnetic field. The mutual inductance will inject a voltage noise onto the victim proportional to the rate of change of the current on the driver line. Since the induced noise is proportional to the rate of change, mutual inductance becomes very significant in high-speed digital applications.

## Slide 7: Capacitive Coupling
Wire A
Wire B
Capacitive Coupling
Notes: The main reason of SI problems is the parasitic capacitive coupling between parallel interconnects located near each other. With the scaling to deep sub-micron processes capacitive coupling has become a major concern because in case of submicrometer designs routing complexity has increased dramatically and as a result more metal layers are being added to silicon. The width of the metal is continuously being decreased whereas to keep the metal resistance low, the height of the metal wires is being increased. Furthermore, metal wire lengths are now longer than ever. All this leads to considerable increase of capacitive coupling.
7

## Slide 8: Noise Effects Types
Delay
  Coupling of switching activity of the victim with the switching activity of the aggressors
Glitch
  Noise caused on a steady victim signal

## Slide 9: Crosstalk Delay
Cload
Timing Error
1.5V
1.5V
0V
0V
Crosstalk Delay
1.5V
0V
Notes: 9
SI issues result in two primary failure modes: timing and functional.
The first problem that crosstalk created, is in Crosstalk Delta Delay. It occurs in case when both aggressor and victim nets are switching. In that case crosstalk delay changes the signal propagation on some of the nets, reducing achievable clock speed. Crosstalk can decrease or increase the delay depending on whether the victim and aggressor are switching in the same or different direction.
In case of passing into submicrometer technologies, timing problems become stricter because each new generation brings shrinking feature sizes, wire width, and wire spacing. The reduction in wire width means a decrease in total wire capacitance. However, it also means a dramatic increase in the fraction of wire capacitance resulting from lateral coupling. Improved performance translates to higher clock frequencies, with much faster switching signal slew rates. As signal slew rates increase, more noise couples onto neighboring nets.

## Slide 10: Crosstalk Glitch
A steady signal net can have a glitch due to charge transferred by the switching aggressors through the coupling capacitances
1
0
Aggressor net
Glitch
Victim net
Cc

## Slide 11: Factors Affecting Glitch
Factors for large magnitude of glitch:
  Large coupling capacitance
  Fast slew time on the aggressor
  Smaller victim net grounded capacitance
  Smaller victim net driving strength

## Slide 12: Types of Glitches
Rise and fall glitches
Overshoot and undershoot glitches
Victims
Aggressor
Fall
glitch
Rise
glitch
Undershoot
Overshoot

## Slide 13: DC Noise Margins
DC noise limits on the input of a cell while ensuring proper logic functionality
VIH and VIL are steady state noise limits
  Whether a glitch will propagate through cell
VOHmin
VOLmax
VILmax
VIHmin
Vin
Vout
Unity gain
point
Unity slope points
DC characteristics of an inverter

## Slide 14: DC Margin Limits
DC noise margin can be fixed to the same limit for all nets in the design
  Glitch level is less than VILmax and greater than VIHmin
Vdd
Vih_min
Vil_max
Vss
Safe glitches
Potentially hazardous
glitches
Glitch propagation possibility

## Slide 15: DC Margin Limits (2)
Glitches magnitude is not enough to affect output of a cell
  narrow width glitch  no effect
DC margin checks only noise rejection level is used typically
Noise height
DC noise margin
(Noise rejection level)
Safe glitches in this area
Noise width
DC Margin

## Slide 16: AC Noise Limits
Too narrow or too short glitches are safe
AC noise rejection region can be specified
Glitch height
Safe
glitch
DC noise
rejection level
Glitch width
Hazardous
glitches
AC noise rejection level

## Slide 17: Basic Glitch Removal
Smaller glitch
Cmedium
No glitch at output
Chigh
No capacitive load
Medium capacitive load
Large capacitive load

## Slide 18: Multiple Aggressors
Victim net may be capacitive-coupled to many nets
The crosstalk coupling noise effect is accumulated due to multiple aggressors
STA includes the timing correlation of the aggressor nets and determine multiple aggressors exist
1
0
Aggressor net
Glitch
Victim net
Coupling cap, Cc

## Slide 19: Crosstalk Delay Analysis
Capacitance extraction for a net consists of different capacitances
  Capacitance Cg to ground
  Coupling capacitance Cc to a neighboring net
= Distributed
RC
1.2V
0
Aggressor
Cg
Victim
Cc

## Slide 20: Crosstalk Scenarios
Aggressor net stable
  Victim net provides the charge for Cg and Cc to be charged to Vdd
  Total charge= (Cg + Cc) * Vdd
Aggressor switching in same direction
  If aggressor slew is similar  total charge by the driving cell is (Cg * Vdd)
  If aggressor slew is faster  charge smaller than (Cg * Vdd)
Aggressor switching in opposite direction
  Cc is charged from -Vdd to Vdd
  Charge on Cc changes by (2 * Cc * Vdd) before and after transitions
1.2V
0
Aggressor
Cg
Victim
Cc

## Slide 21: Positive Crosstalk
Aggressor and victim are switching in opposite directions
  Increases the amount of charge required from victim driver
  Victim delay increases
Cg
Cc
Timing Error!
1.2V
0
1.2V
0
Crosstalk delay
1.2V
0

## Slide 22: Negative Crosstalk
Aggressor and victim are switching in the same directions
  Charge on Cc remains the same before and after transitions
  Victim delay reduced
Cg
Cc
Timing Error!
1.2V
0
1.2V
0
Crosstalk delay
1.2V
0

## Slide 23: Crosstalk Timing Verification
Positive rise delay
  Rise edge moves forward in time
Negative rise delay
  Rise edge moves backward in time
Positive fall delay
  Fall edge moves forward in time
Negative fall delay
  Fall edge moves backward in time

## Slide 24: Setup Analysis
Consider the logic shown below where crosstalk can occur at various nets along the data path and along the clock paths.
The setup (or max path) analysis assumes that:
  Launch clock path sees positive crosstalk delay so that the data is launched late.
  Data path sees positive crosstalk delay so that it takes longer for the data to reach the destination.
  Capture clock path sees negative crosstalk delay so that the datails captured by the capture flip-flop early.
Data path
D Q
D Q
CK
CK
Capture clock path
Common clock
path
Common point
Launch clock path
UFF0
UFF1

## Slide 25: Hold Analysis
The worst condition for hold check occurs when both the launch clock path and the data path have negative crosstalk and the capture clock path has positive crosstalk. There is one important difference between the hold and setup analyses related to crosstalk on the common portion of the clock path.
The worst-case hold (or min path) analysis for STA with crosstalk assumes:
  Launch clock (not including the common path) sees negative crosstalk delay so that the data is launched early.
  Data path sees negative crosstalk delay so that it reaches the destination early.
  Capture clock (not including the common path) sees positive crosstalk delay so that the data is captured by the capture flipflop late.

## Slide 26: Crosstalk Analysis for Complex ICs
Hierarchical Design and Analysis
  Checks that there be no coupling between signals inside the hierarchical block
  Nets routed near boundary of the block should be shielded or avoided
Filtering of Coupling Capacitances
  Small value (below 1fF)
  Coupling ratio (below 0.001)
  Lumping small aggressors together (multiple aggressors with very small contributions)