## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Arithmetic Units

## Slide 4: Unsigned Numbers
Positional Number Systems
Decimal – base or radix=10
Binary – radix=2
А=an-1an-2an-3 . . . a1a0,a-1a-2 . . .а-m ; a{0,1}
There are n digits to the left of the point and m digits to the right of the point.
A=an-1·2n-1+an-2·2n-2+. . .+a1·21+a0·20+a-1·2-1+a-2·2-2+. . .+ a-m·2-m.
Unsigned integer number
Range (0 to 2n-1)
n-1 0

## Slide 5: Signed Numbers
S = 0 – positive number (or zero)
S = 1 – negative number Negative numbers representation
Three major schemes:
  Sign and magnitude - direct code
  One’s complement
  Two’s complement
S
n-1 0

## Slide 6: Sign and Magnitude
A=-an-2an-3 . . .a1a0
Asign&magn=1an-2an-3…a1a0
Example:
+5 – 0101
-5 – 1101
Range –(2n-1- 1) to 2n-1-1
Two representations for 0
Operands have different signs - subtract smaller (by magnitude) from larger and keep sign of the larger

## Slide 7: One’s Complement Two’s Complement
A= - an-2an-3 … a1a0
A1’scom= 1an-2an-3 … a1a0
Example:
+5 - 0101
-5 - 1010
A1’scom= 2n- 1- |A|
Range -(2n-1 -1) to 2n-1-1
A= - an-2an-3 … a1a0
A2’scom= 1an-2an-3 … a1 a0 + 1
Example:
+5 - 0101
-5 - 1011
A2’scom= 2n - |A|
Range -(2n-1) to 2n-1-1

## Slide 8: Example: Tables of Codes (n=8)
а7а6а5а4а3а2а1а0 | Unsigned | Sign&Magn | One’s compl. | Two’s compl.
00000000 | 0 | 0 | 0 | 0
00000001 | 1 | 1 | 1 | 1
. . . | . . . | . . . | . . . | . . .
01111111 | 127 | 127 | 127 | 127
10000000 | 128 | - 0 | - 127 | -128
10000001 | 129 | - 1 | - 126 | - 127
. . . | . . . | . . . | . . . | . . .
11111110 | 254 | - 126 | - 1 | - 2
11111111 | 255 | - 127 | - 0 | - 1

## Slide 9: Two’s Complement Addition
Addition:
  C = A + B
  A 0, B  0, |A|  B
  A2’ scom + B = 2n  |A| + B = B  |A|
The result is positive and carry from sign bit (2n) is discarded.
  А  0, B 0, |A|  B.
  A2’scom + B = 2n  (|A|B)= 2n  |C|= C2’scom
Example:  0011100 = +1 1100100
+ 0000100 0 0000100
 0011000 1 1101000
Example : + 0011111 = +0 0011111
 0000111 1 1111001
+ 0011000 10 0011000

## Slide 10: Two’s Complement Addition (2)
A  0, B  0:
2n  |A| + 2n  |B|= 2n  (|A| + |B|) + 2n = 2n  |C| = C2’com
The result is negative and carry from sign bit (2n) is discarded.
Summary:
  The sign bit participates in operation like other bits.
  The negative result is represented in two’s complement form.
  The carry from the sign bit is ignored
Subtraction: C = A-B = A + (-B) = A + Complemented B
0
Example :  0001101 + 1 1110011
 0011001 1 1100111
 0100110 11 011010

## Slide 11: Example
C=A+B;
A=-15;
B=-64;
|A|= 00001111; A2’comp= 11110001
|B| =01000000; B2’comp=11000000
+11110001
11000000
110110001
C2’comp =10110001
|C|=0100111179; C=-79
C=2n -|A| +2n -|B|= 2n -|C|; |C|=|A|+|B|

## Slide 12: One’s Complement Addition (2)
А  0, B 0, |A|  B.
A1’scom + B = 2n - 1- (|A|B)= 2n -1- |C|= C1’scom
A  0, B  0 +1
2n -1- |A| + 2n  |B|= 2n -1  (|A| + |B|) + 2n -1 = 2n  |C| = C1’scom
In this case end-around carry is generated
Example :  0011100 = + 1 1100011
+ 0000100 = 0 0000100
 0011000 = 1 1100111
Example :  0001101 = 1 1110010
 0011001 = 1 1100110
 0100110 =+111011000
1
1 1011001

## Slide 13: Overflow
If an addition operation produced a result that exceeds the range of the number system, overflow is said to occur.
Addition of two numbers with different signs can never produce overflow (only addition numbers with the same signs).
Example: S=A+B
-64 + 11000000 +50 + 0 0110010
-65 10111111 80 0 1010000
-129 01111111 = +127 130 1 0000010 = - 126
Negative Overflow Positive Overflow
Overflow: if the addends’ signs are the same but the sum’s sign is different from the addends’.
OVF= ~signA~signBsignC + signAsignB~signC
OVF = cncn-1
For unsigned numbers OVF=cn

## Slide 14: Adders
Half Adder
The function of the half adder is to add two binary digits, producing a sum and a carry.
Input a b | Output s cout
0 0 0 1 1 0 1 1 | 0 0 1 0 1 0 0 1
a
b
s
cout
5
s= a  b;
cout = a·b

## Slide 15: Full Adder
The function of the full adder is to add two binary digits and a carry that might be generated or propagated by the previous stage.
Input a b cin | Output s cout
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 0 1 0 0 1 1 0 0 1 0 1 1 1
s – both linear and self-dual function
cout – both majority and self-dual
function

## Slide 16: Full Adder (2)
S=a  b  c;
cout = a·b + a·cin + b·cin (majority function)
or S=~cout(a+b+cin)+a·b·cin
bcin
a
00
01
11
10
0
1
1
1
1
1
S
bcin
a
00
01
11
10
0
1
1
1
1
1
cout

## Slide 17: The Circuit of Full Adder
Cout=ab +cin(ab)
Standard approach – 6 gates
cin
a
b
s
cout
s1
c1
c2
c3

## Slide 18: The Circuit of Full Adder (2)
Cout=ab + cin(ab)= ab  cin(ab)
5 gates
cin
a
b
sum
cout
s1
c1
c2

## Slide 19: Full Adder from Two Half Adders
Half
Adder
A
B
Half
Adder
A  B
Cin
A  B  Cin
S
S
CO
CO
Cin (A  B)
A B
S
CO

## Slide 20: The Serial Adder
an-1 an-2 . . . a1 a0
A B Cin
FA
S
Cout
bn-1 bn-2 . . . b1 b0
sn-1 sn-2 . . . s1 s0
D Q
RA
RB
Clock
RS

## Slide 21: A Parallel Binary Adder
cout
(c4)
A S
B
CIN CO
A S
B
CIN CO
A S
B
CIN CO
A S
B
CIN CO
a0
b0
cin
(c0)
a1
b1
a2
b2
a3
b3
s0
s1
s2
s3
c1
c2
c3
Carry Ripple Adder.
S= A+ B; A= (a0,a1,a2,a3); B= (b0,b1,b2,b3);
S0 = a0  b0  c0; c1= a0b0 + (a0 + b0)c0;
S1 = a1  b1  c1; c2= a1b1 + (a1 + b1)c1;
S2 = a2  b2  c2; c3= a2b2 + (a2 + b2)c2;
S3 = a3  b3  c3; c4= a3b3 + (a3 + b3)c3;
Tadd= (n-1)tc + tsm  n tsm

## Slide 22: Verilog Description for 4-bit CRA
// Define a 4-bit adder
module add4(s, c_out, a, b, c_in); // I/O port declarations
output [3:0] s;
output c_out;
input [3:0] a, b;
input c_in;
// Internal nets
wire c1, c2, c3;

## Slide 23: Verilog Description for 4-bit CRA (2) (Gate Level Description)
// Instantiate four 1-bit full adders.
fulladd fa0(s[0], c1, a[0], b[0], c_in);
fulladd fa1(s[1], c2, a[1], b[1], c1);
fulladd fa2(s[2], c3, a[2], b[2], c2);
fulladd fa3(s[3], c_out, a[3], b[3], c3);
endmodule
// Define a 1-bit full adder
module fulladd(sum, c_out, a, b, c_in);
// I/O port declarations
output sum, c_out;
input a, b, c_in;

## Slide 24: Verilog Description for 4-bit CRA (3)
// Internal nets
wire s1, c1, c2; // Instantiate logic gate primitives
xor (s1, a, b);
and (c1, a, b);
and (c2, s1, c_in);
xor (c_out, c1, c2);
xor (sum, s1, c_in);
endmodule

## Slide 25: Verilog Description for 4-bit CRA (4)
module adder_4_RTL (a, b, c_in, sum, c_out);
output [3:0] sum;
output c_out;
input [3:0] a, b;
input c_in;
assign {c_out, sum} = a + b + c_in;
endmodule

## Slide 26: A 64-bit Adder/Subtractor
Tadd=TFA(A,BCout) + (N-2)TFA(CinCout) + TFA(CinS)
T = O(N) worst case delay.
N – number of bit.
Real Goal: Make the fastest possible carry path.
А S
B
CIN CO
А S
B
CIN CO
А S
B
CIN CO
а0
а1
а63
s0
s1
s63
b0
b1
b63
c64
~Add/Sub

## Slide 27: Adder/Subtractor Module in Verilog
IF (Select == 0) Addition, else Subtraction
//Data-flow description
module addsub(a, b, select, cout, sum); input [7:0] a, b; input select; output [7:0] sum; output cout; assign {cout, sum}=select?(a-b):(a+b); endmodule

## Slide 28: Inversion Property
Boolean functions S and Cout are self-dual.
S’ (A, B, Cin) = S(A’, B’, C’in); C’out (A, B, Cin) = Cout (A’, B’, C’in)
Invertors on the way of carry signal may be removed (this will minimize the critical path of carry chain).
A
B
S
Cin
FA
Cout

A
B
S
FA
Cout
Cin

## Slide 29: Carry Look-Ahead Adders
All carries are produced in parallel
ci+1 = gi + pici, where gi = aibi , pi = ai + bi (or pi=aibi).
gi­ carry generation
pi – carry propagation
Re-express the carry logic for each of the bits:
c1 = g0 + p0c0;
c2 = g1 + p1c1 = g1+ p1g0 + p1p0c0;
c3 = g2 + p2(g1 + p1g0 + p1p0c0) = g2 + p2 g1 + p2p1g0 +
+ p2p1p0c0;
c4 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3 p2p1p0c0;
Each equation corresponds to a circuit with just three levels of delay – one for generate and propagate signals, and two for the sum of products.

## Slide 30: Carry Look-Ahead Adders (2)
Partial FA
Partial FA
Partial FA
Partial FA
Carry Unit
g0
p0
p1
g1
g2
p2
g3
p3
a0
b0
a1
b1
b2
a2
a3
b3
cin
cout
c1
c2
c3
c0
c4
s0
s1
s2
s2

## Slide 31: One Stage of a Carry Look-Ahead Adder


Carry Look-ahead
Logic




ai
bi
hsi
ci
a0
ai-1
b0
bi-1
si
c0

## Slide 32: CRU (Carry Unit)
Look-ahead carry circuit (Carry Unit) forms carry signals
c4 = G + P·c0, where G = g3 + p3·g2 + p3·p2·g1 + p3·p2·p1·g0 and P = p3· p2·p1·p0·c0.
This equations formal coincide with equations ci+1=gi + pi·ci .
Look-ahead carry for 4-bit sections ALU is executed like lookahead carry for separate bits of 4-bit adder.
C0
G0
P0
G1
P1
G2
P2
G3
P3
C1
C2
C3
G
P

## Slide 33: MSI Adders
IC 74x283
Adder produces active-low versions of the carry-generate and carry-propagate signals.
Equations for half-sum:
hsi = aibi = ai·~bi +~ai·bi = =ai·~bi+ai·~ai+~ai·bi+bi·~bi=
=(ai+bi)(~ai+~bi)=(ai+bi)·~(ai·bi)=pi·~gi
And gate can be used instead of XOR gate
Equations for carry is factored
ci+1 = gi+pi·ci=pi·gi+pi·ci=pi·(gi+ci)
C0
A0
B0
A1
B1
A2
B2
A3
B3
S0
S1
S2
S3
C4

## Slide 34: Equations for Carry Signals
c1= p0·(g0+c0)
c2= p1·(g1+c1) = p1·(g1+ p0·(g0+c0))=
= p1·(g1+p0)·(g1+g0+c0)
c3= p2·(g2+c2) = p2·(g2+ p1·(g1+p0)·(g1+g0+c0))=
=p2·(g2+ p1)·(g2+g1 +p0)·(g2+g1+g0+c0)
c4 = p3·(g3+c3)= p3·(g3 + p2·(g2+ p1)·(g2+ g1+p0)·(g2+ g1+g0+c0))=
=p3·(g3 + p2)·(g3+g2+p1) · (g3+g2+g1+ p0)·(g3+g2+ g1+g0+c0)
The propagation delay from the C0 input to the C4 output is very short, about the same as two inverter gates.

## Slide 35: CLA Description in Verilog
module cla(a,b,cin, sum);
parameter n=8;
input [n-1:0] a,b;
input cin;
output [n:0] sum;
reg [n:0] sum;
reg [n:0] carry;
reg [n-1:0] g,p;
integer i;
always @(a or b or cin)
begin carry[0]=cin;
for (i=0; i<n; i=i+1)
begin
g[i] = a[i]&b[i];
p[i]= a[i]^b[i];
carry[i+1] = g[i]|(p[i]&carry[i]);
sum[i]=p[i]^carry[i];
end
sum[n]=carry[n];
end
endmodule

## Slide 36: Multi-bit Adders. Ripple-Block Carry Look-Ahead Adder
C0
Block
0
Block
1
Block
2
Block
3
A[3:0]
B[3:0]
A[7:4]
B[7:4]
A[11:8]
B[11:8]
A[15:12]
B[15:12]
C4
C8
C12
C16
Tadd = (N/B)tcarry_lookahead_logic
B – number of bits in block
tcarry_lookahead_logic – t( c0 c4)

## Slide 37: A 16-bit Group-Ripple Adder
S[0:15]
N- the number of bits, B – the number of bits in group, Tadd=(N/B)·t(c0c4)=4·3=12, where N/B – the number of groups
Cin
Cout
B[0:15]
C0
А0 S0
B0
A1 S1
B1
A2 S2
B2
A3 S3
B3
C4
C0
А0 S0
B0
A1 S1
B1
A2 S2
B2
A3 S3
B3
C4
C0
А0 S0
B0
A1 S1
B1
A2 S2
B2
A3 S3
B3
C4
C0
А0 S0
B0
A1 S1
B1
A2 S2
B2
A3 S3
B3
C4
A[0:15]
1
1
2
2
3
3
4
4
5
6
7
8
8
7
6
5
7
9
9
10
10
11
11
12
12
13
13
14
14
15
15
16
16
1
2
3
4
5
6
8
9
10
11
12
12
13
14
16
Carry look-ahead within block, carry ripple between blocks

## Slide 38: Block Carry Look-Ahead Adder
T = (tcarry_lookahead)3 + tsetup) – worst case delay
Tsetup - time for forming G’s and P’s.
Carry look-ahead within block, carry look-ahead between blocks
CLA
C0
Block 0
CLA
Block 1
CLA
Block 2
CLA
Block 3
CLA
A[3:0]
B[3:0]
A[7:4]
B[7:4]
A[11:8]
B[11:8]
A[15: 12]
B[15:12]
C4
C8
C12
C16
S[3:0]
P0
G1
P1
P2
G2
P3
G3
G0
S[7:4]
S[11:8]
S[15:12]

## Slide 39: Block Carry Look-Ahead Adder
Capital letters G(Group generate),P(Group propagate), C4 – carry from group0
G0 = g3 + p3g2 + p3p2g1 + p3p2p1g0 ; P0 = p3p2p1p0;
C4 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3 p2p1p0c0=G0+P0c0
G1 = g7+p7g6 + p7p6g5 + p7p6p5g4; P1 = p7p6p5p4;
C8 =g7+p7g6 + p7p6g5 + p7p6p5g4 + p7p6p5p4C4 = G1 +P1C4=
= G1+P1G0 +P1P0c0;
G2=g11+p11g10 + p11p10g9 + p11p10p9g8; P2 = p11p10p9p8;
C12=G2 + P2G1 + P2P1G0 +P2P1P0c0;
G3=g15+p15g14 + p15p14g13+ p15p14p13g12; P3 = p15p14p13p12;
C16=G3 + P3G2 + P3P2G1 +P3P2P1G0 + P3P2P1P0c0;
GG= G3 + P3G2 + P3P2G1 +P3P2P1G0; PG= P3P2P1P0c0;

## Slide 40: Block Carry Look-Ahead Adder
The delay signal c16 definition
In general, T = 1 + 2(2L-1) +2, where L – the number of levels
Function | Number of Gates
gi, pi generation | 1
C,G generation | 2
G3, P3 generation | 3 2
Si generation | 2
C16 time generation | 1+ 6 + 2=9

## Slide 41: Carry Bypass Adder (Carry Skip Adder)
The following 3 functions are formed in each bit of the adder:
G = Ai Bi(Generate);
P = AiBi(Propagate)
K= ~Ai~Bi (Annihilate (kill))

## Slide 42: Carry Bypass (Skip) Adder
The idea of carry bypass adder:
P0=a0+b0; P1=a1+b1; P2=a2+b2;P3=a3+b3.
If P0 P1 P2 P3 =1, then Cout=Cin, else Cout = C4 (Generate). BP – block propagation.
FA
FA
FA
FA
MUX
a0 b0
a1 b1
a2 b2
a3 b3
BP = P0P1P2P3
Cin
Cout
C4
S0
S1
S2
S3
0
1

## Slide 43: Carry Bypass (Skip) Adder
Worst-case delay  carry from bit 0 to bit 15 = carry generated in bit 0, ripples through bits 1, 2, and 3, skips the middle two groups (B is the group size in bits), ripples in the last group from bit 12 to bit 15.
Tadd = tsetup + B tcarry + ((N/B) - 2) tskip +(B-1) tcarry + tsum tsetup- time for forming g’s and p’s.
S0 - S3
Cin
B3
Bit 12-15
Setup
Carry Propa-gation and C0
Setup
Carry Propa-gation and C1
Setup
Carry Propa-gation and C2
Setup
Carry Propa-gation and C3
Sum
Sum
Sum
Sum
B0
Bit 0-3
B1
Bit 4-7
B2
Bit 8-11
BP0
BP0BP1
BP0BP1BP2
BP0BP1BP2BP3
Cout
0
1
C0
C1
C2
C3
BP0
BP1
BP2
BP3
S4 – S7
S8 – S11
S12 – S15
0
1
1
1
0
0

## Slide 44: Carry Skip Adder (2)
C0 – carry from B0, C1 – carry from B1, C2 – carry from B2,
C3 – carry from B3.
tsetup - time necessary for creating generation and propagation signals (gi,pi).
tcarry – one bit propagation signal delay.
tbypass – propagation signal delay through bypass multiplexer.
tsum – time required for forming sum of the last bit.
Dependence of timing delay from the number of bits is more acceptable than in CRA (is also linear function but with less angular coefficient).

## Slide 45: Optimal Skip Block Size and Add Time
Carry ripple is implemented in the blocks.
Accept tcarry = tskip = tsetup = 1; then
Тadd =1 + B +(N/B –2) + B + 1 = 2B + N/B-1 ;
dTadd/dB = 2 – N/B2;
dTadd/dB = 0 at Bopt = (N/2)
Topt = 4√(N/2) – 1 = 2√(2N) – 1

## Slide 46: Carry Select Adder
Fixed-block-size carry select adder
Variable-block-size carry select adder
Fixed-block-size CSeA: N bit circuit is divided into M blocks by B bits.
Precompute the carry out of each block for both carry_in = 0 and carry_in = 1 (can be done for all blocks in parallel) and then select the correct one.
The adder circuit is completed about 30%.

## Slide 47: Carry Select Adder
S[k+3:k+0]
Carries generation
Carries generation
A[k+3:k]
B[k+3:k]
C=1
C=0
MUX
Setup
P[k+3:k]
G[k+3:k]
Sum
0
1
C[k+3:k+1]0
C[k+3:k+1]1
0
1
C[k]
C[k+1]

## Slide 48: Carry Select Adder
Cin0
P’s
Setup
Carries 0
Carries 1
MUX0
SUM
Setup
SUM
Setup
SUM
Setup
SUM
0
1
0
1
0
1
0
1
Cout
Block 3
A[15:12],B[15:12]
Block 2
A[11:8] , B[11:8]
Block 1
A[7:4] , B[7:4]
Block 0
A[3:0] , B[3:0]
S[15:12]
S[11:8]
S[7:4]
S[3:0]
C4
C8
C12
1
1
5
6
5
7
8
9
10
G’s
P’s
C’s0
C’s1
P’s
P’s
Carries 0
Carries 1
MUX1
C’s1
P’s
C’s
C’s0
P’s
Carries 0
Carries 1
MUX2
C’s1
P’s
C’s
Carries 0
Carries 1
MUX3
C’s1
P’s
C’s
P’s
C’s
G’s
G’s
G’s
P’s
P’s
P’s
C’s0
C’s0

## Slide 49: Carry Select Adder
N bit circuit is divided into M blocks by B bits.
Precompute the carry out of each block for both carry_in = 0 and
carry_in = 1 (can be done for all blocks in parallel) and then select
the correct one.
The adder circuit is completed about 30%.
Tadd = tsetup + B tcarry + m tmux + tsum;
m=N/B – number of blocks

## Slide 50: Carry Select Adder (Square Root)
The peculiarity of this circuit:
  Time of appearance of carry signals differ.
The result of carry chain are set earlier than signals of multiplexers. Difference in the last cascade - 5 and 8.
Propagation delays in all paths:
  Each next cascade has one bit more than the previous one.

## Slide 51: Carry Select Adder (Square Root) (2)
Cin0
P’s
Setup
Carries 0
Carries 1
MUX1
SUM
Setup
SUM
Setup
SUM
Setup
SUM
0
1
0
1
0
1
0
1
Cout
Block 4
A[19:14],B[19:14]
Block 3
A[13:9], B[13:9]
Block 2
A[8:5], B[8:5]
Block 1
A[4:2], B[4:2]
S[19:14]
S[13:9]
S[8:5]
S[4:2]
C5
C9
C14
1
5
7
5
7
8
9
G’s
P’s
C’s0
C’s1
P’s
P’s
Carries 0
Carries 1
MUX2
C’s1
P’s
C’s
C’s0
P’s
Carries 0
Carries 1
MUX3
C’s1
P’s
C’s
Carries 0
Carries 1
MUX4
C’s1
P’s
C’s
P’s
C’s
G’s
G’s
G’s
P’s
P’s
P’s
C’s0
C’s0
Setup
Carries 0
Carries 1
MUX1
SUM
0
1
S[1:0]
1
3
4
G’s
P’s
C’s0
C’s1
P’s
P’s
C’s
4
6
6
Block 0
A[1:0], B[1:0]

## Slide 52: Carry Save Adder
At addition of N n-bit numbers, the number of bits of sum will equal [log2N]+n. CSA is used for adding more than two numbers together.
Consider addition of three numbers. In this case two vectors are formed: sum vector S and carry vector C:
Example: x+y+z=s+c
x: 1001111
y: 1100100
z: + 0001111
s: 0100100
c: +1001111
sum: 11000010

## Slide 53: Circuit of Adder of 3-х 4-bit Numbers (unsigned)
A B
A B
A B
A B
A B
A B
Cin
Cout S
Cin
Cout S
Cout S
Cin
Cin
Cout S
Cin
Cin
A
B
A
B
FA
FA
FA
FA
HA
HA
FA
FA
Cout
Cout
Cout
Cout
x0 y0 z0
x1 y1 z1
x2 y2 z2
x3 y3 z3
sum0
sum1
sum2
sum3
sum4
sum5

## Slide 54: Conditional Sum Adder
n-bit adder is divided into two groups by n/2 bits. The older
group is duplicated, so three adders by n/2 bits are included in the circuit.
SMLow
ALow
SMHigh
SMHigh
BLow
BHigh
AHigh
MUX
MUX
Cin =1
Cin =0
Cout0
Cout1
CoutL
Cout
Tadd = N/2tcarry + tmux

## Slide 55: Conditional Sum Adder in Verilog
module conditional_sum_adder(A,B, cin, sum,cout);
input [15:0] A,B;
input cin;
output [15:0] sum;
wire[15:0] sum;
output cout;
wire cout, cout_low,cout0,cout1;
wire [7:0] sum_low, sum_high;
wire [7:0] sum_high0, sum_high1;
assign {cout_low, sum_low} = A[7:0] + B[7:0] + cin;
assign {cout0, sum_high0} = A[15:8] + B[15:8];
assign {cout1, sum_high1} = A[15:8] + B[15:8]+1;
assign sum_high = cout_low? sum_high1:sum_high0;
assign sum={sum_high, sum_low};
assign cout = cout_low? cout1:cout0;
endmodule

## Slide 56: The Structure of Execution Unit (EU)
EU – example of digital system.
“Data path” or operational unit - hardware that actually performs the data processing.
Consists of registers, adders, another logical elements and wires.
Controller or control unut (CU) produces control signals, that bring to execution.
Formal model of controller - FSM
Data Path
Controller
Data in
Data out
Command
Done
X
Y
CLK
Separation of the Design into Data Path and Controller

## Slide 57: EU for Integer Multiplication (Unsigned)
RA
 RB
SM
0
MUX
 RC(acc)
CT
n

Control
Unit
multiply
y1 y2 y3
n bit
n bit
n bit
RA – multiplicand, RB – multiplier, RC (accumulator) - product
Possible to combine multiplier and product register (low bits)

## Slide 58: Example of Unsigned Multiplication
Acc(RC) | RB | CT | 
0000 | 1010 | 4 | 
0000 | 0101 | 3 | shift
+ 0000 1101 1101 |  |  | add
0110 | 1010 | 2 | shift
0011 | 0101 | 1 | shift
+0011 1101 10000 | 0100 |  | add
1000 | 0010 | 0 | shift
A=1101; B=1010;
Signed multiplication:
convert negative numbers to positive,
execute unsigned multiplication,
remember the original signs.

## Slide 59: HandShake Protocol
Operation (Req)
2
4
3
1
Data
Ready (Ack)
5
6
Execution

## Slide 60: Behavior Description of Multiplier in Verilog
module multiplier (a, b, mul, clock, result, done); input clock, mul;
parameter n=8; input [n-1:0] a,b;
reg [2*n-1:0] result; output reg done; output [2*n-1:0] result; reg [n:0] rc; reg [n-1:0] ra, rb; always @(posedge mul) begin ra=a; rb=b;
ready=0; rc = 0; repeat (n) begin @(posedge clock) if (rb[0]) rc =rc+ra; rb={rc[0],rb[n-1:1]}; rc=rc>>1; end result={rc[n-1:0],rb}; done=1; end endmodule //multiplier

## Slide 61: RTL Description of Multiplier in Verilog
module multiplier (a, b, mul, clock, result, done); input clock, mul;
parameter n=8; input [n-1:0] a,b;
reg [2*n-1:0] result; output reg done; output [2*n-1:0] result; reg [n:0] rc; reg [n-1:0] ra, rb; always @(posedge mul) begin ra=a; rb=b;
ready=0; rc = 0; repeat (n) begin @(posedge clock) if (rb[0]) rc =rc+ra; rb={rc[0],rb[n-1:1]}; rc=rc>>1; end result={rc[n-1:0],rb}; done=1; end endmodule //multiplier

## Slide 62: RTL Description of Multiplier in Verilog Test_Bench
module mult(a,b,clk,mul,ready,out);
input clk,mul;
input [7:0] a,b;
output reg ready;
output [15:0] out;
reg [3:0]counter;
reg [15:0] out;
reg [7:0] ra,rb;
reg [8:0] acc;
reg start;
always @(posedge clk)
begin
case (mul)
0: start<=1;
1: begin if(start)
begin ra<=a; rb<=b; acc<=0;
ready<=0;
counter<= 4'd8;
start=0;
end
else
begin if (counter!=0)
begin
if(rb[0])
acc<=acc+ra;
else acc<=acc;
rb<={acc[0],rb[7:1]};
acc<=acc>>1;
counter<=counter-1;
end
else

## Slide 63: Multiplier with Control Signals
RA
 RB
SM
0
MUX
 Acc
CT
y1
y1
n
y3
y3

y3
y2
Control
Unit
done
X1
y1 y2 y3
n bit
n bit
n bit
n bit
y1
y1
A
B
RA – multiplicand, RB – multiplier, RC (accumulator) - product
Possible to combine multiplier and product register (low bits)

## Slide 64: ASM Chart for Multiplication
Begin
Multiply?
RA = A; RB =B; CT =n; acc =0; done=0;
Yes
No
Y1
X1
acc = SM
Shift right acc, RB; CT =CT-1
(CT)=0?
End
Yes
Y2
Y3
X2
No
done= 1
Multiply=1?
No
Yes
S0
S1
S2
S3
S4
S0
X1

## Slide 65: State Diagram of Moore FSM
S0/y0
~X1
S1/y1
S2/y2
X1
1
1
S3/y3
~X2
X2
S4/y4
X1
~X1
A={X,Y,S,}
X= {x1,x2}
Y={y1,y2,y3,y4}
x1=Multiply
x2: done,(CT==0)
y0: all control signals equal zero
y1: load of the initial values (operands are written into registers)
y2: acc=adder;
y3: shift right acc, RB; CT=CT-1;
y4: done=1;

## Slide 66: Datapath Circuit for the Multiplier
RA
A
Y1:En(Load)
RB
B
Y1:Load
CLK
CLK
Acc[0]
ACC
CT
SM
-
n
n+1 bit
n
MUX
0
1
Y1:Reset
Y3:Shift right
Y2:ACC=SM (Load)
X2
FSM
Y1:Load
X1
(multiply)
Y1
Y2
Y3
1bit
Ready
Y3:Decrement
Y3:Shift right
Done
(Y4)

## Slide 67: RTL Verilog Description (Declarations)
module shift_right_multiplier(clk,reset, A, B, production, multiply,ready);
parameter n=16, logn=4;
input clk,reset,multiply;
input [n-1:0] A,B;
output [2*n-1:0] production;
output ready;
reg [n-1:0] ra,rb,mux_out;
reg [n:0] acc;
wire [n-1:0] sum;
wire cout;
reg [logn:0] counter;
wire y1,y2,y3,done;
parameter S0=3'b000, S1=3'b001, S2=3'b010, S3=3'b011, S4=3'b100;
reg [2:0] state, next_state;

## Slide 68: Moore FSM Description
//fsm_register
always@(posedge clk or negedge reset)
if(!reset) state<=S0;
else state<=next_state;
//fsm_next_state logic
always @(*)
case(state)
S0: if (multiply) next_state=S1;
else next_state=S0;
S1: next_state=S2;
S2: next_state=S3;
S3: next_state=done?S4:S2;
S4: if (multiply) next_state=S4;
else next_state=S0;
default:next_state=S0;
endcase
//output_logic;
assign y1=(state==S1);
assign y2=(state==S2);
assign y3=(state==S3);
assign done=(state==S4);

## Slide 69: RA, RB, acc, Multiplexer
//Register_A
always @(posedge clk)
if(y1) ra<=A;
else ra<=ra;
//Register_B
always@(posedge clk)
begin
if(y1) rb<=B;
else if(y3)
rb<={acc[0], rb[n-1:1]};
else rb<=rb;
end
//Accumulator
always @(posedge clk)
begin if(y1) acc<=0;
else if(y2) acc<={cout, sum};
else if(y3) acc<={1'b0,acc[n:1]};
else acc<=acc;
end
//Multiplexer
always @(rb,ra)
mux_out=rb[0]? ra:8'b0;

## Slide 70: Counter, Adder
//Counter
always @(posedge clk)
if(y1) counter<= n;
else if(y3) counter<=counter-1;
else counter<=counter;
always @ (counter)
if (counter==0)
done = 1'b1;
else
done = 1'b0;
// Adder
assign {cout, sum}=mux_out+acc;
assign production = {acc[n-1:0], rb};
endmodule

## Slide 71: Multiplying Unit 2
RA
RB
SM
Acc
0
The structure of multiplying unit with the shift of multiplier to the right and multiplicand to the left
A
B
2n bit
2n bit
2n bit
n bit
MUX

## Slide 72: Multiplying Algorithm
Start
Multiply?
RA= A; RB=B; CT=n; Acc=0; Ready=0;
Yes
No
Acc=SM; Shift Left RA;
Shift Right RB
(RB)=0?
Yes
No
(RА) or (RB) =0?
No
End

## Slide 73: Example
RA | RB | Acc
0 0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 | 0 0 0 0 0 1 1 0 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 0 | 0 0 0 0 0 0 1 1 | + 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 0 0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 0
0 0 0 0 0 0 1 0 1 0 1 1 0 1 0 0 | 0 0 0 0 0 0 0 1 | + 0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 0 0 0 0 0 0 0 1 0 0 0 0 0 0 1 1 1 0
0 0 0 0 0 1 0 1 0 1 1 0 1 0 0 0 | 0 0 0 0 0 0 0 0 | 0 0 0 0 0 1 0 0 0 0 0 0 1 1 1 0
C = AB; A= 1 0 1 0 1 1 0 1; B= 0 0 0 0 0110;

## Slide 74: Behavioral Description of Multiplier
module multiplier_2(A,B,production,clk,multiply,ready);
parameter n=8;
input clk, multiply;
input[n-1:0] A,B;
reg [n+n-1:0] ra,rb;
reg [n+n-1:0]ra,acc;
output reg ready;
output[n+n-1:0] production;
always @(posedge multiply)
begin ra=A; rb=B; ready=0;acc=0;
while (rb!=0)
@(posedge clk)
begin if rb[0] acc=acc+ra;
else acc=acc;
ra=ra<<1; rb=rb>>1;end
ready =1; assign production=acc; end
endmodule
Behavioral description can be used for simulation in order to test the device operation algorithm

## Slide 75: Integer Division (Unsigned)
Division is more complex than multiplication Dividend = quotient  divisor + remainder If divisor>dividend, quotient=0, remainder=dividend
Normalization of divisor and defining number of cycles of division:
  Align leftmost 1 bit in the divisor with leftmost 1 bit in the dividend by shifting the divisor left and recording the number of shifts required to make this alignment. k – the number of shifts, k+1 – the number of division cycles.
The definition of quotient
  With restoring
  Without restoring
The definition of remainder Dividend – A, divisor – B, quotient – Q.

## Slide 76: Restoring Division
The first remainder is dividend
  Subtract divisor from remainder. Get Ri.
  If result is positive the current digit of quotient is 1, otherwise the current digit is 0
  Restore value by adding divisor to remainder: Ri + B
  Shift left remainder and quotient: 2(Ri+B)
  Repeat k+1 times.

## Slide 77: Nonrestoring Division
The first remainder is dividend
  Subtract normalized divisor Bn from remainder. Get Ri.
  If result is positive the current digit of quotient is 1 Otherwise the current digit is 0
  Arithmetical shift right divider (Bn/2) and left quotient.
  If partial remainder (Ri) is positive Subtract from Ri divisor Ri+1=Ri –Bn/2 Else add divisor to Ri.  Ri+1=Ri + Bn/2
  Repeat K+1 times (go to 3)
Rationale: If Ri<0 then,Ri+1 = (Ri + Bn) – Bn/2 = Ri +Bn –Bn/2 = Ri+Bn/2

## Slide 78: Example
Acc | Rb_norm - Rb norm |  | Rc | counter
0 0111 0001 | 0 0110 0000 | 1 1010 0000 | 0000 0000 | 5
+ 0 0111 0001 1 1010 0000 |  |  | 0000 0000 | 
0 0001 0001 |  |  |  | 
+ 0 0001 0001 1 1101 0000 1 1110 0001 | 0 0011 0000 | 1 1101 0000 | 0000 0001 | 4
+1 1110 0001 0 0001 1000 1 1111 1001 | 0 0001 1000 | 1 1110 1000 | 0000 0010 | 3
+1 1111 1001 0 0000 1100 0 0000 0101 | 0 0000 1100 | 1 1111 0100 | 0000 0100 | 2
+0 0000 0101 1 1111 1010 1 1111 1111 | 0 0000 0110 | 1 1111 1010 | 0000 1001 | 1
+1 1111 1111 0 0000 0110 0 0000 0101 |  |  | 0001 0010 Quotiеnt 0 0000 0101 Remainder | 0
A=0111 0001,
B=0000 0110;
k=4, n= k+1=5

## Slide 79: Flow-Chart of Integer Division(Unsigned)
Begin
Division?
RB=B; Acc=A; RC=0;done=0
k= LogA- LogB
-
Acc<Rb?
No
Yes
Yes
No
RBN=Barrel_Shifter
(RBN = RBN <<k), Cnt=k+1
Acc=Acc[n]?Acc+RBN:acc- RBN
RC={RC[n-1:0],~Acc[n]}; cnt=cnt-1;
Yes
No
Cnt==0?
Rem=acc[n]?acc+rb:acc;
done=1;
End
RBN= RBN >>1
RC=0; Rem=Acc
k<0?

## Slide 80: Unsinged Integer Division FU Structure
n bit
Acc
0
1
S
Adder
А
Encoder B
Subtractor
Barrel Shifter
Quotient
Encoder A
Counter
Rem
FSM
k
RBN
LogA
LogB
RC
+1
.
.
.
MUX
Control signals
Conditions from Op. U
Complement
-RBN
S
n+1bit
n+1
n bit
n bit
DIV
Down cnt
RB
B

## Slide 81: Signed Division
In division with signed operands, quotient and remainder are defined by:
Dividend=divisor  quotient + remainder; sign (quotient)= sign (dividend)  sign (divisor); sign (remainder) = sign (dividend); |remainder|<|divisor|
Signed division:
  Convert negative numbers to positive
  Execute unsigned multiplication
  Remember the original signs
Examples: C = A/B ; A = BC + R A = 7; B = 3;  C= 2; R= 1; A = -7; B = 3;  C=-2; R=-1; A = 7; B = -3;  C=-2; R= 1; A = -7; B= -3;  C= 2; R= -1.

## Slide 82: Signed Division (2)
The next operation is executed in recurrent iteration of division:
  If sign (remainder)  sign (divisor) =1, then add divisor to 2Ri (doubled current partial remainder); else subtract divisor from 2Ri.
  If sign (remainder)  sign (divisor)=0, then the current digit of quotient is 1; else the current digit is 0.
The correction of quotient is necessary in the following cases:
  A>0 and B<0. Add 1 to quotient.
  A<0 and B>0. If R≠0, add 1 to quotient.
  A<0 and B<0. If R=0, add 1 to quotient.

## Slide 83: Signed Division
Divident/ Remainder | Divisor | Quotient
10111101 + 01001000 00000111 | 01001000 10111000 | 1
00000111 +11011100 11100011 | 00100100 11011100 | 0
11100011 + 00010010 11110101 | 00010010 11101110 | 0
11110101 + 00001001 11111110 | 00001001 11110111 | 0
11111000+1 | Correction of quotient | 
А = 10111101
B = 00001001
BN=01001000
-BN=10111000
log2A =6
log2B =3
n=6-3+1=4

## Slide 84: ALU for Signed Division
Divider
Acc
rq
1
0
S
Adder
FSM
А
B
counter
S
correction
+1

## Slide 85: Multiplication on Signed Numbers (Booth’s Algorithm)
n
RA
SM
ACC
RB RB0
RB-1
0
1
CT
B
A
2
3
0
0
RA

## Slide 86: Booth’s Algorithm
ASR – arithmetical right shift (sign extend when shifting)
Start
No
Multiply?
No
Yes
RA=A, RB=B, CT= n, ACC=0, RB-1=0
RB0,RB-1
ACC=ACC+RA
ACC=ACC+~RA+1
ASR(ACC, RB, RB-1) CT = CT-1
Multiply?
(CT)==0?
Yes
01
10
0011
End

## Slide 87: Example
A = 10010110;
B = 11000111;
- A = 01101010;
Acc | RB | RB-1 | CT
+00000000 01101010 01101010 | 11000111 | 0 | 8
00110101 | 01100011 | 1 | 7
00011010 | 10110001 | 1 | 6
+00001101 10010110 10100011 | 01011000 | 1 | 5
11010001 | 10101100 | 0 | 4
11101000 | 11010110 | 0 | 3
+11110100 01101010 01011110 | 01101011 | 0 | 2
00101111 | 00110101 | 1 | 1
00010111 | 10011010 | 1 | 0
b0, b-1 | Code (-1,0,1)
0 0 | 0
0 1 | 1
1 0 | -1
1 1 | 0

## Slide 88: Substantiation of the algorithm
B>0
A*(00011110)=A*(24 +23 +22 +21) = A*30
The set of addition operations can be replaced only by two operations (addition and subtraction) as the following expressions take place:
2n + 2n-1+ . . . +2n-k = 2n+1 – 2n-k
А*(00011110)=A*(25-21)=A*30.
This can be expanded at any number of consequently following “1s”.This algorithm is called Booth’s recoding.
  (0,1)  (-1,0,1)
  Multiplier: 00011110  0,0,1,0,0,0, -1,0
  Instead of 4 additions - 2.

## Slide 89: Substantiation of the algorithm (2)
B < 0
B= -2n-1 + (bn-2*2n-2) +(bn-3*2n-3) + . . . +(b1*21) + b0*20
Assume B=111110bk-1bk-2 . . . b1b0
Then B= -2n-1+2n-2+. . .+2k+1+bk-1*2k-1+ . . . +b0 *20
2n-2 + 2n-3 + … + 2k+1 = (2n-2 *2 - 2k+1)/(2-1) =2n-1 – 2k+1.
(Sum of n-k terms of geometric progression).
Hence: -2n-1 + 2n-1 – 2k+1 + bk-1*2k-1 + . . . +b0*20= B. For example:
A*(11111010)=A*(-23+22-21); A*(11100111)= A*(-25+23-20).
It is obvious that Booth’s algorithm allows using the least number of additions in comparison with the usual simplest algorithm.
B=11111010  0,0,0,0, -1,1,-1,0; B+=11100111  0,0,-1,0,1,0,0,-1;
Instead of 6 additions 3.

## Slide 90: Booth Multiplier in Verilog
module Booth_multiplier(a,b,clock,
start, ready,result); parameter n=16; input [n-1:0] a,b; input clock, start; output reg [2*n-1:0] result; output reg ready; reg[n-1:0] acc,ra,rb; reg q; always@(posedge start) begin ra =a; rb=b; acc=0; q=0; ready=0;
repeat (n) begin @(posedge clock) if(rb[0]!==q) begin if(q) acc=acc+ra; else acc=acc-ra; end q=rb[0]; rb={acc[0],rb[n-1:1]};
acc={acc[n-1],acc[n-1:1]};//arithm. shift right end result={acc,rb}; ready =1; end endmodule//Booth_multiplier

## Slide 91: Modified Booth Algorithm
Radix-4 multiplication
Booth recoding: {0,1}  {-2, -1, 0, 1, 2}.
Each number in this system is a factor that multiplies the multiplicand before adding to the sum of the partial products. Simultaneously analyzed three digits of the multiplier b1,b0,b-1 (two current bits b1, b0 and older bit b-1 from the previous triple).

## Slide 92: Modified Booth Algorithm (2)
b1 b0 b-1 | Code {-2,-1,0,1,2} | Operation
0 0 0 | 0 | Add 0
0 0 1 | 1 | Add A
0 1 0 | 1 | Add A
0 1 1 | 2 | Add 2*A
1 0 0 | -2 | Add -2*A
1 0 1 | -1 | Add -A
1 1 0 | -1 | Add -A
1 1 1 | 0 | Add 0

## Slide 93: Multiplication Unit Flow-Chart
RA
0
1
Adder
Acc
RB
CT
Control Unit
n
n+2
n
A
B
q
CT
Complement
2
3
4
5
6
7
MUX
S
S
A
-
0
0
0
0
-A
done
n+1

## Slide 94: Flow-Chart of Modified Booth Algorithm
A1No
Begin
Multiply==1?
No
RA=A, RB=B; acc=0; RB-1=0; CT=n/2; done=0
RB={acc[1:0], rb[n-1:2] Acc=>>2; CT=CT-1
CT==0?
No
End
Adder=acc+Mux; acc=Adder
done=1
Yes
Yes
Multiply==1?
No
Yes

## Slide 95: Radix-16 Multiplier
RB
RA
0
0
0
0
8А
4А
2А
А
0
1
1
0
0
1
1
0
A
B
b0
b1
b2
b3
0
0
0
Ab0
2Ab1
4Ab2
8Ab3

## Slide 96: Radix-16 Multiplier (2)
CSA1
CSA2
CSA3
CSA4
Reg_SUM
Reg_Carry
FF
SM1
3 bit
4 bit
SM2
Prroduction
Production
S’s
C’s
S’s1
C’s1
C’s2
S’s2
S’s3
C’s3
S’s4
C’s4
Ab0
2Ab1
4Ab2
8Ab3
Upper bits
Low bits

## Slide 97: Earlier Termination of Multiplication Operation
А
B
Encoder A
Encoder
Multiplier
RА
RB
Result C
Mux A
Мux B
Sign
Sign
Sign
to RA
to RB
0
1
0
1
Subtractor
Check operands to 0, or 1…1.
Replacement of operands

## Slide 98: Combinational Multipliers
Acceleration methods of multiplication:
  Parallel computing of partial products
  Reduction of number of additions
  Reduction of propagation time delay
Two types of multipliers are used – matrix and tree-like structure.
  Propagation delay of matrix multipliers – О(n).
  Propagation delay of tree structured multipliers – O(log2n).

## Slide 99: Partial Products in an 44 Multiplier
a3b0
a2b0
a1b0
a0b0
a3b1
a2b1
a1b1
a0b1
a3b2
a2b2
a1b2
a0b2
a3b3
a2b3
a1b3
a0b3
p0
p1
p2
p3
p4
p5
p6
p7
+
b3
b2
b1
b0
a3
a2
a1
a0


## Slide 100: Matrix Multiplier Based on CRA
Matrix multiplier contains n2 “AND” gates to form partial products
Multiplier based on CRA contains(n-1)n adders
The number of HA – n
The number of FA is n2 -2n
In the worst case the propagation delay equals 3n-4.

## Slide 101: Matrix Multiplier Based on CRA Structure
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
+
+
+
+
a0b2
а1b2
а2b2
а3b2
+
+
+
+
a0b3
а1b3
а2b3
а3b3
+
+
+
+
0
0
0
0
P7
P6
P5
P4
P3
P2
P1
P0

## Slide 102: Matrix Multiplier with Carry Save Addition
Matrix multiplier using carry-save addition contains the same number of elements.
It is faster because its propagation delay is shorter.
The last (n) stage corresponds to CRA.
Its worst-case carry propagation path goes through 2n-2 adders.

## Slide 103: Matrix Multiplier using Carry Save Addition
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
+
+
+
a0b2
a1b2
a2b2
a3b2
+
+
+
a0b3
a1b3
a2b3
a3b3
+
+
+
p0
p1
p2
p3
p4
p5
p6
p7
+
+
+

## Slide 104: Treelike Multipliers
Treelike multipliers contain three stages:
  Generation of bits of partial products. This stage consists of n2 of “AND” gates.
  Compression of partial products. Implemented as a tree of parallel adders.
Final addition. Addition of sum vector and carry vector.
While using in multipliers, full adders and half adders are usually called compressors and counters (3,2) и (2,2).

## Slide 105: Wallace-tree Multiplier
s23 c22
c31
s24 c23
c32
c24 a3b3
c33
s13 c13 a0b3
s14 c14 a1b3
c15 a3b2
a2b3
a2b0 a1b1 a0b2
a3b0 a2b1 a1b2
a3 a2 a1 a0
b3 b2 b1 b0
a0b0
a3b1 a2b2 a1b3
a3b2 a2b3
a3b3
c15 s14 c14 s13 c13 s12 c12 s11
a0b0
s11
a1b0 a0b1
s12 c12
a3b3
c24 s24 c23 s23 c22 s22 c21
s11
s21
a0b0
s22 c21

s31
s32
s33
s34
c34
s21
p0
p1
p2
p3
p4
p5
p6
p7

## Slide 106: Wallace-tree Multiplier (2)
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
+
a0b2
a1b2
a2b2
a3b2
+
+
+
a0b3
a1b3
a2b3
a3b3
+
+
+
+
+
+
+
+
P7
P6
P5
P4
P3
P2
P1
P0

## Slide 107: Wallace-tree
Lines of matrix of partial products are grouped in three.
For the compression of columns with three bits FA is used. For compression of columns with two bits HA is used.
Lines that are not included in a set of three lines are accounted in the next reduction cascade.
Wallace scheme is considered to be the fastest, but at the same time its structure is the least regular.
The main field of application - the multiplication of multi-bit numbers.

## Slide 108: Dadda Multiplier
p7 p6 p5 p4 p3 p2 p1 p0
a3b1 a2b2 a1b3
a0b0
a1b0 a0b1
a2b0 a1b1 a0b2
a3b0 a2b1 a1b2 a0b3
a3b2 a2b3
a3b3
c12 s12 c11 s11
s11
a0b3
s12
c11
a3b2 a2 b3
c12
a2b0
a1b1
a0b2
c24 s24 c23 s23 c22 s22 c21 s21
a3b3
c36 s36 s35 s34 s33 s32 s31
c24
a3b3
c35
s24
c23
c34
s23
c22
c33
s22
c21
c32
s21
c31
x
a3 a2 a1 a0
b3 b2 b1 b0
a1b0 a0b1

## Slide 109: Dadda Multiplier (2)
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
a0b2
a1b2
a2b2
a3b2
a0b3
a1b3
a2b3
a3b3
+
+
+
+
+
+
+
+
+
+
+
+
p7
p6
p5
p4
p3
p2
p1
p0

## Slide 110: Dadda Multiplier (3)
The difference in Wallace and Dadda methods is the different approach in the solution of addition “compression” problem.
Wallace algorithm compresses codes as soon as possible, at the early stages.
Dadda algorithm provides the highest level of compression at the late stages.
A Wallace-tree multiplier works forward from the multiplier inputs.
The Dadda multiplier works backward from the final product.
The number of cascades is the same in the both multipliers.
Both lack structure regularity.
The number of stages and thus delay (in units of an FA delay—excluding the CPA) for an n-bit tree-based multiplier using (3, 2) counters is
log1.5.n = log10 n/log101.5 =log10n/0.176

## Slide 111: Floating Point Data
Single Precision/Double Precision – 32/64 bit (IEEE 754).
Extended Precision – 80-bit, Double Extended Precision – 128-bit.
Normalized form: the integer bit of the significand is “1”, it is not stored in memory (hidden 1).
Single precision: A = (-1)S2E-127 1.F
Double precision: A = (-1)S2E-1023 1.F
Range for significand– 1.0…0 to 1.1…1(1 to 2-2-23) or (1 to 2–2-52)
Biased exponent – allows simplifying the execution add/sub and comparing operations.
S E F
1
8
23
S E F
1
11
52
Notes: 111

## Slide 112: Floating Point Data (2)
-127 0 127
(-1023) (1023)
0 127 254
(1023) (2046)
Biased Exponents
Real Numbers
3.14 1038
-2-126 0 2-126
-2127 (2-2-23)
2127(2-2-23)
-3.14 1038
-1.79 10308
-2.23 10-308
-1.18 10-38
1.18 10-38
1.79 10308
2.23 10-308
Normalized numbers
Normalized numbers
Denormalized numbers
Notes: 112

## Slide 113: Floating Point Data (3)
Extended precision – 80 bit
Internal format - to provide additional range and precision for constants and intermediate results.
IEEE 754-2008 standard added half-precision (16-bit) and quard-precision 128-bit floating point operations.
Half-precision: S-1bit, E – 5 bit, F – 10 bit.
Quard-precision: S-1bit, E – 15 bit, F – 112 bit.
S E 1 F
1
15
64
Notes: 113

## Slide 114: IEEE 754-2008
S E F
1
5
10
S E F
1
15
112
This NVIDIA format is used in several computer graphics environments
This format is used in double-double arithmetic

## Slide 115: Example
Single Precision:
A = 1
A = (-1)02E-127 1.F
E-127=0; E=127; M=1.00…0
Hexadecimal  3F800000
Double Precision:
1. A = (-1)02E-1023 1.F
0 01111111 0. . . . . . . . . . . 0
1
 8 
 23 bits 
0 01111111111 0 . . . . . . . . . . . 0
1
 11 
 52 bits 
Hexadecimal  3FF0000000000000
Notes: 115

## Slide 116: Example (2)
A = -131.5625
(A)2 = - 10000011,1001= (-1)1 1.00001001001 27
E-127 = 7; E=134;
A = 25/128
(A)2 = 0.0011001= (-1)0 1.1001 2-3
E-127 = -3; E=124;
1 10000110 000010010010…
1
 8 
 23 bits 
Hexadecimal  C3849000
0 01111100 10010 …
1
 8 
 23 bits 
Hexadecimal  3E480000
Notes: 116

## Slide 117: Special Values in IEEE Format
Special values: 0,  
Denormalized Number:
Not a Number (NaN)
 | F=0 | F≠0
E=0 | 0 | Denormalized
E=255 |  | NaN

## Slide 118: Special Values in IEEE Format
Denormalized Number:
  No hidden bit - significands not normalized
  Smallest normalized number in Single Precision is 1*2-126;
  Smallest representable number is 2-23*2-127=2-150. 2-150 – underflow
  Denormalized number reduces gap between smallest representable number and zero.
Not a Number (NaN)
  Two kinds: Signaling NaN (or trapping) - SNaN and Quiet NaN (nontrapping)-QNaN

## Slide 119: Floating Point Arithmetic
Numbers are represented by:
A=(-1)S2E-1271.F (IEEE standard)
S E F
1
8
23
Addition/subtraction
Exponents of both operands must be equal before adding or subtracting significands.
A = 2Ea MA
B = 2Eb MB
A+B = (MA  2Ea-Eb +MB) 2Eb
A-B = (MA  2Ea-Eb -MB) 2Eb
Single precision format

## Slide 120: Addition/Subtraction of Floating Points Numbers
Calculate differences of the two exponents d=|Ea - Eb|
Shift significand of smaller number by d positions to the right
Add aligned significands and set exponent of result to exponent of larger operand
Normalize resultant significand and adjust exponent if necessary
Round resultant significand and adjust exponent if necessary
Renormalize result if necessary.

## Slide 121: Example
1 10001000 11100000000
1 10001001 0000111000
1 10000101 1110000000
A
B
8 bit
23 bit (10)
1 bit
C = A + B
d = EA – EB = 3
MB’ = MB×2-3 = 0,0011110000
MA+ MB’ =MC ; EC= 10001000
1,1110000000
+0,0011110000
10,0001110000
After Normalization
MC =1,0000111000
EC = 10001001

## Slide 122: Floating Point Multiplication
A  B = (MA  MB) 2Ea+Eb-bias
Add biased exponents, subtract bias
Multiply significands
Normalize product
Round significand of product
Compute sign of product

## Slide 123: Floating Point Division
A/B = (MA/MB) 2Ea-Eb+bias
Subtract biased exponent, add bias
Divide significands
Normalize quotient
Round quotient
Compute sign of quotient
Floating-point remainder calculated separately - only when required.

## Slide 124: Binary Codes for Decimal Numbers
Decimal numbers is represented in a digital system by a string of bits
Decimal | BCD(8421) | 2421 | Excess-3 | Biquinary | 1-out-of-10
0 | 0000 | 0000 | 0011 | 0100001 | 10000000000
1 | 0001 | 0001 | 0100 | 0100010 | 0100000000
2 | 0010 | 0010 | 0101 | 0100100 | 0010000000
3 | 0011 | 0011 | 0110 | 0101000 | 0001000000
4 | 0100 | 0100 | 0111 | 0110000 | 0000100000
5 | 0101 | 1011 | 1000 | 1000001 | 0000010000
6 | 0110 | 1100 | 1001 | 1000010 | 0000001000
7 | 0111 | 1101 | 1010 | 1000100 | 0000000100
8 | 1000 | 1110 | 1011 | 1001000 | 0000000010
9 | 1001 | 1111 | 1100 | 1010000 | 0000000001

## Slide 125: BCD Addition
Addition is similar to adding 4-bit binary numbers, except that a correction must be made if a result exceeds 9 (1001).
The result is corrected by adding 6.
Examples;
2 0010 5 0101
+ 7 +0111 +8 +1000
9 1001 13 1101
+0110 - correction
10011
Carry_out=1
4 0100 9 1001
+9 +1001 +9 +1001
1101 18 10010
+0110 - correction + 0110 - correction
10011 11000
carry_out
carry_out