## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Programmable Logical Integrated Circuits (PLDs)

## Slide 4: Memory Hierarchy
Lower Level
Speed
Secondary memory HDD, SSD
Remote secondary memory, WEB servers
Capacity
Faster
Regis- ters
Cache
Larger
Upper Level
1GB…2TB
HDD։
512GB …6TB
SSD:
256GB-1TB
<1KB
L1-256KB
L2-256KB
L3- 4MB-16MB
L1-1ns
L2-10ns
L3- 20ns
100 ns
HDD-20 ms SSD - 1ms
(0.5-1)ns
Computer memory should be fast, large & inexpensive
Main Memory

## Slide 5: Computer Memory
Semiconductor Memory
Volatile
NonVolatile
RAM
SRAM
DRAM
ROM
FLASH
PROM
EEPROM
Two primary categories of memory in digital system volatile and nonvolatile.

## Slide 6: RAM Memory
Main memory – random access memory (RAM). The time it takes to read or write a word is independed of a word location in a RAM.
Main memory stores data and programs during computer operation.
2n words
2n words
m bit per word
n address lines
m data input lines
m data output lines

## Slide 7: RAM
Read-Write Memory
Two types
  SRAM
  DRAM
  SRAM
    memory cell – flip-flop
  DRAM
    memory cell – capacity (drain – substrate of MOS-transistor).
The kinds of IC memory organization:
  Linear-select (2D), two-dimensional (3D), compromise (2DM).

## Slide 8: Static RAM (SRAM)
SRAM is generally used as a cache to hold recently used instructions and data, to store data in small microprocessor systems, often in “embedded” systems. SRAM cell is RS or D latch.
Select
Input
Write Enable
S
R
Out
S
I
W
O

## Slide 9: SRAM Memory Cell (D Latch)
D
C
IN
SEL_L
WR_L
OUT
IN
OUT
S
WR

## Slide 10: Linear Select SRAM (Internal Structure)
O0
S
S
I
W
O
S
I
W
O
S
I
W
O
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
S
I
W
O
Write
Read
O3
O2
O1
DC
D3
D2
D1
D0
A0 A1
Four-address memory with 4 bits per word

## Slide 11: Two-dimensional Memory Cell
Out
S2
S1
I O W
S T
R
Select 2
Select 1
Input
Write
Enable

## Slide 12: Two-dimensional Memory Cell
D
C
IN
SEL_L1
WR_L
OUT
SEL_L2
S1
S2
OUT
IN
WR

## Slide 13: SRAM Cell
Word Line
Bit Line
~Bit Line

## Slide 14: Two-dimensional IC Memory Organization
All “O” outputs from cells are connected to this point
Read
CS
Memory cells matrix
A2 (n/2bits)
Row
deco-der
(DCX)
Column decoder (DCY)
A1 (n/2bits)
CS
S1
S1
S1
S1
S1
S1
S1
S1
S1
S2
S2
S2
S2
S2
S2
S2
S2
S2
O I W
O I W
O I W
O I W
O I W
O I W
O I W
O I W
O I W
Input
Output
Write

## Slide 15: Two-Dimensional Memory Structure
DCY
Data
Address
n/2
DCX
n/2
Address
Arrays of memory cells

## Slide 16: Structure of IC with Selectors (2DM)
MUX/ DMUX
MUX/ DMUX
MUX/ DMUX
An-1 . . .Ak
n-k
k
Ak-1 . . .A0
R/W
Dm-1
Dm-2
D0
0
1
2n-k
2к
2к
2к
DC
Memory
Cell

## Slide 17: SRAM
The linear-select organization is used for IC memory with small capacity. Address decoder is complicated:
2n AND elements (with n inputs).
Address decoder for two-dimensional IC organization is simpler:
2 2n/2 AND elements (with n/2 inputs).
Properties of SRAM:
Fast
Density is not very large – six transistors per bit
Doesn’t need to be refreshed (data stays as long as power is on).
Basically is used for cache memory.

## Slide 18: Example: HM62 256 SRAM IC Memory
A0
A1
A14
WE
OE
CS
0
1 SRAM 0
. 1
. 2
. 3
14 4
5 WE 6
OE 7
CS
.
.
.
SRAM has bidirectional data bus – use the same data pins for both reading and writing.
CS | OE | WE | I/O pins | Mode
1 | x | x | z | Not selected
0 | 1 | 1 | z | Output disable
0 | 0 | 1 | Dout | Read
0 | x | 0 | Din | Write

## Slide 19: HM62 256 SRAM IC Structure
CS
WE
OE
Read/Write
Control
0
1
2



511
Row
Deco-der
Memory Array
512826
bit
Input
data
control
Column I/O
Multiplexers









A0 A1 A7 A10 A12 A14
Din/out 0
…
Din/out 7



A2
A3
A4
A5
A6
A8
A9
A11
A13




## Slide 20: Timing Waveforms
Read Cycle
Write Cycle1
Write Cycle2
(CS Controlled)
(WE Controlled)
ADDR
~CS
~OE
~WE
DATA
Dout
Din
Din
TAA

## Slide 21: Read Cycle
WE
Data
tAOE
Valid Data
ADDR
CS
OE
tAA
tACS
tCLZ
tOLZ
tRC
tOH
tCHZ
tOHZ

## Slide 22: Write Cycle
WE
Data in
Valid Data
ADDR
OE
CS
tAS
tCW
tWC
tAW
tWP
Data out
tOHZ
tDW
tDH
tWR
OE=1
Writing occurs during the overlap of low level CS and low level WE. The signal at the OE input acts as a clock signal.

## Slide 23: Write Cycle (2)
WE
Data in
Valid Data
ADDR
CS
tAS
tCW
tWC
tWP
Data out
tDW
tDH
tWR
tAW
OE=0

## Slide 24: Asynchronous RAM in Verilog
RAM with CS, WE
module memory (cs, address, data_in,
data_out, we);
input cs, we;
input [7:0 ] data_in; input [5:0] address;
output reg [7:0] data_out;
reg [7:0] mem[0:63]; // 648 memory
always @(data_in or cs or address or we)
if (cs)
if (!we) mem[address] = data_in; // write
else data_out = mem[address]; // read
else data_out=8’bz;
endmodule
A0
A1
A2
A3
A4
A5
A6
0
1
2
3
4
5
6
7
Address
inputs
Chip select
0
1
2
3
6
4
5
7
Write enable
WE
CS
Data in
Data out
SRAM

## Slide 25: Asynchronous RAM in Verilog (2)
RAM with CS, WE, OE
module ram_asyn(address, data, cs, we, oe);
parameter N=10, M=8;
parameter RAM_size = 1<<N;
input [N-1:0] address;
input cs, we, oe;
inout [M-1:0] data; // bidirectional data
// internal variables
reg [M-1:0] data_out ;
reg [M-1:0] mem[0:RAM_size-1];
// Tri-State Buffer control
// output : When we = 1, oe = 0, cs = 0
assign data =(!cs && !oe && we)?data_out:8'bz;
A0
A1
A2
A3
A4
A5
A6
A7
0
1
2
3
4
5
6
7
Address
inputs
Write enable
A8
A9

## Slide 26: Asynchronous RAM in Verilog (3)
// Memory Write Block
// Write Operation : When we = 0, cs = 0
always @ (*)
begin
if ( !cs && !we )
mem[address] = data;
end
// Memory Read Block
// Read Operation : When we = 1, oe = 0, cs = 0
always @ (*)
begin
if (!cs && we && !oe)
data_out = mem[address];
end
endmodule

## Slide 27: Logic Symbols for SRAMs
128 Кbyte
HM628 128
A0
A1
A2
A16
WE CS1
CS2
OE
IQ0
IQ1
IQ2
IQ3
IQ4
IQ5
IQ6
IQ7
.
.
.
512 Кbyte
A0
A1
A2
.
A17
A18
WE CS
OE
IQ0
IQ1
IQ2
IQ3
IQ4
IQ5
IQ6
IQ7
HM628 512
.
.
Examples of IC SRAM

## Slide 28: Design of SRAM Module (Example1)
Implement a 1М×8 SRAM module using 512К×8 IC
Data bus
Signal MEM – memory request . Signal ~WR/RD specifies operation
A0
A18
WE CS
OE
IQ0
IQ7
.
.
.
.
.
.
IQ1
A0
A18
WE CS
OE
IQ0
IQ7
.
.
.
.
.
.
IQ1
A0
A18
A0
A18
D0
D1
D7
D7
D1
D0
.
.
.
D1
D0
D7
A0
A1
A18
A19
MEM
~WR
~CS0
~WR
~CS1
~CS0
~WR/RD
~CS1
.
.
.
.
.
.
Address bus
Control signals
~WR
~RD
~RD
~RD

## Slide 29: Example 2
Implement
a 512К ×16
SRAM module
using 128 К×8 IC
0
1
2
3
A0
A1
A16
CS
A0
A1
A16
CS
A0
A1
A16
CS
A0
A1
A16
CS
WE
WE
OE
OE
WE
WE
OE
OE
OE
A0
A1
A16
CS
WE
OE
A0
A1
A16
CS
WE
OE
A0
A1
A16
CS
WE
OE
A0
A1
A16
WE
CS
A0
A1
A2
A16
A17
A18
A17
A18
0
1
EN
MEM
~WR/
RD
~MEM
~RD
~WR
A0
A1
A16
A1
A0
A16
A0
A1
A16
A0
A0
A1
A1
A0
A0
A0
A1
A16
A16
A16
A16
CS0
CS0
CS0
CS1
CS1
CS1
CS2
CS2
CS2
CS3
CS3
CS3
~WR
~WR
~WR
~WR
~WR
~WR
~WR
~RD
~RD
~RD
~RD
~RD
~RD
~RD
~RD
D0
D0
D1
D7
D7
D1
D0
D1
D7
D0
D1
D7
D8
D8
D8
D8
D9
D9
D9
D9
D15
D15
D15
D15
D0
D1
D15

## Slide 30: Asynchronous RAM 648 bit
module memory (cs, addr, data_in, data_out, we);
input cs, we; //chip select, write enable/read enable
input [7:0] data_in;
input [5:0] addr;
output reg [7:0] data_out;
reg [7:0] mem[0:63]; // 648 memory
always @(data_in or cs or addr or we)
if (cs)
if (!we) mem[addr] = data_in; // write
else data_out= mem[addr]; // read
endmodule
data_in and data_out are separated

## Slide 31: RAM in System Verilog
module ram #(parameter N = 6, M = 32)
(input logic clk,
input logic we,
input logic [N–1:0] addr;
input logic [M–1:0] din;
output logic [M–1:0] dout);
logic [M–1:0] mem [2**N–1:0];
always_ff @(posedge clk)
if (we) mem [addr] <= din;
assign dout = mem[addr];
endmodule

## Slide 32: Synchronous SRAM
CE
ADDRESS
CS WE
DIN
CREG
INREG
OUTREG
Control Logic
ADDR
ADS_L
CLK
CS
GW_L
DIO
OE
AREG
DOUT

## Slide 33: Synchronous SRAM (2)
AREG, CREG, INREG - store address, control signals and data input by rising edge of the clock.
An operation that is set up before the rising edge of the clock is performed internally during a subsequent clock period.
The result of previous read operation is placed in OUTREG.
The device supports a burst mode (data at a sequence of addresses is read). AREG behaves as a counter.
Burst mode for write (sequence of addresses can be written without supplying a new address).
SSRAM is used in high-performance systems.
ADS_L – Address Set
GW_L – Global Write

## Slide 34: Synchronous SRAM Modes
Flow-Through (Late-write)
Pipelined Outputs (add OUTREG)
Burst (AREG is counter)
Zero-Bus-Turn-Around (ZBT)

## Slide 35: Timing Waveforms for SSRAM
Read-timing
behavior for
late-write SSRAM with
pipelined
outputs
CLK
CS,
ADDR
ADS_L
AREG,
CREG
Reading
OUTREG
X
Y
Z
X
Y
Z
X
Y
Y+1
Y+2
Y+3
Z
X
Y
Y+1
Y+2
Y+3
Z
X
Y
Y+1
Y+2
Z
X
Y
Y+1
Y+2
Z
DIO (out)

## Slide 36: Timing Waveforms for SSRAM (Write Operations)
CLK
CS,
ADDR
ADS_L
AREG,
CREG
GW_L
DIO (in)
X
Y
X
Y
Z
X
Y
Y+1
Y+1
X
X
Y+1
Y
INREG
Y
Y+1
Y+2
Y+2
Z
Z
X
Y+1
Y
Z
X
Y
Y+1
Y+2
Z
Y+2
Z
Y+2
Z
idle
idle
idle
idle
SRAM
writing

## Slide 37: RAM 2NM Bit in Verilog
module ram (clk,we,addr,din,dout);
parameter N=11, M=16;
input clk,we;
input [N-1:0] addr;
input [M-1:0] din;
output [M-1:0] dout;
reg [M-1:0] mem[2**N-1:0];
always @(posedge clk)
if (we) mem[addr] <= din;
assign dout = mem[addr];
endmodule
Synchronous Write, asynchronous Read

## Slide 38: Pipelined SSRAM
module SSRAM_pipelined (clk, we, addr, ce, din, dout);
input clk,we,ce;
input [8:0] addr;
input [3:0] din;
output reg[3:0] dout;
reg [3:0] RAM [511:0];
reg [3:0] pipe_reg;
always @(posedge clk)
begin if(!ce) dout<=4’hz;
else if (we)
RAM[addr] <= din;
else begin
pipe_reg <= RAM[addr];
dout <= pipe_reg; end
end
endmodule

## Slide 39: Dual-Port Memory
Types of dual-port memory:
True dual-port memory: completely independent access ports A and B (both ports are designated as a Write/Read ports
  Each port has its own address, data in, data out, clock, clock enable, and write enable.
Simple dual-port memory: port A is designated as the Read port and port B as the Write port.
  When the Read and Write port access the same data location at the same time, it is treated as a collision, similar to the port collision in true dual-port mode.
  Sometimes one port is designated as write/read port and other – as read port (example –distributed memory in FPGA)

## Slide 40: Dual-Port Memory (2)
Port
A
Port
B
DC
A
DC
B
DUAL/PORT
RAM
MEMORY
CELLS
CONTROL LOGIC
CPU or I/O device
CPU or I/O device
Data
Data
Address
Address

## Slide 41: Dual-Port SRAM Cell (8T)
Word Line B
VDD
Data-Port B
Data-Port A
Data-Port B
Data-Port A
Word Line A
T5
T5
T6
T7
T8

## Slide 42: Asyncronous Dual-Port RAM Arbiter
= =
CompA
= =
CompB
A address
B address
~BusyA
CEA
~BusyB
CEB
~Write InhibitA
~Write InhibitB
Latch
3
1
4
А
B
2
01
01
01
10
01
Delay
Delay

## Slide 43: Conflict Situations
Conflicts occur while handling two independent active devices to the same memory location in the following operations:
Writing using Port A - Writing using Port B
Writing using Port B - Reading using the Port A
Writing using Port A - Reading using the Port B
These situations are rare and account for about 0.1%.
Despite this, there is an asynchronous memory arbitration scheme
Software arbiters – semaphores.
Semaphores regulate the order of handling two or more independent active devices to a shared resource.
For synchronous memory additional logic (arbitration, semaphores or interrupts) for conflict resolution is not required.

## Slide 44: Associative Memory
SRAM
Search argument
. . .
= =
= =
= =
= =
. . .
Tag 1
Tag 2
Tag 3
Tag i
Data 1
Data 2
Data i
Data 3
CD
DC
Two modes: comparison mode
write mode

## Slide 45: Associative Memory (2)
SRAM
Address
DC
CD
En
Command
Tag Offset
Control Logic
bit
Data
CAM
CAM
CAM
~bit
bit
~bit
CAM
Counter
Sense amplifiers
Tag

## Slide 46: CAM Cell (NAND)
VDD
Word Line
T2
T4
T5
T7
T6
T1
T3
T9
T8
Match line
Bit
Bit
S
S
int

## Slide 47: CAM Cell (NOR)
T1
T6
S
Word line
S
Match line
Bit
~Bit
T2
T3
T4

## Slide 48: Register File
4
4
4
16
16
16
A1
A2
A3
WD3
RD1
RD2
WE3
>
CLK
Port 1 reads the data from address A1 onto the read data output RD1.
Port 2 reads the data from address A2 onto the read data output RD2.
Port 3 writes data from the write data input WD3 into address A3
on the rising edge of the clock if the write enable WE3 is asserted.
Read operations - asynchronous.
Three-ported memory with two read ports and one write port
Conflicts are resolved with help of instruction scheduler.

## Slide 49: General Purpose Registers (GPRs)
ADDR_1 (Read1_port1)
D[15:0]
CE
D
CE
D
CE
0
1
15
15
0
1
Reg 0
Reg1
Reg 15
0
1
15
DC
A1[3:0]
Clk
Port 1
RD1
Output (SPO)
Port 2
RD2
WD3[15:0]
A2[3:0]
ADDR_2 (Read2_port2)
WE3
En
A3[3:0]
Addr_3 (Write_port3)

## Slide 50: Verilog Description of RegFile
module regfile(clk, we, a1, a2, a3, wd3,rd1, rd2);
input clk,we;
input [3:0] a1,a2,a3;
input [15:0] wd3;
output [15:0] rd1, rd2;
reg [15:0] reg_file[0:15];
always @(posedge clk)
begin
if (we)
reg_file[a3] <= wd3;
end
assign rd1 = reg_file[a1];
assign rd2 = reg_file[a2];
endmodule

## Slide 51: FIFO Buffer
SRAM
Write Counter
Read Counter
Control Logic
WEN
RDEN
WRCLK
RDCLK
Reset
OE
RD
WE
Write Count
Read Count
Data_In
Data_Out
Full
Empty
FIFO - First-In, First-Out. Double-Port Memory
Full – if(write && ( write_count==read_count)) FIFO queue is full
Empty - if(read &&(read_count==write_count)) FIFO queue is empty
WEN – write enable, RDEN – read enable

## Slide 52: Dynamic Random Access Memory (DRAM)
Bit stores as a charge in capacitor Cc
“wordline”
(select)
Cc
Rн
Cl
n+
n+
Cc
Polysilicon
(WL)
Select
DRAM memory cell construction
SiO2
p-Si
(BL)
“bitline”
Sense amplifier

## Slide 53: DRAM (One-transistor Cell)
Write operation
To store a 1, the bit is accessed and a high voltage is placed on the bit line, which charges the capacitor through the “on” transistor.
To store a 0, a low voltage placed on transistor opens and the capacitor is charged on the bit line discharges the capacitor (if “1” has been stored).
Read operation
To read a DRAM cell the bit line (BL) is first precharged to a voltage halfway between High and Low - VPRE. Depending on whether the capacitor voltage is Hign or Low, the precharged BL is pulled slightly higher or slightly lower.
A sense amplifier detects this small change and recover “1” or “0” accordingly.
Read operation is destructive: data must be written back immediately.

## Slide 54: Properties of DRAM
High density (1 transistor for DRAM vs 6 (or 4) transistors for SRAM)
Destructive read (capacitor discharge on a read)
  Read is automatically followed by a write (to restore)
  Charge leaks away over time (need to refresh)
  DRAM use refresh cycles to update every memory cell periodically, typically once every 64 ms.
0
1
refresh
refresh
refresh
Vcc
Vcap
0V
time

## Slide 55: The Matrix of Memory Elements
Column 0
Column 1
Column 2
Column 3
Row 0
Row k-1

## Slide 56: Asynchronous DRAM Chip Organization
Memory Array
(square matrix)
Column decoder
Column I/O
Column address buffer
Row address buffer
Din
Dout
Row decoder
A0 . . . An-1
CAS
RAS
WE
MUX
Address
row buffer

## Slide 57: DRAM
Multiplexed address lines
To perform the operation, these cycles are needed:
  Put row address on lines
  Set row address strobe (RAS)
  Read row into row buffer
  Put column address on line (to switch external multiplexer)
  Set column address strobe (CAS)
  Read column bits out of internal row buffer
  Write row bits content to row
  Return RAS and CAS to inactive state

## Slide 58: Example: Asynchronous IC DRAM
А0 DRAM
А1
.
.
.
А10
WE
RAS
CAS
Din/out
MA
IC capacity:
211+114 bit =
= 222 4 bit =
= 4M 4 bit

## Slide 59: Comparison SRAM with DRAM
SRAM is faster than DRAM:
1/4 - 1/8 access time of DRAM
The density SRAM is lower than DRAM
1/4 density of DRAM.
Static: bit is not erased on a read
SRAM does not need to refresh
Unlike DRAM, there is no difference between access time and cycle time.
Access time: time to read
Cycle time: time between reads > access time (DRAM)
Cycle time = access time (SRAM)
SRAM address lines are not multiplexed
SRAM is more expensive than DRAM: about 8-16 times.

## Slide 60: DRAM Optimization
Standard DRAM chip - operation: read row into buffer, read column from buffer.
Methods to improve standard DRAM chip performance:
Nibble mode: additional bits per access
Fast page mode: change column address
Static column mode (SCRAM): don’t toggle CAS
Cached DRAMs: multiple row buffers
Further improvement: synchronous DRAM
SDRAM, DDR SDRAM, DDR2 SDRAM, DDR3, DDR4,
DDR3 has the most potential possibilities to increase performance
Rambus – interface fast, but IC is expensive.

## Slide 61: Timing Waveforms IC DRAM
CAS
MA
WE
Data
Read cycle
Write cycle
tRCD
tRAC
Z
Data Out
Data In
tCAC
tRAS
tWCH
tRP
tCP
Row
Address
Row
Address
Column
Address
Column
Address
tRC
tCAS
RAS

## Slide 62: Timing Parameters
trac (access time from RAS)–delay of appearance of real data on the outputs regarding RAS negative edge. For contemporary ICs – 40-100ns.
tRC- time of read cycle or write cycle – minimum period between the beginnings of neighboring cycle of accesses (75 – 125ns).
tPC - period of CAS sequence in page mode.
tRAS, tCAS – minimum duration of low level of RAS and CAS signals.
tRP - ~RAS Precharge time
tCP - ~CAS Precharge time
tRCD - ~RAS to ~CAS delay time
tCAC (access time from CAS) - Data delay regarding CAS#.

## Slide 63: Refresh
Refresh – distributed (earlier – burst)
RAS only refresh (ROR)
CAS before RAS (CBR)
RAS
CAS
MA
tRF
tRF= TRF/n  15,6 s
TRF
Distributed
Burst

## Slide 64: Structure of Module of Asynchronous DRAM
Memory address
Write
Read
AR
Matrix of Memory ICs
WR RAS CAS0 CAS1..
Controller
Refresh
timer
Refresh
Decoder of high address bits
Address
multiplexer
Data buffer
Mem
Din/out

## Slide 65: Synchronous DRAM (SDRAM)
Difference from asynchronous DRAM:
Synchronous method of data transfer on bus
Pipelining
Application of several memory banks
Transfer of part of control functions to IC memory
Partitioning into banks allows combining access to a cell of one bank prepared for the next operation in other banks.
At recurrent access to the banks, the frequency of accesses to other banks reduces.

## Slide 66: DDR SDRAM IC Memory Structure
I/O gates
Mode Register
Control Logic
Addr.
Reg.
A0-A12
BA0,BA1
Refresh
Counter
Row
Address
MUX
Bank
Control
Column
Address
Counter/latch
15
13
2
11
Row Address
Latch and DC
Read latch
Write FIFO and drivers
DLL
receivers
drivers
DQS generator
CK
DQ
DQS
DM
CKE
CK#
CS#
WE#
CK
CAS#
RAS#
10
1
Column0
Column0
Bank 0,
Row
Latch,
Decoder
Bank 0,
Memory
Array
8192×1024×8
8192
Column
Decoder
1024
4
4
8
1
1
4
4
4
4
8
4
1

## Slide 67: DDR SDRAM
Controlled by both edges of clock (it duplicates throughput of memory interface)
Clock is carried out as usual in internal blocks of ICs
Synchronization of DDR technology has the following requirements:
Clock are generated and transferred in differential form (simultaneously CLK and ~CLK).
Special signal DQS (DQ Strobe) is inserted for data synchronization.
DLL blocks are inserted to IC for self-tuning of the delay.
DLL (Delay Locked Loops) corrects clock skew and multiplies frequency if necessary.
Timings – the number of cycles required to read the first four memory elements

## Slide 68: Examples
Wintec AMPO 1GB 184-Pin DDR SDRAM DDR 400 (PC 3200) Samsung Desktop Memory Model 3AMD1400-1GB-R
SAMSUNG 8GB (2 x 4GB) 240-Pin DDR3 SDRAM DDR3 1600 (PC3 12800) Desktop Memory Model MV-3V4G3D/US

## Slide 69: SDRAM (Single Data Rate)
133 МHz
Input/Output Buffers
133 МHz
133 МHz
Memory
Core
Input/Output Buffers
Core Frequency
Clock Frequency
Data Frequency
The transfer of each bit of the buffer occurs with every clock of the memory core

## Slide 70: DDR SDRAM (Double Data Rate)
The transfer of two bits in the I/O buffer is carried out on the positive edge of clock
Issuance bits to the I/O bus is carried out both on the positive and the negative edge of clock
It provides twice the memory bandwidth.
133 МHz
Input/Output Buffers
133 МHz
266 МHz
Memory
Core
Input/Output Buffers
Core Frequency
Clock Frequency
Data Frequency

## Slide 71: DDR2 SDRAM
Memory
Core
Input/Output
Buffers
133 MHz
Input/Output Buffers
266 MHz
533 MHz
Core Frequency
Clock Frequency
Data Frequency
4n – prefetch mechanism

## Slide 72: DDR3 SDRAM
Memory Core
Input/Output
Buffers
100 MHz
Input/Output Buffers
400 MHz
800 MHz
Clock Frequency
Data Frequency
Example: DDR3-2400, core frequency 300 MHz, Cycle time 3,33 ns, data frequency 1200 MHz, peak data transfer rate 19200MB/s.
8n – prefetch mechanism

## Slide 73: Evolution of DDR SDRAM
Memory array (100-150MHz)
Memory array (100-1200Hz)
Memory array (100-200MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
1N
2N
4N
8N
I/O (100-150MHz)
I/O (100-200MHz)
I/O (200-533MHz)
I/O (400-1066MHz)
MUX
MUX
MUX
100-150Mbps
200-400Mbps
400-1066Mbps
800-2133Mbps
SDR
DDR/
LPDDR
DDR2/
LPDDR2
DDR3/
LPDDR3
Prefetch

## Slide 74: DDR4 SDRAM
If the trend shown earlier were followed with DDR4, DDR4 would have a prefetch of sixteen, but we have seen that is not desirable.
DDR4 avoids this issue by introducing the concept of bank groups.
With bank groups, a prefetch of eight is executed in one bank group, and another prefetch of eight can be executed in another independent bank group.
The bank groups are separate entities, such that they allow a column cycle to complete within a bank group, but that column cycle does not impact what is happening in another bank group.
Effectively, the DDR4 SDRAM can time division multiplex its internal bank groups in order to hide the fact that the internal SDRAM core cycle time takes longer than a burst of eight requires on the interface.

## Slide 75: DDR4 Solution to Prefetch of Eight
8N
8N
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
Memory array (100-266MHz)
MUX
MUX
MUX
I/O (667-1600MHz)
Bank Group 0
Bank Group 1
DDR4
1333-3200Mbps

## Slide 76: Read Only Memory (ROM)
ROM is non-volatile memory
ROM is a combinational circuit with n inputs and m outputs
Types of ROM: mask ROM, programmable ROM, erasable ROM
2n×m ROM
A0
A1
A2
An-1






Address
inputs
Data
outputs
D0
D1
Dm-1

## Slide 77: Internal ROM Structure
Horizontal lines – lines of word selection, Vertical lines – lines of bit selection.
m output lines
Decoder
0
1
2
2n-1
n address
lines
A0
A1
A2n-1

## Slide 78: Mask Programmable ROM
Information is recorded with the help of mask in the final stage of technological process.
As a connecting link diodes or MOS transistors are used.
11010001
10101011
Word line
bit line
+5V
Active low word line (WL)

## Slide 79: Programmable ROM
A PROM chip is manufactured with all its diodes or transistors “connected”.
The customer may program the ROM using PROM programmer.
A link is vaporized by selecting it using PROM address and data lines and then applying a high voltage pulse (10-30V) to the device through a special input pin (for programming).
DC
0
1
2
0
1
2
3
4
5
6
7
Fuse
OR Matrix

## Slide 80: Application of MOS Transistors as Memory Cells
DC



VDD
  
  
A0
A1



An-1
~D0
~D1
~D’7
Active high word line
Active low bit lines

## Slide 81: Erasable PROM
Erasing old information and its replacement with the new one is possible.
Erasing is carried out by ultraviolet rays in EPROM (erasable PROM).
In EEPROM (electrically PROM) – by electrical signals.
Floating gate of MOS transistors is used as connection links.
Floating gate
Source
Substrate
Gate
Drain
n
+
p
Device cross-section
n
+
Polysilicon
SiO2
Si
G
S
D

## Slide 82: Floating-gate Avalanche-Injection MOS (FAMOS)
Reprogramming:
Erase the programmed values
Record the new values
Recording information (the programming) is much slower (on the order of magnitude) than reading.
The property of this device - a programmable threshold voltage.
D
n+
n+
20 V
20 V
-
-
-
-
-
-
-
-
-
-
D
S
n+
n+
D
0 V
0 V
-
-
-
-
-
-
D
S
-
-
-
-
Recording
Storage

## Slide 83: Electrically Erasable Programmable Read-Only Memory(EEPROM)
FLOTOX-транзистор (Floating-Gate Tunneling Oxide Transistor)
10 V
-10V
V
I
Fowler-Nordheim I-V characteristic
n+
n+
Source
Gate
Drain
Floating Gate
SiO2
Polysilicon
10nm
Substrate

## Slide 84: Two Transistor Cell
A circuit with two transistors takes up more space on the chip.
The advantage - a large number of erase cycles up to 105.
When programming the threshold T1 is higher than VDD, and therefore the cell is switched off
VDD
Word line
Bit line
Threshold control
with two transistors
Т1
Т2

## Slide 85: Examples of EEPROM IC
~CS | ~OE | ~WE | Inputs/Outputs | Mode
1 | x | x | z | Not Selected
0 | 1 | 0 | Inputs | Write
0 | 0 | 1 | Outputs | Read
A0
WE
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
A15
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
CS
OE
128K8
A16
512K8
A1
WE
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
A15
A16
A17
A18
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
CS
OE
A0
A0
WE
A1
A2
A3
A4
A5
A6
A8
A9
A10
A11
A12
A13
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
CS
OE
32K8
A7
A14

## Slide 86: Atmel 256K (32K x 8) – Paged Parallel EEPROM (AT28C256)
The AT28C256 is accessed like a Static RAM.
Read
  When ~CE and ~OE are low and ~WE is high, the data stored at the memory location determined by the address pins is asserted on the outputs.
Byte Write
  A low pulse on the ~WE or ~CE input with ~CE or ~WE low (respectively) and ~OE high initiates a write cycle. The address is latched on the falling edge of CE or WE, whichever occurs last.
Page Write
  The page write operation allows 1 to 64 bytes of data to be written into the device during a single internal programming period.
  A page write operation is initiated in the same manner as a byte write; the first byte written can then be followed by 1 to 63 additional bytes.

## Slide 87: Organization of IC size 32Kx8
DC
Matrix
512x64
Matrix
512x64
Matrix
512x64
Matrix
512x64
Matrix
512x64
Matrix
512x64
Matrix
512x64
Matrix
512x64
D7
D6
D5
D4
D3
D2
D1
D0
A6
A14
A0
A5
64-1 MUX
64-1 MUX
64-1 MUX
64-1 MUX
64-1 MUX
64-1 MUX
64-1 MUX
64-1 MUX
0
1
511




## Slide 88: Using ROM To Implement Integer Multiplication
A0
A1
A2
A3
A4
A5
A6
A7
CS
A0
A1
A2
A3
B0
B1
B2
B3
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
A,B – 4-bit integer unsigned
A= (a3a2a1a0)
B=(b3b2b1b0)
A×B = P
A7A6A5A4A3A2A1A0 | Q7Q6Q5Q4Q3Q2Q1Q0
B3B2B1B0A3A2A1A0 | P7 P6 P5P4P3P2 P1 P0
0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 1 | 0 0 0 0 0 0 0 0
   |   
0 0 1 1 0 1 1 1 | 0 0 0 1 0 1 0 1
0 0 1 1 1 0 0 0 | 0 0 0 1 1 0 0 0
0 0 1 1 1 0 0 1 | 0 0 0 1 1 0 1 1
   |   
1 1 1 1 1 1 0 1 | 1 1 0 0 0 0 1 1
1 1 1 1 1 1 1 0 | 1 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1 | 1 1 1 0 0 0 0 1

## Slide 89: Using ROM To Implement Logic Functions (LUT)
A0
A1
A2
A3
A4
A5
A6
A7
CS
X8
X7
X6
X5
X4
X3
X2
X1
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
x1x2x3x4x5x6x7x8 | y1y2y3y4y5y6y7y8
0 0 0 0 0 0 0 0 | 0 0 1 0 1 0 0 0
0 0 0 0 0 0 0 1 | 1 1 1 0 1 0 0 0
0 0 0 0 0 0 1 0 | 0 1 0 0 1 0 0 0
0 0 0 0 0 0 1 1 | 1 0 0 0 0 0 1 0
0 0 0 0 0 1 0 0 | 0 1 1 0 0 1 0 0
0 0 0 0 0 1 0 1 | 1 0 0 1 0 1 0 1
   |   
1 1 1 1 1 1 0 1 | 1 0 0 1 0 1 1 1
1 1 1 1 1 1 1 0 | 1 1 0 0 1 0 1 1
1 1 1 1 1 1 1 1 | 0 0 1 1 1 0 0 1

## Slide 90: Flash Memory
Flash memory similar to EPROM. Particular qualities:
Data erasing is accomplished by blocks (not separate words).
EPROM
EEPROM
Flash
+
=
2 power supplies
ultra-violet erasing
1-transistor cell
1 power supplies
electrical signals erasing
2-transistors cell
1 or 2 power supplies
electrical signals erasing
1-transistor cell

## Slide 91: Flash Memory (2)
Erasing: 12 V – source, 0 V – control gate
Programming – 12 V control gate, 12 V – drain, 0 V - source
Erasing occurs over the entire crystal or just one area of memory
(access transistor is not needed).
The control unit regularly checks the value of the threshold in the process of erasure and the erasure time of dynamic change.
n+
n+
Control
Gate
-
-
D
S
-
-
Floating Gate
Thin tunneling oxide
Erasure
Programming
ETOX Cell

## Slide 92: Erasing Flash Memory (NOR)
0 V
12 V
0 V
BL0
BL1
Open
Open
  
S
D
G
12 V

## Slide 93: Programming Flash Memory
0 V
12 V
0 V
BL0
BL1
6 V
0 V

S
D
G
12 V
6 V
Writing

## Slide 94: Reading from Flash Memory
   
S
D
G
5 V
1 V
Reading
0 V
5 V
0 V
BL0
BL1
1 V
0 V
WL0
WL1

## Slide 95: NOR Flash Memory
To form a low level in the output F, the presence in chain of transistors even if one “on transistor” is enough.
All transistors, except addressable, must be closed.
Fast access at random sample.
X1
X2
Xm
R
VDD
F

## Slide 96: NAND Flash Memory
All transistors, except addressable, must be open.
Compact structure, but random mode is not provided.
Word 0
Word 7



Word 6
Select gate 1
Select gate 2
Bit Line 0



Bit Line n-1
Cells can
be accessed serially
Cells 5 to1 not shown

## Slide 97: The Structure of Matrix Based on NOR Gates
Word
lines
Bit lines
VDD

## Slide 98: NAND and NOR Architecture
NAND and NOR architectures do not compete because they are used in various fields of data storage.
The design of NAND - three-dimensional array. The basis of the same matrix as the NOR, but instead of a transistor at each intersection - column from the set of series-connected cells.
NOR –faster than NAND
NAND– more compact.

## Slide 99: AM 28F010 Flash Memory Logic Symbol
A0
A1
A16
DQ0
DQ1
DQ7
CE
OE
WE
CN
5V Supply Operation
Access Time: 150ns
Low Power Consumption
Fast Programming
Sector Protection
100,000 Erase Cycles
Features

## Slide 100: RAM Initialization
module ram (clk, we, addr, din, dout);
input clk,we;
input [3:0] addr;
input [15:0] din;
output [15:0] dout;
reg [15:0] ram [15:0];
reg [15:0] dout;
initial begin
ram[15]=16’h020A; ram[14]=16’h0030; ram[13]=16’h0810; ram[12]=16’h02BA; ram[11]=16’h073F; ram[10]=16’hC810; ram[9]=16’h92BA; ram[8]=16’h073E; ram[7]=16’hCA10; ram[6]=16’h129A;ram[5]=16’h073;ram[4]=16’hC810;ram[3]=16’h02BA; ram[2]=16’h073;ram[1]=16’hC810;ram[0]=16’h9700;
end
Example 1

## Slide 101: RAM Initialization
Example 2
reg[15:0] ram[0:255];
integer k;
initial begin
for (k=0;k<=100; k=k+1)
ram[k]=16’h1234;
ram[101]=16’h1111;
ram[102]= 16’h2222;
for(k=103; k<=255; k=k+1)
ram[k]=16’hFFFF;
end

## Slide 102: RAM Initialization
Example 3
module ram (clk, we, addr, din, dout);
input clk,we;
input [5:0] addr;
input [31:0] din;
output [31:0] dout;
reg [31:0] ram [0:63];
reg [31:0] dout;
initial begin
$readmemb("ram_data",ram);
end
always @(posedge clk)
begin if (we)
ram[addr] <= din; dout <= ram[addr];
end
endmodule

## Slide 103: Examples of ROM Description
module rom (addr,dout);
input [2:0] addr;
output reg[7:0] dout;
reg [7:0] rom[0:7] ;
always @(addr)
case(addr)
3’d0: dout = 8’d10;
3’d1: dout = 8’d11;
3’d2: dout = 8’d20;
3’d3: dout = 8’d135;
3’d4: dout = 8’d140;
3’d5: dout = 8’d230;
3’d6: dout = 8’d77;
3’d7: dout = 8’d1;
endcase
ROM description using case statement

## Slide 104: ROM Description
module rom (addr);
input [2:0] addr;
reg[7:0] rom[0:7];
initial
begin
rom[0] = -15;
rom[1] = 25;
rom[2] =12;
rom[3] = -100;
rom[4] =127;
rom[5] = 75;
rom[6] =11;
rom[7] = 48;
end
endmodule
ROM description using initial block

## Slide 105: ROM Description
module rom_using_file (address, data, read_en ,ce);
input [7:0] address;
output [7:0] data;
input read_en; //Read Enable
input ce; //Chip Enable
reg [7:0] mem [0:255] ;
assign data = (ce && read_en)?mem[address] : 8'b0;
initial begin
$readmemb("rom_content", mem); // rom_content is memory file
end
endmodule
ROM description using external file

## Slide 106: Reading from a ROM
. . .
reg [15:0] rom[16383:0];
always @ (posedge clk)
if(clk_en == 1'b1)
out <= rom[address];
else out <= {16{1'bz}};