## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Memory Devices

## Slide 4: Programmable Logic Devices
Programmable Logic
Simple PLD
FPGA
PLA
PROM
PAL
CPLD
Complex
PLD
Systems on Chip (SOPC)
GAL
A simple PLD can replace a number of standard logic gates.
Usually re-programmable PLDs are used during the development phase.
One-time programmable – during production.

## Slide 5: Three Types of Simple PLD
Fixed AND (Decoder)
Programmable OR
Programmable Read Only Memory - PROM
Programmable And
Programmable OR
Programmable Array Logic Device - PAL, GAL
Programmable And
Programmable OR
Programmable Logic Array Device - PLA
Inputs
Outputs
Inputs
Outputs
Outputs
Inputs

## Slide 6: Simple PLD (PLA)
Input Buffers
and
Invertors
AND
Matrix
OR
Matrix
Output Buffers
x1
x2
xn
I1
I2
.
I2n






t1 t2    tk






O1
O2
Om
y1
y2
ym

## Slide 7: Types of Programmable Links
Fuse logic:
Materials - nichrome, polysilicon
At applying high - voltage pulse fuse is vaporized
Non-volatile, radiation-hardened
One-time programmable
Antifuse logic:
Non-volatile, radiation tolerant
Typical programmed resistances range from 5 to 500.

## Slide 8: Anti-fuse
n+
Polysilicon
SiO2
Dielectric ONO (oxide-nitride-oxcide)
n+
Before programming
After programming
A programming pulse breaking-down three-layered dielectric and ONO creates conductive channel.

## Slide 9: Simple PLD: PLA
The first PLD – PLA (programmable logic arrays)
PLA – combinational two-level AND-OR device that can be programmed to implement any some-of- product logic expression.
The PLA is characterized by:
Number of inputs (n)
Number of outputs (m)
Number of product term (p)
“n×m PLA with p product terms” contains:
p 2n-input AND gates
m p-inputs OR gates
p<<2n

## Slide 10: PLA
w
a
x
y
z
b
c
Inputs:
Outputs:
Programmable OR matrix
Program-
mable AND
matrix
A 3×4 PLA with six product terms

## Slide 11: Programmable AND Logic
A
~A
B
~B
+VS
Diode link
CMOS Transistor link
P

## Slide 12: Programmable OR Logic
CMOS Transistor link
P1
P2
P3
P4
0V
Diode link
0V
Out

## Slide 13: Fragment of PLA
A
~A
Y=A·B + C
~B
+5VS
B
C
A·B
C

## Slide 14: PLA Programmed with a Set of Four Logic Functions
w=a~b + ~ac; x=a + c;
y=a~b + ~bc; z=~a~b + c
w
a
x
y
z
b
c
a~b
~ac
a
~bc
~a~b
c

## Slide 15: Logic Symbols
= =
= =
= =

## Slide 16: PLA 16×8 with 48 Terms
0 PLA
1
.
.
.
.
.
15
x0
x1
x15
CS
y0
y1
y2
y3
y4
y5
y6
y7
0
1
2
3
4
5
6
7
PROM is a programmable device, too: fixed AND matrix, programmable OR matrix.

## Slide 17: Full Adder Implementation
S
Cout
a
b
cin
a’b’cin
ab

a’bcin’
ab’cin’
abcin
acin
bcin
S=a’b’cin + a’bc’in + ab’c’in + abcin;
Cout = ab + acin + bcin

## Slide 18: PLA Programming Table
а b cin | S Cout
0 0 1 | 1 –
0 1 0 | 1 –
1 0 0 | 1 –
1 1 1 | 1 –
1 1 – | – 1
1 – 1 | – 1
– 1 1 | – 1

## Slide 19: FSM Implementation by PLA
0 PLA
1
2
3
4
5
.
.
.
15
CS
D0 Rg
D1
D2
D3
C
R
q0
q1
q2
q3
CLK
Reset
y1 y2 y3 y4
x1
x2
x3
x4
0
1
2
3
4
5
6
7
X1,x2,x3,x4 – FSM inputs, y1, y2,y3, y4 – FSM outputs.
Combinational circuit is implemented in the PLA. Rg – state register

## Slide 20: Programming of Output Polarity (EEPROM)
Minimal sum-of-product is defined for both the function F and its inversion, because F and ~F expressions are not identical.
It is necessary to choose simpler expression.
T transistor programs the polarity.
If transistor is opened F= F*,
else F=1F*=~F*
F*
R
VCC
T
F

## Slide 21: Flip-Flops Programming
Mux1, Mux2 – programmed multiplexers
Mux1 programs the type of flip-flop.
If S1=0, then FF operates as D flip-flop, else as T flip-flop.
Mux2 programs the type of output.
If S2=0, then type of output is register else combinational.
D
T
C
R
D
C
F
Output
Clock
Q
Mux1
Mux2
S1
S2
FF

## Slide 22: Programmable Arrays Logic (PAL)
a
b
c
z
y
x
w
AND Matrix
OR Matrix
PAL offers less flexibity than PLA

## Slide 23: Example
Y3
Y2
Y1
A
B
C
D
Y1= AB+CD
Y2=A+D
Y3= AB+CD + AD

## Slide 24: PAL 16L8
PAL 16L8:
Fixed OR array (7 AND gates permanently connected to each OR gate). AND gate outputs cannot be shared.
Each output has an individual three-state output enable signal, controlled by a dedicated AND gate.
Six of the output pins (I/O pins) may also be used as an input.
I1
I2
I3
I4
I5
I6
I7
I8
I9
I10
O1
IO2
IO3
IO4
IO5
IO6
IO6
O8
Technology: bipolar, one-time programmable.
Replaced by V-series PALs and GALs
Less expensive than PLA

## Slide 25: PAL 16L8 (2)
IK
  
  
IOK
Ip
IOP




## Slide 26: Registred PAL16R8
Output
  
  
D
Tri-state control
Clock
Input
Use for sequential logic design

## Slide 27: Versatile PAL – PAL16V8. Macrocell Structure
Input/Output
D
CLK
0
1
00
01
10
11
AR
SP
MUX
MUX
S1 S0
D-триггер:
AR – Asynchronous Reset и SP – Synchronous Preset
S1 S0 | Output
0 0 | Registered, active low
0 1 | Registered, active high
1 0 | Combinational active low
1 1 | Combinational active high
Output options

## Slide 28: Generic Array Logic (GAL Device)
GAL 16V8 – a single GAL device type
GALs use floating-gate/electrical erase technology
Can be configured to emulate of any PAL device structure
Inputs -10, outputs – 8, product terms -8, feedback – 6.
Technology: CMOS, re-programmable
Delay time input-to-output – 3.5 ns.

## Slide 29: PLD GAL16V8, GAL22V10
I2
I3
I9
Output
Logic
Macro-
cell
Output
Logic
Macro-
cell
Output
Logic
Macro-
cell
I1
IО8
I11

## Slide 30: Macrocell Structure
CLK
D
CLK
10
00
Input/
Output
01
11
VCC
FMUX
10
00
01
1
0
0
1
OE
OE
Feedback Signal
Signals
from AND
Matrix
OMUX
TSMUX
PTMUX
To FMUX input of the next cell
From the output of the next cell
S0 S1(i)
S0 S1(i)
XOR=1

## Slide 31: Output Logic Macrocell of GAL 16V8
OMUX specifies the mode of output – combinational (OR gate) or registered (D flip-flop).
TSMUX – controls of enable input
FMUX – selects feedback signal
PTMUX – transfers 8-th conjunction or 0 to OR gate
S1 S0 | Tri-state Buffer Output
0 0 | The output signal is allowed by VCC
0 1 | Z Output
1 0 | The output signal is allowed by OE
1 1 | The output signal is allowed by 8-th conjunction

## Slide 32: D Latch Implementation (Complex Mode)
CS
D
EN
O1
Q=DEN+QEN
XOR=1

## Slide 33: Registered Mode
OE
CLK
D
EN
O1
XOR=1
D
D
O1

## Slide 34: CPLD
CPLD – Complex Programmable Logic Device
CPLD comprises multiple PLA or PAL blocks. These blocks are connected to a set of interconnection wires.
PAL – blocks implement logic conversions.
Programmable Interconnection Array – PIA is programmable.
All the connections are identical in CPLD.
PIA allows connecting the output of any functional unit with any other input blocks.
The inputs of blocks are associated with the horizontal lines that cross all vertical lines of the matrix.
A configuration memory cell is floating gate MOS transistor (EEPROM or Flash).

## Slide 35: CPLD
IOB
PIA
IOB
PAL
PAL
PAL
PAL
PAL
PAL
PAL
PAL
IOB – Input/Output Block
PIA – Programmable Interconnect Array

## Slide 36: Interconnection Wires
PAL
PAL
PAL
PAL
PIA

## Slide 37: Section CPLD
  
  
  
D
D
D
  
  
  
  
  
  
  
  
  
  
  
PAL block
PAL block

## Slide 38: FPGA
FPGA chips are divided into classical and combined.
Combined FPGA contains CPLD elements.
There are several types of FPGA:
SRAM-based configuration memory (XILINX, Altera)
Once programmable (anti-fuse logic) - Actel (MicroSemi), QuickLogic
Flash-Memory configuration (Actel, ProASIC)
Combined architecture, development of which began with the design by Altera family FLEX8000.
FPGA consists of the following parts:
Functional blocks
Programmable interconnect
I/O logic cells

## Slide 39: FPGA (2)
Classic FPGA is two-dimensional array of identical configurable logic blocks.
All FPGAs have the following key elements:
The programming technology
The basic logic cells
The I/O logic cells
Programmable interconnect
Software to design and program the FPGA
As result of programming functional circuit is implemented in internal area of FPGA.
I/O blocks provide FPGA interface with other circuits.
Typical functional blocks FPGA:
Programmed multiplexers
Look-up tables (Programmable ROM, SRAM)

## Slide 40: SRAM-based PLD
SRAM Cell
a
b
T2
T1
Select
Write/read line
Advantages: re-programmable
Disadvantage:
occupy more space
more power consumption
Each link consists of a flip-flop with a transistor switch.
T2 closes or breaks the circuit section a and b depends on the state of flip-flop.
At programming T1 is switched on and flip-flop is set.
T1 is closed at operative mode. The flip-flop holds its state.

## Slide 41: SRAM Cell
Word Line
~ Bit Line
Bit Line

## Slide 42: Transmission Gate as SRAM Cell Controlling
SRAM Cell
A
B
Configuration
Control
Write
Read
Interconnect path
EN
The connection is off, if EN=1.
The connection is established when the transmission gate is on (i.e. EN=0). 0 is applied at the gate of the p-channel transistor and 1 is applied at the gate of the n-channel transistor. The device can reprogrammed simply by changing the content of the controlling memory cell.

## Slide 43: Flash Switch
а
b
State, Write
Word line
Floating Gate
Sensing
Switching
The sensing transistor is only used for writing and verification of the floating gate voltage.
The switching transistor is used to connect or separate routing nets, or to configure VersaTile logic. It is also used to erase the floating gate.
Program and erase are accomplished Fower–Nordheim
Tunnelling where the floating gate overlaps the source and drain.

## Slide 44: FPGA (2)
I/O block
I/O block
I/O block
I/O block
CLB –
Configurable logic block
Interconnection Switches
Conceptual FPGA

## Slide 45: XILINX 4000 Series (Example)
Distributed RAM bits – 1 038 336
Device | CLB matrix | Total CLBs | Max. I/O | Flip-Flops | Max RAM Bits | Max. Gates (no RAM) | Typical Gates range Logic and RAM)
XC4002 XL | 8×8 | 64 | 64 | 256 | 2048 | 1600 | 1000-3000
XC4003 E/XL | 10×10 | 100 | 80 | 360 | 3200 | 3000 | 2000-5000
XC4085 XL | 56×56 | 3 136 | 448 | 7 168 | 100352 | 85000 | 55000-180000

## Slide 46: Boolean Functions Implementation
In the LUT at A3, A2, A1, A0 “1” is written, if the address code is a minterm given by 4-input logic function. For example, if it is written at 1,1,1,1 address “1”, and for other addresses - zero, then the LUT implements 4-variables AND function.
A3
A2
A1
A0
G
G4
G3
G2
G1
Look-up Table (4-LUT block)

## Slide 47: Example
G = G1  G2  G3 G4
0,3,5,6,9,10,12,15 at addresses are recorded 0, and for other addresses - 1.
G4 G3 G2 G1 | G
0 0 0 0 | 0
0 0 0 1 | 1
0 0 1 0 | 1
0 0 1 1 | 0
0 1 0 0 | 1
0 1 0 1 | 0
0 1 1 0 | 0
0 1 1 1 | 1
1 0 0 0 | 1
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 1
1 1 0 0 | 0
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 0

## Slide 48: Example. Implementation Function of Five Variables
LUT
a0
a1
a2
a3
а0
а1
а2
а3
y=f(a0,a1,a2,a3,a4)
a4
LUT

## Slide 49: Implementation of Two Functions
LUT
a0
a1
a2
a3
LUT
Y0
Y1

## Slide 50: One Possible Implementation of a 3-LUT
Y
A0
A1
A2
0/1
0/1
0/1
0/1
0/1
0/1
0/1
0/1
111
110
101
100
011
010
001
000
LUT-3
A0
A1
A2
A0
A1
A2
Y

## Slide 51: Programmable Multiplexers
Multiplexers can operate as universal logical modules:
Address inputs – function variables
Information inputs – adjustment signals
00
01
10
11
I0
I1
I2
I3
x1 x0
f (00)
f (01)
f (10)
f (11)

## Slide 52: CLB
Y
XQ
X
G(G1…G4)
G4
G3
G2
G1
F(F1…F4)
F4
F3
F2
F1
H(F,G,H1)
S/R
control
D Q
CLK
EN
1
S
R
S/R
Contr
D Q
CLK
EN
S
R
1
K
(CLK)
4
4
4
4
C1 – C4
YQ
M1
M2
M3
M4
M5
M6
M7
M8
M9
M10
M12
M13
M14
M15
M16
M11
DIN/H2
SR/H0
EC
H1

## Slide 53: CLB
Each CLB has two 4-input LUTs (RAM with organization 16×1) and two registers.
F, G: 4-input -> 16 bits of RAM (each)
H: 3-input –> 8 bits of RAM
RAM is loaded at system initialization from external PROM
Two LUTs implement two independent logic functions F and G.
The outputs F and G can be combined to form a more complex function H.
For the 4000E families, each CLB can be configured as synchronous RAM. Write address, data, and control are synchronized to write clock. This is called distributed RAM.
Possible configurations are:
Two independent 16 x 1 RAMs
One 32 x 1 or 16 x 2 RAM
One 16 x 1 dual-port RAM (second port is read-only)

## Slide 54: XILINX FPGA (XC4000)
At the Y output values of G and H function are supplied depending on multiplexer M8 programming. While at the X output values of F and H functions are supplied.
It’s possible to get:
3 separate functions of independent variables (two of 4 arguments and one of three)
Any function of 5 arguments
Some functions up to 9 variables
Depending on M7and M12 multiplexer programming flip-flops receive data from LUTs or external DIN input.
Multiplexers M9 and M14 allow CLK polarity programming.
EN is also programmable.

## Slide 55: Example
P = a0  a1  a2  a3  a4  a5  a6  a7  a8  a9  a10  a11
a0
a1
a2
a3
a4
a5
a6
a7
G-LUT
F-LUT
H-LUT
a8
a9
a10
a11
G4
G3
G2
G2
F4
F3
F2
F1
H3
H2
H1
G4
G3
G2
G2
G-LUT
CLBi
CLBj
P

## Slide 56: IOB
7
1
2
5
6
8
D
CLK
EN
1
D
CLK
EN
2
Delay
I/O
T
OUT
OCLK
I1
I2
4
ICLKEN
ICLK
FF1
FF2
3
Slew rate control
Program. logic

## Slide 57: IOB
I/O unit has two channels for input and output signals I/O pins can be used as an input and as an output
A direct delivery signal to the output or from flip-flop is possible.
To ensure the pipeline mode of input with the M8 on the way to the D input of FF2 can be introduced delay. The effect is to delay D-input relative to the FPGA’s internal copies of the system clock, quaranteeing that the input will have a zero hold-time requirement with respec to external system clock. This benefit comes at expense increasing setup time.
With the M1-M4 polarity of input signals are selected.
Management of the analog output parameters:
  Slew rate control
  A resistor can be included between I/O pin and bus power or ground.

## Slide 58: Programmable Interconnect
Direct connect
Global Clock
3
8
4
3
CLB
2
2
Single
Double
Long
Direct connect
Long
Single
Double
Long
6
4
8
4
2
2
The number of wires
Tri-state driver

## Slide 59: Programmable Interconnect (2)
Four wires of “Global Clock” are used as clock providing short delay and minimal skew.
Single – flexible connectivity between adjacent blocks
Direct connection
Double – connection past two CLBs before heatting a switch (shorter delays for longer connections)
Long – real long connection (travel all the way across or down a row or column and are driven to tri-state drivers near the CLB)

## Slide 60: Programmable Interconnect (XC4000)
Programmable Switch Matrix
PSE – Programmable switch element
A few possible connections

## Slide 61: Two-bit Down Counter Implementation
q1 q2 | d1 d2
0 0 | 1 1
1 1 | 1 0
1 0 | 0 1
0 1 | 0 0
C
D
q2
q1
C
D
Clk

## Slide 62: Two-bit Down Counter Implementation
F4F3F2F1 | F
x x 0 0 | 1
x x 0 1 | 0
x x 1 0 | 0
x x 1 1 | 1
G4G3G2G1 | G
x x x 0 | 1
x x x 1 | 0
q1
q2
d1
q2
d2
G4
G3
G2
G1
F4
F3
F2
F1
D
0
0
0
0
0
q2
q1
d1
d2
Clk
D

## Slide 63: Functions Implementation Using MUXs (3-LUT Block)
0/1
0/1
0/1
0/1
0/1
0/1
0/1
0/1
x3
x2
x1
y
BDD implementation
Q
~Q
0
0
1
1
0
1
0
1
0
1
0
1
0
1
1

## Slide 64: Example: Majority Function Implementation y = ac+ab+bc
0
0
0
1
0
1
1
1
c
b
а
y
0
1
0
0
1
1
1
1
1
1
0
0
0
0
а b c | y
0 0 0 | 0
0 0 1 | 0
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 1
1 1 1 | 1

## Slide 65: Actel FPGAs
1. Antifuse technology
  Based on channelled gate array architecture
  Each logic element is a combination of multiplexers which can be
  configured as a multi-input gate
2. EEPROM
3. Flash Based

## Slide 66: Actel (MicroSemi) ACT1 module
A0
A1
B0
B1
SA
S0
S1
SB
F
1
1
0
a
0
b
0
c
0
1
0
1
F
0
1
F = b + ac
d
1
d
1
c
b
0
a
0
1
0
1
F
0
1
F = a·b+b·c+d

## Slide 67: Actel (MicroSemi) ACT2 module
Out
00
01
10
11
D00
D01
D10
D11
S0
S1
A1
B1
A0
B0
C-module
00
01
10
11
D00
D01
D10
D11
S0
S1
A1
B1
A0
CLR
CLK
D
Q
S-module

## Slide 68: ACT3
D1
Q1
D00
D01
D10
D11
0
1
2
3
A1
B1
A0
B0
CLK
CLR
SE
Q

## Slide 69: Shannon Expansion Theorem
F = AB + ~BC +D
= B [AB + ~BC + D] + ~B[A  B + ~B  C + D]
= A  B + B  D + ~B  C + ~B  D
= B (A+D) +~ B (C+D);
Y=(A+B)(C+D)
Design a PLA, PAL and ROM at a gate level to implement the following sum of product functions:
X(A,B,C)=AB+A  B  C+A  B  C
Y(A,B,C)=A  B+A  B  C
Z(A,B,C)=A+B

## Slide 70: Programming Technologies
Modern FPGA architectures (SRAM-based, flash-based, antifuse-based)
and their applications.
FPGA devices are produced by a number of semiconductor companies: Xilinx, Altera, Actel, Lattice Semiconductors, QuickLogic and Atmel.
  SRAM-based FPGAs
SRAM-based FPGA stores logic cells configuration data in the static memory (organized as an array of latches). Since SRAM is volatile and can't keep data without power source, such FPGAs must be programmed (configured) upon start.
SRAM-based FPGAs include most chips of Xilinx Virtex and Spartan families and Altera Stratix and Cyclone.

## Slide 71: Programming Technologies
SRAM-based FPGAs with an internal flash memory
This type of FPGA is generally like the previous, except that these chips contain internal flash memory blocks, thus eliminating the need to have an external non-volatile memory.
Examples:
  Xilinx Spartan-3AN family. Each model of Spartan-3AN has an in-chip flash memory module with an SPI interface capable of storing two or more configuration bitstreams. The bitstream can be chosen during startup.
  LatticeXP family by Lattice Semiconductors.
  Using internal non-volatile memory can be also useful to prevent unauthorized bitstream copying.

## Slide 72: Programming Technologies
Flash-based FPGAs
The SRAM-based FPGAs with internal flash memory use flash only during startup to load data to the SRAM configuration cells. On the contrary, true flash-based FPGA uses flash as a primary resource for configuration storage, and doesn't require SRAM.
Аdvantage:
  less power consumptive.
  more tolerant to radiation effects.
Flash-based FPGA families such as Igloo and ProASIC3 are manufactured by Actel.
  using flash-based FPGAs can be a solution to prevent unauthorized
  bitstream copying

## Slide 73: Programming Technologies
Antifuse-based FPGAs
Antifuse-based FPGAs are different from the previous ones in that they can be programmed only once.
The antifuse is a device that doesn't conduct current initially, but can be “burned” to conduct current (the antifuse behavior is thus opposite to that of the fuse, hence the name).
Antifuse-based device families include Axcelerator produced by Actel.
Conclusion
  Modern SRAM-based FPGAs have highest densities, but consume a lot of power and need an external non-volatile memory to store configuration bitstream.
  SRAM-based FPGAs with an internal flash module doesn't need an external configuration memory.
  Flash-based and Antifuse-based FPGAs consume much less power than their SRAM-based counter parts.

## Slide 74: Comparison of Programming Technologies
Program. technology | Volatile/ nonvolatile | Reprogramming | Area | Resistance | Capasitance
SRAM | Volatile | In-circuit reprogrammable | High | High | High
EPROM | Nonvolatile | Out-of-circuit reprogrammable | Small | High | High
EEPROM/ flash | Nonvolatile | In-circuit reprogrammable | Medium to high | High | High
Antifuse | Nonvolatile | Not reprogrammable | Small | Small | Small

## Slide 75: Commercial FPGAs
Company | Divice name | General architecture | Logic block type | Programming technology
Microsemi | IGLOO | Sea of tiles | MUXs and gates | LUT/Flash
 | Pro/ASIC | Sea of modules | MUXs and gates | Flash,SRAM
 | Axcelerator | Sea of modules | MUXs and gates | SRAM
XILINX | Virtex,Artix, Kintex Spartan | Symmetrical Array | LUT | SRAM
Altera | Cyclone II Stratix II | 2-dimensional Row and column based | LUT | SRAM
Quicklogic | Eclipse | Flexible cell based | LUT | SRAM
Atmel | ATM40KAL | Cell-based | MUXs and basic gates | SRAM

## Slide 76: Modern XILINX FPGA
The basic XC4000 series - main item of equipment is considered CLB, consisting of two flip-flops and two LUTs. In the new series of FPGA the number of LUTs and flip-flops have increased several times.
Modern FPGA logic blocks are divided into several slices.
Each slice contains some of the same types of logic elements (schemes).
For example, CLB Virtex series consists of two sections, a series VirtexII - four sections.

## Slide 77: FPGA Resources
Virtex-7 7VHX580T
Total slices – 90 700
SLICELs – 55 300
SLICEMs – 35 400
Number of 6-Input LUTs – 362 800
Maximum Distributed RAM (KB) – 8 850
Shift Register (KB) – 4 425
Number of Flip-Flops – 725 600

## Slide 78: Virtex-7 CLB
Arrangement of slices within the CLB
Switch
Matrix
Slice(0)
Slice(1)
Cin
Cin
Cout
Cout
CLB

## Slide 79: Row and Column Relationship between CLBs and Slices
Slice
X0Y1
Slice
X1Y1
Cin
Cin
Cout
Cout
CLB
Slice
X0Y0
Slice
X1Y0
Cout
Cout
CLB
Slice
X2Y1
Slice
X3Y1
Cin
Cin
Cout
Cout
CLB
Slice
X2Y0
Slice
X3Y0
Cout
Cout
CLB

## Slide 80: SLICEM
LUT
FF
Cout
FF or Latch
LUT
FF
FF or Latch
LUT
FF
FF or Latch
LUT
FF
FF or Latch
DX
DI
CX
BX
BI
CI
AX
AI
RS Clk CE
Dmux
D
DO
Cmux
C
CO
Bmux
B
BO
AO
Amux
A

## Slide 81: Logic Resources in One CLB
А6:А1
WA6:WA1
O6
O5
DI2
DI1
MC31
CK
WEN
DI1
LUT in SLICEM
А6:А1
O6
O5
LUT in SLICEL
Slices | LUTs | Fliip/flops | Arithmetic and Carry Chains | Distributed RAM | Shift Register
2 | 8 | 16 | 2 | 256 bits | 128 bits

## Slide 82: Look-up Table (LUT)
The function generators are implemented as six-input LUTs
LUT can implement:
Any arbitrarily defined six-input Boolean function
  Two arbitrarily defined five-input Boolean functions
A six-input function uses:
  A1-A6 inputs
  O6 output
Two five-input or less functions use:
  A1-A5 inputs
  A6 driven High
  O5 and O6 outputs

## Slide 83: Distributed RAM
The function generators (LUTs) in SLICEMs can be implemented as a synchronous RAM ( distributed RAM elements).
  Single-Port 32 x 1-bit RAM (1 LUT)
  Dual-Port 32 x 1-bit RAM (2LUT)
  Quad-Port 32 x 2-bit RAM (4LUT)
  Simple Dual-Port 32 x 6-bit RAM (4 LUT)
  Single-Port 64 x 1-bit RAM (1 LUT)
  Dual-Port 64 x 1-bit RAM (2 LUT)
  Quad-Port 64 x 1-bit RAM (4 LUT)
  Simple Dual-Port 64 x 3-bit RAM (4 LUT)
  Quad-Port 64 x 1-bit RAM (4 LUT)
  Single-Port 128 x 1-bit RAM (2 LUT)
  Single-Port 256 x 1-bit RAM (4LUT)

## Slide 84: ROM -Memory
Each function generator in SLICEMs and SLICELs can implement a 64 x 1-bit ROM. Three configurations are available: ROM64x1, ROM128x1, and ROM256x1. ROM contents are
  Loaded at each device configuration.
  ROM 641 (1 LUT)
  ROM 1281 (2 LUT)
  ROM 2561 (4LUT)

## Slide 85: Block Diagram of a Dual-Port Distributed Memory
A[5:0]
D
CE
D
CE
D
CE
0
1
63
63
0
1
Bit 0
Bit 1
Bit 63
0
1
63
DC
A[5:0]
Read /write shared address
Address read-only
Single Port
Output
Double Port
Output
Din
EN
WE
CLK

## Slide 86: Dual-Port RAM in Verilog (64x16)
module dual_port_ram (clk, we, a, dpa, din, spo, dpo);
input clk,we;
input [5:0] a, dpa;
input [15:0] din;
output [15:0] spo;
output [15:0] dpo;
reg [15:0] ram [63:0];
always @(posedge clk)
begin
if (we)
ram[a] <= din;
end
assign spo = ram[a];
assign dpo = ram[dpa];
endmodule
WE
D
WCLK
A0
A5
DPA0
A1
A2
A3
A4
DPA1
DPA2
DPA3
DPA4
DPA5
SPO
DPO

## Slide 87: RAM 641S
А6:А1
WA6:WA1
O6
DI1
CK
WEN
Output
D
Registered
Output
D
A[5:0]
WCLK
WE
6
SPRAM64

## Slide 88: RAM 1281S
А[6:1]
WA[7:1]
O6
DI1
CK
WEN
Output
D
Registered
Output
D
A[6:0]
WCLK
WE
A[6]
А[6:1]
WA[7:1]
O6
DI1
CK
WEN
A[5:0]
SPRAM64
SPRAM64

## Slide 89: Dual-Port RAM 64x1
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
Output
D
Registered
Output
D
A[5:0]
WCLK
WE
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
D
Registered
Output
Output
SPO
DPO
DPRA[5:0]
DPRAM64
DPRAM64
DPRAM64

## Slide 90: Simple Dual Port RAM 32X1D
DPRA[4:0]
А6:А1
WA6:WA1
DI1
CK
RAM 32X1D
WE
O6
O5
A[4:0]
D
SPO
DPO
Port1: A[4:0], D
Write Only
Port2: DPRA[4:0], O6
Read Only Only

## Slide 91: Simple Dual Port RAM 326 SDP
А[6:1]
WA[6:1]
DI1
CK
WEN
DPRAM32
DI2
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
DPRAM32
DI2
O5
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
DPRAM32
DI2
O5
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
DPRAM32
DI2
O5
unused
unused
WADDR[5:1]
WADDR[6]=1
Data[1]
Data[2]
O[2]
Data[4]
Data[3]
Data[6]
Data[5]
RADDR[5:1]
ADDR[6]=1
O[1]
O4]
O[3]
O[6]
O[5]
WCLK
WED
D[5:1]
C[5:1]
B[5:1]
A[5:1]
RAM 32X6SDP
Port 1 - Write Only
Port 2 - Read Only

## Slide 92: Quad Port RAM
А[6:1]
WA[6:1]
DI1
CK
WEN
DPRAM64
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
DPRAM64
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
DPRAM64
А[6:1]
WA[6:1]
O6
DI1
CK
WEN
DPRAM64
Data_In_D
ADDRD[6:1]
DOD
ADDRC[6:1]
DOC
WCLK
WE
ADDRB[6:1]
ADDRA[6:1]
O6
DOB
DOA
D
D
D
D
Port1 –Read/Write
Port2, port3, port4 – Read-Only
RAM64X1Q

## Slide 93: Shift Operations
Shift Operation
  The shift operation is a single clock-edge operation.
  When CE is High, the input (D) is loaded into the first bit of the shift register.
  Each bit is also shifted to the next highest bit position. In a cascadable shift register configuration, the last bit is shifted out on the M31 output.
  The bit selected by the 5-bit address port (A[4:0]) appears on the Q output.
Dynamic Read Operation
  The Q output is determined by the 5-bit address. Each time a new address is applied to the 5-input address pins, the new bit position value is available on the Q output after the time delay to access the LUT. This operation is asynchronous and independent of the clock and clock-enable signals.

## Slide 94: Shift Register
32-bit Shift Register
Shift_in (D)
WE
CLK
SHIFTOUT
Q31
Q
Address (A[4:0])
  
• Operates on a single clock edge
• Enabled by an active-High clock enable
• The input (D) is loaded into the first bit of the shift register
• Each bit is also shifted to the next highest bit position

## Slide 95: 32-bit Shift Register (Configuration)
CLK
D
D
D
D
0
1
31
30
Q
D
A[4:0]
CE
Q0
Q1
Q30
Q31
Q31

## Slide 96: 32-bit Shift Register
DI1
A[6:2]
MC31
CLK
CE
D
Registered Output
Output Q
Output Q31
Shiftin (MC31 of previous LUT)
Din
A[4:0]
CLK
CE
WE
O6
SRL32

## Slide 97: 128-bit Shift Register
Registered
Output
Output
DI1
A[6:2]
O5
CLK
WE
Din
CLK
CE
DI1
A[6:2]
O6
CLK
WE
MC31
A[4:0]
MC31
DI1
A[6:2]
O6
CLK
WE
MC31
DI1
A[6:2]
O6
CLK
WE
MC31
D
Shiftout (Q127)
A[5]
A[5]
A[6]
SR1
SR3
SR2
SR4
SRL32
SRL32
SRL32
SRL32

## Slide 98: Four MUX 4:1
A[6:1]
O6
Output
D
Registered
Output
A[6:1]
O6
Output
D
Registered
Output
A[6:1]
O6
Output
D
Registered
Output
A[6:1]
O6
Output
D
Registered
Output
D[6:1]
A[6:1]
C[6:1]
B[6:1]
CLK
A - Sel A[1:0] DataA[3:0]
B - Sel B[1:0] DataB[3:0]
C - Sel C[1:0] DataC[3:0]
D - Sel D[1:0] DataD[3:0]

## Slide 99: MUX 16:1 (One Slice)
A[6:1]
O6
8:1 MUX
output1
Registered
Output
A[6:1]
O6
8:1 MUX output2
A[6:1]
O6
A[6:1]
O6
D[6:1]
A[6:1]
C[6:1]
B[6:1]
0
1
D
>
0
1
D
>
Registered
Output
SELD[1:0],
DATA[3:0]
Input1
SELC[1:0],
DATA[3:0]
Input1
SELB[1:0],
DATA[3:0]
Input2
SELA[1:0],
DATA[3:0]
Input2
F7BMUX
F7AMUX
CLK
SELF7(1)
SELF7(2)
(AX)
(CX)
(CMUX)
(AMUX)

## Slide 100: Hard-blocks located in FPGA
Dual Port Synchronous Block RAM
XtremeDSP;
Generators of clock signals MMCM (Multi-Mode Clock Managers) and PLL (Phase-Locked Loop);
High-speed serial transceivers (MGT, Multi-GigabitTransceivers);
Ethernet MAC controllers (Virtex-4, 5, 6);
PCI Express endpoint controllers;
Processor cores PowerPC 405(Virtex-II Pro, Virtex-4 FX), PowerPC 440 with FPU (Virtex-5 FXT), ARM Cortex A9 with FPU (Zynq-7000).

## Slide 101: Look-up-Tables
LUT can realize:
  1 function of 6 arguments (output O6)
  2 functions of 5 arguments (outputs O5,O6)
  2 or 3 functions (outputs O5, O6)
Slice can realize:
  1 function of 8 arguments
  2 functions of 7 arguments
  4 functions of 8 arguments
  5 functions of 5 arguments
  4 functions of 3 arguments (or less number of arguments)
  4 functions of 2 arguments (or less number of arguments)
To implement the functions that have more than 8 arguments are used interconnections resources.

## Slide 102: Embedded RAM (Block RAM)
The block RAM in Virtex®-7 FPGAs stores up to 36K bits.
Capabilities оf configuration of 36Kbit block
  64К1 - (when cascaded with an adjacent 36 KB block RAM)
  32K1
  16K2
  8K4
  4K9
  32K1
  2K18
  1K36
  51272
Read and Write operations are synchronous.
  Block RAM also enables efficient embedded processor applications. RAM performs a variety functions in an embedded processor: ROM, FIFO, CAM, circular buffer, LIFO . . .

## Slide 103: Block RAM in Virtex-7 (One port)
SRAM
Memory array (common
to both ports)
Write
Strobe
Read
Strobe
Control Engine
Latches
Register
Optional invertor
Din
Address
Dout
Latch
Enable
D
Q
Clock
RDEN
WREN
Configurable options

## Slide 104: Outputs
All outputs have a read function or a read-during-write function, depending on the state of the write enable (WE) pin.
The outputs are available after the clock-to-out timing interval.
The read-during-write outputs have one of three operating modes:
WRITE_FIRST, READ_FIRST, and NO_CHANGE.

## Slide 105: Read-Write Port Modes
The following synchronization modes are used for a given read-and-write port:
Read-first
Old contents are read before new contents are loaded.
Write-first (also known as read-through):
The default mode. WRITE_FIRST outputs the newly written data onto the output bus.
No-change
Data output does not change while new contents are loaded into RAM.
NO_CHANGE maintains the output previously generated by a read operation.

## Slide 106: Write_First Mode
CLK
WE
DI
Address
DO
EN
xxxx
1111
2222
A1
A2
A3
A4
Mem(A1)
Mem(A4)
1111
2222
Disable
Read
Write
Mem(A2)=1111
Write
Mem(A3)=1111
Read
0000

## Slide 107: Read_First Mode
Disable
Read
Write
Mem(A2)=1111
Write
Mem(A3)=1111
CLK
WE
DI
Address
DO
EN
xxxx
1111
2222
A1
A2
A3
A4
Mem(A1)
oldMem(A4)
oldMem(A2)
oldMem(A3)
Read
0000

## Slide 108: No_Change Mode
CLK
WE
DI
Address
DO
EN
xxxx
1111
2222
A1
A2
A3
A4
Mem(A1)
Mem(A4)
Read
Disable
Write
Mem(A2)=1111
Write
Mem(A3)=1111
Read
0000

## Slide 109: Single-Port Block RAM Read-First Mode Verilog Coding Example
module RAM_Read_First (clk, en, we, addr, din, dout);
input clk, we,en;
input [5:0] addr;
input [15:0] din;
output [15:0] dout;
reg [15:0] RAM [63:0];
reg [15:0] dout;
always @(posedge clk)
begin
if (en)
begin
if (we)
RAM[addr]<=din;
dout <= RAM[addr];
end
end
endmodule

## Slide 110: Single-Port Block RAM Write-First Mode Verilog Coding Example
module RAM_Write_First (clk, we, en, addr, din, dout);
input clk,we,en;
input [5:0] addr;
input [15:0] din;
output [15:0] dout;
reg [15:0] RAM [63:0];
reg [15:0] dout;
always @(posedge clk)
begin
if (en)
begin
if (we)
begin
RAM[addr] <= din;
dout <= din;
end
else
dout <= RAM[addr];
end
end
endmodule

## Slide 111: Single-Port Block RAM No-Change Mode Verilog Coding Example
module RAM_No_Change (clk, we, en, addr, din,dout);
input clk,we,en;
input [5:0] addr;
input [15:0] din;
output [15:0] dout;
reg [15:0] RAM [63:0];
reg [15:0] dout;
always @(posedge clk)
begin
if (en)
begin
if (we)
RAM[addr] <= di;
else
dout <= RAM[addr];
end
end
endmodule

## Slide 112: True Dual-Port Block-RAM
DIA|B – Data Input Bus
DIPA|B – Data Input Parity Bus, can be used for additional data inputs.
ADDRA|B – Address Bus
WEA|B- Write Enable
ENA|B – When inactive no data is written to the block RAM and the output bus remains in its previous state.
RSTREGA|B – Synchronous Set/Reset the output registers
DOA|B - Data Output Bus
DOPA|B- Data Output Parity Bus (or additional data)
RSTRАМA|B - Synchronous Set/Reset the output registers
CLKA|B – Clock input
REGCEA|B – Output Register clock enable
CASCADEIN[A|B] - Cascade input for 64K x 1
CASCADEOUT[A|B] – Cascade output for 64Kx1 mode.
DIA
DIPA
ADDRA
WEA
ENA
RSTREGA
RSTRAMA
CLKA
REGCEA
DIB
DIPB
ADDRB
WEB
ENB
RSTREGB
RSTRAMB
REGCEB
CLKB
DOA
DOPA
DOB
DOPB
CascadeINA
CascadeINB
CascadeOUTA
CascadeOUTB

## Slide 113: Conflict Avoidance
There is no dedicated arbiter.
Synchronous clocking:
The active edges of both port clocks occur simultaneously.
There are no timing constraints when both ports perform a read operation.
When one port performs a write operation, the other port must not write into the same location, unless both ports write identical data.
When one port performs a write operation, the write operation succeeds; the other port can reliably read data from the same location if the write port is in READ_FIRST mode.
DATA_OUT on both ports will then reflect the previously stored data.
If the write port is in either WRITE_FIRST or in NO_CHANGE mode, then the DATA_OUT on the read port would become invalid (unreliable). The mode setting the read-port does not affect this operation.

## Slide 114: Conflict Avoidance (2)
Asynchronous Clocking – more general case
Active edges of both clocks do not occur simultaneously.
There are no timing constraints when both ports perform a read operation.
When one port performs a write operation, the other port must not read- or write access the exact same memory location.
If this constraint is not satisfied, then the data on another port will be uncertain.
To avoid simultaneous access use EN input.

## Slide 115: One Block RAM Becomes Two Independent Single-Port RAMs
CLKA
ENA
DIA
ADDRA[m-1:0]
WEA
CLKB
ENB
WEB
ADDRB[n-1:0]
DIB
ADDRB[n]
ADDRA[m]
DOA
DOB
Both ports are independent, each with
its own memory organization, data
inputs and outputs, clock input and control signals.
For example, Port A could be 256x36 while Port B is 2Kx4.
Single-
Port A
Single-
Port B

## Slide 116: Block RAM Applications
Typically, block RAM is used for a variety of local storage applications. However, the following section describes additional, perhaps less obvious block RAM capabilities, illustrating some powerful capabilities to spur the imagination.
  Creating large RAM structure
  Block RAM as Read-Only-Memory
  FIFOs
  Two Independent Single-port RAMs Using One Block RAM
  A 512x72 Single-Port RAM Using One Block RAM
  Circular Buffers, Shift Registers, and Delay Lines
  Fast Complex State Machines and Microsequencers
  Fast, Long Counters Using RAM
  Four-Port Memory
  Content-Addressable Memory (CAM)
  Implementing Logic Functions Using Block RAM

## Slide 117: 7 Series FPGAs FIFO Architecture
FIFO - First-In, First-Out. Simple Double-Port Memory
SRAM
Write Counter
Read Counter
Status Flag
Logic
WEN
RDEN
WRCLK
RDCLK
Reset
OE
RD
WE
Write Count
Read Count
Data_In
Data_Out
Full
Empty
Almost
Full
Almost
Empty
RDERR
WRERR
waddr
raddr

## Slide 118: Fast Complex State Machines and Microsequencers
Because block RAMs can be configured with any set of initial values, they also make excellent dual-ported registered ROMs that can be used as state machines. For example, a 128-state, 8-way branch finite state machine with 38 total state outputs, fits in a single block RAM.
1Kx9
128x36
7 bit
7 bit
7 bit
36 bit
7+2 bits
FSM inputs
(branch control)
Output control
7 state bits,
38 output bits
Next_state
Current_state
Outputs
Moore FSM

## Slide 119: Fast Complex State Machines and Microsequencers
The two-port memory is divided into 2 independent single-port memories, the size of which is half of the total memory size (the highest bit of the 1st port is "1", the high bit of the second port is "0").
Port A is configured as 2Kx9, but only 1Kx9bit is used. The 7-bit output of port B is fed to the FSM (feedback) input.
Port A has 10 lines of address: 7 lines - from the outputs of the current state and 3 - branch signals. Fragment of the transition graph:
Si/yj
Sk/yl
Sm/yv
Sm/yv
Sp/yq
0
1
2
k
7
0, 1, 2 . . . - sets of inputs
yk, yl, . . . . - 36-bit sets of outputs
Port A Addresses
Current state
Condition code
7 bit
3 bit

## Slide 120: Fast, Long Counters Using RAM
A counter is an example of a simple state machine, where the next state depends only on the current state. A binary up counter, for example, simply increments the current state to create the next state.
TC – terminate count
>
>
CLK
TC
En
TC
CNT[9:0]
CNT[9:0]
10
10

## Slide 121: 20-bit Binary Up Counter
ADDRA[9:0]
DOA[9:0]
DOA[10]
DOA[17:11]
WEA
ENA
SSRA
CLK
>
ADDRB[9:0]
DOB[9:0]
DOB[10]
>
CLK
SSRB
WEB
ENB
Terminate Count
Unused
Unused
Count[19:11]
Count[9:0]
SSR
CLK
Count_EN
Terminal count from portB enables portA every 1024 clock cycles
DOB[17:11]

## Slide 122: 20-bit Binary Up Counter
A 20-bit binary counter can be constructed from two identical 10-bit binary counters, with the lower 10-bit counter enabling the upper 10-bit counter every 1024 clock cycles.
In this example, Port B is a 1Kx18 ROM (web is Low) that forms the lower 10-bit counter.
The 10 less-significant data outputs, representing the current state,
connect directly to the 10 address inputs, ADDRB[9:0].
The next state is looked up in the ROM using the current state applied to the address pins.
The eleventh data bit, D[10], forms the terminal-count output from the
counter. In this example, the upper seven data bits, DOB[17:11] are unused.

## Slide 123: Next-State Logic for Binary Up Counter
Present State | State Outputs | Next State
ADDR[9:0] HEX | TC D[10] | Count D[9:0]
0 | 0 | 1
1 | 0 | 2
2 | 0 | 3
. . . |  | 
3FF | 1 | 0

## Slide 124: Next-State Logic for Binary Up/Down Counter
Up/Down Control | Present State | State Outputs | Next State
ADDR[9] | ADDR[8:0] HEX | TC D[10] | Count D[8:0]
0 (Up) | 0 | 0 | 1
0 | 1 | 0 | 2
0 | 2 | 0 | 3
0 | . . . |  | 
0 | 1FF | 1 | 0
1(Down) | 1FF | 0 | 1FE
1 | 1FE | 0 | 1FD
1 | . . . |  | 
1 | 1 | 0 | 2
1 | 0 | 1 | 1FF

## Slide 125: Carry Look-Ahead Logic
All modern FPGAs contain fast lookahead carry logic.
In addition to function generators, dedicated carry logic is provided to perform fast arithmetic addition and subtraction in a slice.
A Virtex-6,7 FPGA CLB has two separate carry chains.
The dedicated carry path and carry multiplexer (MUXCY) can also be used to cascade function generators for implementing wide logic functions.

## Slide 126: Carry Logic
0 1
CIN
CYIN
S3
COUT
DI3
S2
DI2
S1
DI1
S0
DI0
O3
O2
O1
O0
CO2
CO1
CO0
CO3
O6, LUTD
O5, LUTD
DX
O6, LUTC
O5, LUTC
CX
O6, LUTB
O5, LUTB
BX
O6, LUTA
O5, LUTA
AX

## Slide 127: Adder in FPGA
LUT
Carry_in
a0
b0
FF
S0
Dedicated
Carry Chain
LUT
FF
Sn-1
Dedicated
Carry Chain
LUT
FF
an-1
an-1
Carry_out
Each LUT generates the sum bit of the corresponding input bits (a, b, and Carry-in).
The carry chain generates the carry in parallel and feeds it using the dedicated interconnect to
the LUT, implementing the sum of the next bit.

## Slide 128: Digital Signal Processing
Digital processing - arithmetic processing in real-time sequence of values ​​of the amplitude of the signal received at regular intervals.
Examples:
Filtering the signal
Mixing two signals
Computation of the correlation function of two signals
Amplification, restriction or transformation of the signal
Direct / inverse Fourier transform

## Slide 129: Digital Signal Processing (2)
Аnalog input
Аnalog output
Оperation DSP
ADC
DAC

## Slide 130: Multiply and Accumulate
x
A[n-1:0]
B[n-1:0]
+
Multiplier
Adder
Accumulator
MAC – one of the most common operations used in digital signal processing

## Slide 131: MAC in Verilog
module v_multiply_accum_2 (clk, rst, A, B, RES);
input clk;
input rst;
input [7:0] A, B;
output [15:0] RES;
reg [15:0] mult, accum;
reg [7:0] rA, rB;
always @(posedge clk)
begin
if (rst) begin
rA <= 8’b00000000;
rB <= 8’b00000000;
mult <= 16’b0000000000000000;
accum <= 16’b0000000000000000;
end
else begin
rA <= A;
rB <= B;
mult <= rA * rB;
accum <= accum + mult;
end
end
assign RES = accum;
endmodule

## Slide 132: FPGA Configuration Memory
Select
VDD
T1
T2
T3
T4
T5
Data
A
B
Five-transistor cell

## Slide 133: Connection of Configuration Cells
VDD
Data line
VDD
Select line 1
Select line 2

## Slide 134: SRAM-Based FPGA
Configuration Data Input
Configuration Data Output
I/O Pins
SRAM Distributed SRAM Cells

## Slide 135: ASICs and FPGAs
ASIC | FPGA
Designs must be sent for expensive and time consuming in semiconductor foundry | FPGAs can be bought ready-made and reconfigured by designers
Designed al the way from behavioral description to physical layout | No physical layout design. Design ends with a bitstream used to configure a device
Low cost in high volume of device | Low development cost
High performance | Reconfigurability and short time to market

## Slide 136: Configuration Modes
Master-Serial configuration mode
Slave-Serial configuration mode
Master SelectMAP (parallel) configuration mode
Slave SelectMAP (parallel) configuration mode
JTAG/boundary-scan configuration mode
Master Serial Peripheral Interface (SPI) flash configuration mode
Master Byte Peripheral Interface (BPI) flash configuration mode using parallel NOR flash.

## Slide 137: Design Flow
Specifications
HDL
Synthesis
Place&Route
Bit-file
Simulation
FPGA
Simulation

## Slide 138: FPGA Design Flow
Project Creation
Translate Design
Files
Map Design Elements
To Device Resources
Place and Route Design Resources
Perform Timing Analysis
Generate Programming File
Xilinx ISE Design Suite
NGDBUILD
Quartus_map
MAP
PAR
Quartus_fit
Quartus_tan
Quartus_ams
TRCE
BITGEN
Altera Quartus

## Slide 139: FPGA Applications
Construction of reconfigurable systems
Final product in the manufacture of small production lots
Debugging of prototypes in the design (prototyping)
Embedded Systems
Glue Logic (interface between module and components)
Hardware Accelerators/Coprocessors FPGA-based hardware is used for several applications, including computer architecture simulator acceleration, emulation boards, hardware test/verification, among others.