## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Boolean Functions Minimization. Combinational Logic Design Principles

## Slide 4: Synthesis Flow
Specifying the function (usually by means of truth tables and equations
Minimizing Boolean functions. Getting equations
Creating a circuit corresponding to outputs’ equations

## Slide 5: Two-Level Circuit Implementation
z
a
b
c
d
y
a
b
c
d
SOP
Two-level AND-OR circuit
Example: y=ab +cd’
POS
Two-level OR-AND circuit
Example: z =(a+b’)(c+d)

## Slide 6: Definitions
Implicant: Product (cube) that covers only 1-values of the function (hypercube in the Boolean space).
Minterm: Product of all input variables implying a value of the function (usually 1). Vertex in the Boolean space.
Prime implicant (or prime): Implicant not contained by any other implicant.
  Moving away any literal from prime implicant is impossible (obtaine product does not imply a value of the function).
  Quine’s theorem: a minimal sum of product is a sum of prime implicant (the rule of contraries).

## Slide 7: Incompletely Specified Functions
F = (f, d, r) : Bn  {0, 1, *} where * represents “don’t care”.
  f = onset function f(x)=1  F(x)=1
  r = offset function r(x)=1  F(x)=0
  d = don’t care function d(x)=1  F(x)=*
  (f,d,r) forms a partition of Bn. i.e.
  f + d + r = Bn
  fd = fr = dr =  (pairwise disjoint)

## Slide 8: Minimization Stages
Finding all prime implicants
Covering a function with minimum number of implicants.
Goals:
  Reduce the number of implicants
  Reduce the number of literals

## Slide 9: Examples
 | x1x2x3x4 | f
0 | 0 0 0 0 | 0
1 | 0 0 0 1 | -
2 | 0 0 1 0 | 0
3 | 0 0 1 1 | 1
4 | 0 1 0 0 | 0
5 | 0 1 0 1 | 0
6 | 0 1 1 0 | 1
7 | 0 1 1 1 | 0
 | x1x2x3x4 | f
8 | 1 0 0 0 | 0
9 | 1 0 0 1 | 1
10 | 1 0 1 0 | 0
11 | 1 0 1 1 | 1
12 | 1 1 0 0 | 1
13 | 1 1 0 1 | 1
14 | 1 1 1 0 | -
15 | 11 1 1 | -

## Slide 10: Minimization using Karnaugh Map
f(x1x2x3) = P1+ P2+ P3=
= x1x2 + x2x4 + x2x3x4
x1x2
x3x4
00
01
11
10
10
11
01
00
x1
x3
x4
1
1
1
1
1
f
-
-
-
1
P1
P2
P2
P3

## Slide 11: Minimized AND-OR Circuit
x1
x2
x3
x4
x1x2 + x2x4 + x2x3x4

## Slide 12: POS minimization
x1
P2
x1x2
x3x4
00
01
11
10
10
11
01
00
x3
x4
1
1
1
1
f
-
-
-
1
P1
P2
0
0
1
0
0
0
0
0
P2
P2
P2
P3
x2
Define primes for f :
P1=x1x3
P2=x2x4
P3=x1x2x4
f min = x1 x3 + x2x4 +x1x2x4
According to the principle of
duality,
fmin = (x1+x3)(x2+x4)(x1+x2+x4)

## Slide 13: Minimized OR-AND circuit
x1
x2
x3
x4
(x1+x3)(x2+x4)(x1+x2+x4)

## Slide 14: Implementation in NAND basis
x1x2 + x2x4 + x2x3x4
y = x1x2 + x2x4 + x2x3x4= x1x2 + x2x4 + x2x3x4
Applying de Morgan’s law, the following will be obtained:
Y=x1  x2 x2x4  x2 x3 x4
x1
x2
x3
x4

## Slide 15: Implementation in NOR basis
y=(x1+x3)(x2+x4)(x1+x2+x4)= (x1+x3)(x2+x4)(x1+x2+x4)
Applying de Morgan’s law, the following will be obtained:
y = (x1+x3)+(x2+x4)+(x1+x2+x4)
(x1+x3)(x2+x4)(x1+x2+x4)
x1
x2
x3
x4

## Slide 16: Two-Level Logic Minimization Programmed Methods
Exact methods
  Compute minimum cover
  Often difficult/impossible for large functions
  Based on Quine-McCluskey method
Heuristic methods
  Compute minimal covers (possibly minimum)
  Large variety of methods and programs
  MINI, PRESTO, ESPRESSO

## Slide 17: Exact Logic Minimization
Quine’s theorem:
There is a minimum cover that is a cover of prime implicants (the rule of contraries).
Consequence:
  Search for minimum cover can be restricted to prime implicants.
  Quine-McCluskey method:
  Compute prime implicants
  Determine minimum cover
  Find such cover which contains the minimal number of implicants with minimal number of literals.

## Slide 18: Example
Given a function: F(x1x2x3) = (1,2,4,6), d(x1x2x3) = (7).
  Finding all prime implicants
  Arrange the binary representations in a table with different number of 1s in each section (only for 1s and don’t cares).
Class | x1 | x2 | x3 | F | 
 | 0 | 0 | 1 | 1 | 
S1 | 0 | 1 | 0 | 1 | 
 | 1 | 0 | 0 | 1 | 
S2 | 1 | 1 | 0 | 1 | 
S3 | 1 | 1 | 1 | - | 
S1’ | x | 1 | 0 |  | 
 | 1 | x | 0 |  | 
S2’ | 1 | 1 | x |  | 
S0 –zero “1”, S1 – one “1”, S2 – two “1”s, S3 – three “1s”.
Perform matches between entries of nearby sections (S1 with S2, S2 with S3 …)
Two term match if they differ in exactly one position.
New term is formed with a (x) substituted in the position where the two binary values differ. New sections is formed (S1`). And then S1`, is compared with S2`. New implicants do not occur.

## Slide 19: Example (Covering Table)
Selecting minimal set of prime implicants that covers the function.
Covering Table: columns – minterms of F, rows – all prime implicants. Exponential size - up 3n/n implicants
Definition: An essential prime is any prime that uniquely covers a minterm of F.
  Row incident to one (or more) columns with single 1.
 |  | C1 | C2 | C4 | C6
P1 | ~x1~x2x3 | 1 |  |  | 
P2 | x2~x3 |  | 1 |  | 1
P3 | x1~x3 |  |  | 1 | 1
P4 | x1x2 |  |  |  | 1

## Slide 20: Covering Table
Iteratively identify essential implicants, save them in the cover. Remove covered minterms and remove essential implicants.
Column Equality: In practice, many columns are identical, i.e. there exist minterms that are contained in the same set of primes.
Definition: A column j1 whose set of primes is contained in the set of primes of column j2 is said to dominate j2.
Example: j1 j2
0 0
1 1
1 1
0 1
1 1
0 0 j1 dominates j2
Column j2 can be removed, because a prime to cover j1 must be selected, and any such prime also covers j2. So j2 is automatically covered.

## Slide 21: Covering Table (2)
Definition: A row i1 whose columns is a superset of another row i2 is said to dominate i2.
Example:
i1 101001
i2 001001
i1 dominates i2
Row i2 can be removed since i1 covers all those columns and more. i2 in a minimum cover will never be selected since it can always be replaced by i1.
F = P1 + P2 +P3 = ~x1·~x2·x3 + x2·~x3 + x1·~x3

## Slide 22: Covering Problem
Steps:
  Define all essential primes.
  Remove covered minterms (columns) and essential primes (strings).
  Remove all strings and columns whose have dominating strings and columns.
  It result in a covering table of smaller size
  Then define all secondary essential primes.
  If all remaining minterms are covered with essential prime then problem is solved else we have cyclic table.
Computationally intractable problem:
  Exact solution method: branch and bound algorithm
  Several heuristic approximation methods

## Slide 23: Cyclic Core: Petrick’s Method
 | C1 | C2 | C3 | C4 | C5 | C6 | C7
P1 P2 P3 P4 P5 P6 | 1 1 | 1 1 1 | 1 1 | 1 1 1 | 1 1 1 | 1 1 | 1 1 1
Any column Cj can be covered with any prime that has “1” in this column.
C1…C7 – minterms of function . (P1+P3)(P1+P2+P6)(P1+P3)(P2+P3+P5)(P4+P5+P6)(P1+P4)(P4+P5+P6) = P1P5 + P1P2P4 + P1P2P6 + P2P3P4 + P3P4P6 + P1P3P4 + P1P3P6
Minimal cover – {P1,P5}

## Slide 24: Multiple Outputs Functions
1
x
y z
00
01
11
10
0
1
1
1
y z
x
10
11
01
00
1
0
1
1 1
f : Bn → Bm In practice most of combinational circuits have multiple outputs.
Example 1:
Consider the following functions:
F = x,y,z (3,6,7)
G = x,y,z (0,1,3)
F = x·y + y·z; G = x'·y‘ + x'·z;

## Slide 25: Multiple Outputs Functions (2)
F = x·y +y·z
z
x
y
G =x·y +x·z
F = x·y + y·z

## Slide 26: Multiple Outputs Functions (2) Contd.
1
1
x
y z
y z
x
00
01
1
10
10
11
01
00
0
1
0
1
1
1
1
1
Common term is x·y·z; F = x·y + x·y·z; G = x·y + x·y·z;
This circuit is simpler than previous one.
z
x
y
F = x·y +x·y·z
G = x·y+x·y·z

## Slide 27: Multi-Level Logic Optimization
a
b
c
d
y
y
a
b
d
c
Example:
y = аc + bc + ad +bd or y = (a+b)(c+d)

## Slide 28: Multi-Level Logic Optimization (2)
Consider two important design criteria: delay and size.
Delay - the time from inputs changing to new correct stable output
Size - the number of transistors.
Assume:
  Every gate has delay of “1 gate-delay”
  Every gate input requires 2 transistors
  Ignore inverters
Then both circuits have equal delays – 2 gates.
The number of transistors: 24 (circuit 1) and 12 (circuit 2).
Multiple levels may yield fewer gates.

## Slide 29: Multi-Level Logic Optimization (3)
There are many functions which represent factored form simpler than two-level form.
The number of terms in SOP or POS can depend on n exponential, but in factored form - polynomial.
Example: Achilles’ heel function:
  Y=(x1+x2)(x3+x4) . . . (xn-1+xn)
There are n literals in the factored form and (n/2)2n/2) literals in the SOP form.
2-level optimization: control logic design;
multi-level optimization: all logic, datapath logic or random logic.

## Slide 30: Factored Forms
A factored form can be defined recursively by the following rules. A factored form is either a product or sum where:
  A product is either a single literal or product of factored forms
  A sum is either a single literal or sum of factored forms.
Actually a factored form is a product of sums of products or a sum of products of sums.
Any logic function can be represented by a factored form, and any factored form is a representation of some logic function. The factored forms are not canonical:
Example:
  Three equivalent factored forms:
  ab+c(a+b) bc+a(b+c) ac+b(a+c)

## Slide 31: Multilevel Combinational Circuits
Given two simple functions expressed in 2-Level:
f1= ab + ac + ad
f2= a’b + a’c + ae
6 product terms which cannot be shared.
36 transistors in CMOS may be more efficient in multi-level:
f1= a(b+c) +ad; f2=a’(b+c) + ae
b + c is a common term in f1 and f2
K = b + c
24 transistors in CMOS not counting inverters:
f1 = aK + ad
f2 = a’K+ a e
3 levels.

## Slide 32: Threshold Logic

x1
x2
xn-1
xn
y
w1
w2
wn-1
wn
The formal model of the neuron can be presented as follows:
(McCulloch, Pitts - neuron, 1943)
if  wixi   y=1, else y=0;
  where wi is the weight of xi input,  - threshold value.
When the threshold and weight values change, logical functions of the neuron change, too.

## Slide 33: Example
x1x2x3 | y | 2*x1 + 2*x2 +2*x3
0 0 0 | 0 | 0 < 3
0 0 1 | 0 | 2 < 3
0 1 0 | 0 | 2 < 3
0 1 1 | 1 | 4 > 3
1 0 0 | 0 | 2 < 3
1 0 1 | 1 | 4 > 3
1 1 0 | 1 | 4 > 3
1 1 1 | 1 | 6 > 3
Define Boolean function which is implemented with the help of the threshold element with three inputs.
=3, w1=w2=w3 =2; y=1, if 2*x1 + 2*x2 +2*x3  3
Truth table of the function

## Slide 34: Two-inputs Neuron

x1
x2
y
w1
w2
Σ= w1*x1 + w2*x2;
Let w1 = w2 =1;
Then  = x1 + x2.
If  = 1, then y = x1x2.
Inverse problem:
Determine weight values and threshold for the given neuron, so that this neuron executes the given Boolean function (e.g. AND). The system of four inequalities must be solved.

## Slide 35: Example (1)
00 |  = w1*x1+w2*x2 = 0 <  (since 0&0=0)
01 |  = w1*x1+w2*x2 = w2 <  (since 0&1=0)
10 |  = w1*x1+w2*x2 = w1 <  (since 1&0=0)
11 |  = w1*x1+w2*x2 = w1+w2   (since 1&1=1)
Task solution:  =2, w1=w2=1

## Slide 36: Example (2)
00 | 0< (since 0  0 = 0)
01 | w2 (since 0  1= 1)
10 | w1 (since 1  0= 1)
11 | w1+w2< (since 1  1 = 0)
There is no existing element in the threshold logic with two inputs that executes XOR function.
 > w1 + w2  2. It is contradiction.

## Slide 37: Perceptron
inputs
Perceptron is a single layer neural network and a multi-layer perceptron is called Neural Networks.
1
x1
Xn-1
xn

w0
w1
wn-2
wn-1
y
output
if (xi) y=y+wi; else y=y-wi
F. Rosenblatt, 1958

## Slide 38: Multi-Layer Neural Network

## Slide 39: Majority Functions
An n-input majority function takes the value "1" if the most of its inputs are "1". If n - an even number, a value equal to "1" need to have n/2 +1 inputs.
The majority element often has odd number of inputs (usually 3 or 5)

## Slide 40: 3-input Majority Element
x2x3
F
x1
00
01
11
10
0
1
1
1
1
1
x2x3
x1
00
01
11
10
0
1
1
1
1
1
a0
x1
x2x3
00
01
11
10
0
1
1
1
1
1
a1
x1x2x3 | F | a1a0
0 0 0 | 0 | 0 0
0 0 1 | 0 | 1 1
0 1 0 | 0 | 1 0
0 1 1 | 1 | 0 1
1 0 0 | 0 | 0 1
1 0 1 | 1 | 1 0
1 1 0 | 1 | 1 1
1 1 1 | 1 | 0 0
F = x1·x2 + x1·x3 +x2·x3
a0 = ~x1·x3 + x1·~x3 = x1 x3
a1 = ~x2·x3 + x2·x3 = x2  x3

## Slide 41: Combinational Circuits Description in Verilog
x1
x2
x3
y
g
f
k
module comb_logic1 (x1,x2,x3,y);
input x1, x2, x3 ;
output y;
//internal wire declaration
wire k,g,f ;
not (k, x2);
and (g, x1, k);
and (f, x2,x3);
or (y,g,f);
endmodule
module comb_logic2 (x1,x2,x3,y);
input x1, x2, x3 ;
output y;
assign y = (x1&~x2)|(x2&x3)
endmodule

## Slide 42: Behavioral Description
Sensitivity List
module comb_logic3 (x1,x2,x3,y);
input x1, x2, x3 ;
output y;
reg y;
always @(x1 or x2 or x3)
if (x2==0)
y=x1;
else
y=x3; endmodule

## Slide 43: ROBDD
Given Boolean function Y= ab + acd
Construction of ROBDD
Define the Shannon’s cofactors
Y|a=0 = cd; Y|a=1 =b;
Y|a=0,b=0 =cd; Y|a=0,b=1 =cd;
Y|a=1,b=0 =0; Y|a=1,b=1 =1;
cd|c=0 =0; cd|c=1 =d;
a
b
c
d
cd
0
1
b
d

## Slide 44: Apply Operator
f|x=b - substitution of b for x
f - changing the values ​​of the terminal nodes {0,1} to {1,0}.
f g, where  stands for any Boolean operator (AND, OR, XOR, )
    fg = x (fx gx) + x’(fx’ gx’)

=
f
g
f  g

## Slide 45: Application of the Operator  (Apply Operator)
v1
v2

p0
p1
q0
q1
=
v1
p0
p1

v2
q0
q1

v2
q0
q1
Index v1< index v2

## Slide 46: Apply Operator
v1
v2

p0
p1
q0
q1
=
v2
q0
q1

v1
p0
p1

v1
p0
p1
Index v1 > index v2

## Slide 47: Apply Operator
v1
v2

p0
p1
q0
q1
=
v2
q0
q1

p0

p1
Index v1= index v2

## Slide 48: Representation of Logic Circuit in the Form of BDD
a
c
z
x
y
b
b
0
c
1
y=bc
a
0
c
1
x=ac
+
=
a2
a1
7
a
b+0
0
c
1
b
c
c
a
b
0
c
1
z
a3
a4
b1
b2
b3
b4
a1,b1
a3,b1
a3,b3
a3,b2
a2,b1
a2,b3
a2,b2

## Slide 49: ROBDD Construction
a
b
z
x
y
d
c
b4
a3
a4
b3
a4,b4
a4,b3
a4,b4
a
0
1
b
a+b
c
0
1
d
c+d
a
b1
b2
b
a1,b1
0
a4,b2
a3,b1
c
a4,b1
d
a1
a2
0
a4,b3
1
c
a4,b1
a4,b2
d
0
1
=
&
Order abc d

## Slide 50: ROBDD Construction
a
b
0
c
d
0
1
c
d
0
1
After reduction
New Created Graph
a
b
c
d
0
1
=

## Slide 51: The Transition from Circuit to ROBDD
a
b
c
Y
d
y2
y1
y4
y3
BDD is constructed for all intermediate functions y1, y2, y3, y4 scheme using operator Apply. Obtain BDD, matching function Y.
Need to check whether a given circuit implements the function Y= ab + acd

## Slide 52: BDD for y1, y2, y3
a
1
0
y1=a
a
0
1
b
y2=ab
y3=y1c
a
0
1
c

## Slide 53: BDD for y4, Y
y4=y3d
a
c
0
1
d
+
=
a
0
1
b
y2=ab
High v1
Low v1
v1
v2
Low v2
High v2
a
0
1
d
b
Y=y2+ y4
c
If ROBDD function realized by the combinational scheme and given function match, the scheme corresponds its specification

## Slide 54: Timing. Propagation and Contamination Delay
a
y
a
y
tcd
tpd
The propagation delay tpd is the maximum time from when an input changes until the output or outputs reach their final value.
The contamination delay tcd is the minimum time from when an input changes until any output starts to change its value.
Causes of delays
time required to charge the capacitance in a circuit
Different rising and falling delays
Multiple inputs and outputs, some of which are faster than others
Circuits slowing down when hot and speeding up when cold.

## Slide 55: Critical Path
a=10
b=0
c=0
d=0
Y=10
n1
n2
Critical path
a
n1
n2
y
tpd
y= a  b  c  d
Critical path - 3 tpd_XOR
tpd = 3 tpd_XOR ; tcd= tpd_XOR

## Slide 56: Short Path
a=1
b=0
c=0
d=0
Y=10
n1
n2
d
y
tcd
Short path
y= a  b  c  d
Short path – tpd_XOR
d=01