## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Introduction to Verilog

## Slide 4: Program Structure
Module – the basis unit of design
Declarations describe the name and types of the module’s inputs and outputs, as well as local signals, variables, constant and functions that are used internally to the module and are not visible outside.
declarations
statements

## Slide 5: Module
A module is the basic building block in Verilog
Can be an element or a collection of lower-level design blocks
Provides necessary functionality to the higher level block through its port interface (I/Os)
Hides the internal implementation

## Slide 6: Hierarchy Structure of Modules
module A
module B module D
module G module E
Declarations
Statements
  
Declarations
Statements
  
Statements
  
Declarations
Statements
  
Declarations
Statements
  
Declarations
Statements
  
Declarations
module C

## Slide 7: Syntax of Module Declaration
module module_name (port_name, port_name, …port_name);
input declarations;
output declarations;
inout declarations;
net declarations;
variable declarations;
parameter declarations;
function declarations;
task declarations
concurrent statements
endmodule
Keywords are labeled in blue color.

## Slide 8: Input/Output Declaration
module module_name (port_name1, port_name1, …port_name k);
input port_name1; // 1-bit signal is input of module
output port_name2; // 1-bit signal is output
inout port_name k; // 1-bit signal can be used as module // input or output
input [n-1:0] port_name; //n-bit input signal
output [n:1] port_name; // n-bit output signal
inout [m:2] port_name; //(m-2-bit) signal
Ports provide the interface by which a module can communicate with its environment
Types: input  input port; output  output port;
inout  bidirectional port.

## Slide 9: Data Types. Nets
Basic type: signals
Default value x(z?). Default size: 1 bit
Alphabet  4-valued: {0,1,x,z}.
x - unknown logic value; z – high impedance
Verilog has two classes of signals:
  Nets
  Registers
Net corresponds to a wire in circuit, provides connectivity between modules.
Net types: wire, tri, triand, trior, tri0, tri1, supply0, supply1.
supply0 and supply1 are considered to be permanently wired to the power-supply (source “constant-0” or “constant-1”).
Net does not store its state.
input and inout ports are normally declared as wires (“wire”).

## Slide 10: Registers
Registers (keyword – reg) store values during a Verilog program execution. Retain value until another value is placed onto them.
They are used only in “procedural code”.
A value of reg must be assigned obviously.
Integer variable (keyword integer) is typically used to control repetitive statement. Its value is 32 bit or large integer (depending on word length used by simulator).
  wire identifier,…identifier;
  wire [msb:lsb] identifier, identifier;
  reg identifier,… identifier;
  reg [msb:lsb] identifier, identifier;
  integer identifier,… identifier;

## Slide 11: Examples
reg a; // scalar reg variable
wire w1, w2; // two 1-bit nets declaration
reg [3:0] v; // 4-bit register including v[3], v[2], v[1], v[0]
tri [15:0] busc; //16-bit three state bus с
reg signed [0:3] b; // b register; its content is mentioned as integer // number in the range of [-8
Arrays
reg data [7:0] ; // 8 1-bit elements
reg [3:0] out[31:0]; // 32 4-bit element
Memories
Memories are simply an array of registers
reg [15:0] mem16_1024 [1023:0]; // memory mem16_1024 is //1K of 16 bit elements
mem16_1024[300]; // referencing element 300 of mem16_1024

## Slide 12: Memories
Verilog allows arrays of reg and wire to be defined as in the
following two examples:
reg [3:0] mem_array [31:0];
The above describes an array of 32 elements each, 4 bits wide which
can be assigned via behavioral verilog code.
wire [7:0] mem_array [63:0];
The above describes an array of 64 elements each 8 bits wide which
can only be assigned via structural Verilog code.

## Slide 13: Multi-Dimensional Arrays
Multi-dimensional arrays can be wire or reg data type.
  You can do assignments and arithmetic operations with arrays
  You cannot select more than one element of an array at one time.
  You cannot pass multi-dimensional arrays to system tasks or functions, or regular tasks or functions.
Examples of a declaration:
wire [7:0] array2 [0:255][0:15];
  This statement describes an array of 256 x 16 wire elements each 8 bits
  wide, which can only be assigned via structural Verilog code.
reg [63:0] regarray2 [255:0][7:0];
  This statement describes an array of 256 x 8 register elements, each 64 bits wide, which can be assigned via behavioral verilog code.

## Slide 14: Numbers
Numbers are specified by <size>'<base><number> : for a full description
<base> - binary (b), decimal (d), hexadecimal (h), octal(o)
x represents an unknown, and z a high impedance value.
An x declares 4 unknown bits in hexadecimal, 3 in octal and 1 in binary. z declares high impedance values similarly.
Alternatively z, when used in numbers, can be written as ? This is advised in case expressions to enhance readability.
5’d3 16’h4xa 6’oz5 -8’d7 | Equal 5’b00011 Equal 16’b0000 0100 xxxx 1010 Equal 6’bzzz101 2’s complement of 7, held in 8 bits

## Slide 15: Examples
0 // number 0
1 // number 1
10 // decimal number 10
'b10 //binary number 10=210
4'b100 //binary number 0100
4'bx // xxxx
8'hfx //1111xxxx
16'h8xc //0000 1000 xxxx 1100
5'd3 //00011
-8’d3 //1111 1101 (two’s complement -3)

## Slide 16: Numbers
Real numbers can be in either decimal or scientific format:
  Decimal numbers
Value_i.value_f
  5.7; 72348.06543;
  3.e4=3104
  5.7e-9 = 5.710-9= 0,0000000057;
  4.5 E8 = 4.5 108 =45000000000;
Strings
  Strings are delimited by " ... ", and cannot be on multiple lines.
  "hello world"; // legal string
White space
  The white space characters are space (\b), tabs (\t), newlines (\n). These are ignored except in strings.
Comments: Two types of comments are supported, single line comments starting with // and multiple line comments delimited by /* ... */. Comments cannot be nested.

## Slide 17: Time in Verilog
Time is specific integer information carrier.
Time keeping is stored in special register and its value can be assigned to variable of type time with the help of system function $time.
Example:
  time current_time_mark, next_event_time; //declaration time variables
  current_time_mark = $time; //assignment the variable current time
  next_event_time=current_time_mark+5; //computation time of future event
  Time - dimensionless quantity
  Time scale is defined using `timescale compiler directive
  `timescale 1ns/10ps

## Slide 18: Data Types in SystemVerilog
SystemVerilog introduces the logic type (synonym a reg ).
Advantages:
Logic avoids misleading users about whether it is actually a flip-flop.
SystemVerilog relaxes the rules on assign statements and hierarchical port instantiations so logic can be used outside always blocks where a wire traditionally would have been required.
Nearly all SystemVerilog signals can be logic.
  Integer data types. SystemVerilog provides new data types:
  bit
  byte (8 bit)
  shortint (16 bit)
  int (32 bit)
  longint (64bit)

## Slide 19: Verilog and SystemVerilog
Type of signal | Verilog | Type of signal | SystemVerilog
wire {0,1,x,z} | left hand side of = in assign statement. One driver | logic, one driver | nearly all SystemVerilog signals
reg | left hand side of <= or = in an always block | Logic, one driver | Synonym a reg
tri | wire | tri | Multiple drivers
 |  | bit {0,1}, byte | 
Signals with multiple drivers (e.g.,a tristate bus) must be declared as a net.

## Slide 20: Table of Operations
Operations | Symbols |  | Real?
Concatenation | { , , …, } | Concatenate different operands into a single operand | No
Replication | {n{ , , …, }} | Repeat an operand in several times | 
Arithmetic operators | +,- +, -, *, / % | Unary, Binary, module of number | Yes Yes No
Shift operators | >>, << | Shift right, shift left | No
Relational operators | >, >=, , <= |  | Yes
Equality | = =, ! = = = =, ! = = | Equal – not equal bits x and z are involved in the operation | Yes

## Slide 21: Examples
reg A; reg[1:0] B,C; reg[2:0] D;
A=1’b1; B=2’b00; C=2’b10; D=3’b110;
Y={B,C}; //Y=4’b0010
Y={4{A}}; //Y=4’b1111
Y={4{A}, 2{B}, C,2{D}}; // Y=16’b11110000_10110110

## Slide 22: Table of Operations
Reduction operators | &, ~& ¦, ~¦ ^ ^~ or ~^ | AND , NAND OR ,NOR XOR XNOR | No
bitwise operators | ~ &, ~& ¦, ~¦ ^ ^~ or ~^ | Not AND, NAND OR, NOR XOR XNOR | No
Logic operators | ! && ¦ ¦ | Not AND OR | Yes
Ternary operator (conditional) | ? | r = s ? t:u; //r=(if s is true, then t else u) c=(a>b)? 3’b100:3’b111; | Use in C, Java

## Slide 23: Example (Verilog 2005)
module gates (input [3:0] a,b, output wire [3:0] y1,y2,y3,y4,y5,y6);
  /* Six two-input logic gates acting on 4 bit busses*/
assign y1=a&b; //AND
assign y2=a|b; //OR
assign y3=a^b; //XOR
assign y4=~(a&b); //NAND
assign y5=~(a|b); //NOR
assign y6=a^~b; //XNOR
endmodule

## Slide 24: System Verilog: Module Gates
module gates( input logic [3:0] a, b,
output logic [3:0] y1, y2, y3, y4, y5,y6);
  /*six different two-input logic gates acting on 4-bit busses */
assign y1 = a & b; // AND
assign y2 = a |b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a |b); // NOR
assign y6=a^~b; //XNOR
endmodule
Verilog, SystemVerilog are case-sensitive. y1 and Y1 are different signals. VHDL is not case-sensitive.

## Slide 25: Parameter Declaration
parameter identifier=value; parameter identifier =value, identifier=value, identifier=value;
Verilog provides a facility for defining named constants within a module (to improve readability).
parameter wide = 32;
wire [wide-1:0] bus;
parameter ESC=7’b0011011;

## Slide 26: Procedures and Assignments
There are two types of assignment in Verilog:
Continuous (parallel) and procedural (sequential).
Procedural statements are used within an always or initial blocks.
Procedure executes concurrently with other procedures.
Continuous assignments appear outside procedure.
Procedural assignments appear inside procedure.
Sequential block is a group of statements between a begin and end.
Continuous assignment statements allow Verilog to describe a combinational circuit in terms of the flow of data and operations on the circuit: dataflow description.

## Slide 27: Continuous Assignment
Continuous assignment statement are used to assign a wire like a real logic gate drives a real wire. Continuous assignment is executed at any changing of signal on the right-hand side .
Continuous assignment statements describe combinational logic.
assign {c0, sum} = a + b;
Left-hand side = right-hand side
nets (wire)
nets (wire)
variable (reg)
numbers
function call

## Slide 28: Continuous Assignment
Examples:
Explicit continuous assignment
  wire [2:0] w;
  assign w=a&b; Implicit continuous assignment
  wire w1=~a[1];
assign net_name=expression;
assign net_name[index] =expression;
assign net_name[msb:lsb] =expression;
assign net_concatenation =expression;

## Slide 29: Example 1
Verilog 95
module full_adder (cin, a,b, s,cout);
input cin, a,b;
output s,cout;
assign s=a^b^cin;
assign cout=(a&b)|(a&cin)|(b&cin);
endmodule
Verilog 2001
module full_adder ( input cin, a,b,
output s,cout);
assign s=a^b^cin;
assign cout=(a&b)|(a&cin)|(b&cin);
endmodule

## Slide 30: Example 2
module adder_n(a,b,s1,s2);
parameter n=4;
input [n-1:0] a,b;
output [2*n-1:0] s1,s2;
assign s1=a+b,
s2={n{a[n-1]},a}+{n{b[n-1]},b};
endmodule
In this example, formed by two sums: s1 and s2.
s1: Verilog compiler adds two numbers with a sign, extending them to the four high bits with zeros.
s2: Verilog compiler expands each term of up to eight bits of the sign bits.
Let a = 1011, b= 0 110;
s1=00010001; s2=00000001;

## Slide 31: Delays
Continuous Assignment
Regular Assignment Delay
  assign #10 out = in1 & in2;
  Inertial delay: an input pulse that is shorter than the delay of the assignment statement does not propagate to the output.
  Implicit Continuous Assignment Delay
  wire #10 out = in1 & in2;
  Net Declaration Delay
  wire # 10 out;
  assign out = in1 & in2;
  The above two statements have the same effect as the following.
  wire out;
  assign #10 out = in1 & in2;

## Slide 32: Gate Instantiation
wire OUT, IN1, IN2; // basic gate instantiations.
and a1(OUT, IN1, IN2);
nand na1(OUT, IN1, IN2);
or or1(OUT, IN1, IN2);
nor nor1(OUT, IN1, IN2);
xor x1(OUT, IN1, IN2);
xnor nx1(OUT, IN1, IN2); // More than two inputs; 3 input nand gate
nand na1_3inp(OUT, IN1, IN2, IN3); // gate instantiation without instance name
and (OUT, IN1, IN2); // legal gate instantiation

## Slide 33: Verilog Gates Table
Name | Expression | Verilog gate instantiation
and | y =(ab . . .) | and (y,a,b, . . .)
nand | y =(ab . . .) | nand (y,a,b, . . .)
or | y =(a+b+ . . .) | or (y,a,b, . . .)
nor | y =(a+b+ . . .) | nor (y,a,b, . . .)
xor | y =(ab . . .) | xor (y,a,b, . . .)
xnor | y =(1ab . . .) | xnor (y,a,b, . . .)
not | y =~a | not (y,a)
buf | y=a | buf (y,a)
notif0 | y= (!e?~a:’bz) | notif0 (y,a,e)
notif1 | y= (e?~a:’bz) | notif1 (y,a,e)
bufif0 | y= (!e?a:’bz) | bufif0 (y,a,e)
bufif1 | y= (e?a:’bz) | bufif1 (y,a,e)

## Slide 34: Truth Tables for Gates
AND NAND
in1
in2
0
1
x
z
0
1
x
z
0
0
0
0
0
1
x
x
0
x
x
x
x
x
x
0
in1
in2
0
1
x
z
0
1
x
z
1
1
1
1
1
0
x
x
1
x
x
x
x
x
x
1

## Slide 35: Truth Tables for Gates (2)
OR NOR
in1
in2
0
1
x
z
0
1
x
z
0
1
x
x
1
1
1
1
x
1
x
x
1
x
x
x
in1
in2
0
1
x
z
0
1
x
z
1
0
x
x
0
0
0
0
x
0
x
x
0
x
x
x

## Slide 36: Truth Tables for Gates (3)
XOR XNOR
in1
in2
0
1
x
z
0
1
x
z
0
1
x
x
1
0
x
x
x
x
x
x
x
x
x
x
in1
in2
0
1
x
z
0
1
x
z
1
0
x
x
0
1
x
x
x
x
x
x
x
x
x
x

## Slide 37: Gate Level Description of Logic Circuits
Verilog includes a set of gate level primitives.
  These primitives are instantiated like modules except that they are predefined in Verilog and do not need a module definition.
Examples:
  Two-input AND gate with inputs x1 and x2 and output y: and (y,x1,x2)
  Four-input OR gate: or (y,x1,x2,x3,x4)
  And/or gates have one scalar output and multiple scalar inputs
The NOT gate: not (y,x)
  The keywords NAND and NOR are used to define NAND and NOR gates
  The keywords XOR and XNOR are used to define XOR and XNOR gates
  The keywords BUF buf (out,in)
in
out

## Slide 38: Example
module example(a,b,c,d,y);
input a,b,c,d;
output y;
wire v,w,z;
and (v,a,b);
not (z,d);
and (w,c,z);
or (y,v,w);
endmodule
a
b
c
d
y
v
w
z

## Slide 39: Behavioral Description of Logic Circuits
module example(a,b,c,d,y);
input a,b,c,d;
output reg y;
always @(a,b,c,d) // sensitivity list
if (a==1)&&(b==1) y=1;
else if (d==0) y=c;
else y=0;
endmodule
Instead of listing the relevant signals in the sensitivity list, it is possible to write simply
always @(*) or always @*
For example we can write
module example (input a,b,c,d, output reg y);

## Slide 40: Procedural Assignment (Verilog)
Always block:
Starting with Verilog 2001 – instead “or” can be used “,”.
Sensitivity_list – a list of signals that directly affects the output results generated by the always block.
always @(sensitivity_list)
[begin]
[procedural assignment statement]
[if-else statement]
[case statement]
[while, repeat, and for loops]
[task and function calls]
[end]

## Slide 41: Always Block
Always block resumes execution starting with its first procedural statement and continuing until the end.
Example:
аlways a = ~a; will execute forever with zero delay
always #delay a = ~a; It is pulse generator with clock period 2*delay.
Any signal assigned a value in procedural block has to be a variable type reg or integer.

## Slide 42: Example
module clock_gen (clock);
output clock;
reg clock;
//Initialize clock at time zero
initial clock = 1'b0;
//Toggle clock every half-cycle (time period = 20)
always #10 clock = ~clock;
Initial
#1000 $finish;
endmodule

## Slide 43: Example (2)
// A level-sensitive latch with asynchronous reset
always @( reset or clock or d) // wait for reset or clock or d to change
begin if (reset) // if reset signal is high, set q to 0.
q = 1'b0;
else if (clock) // if clock is high, latch input
q = d;
end
Verilog 2001 (v2k): always @( reset,clock,d)

## Slide 44: Example (3)
A positive edge triggered D flip-flop with asynchronous falling reset:
always @(posedge clk or negedge reset)
if (!reset) q <=0;
else q <=d;
end
posedge, negedge are events
When the number of input variables to a combination logic block is very large, sensitivity lists can become very lengthy. To avoid that Verilog HDL contains two special symbols: @* and @(*).

## Slide 45: Always Statements in System Verilog
In Verilog always statements can be used to imply flip-flops, latches, or combinational logic, depending on the sensitivity list and statement.
Because of this flexibility, it is easy to produce the wrong hardware inadvertently.
SystemVerilog introduces always_ff, always_latch, and always_comb to reduce the risk of common errors.
always_ff behaves like always but is used exclusively to imply
flip-flops and allows tools to produce a warning if anything else
is implied.

## Slide 46: always_ff
module sync(input logic clk,
input logic d,
output logic q);
logic synch;
always_ff @(posedge clk)
begin
synch <= d; // nonblocking
q <= synch; // nonblocking
end
endmodule
clock
D
Q
A
D
Q
B
synch
q
d

## Slide 47: always_latch (D-Latch)
always_latch is equivalent to always @(clk, d) and is the preferred idiom for describing a latch in SystemVerilog.
SystemVerilog
module latch(input logic clk,
  input logic [3:0] d,
  output logic [3:0] q);
  always_latch
  if (clk) q <= d;
  endmodule

## Slide 48: always_comb (Full Adder)
always_comb reevaluates the statements inside the always
statement any time any of the signals on the right hand side
of <= or = in the always statement change.
If the code inside the always block is not combinational logic,
SystemVerilog will report a warning.
always_comb is equivalent to always @(*), but is preferred in SystemVerilog.
module fulladder(input logic a, b, cin, output logic s, cout);
logic p, g;
always_comb
begin
p = a ^ b; // blocking
g = a & b; // blocking
s = p ^ cin; // blocking
cout = g |(p & cin); // blocking
end
endmodule

## Slide 49: Initial Statement
Initial statement is used either to set the initial states in the simulated device, or by writing simulation programs. It executes only once at the beginning of a simulation. If there is more than one block, they execute concurrently.
Example:
initial c = 1’b1; initial begin a = 3‘b000; #100 a=3’b110; #100 a=3’b111; #100 a=3’b110; end initial begin $monitor ($time, , “a=%b”, b=%b”, a, b); #1000 $finish; end endmodule

## Slide 50: Seven-Segment Display Decoder
A seven-segment display decoder takes a 4-bit data input x[3:0] and produces seven outputs to control light-emitting diodes to display a digit from 0 to 9 and letters a,b,c,d,e,f.
Seven-segment display decoder
d
a
b
c
e
g
f
dp
b
c
d
e
f
g
dp
a
LED
R
x[0]
x[1]
x[2]
x[3]
y[0]
y[1]
y[2]
y[3]
y[4]
y [5]
y [6]
y [7]
dp

## Slide 51: Seven-Segment Display Digits and Letters
a
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
a
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
b
c
d
e
g
f
a
a
a
a
a
a
a
a
a
a
a
a
a
a

## Slide 52: Table of Implementing Functions
Symbol | X x1 x2 x3 x4 | Y a b c d e f g
0 | 0 0 0 0 | 1 1 1 1 1 1 0
1 | 0 0 0 1 | 0 1 1 0 0 0 0
2 | 0 0 1 0 | 1 1 0 1 1 0 1
3 | 0 0 1 1 | 1 1 1 1 0 0 1
4 | 0 1 0 0 | 0 1 1 0 0 1 1
5 | 0 1 0 1 | 1 0 1 1 0 1 1
6 | 0 1 1 0 | 1 0 1 1 1 1 1
7 | 0 1 1 1 | 1 1 1 0 0 0 0
8 | 1 0 0 0 | 1 1 1 1 1 1 1
9 | 1 0 0 1 | 1 1 1 1 0 1 1
A | 1 0 1 0 | 1 1 1 1 1 0 1
B | 1 0 1 1 | 1 1 1 1 1 1 0
C | 1 0 1 1 | 1 0 0 1 1 1 0
D | 1 0 1 1 | 0 1 1 1 1 0 1
E | 1 0 1 1 | 0 1 0 0 1 1 1 1
F | 1 0 1 1 | 0 1 0 0 0 1 1 1

## Slide 53: Verilog Description
module hex_to_sevenseg(
input wire [3:0] x,
input wire dp,
output reg [7:0] y);
always @*
begin
case (x)
4’h0: y=7’b 1111110;
4’h1: y=7’b 0110000;
4’h2: y=7’b 1101101;
4’h3: y=7’b 1111001;
4’h4: y=7’b 0110011;
4’h5: y=7’b 1011011;
4’h6: y=7’b 1011111;
4’h7: y=7’b 1110000;
4’h8: y=7’b 1111111;
4’h9: y=7’b 1111011
4’ha: y=7’b 1110111;
4’hb: y=7’b 0011111;
4’hc: y=7’b 1001110;
4’hd: y=7’b 0111101;
4’he: y=7’b 1001111;
default: y=7’b1000111;
endcase
y[7]=dp;
end
endmodule

## Slide 54: Test-Bench
module test_bench;
reg [3:0] x,
reg dp,
wire [7:0] y);
integer k;
hex_to_sevenseg my_7_seg (x,dp,y);
initial begin
dp=0;
for (k=0; k<5; k=k+1)
x= #5 k;
#5 dp=1;
for (k=5; k<10; k=k+1)
x= #5 k;
#5 dp=0;
for (k=10; k<16; k=k+1)
x= #5 k;
end endmodule

## Slide 55: Blocking and Nonblocking Assignment
Blocking assignment statements are executed in the order they are specified in a sequential block.
The “=“ operator is used to specify blocking assignments.
This assignment will not block execution of statements that follow in a parallel block.
Nonblocking assignments allow scheduling assignments without blocking execution of statements that follow in a sequential block.
The <= operator is used to specify nonblocking assignments.

## Slide 56: Blocking Assignment
Executed at time=0
Executed at time=20
Executed at time=35
reg a, b, c,d;
reg [15:0] reg_1, reg_2;
integer count;
initial begin
a = 0; b = 1; c = 1; d=0;
count = 0;
reg_1 = 16'b0;
reg_2 = reg_1;
#20 reg_1[2] = 1'b1;
#15 reg_2[15:12] = {a, b, c,d}
count = count + 1;
end

## Slide 57: Nonblocking Assignment
If blocking assignments are not properly ordered, a race condition can occur:
When the RHS (right hand side) variable of one assignment in one procedural block is also the LHS (left hand side) variable of another assignment in another procedural block and both equations are scheduled to execute in the same simulation time step (e.g. the same clock edge).
Nonblocking assignment is not permitted in continuous assignment.

## Slide 58: Example
It is necessary to form input sequence for signal d
// blocking assignment
initial
begin
d = 1’b0;
#5 d=1’b1;
#15 d=1’b0;
#20 d=1’b1;
#35 d=1’b0;
end
0
5
20
40
75
d

## Slide 59: Example (2)
//nonblocking assignment
initial
begin
d <= 1’b0;
#5 d<=1’b1;
#15 d<=1’b0;
#20 d<=1’b1;
#35 d<=1’b0;
end
30
0
5
10
30
35
d
15
20

## Slide 60: Example (Blocking and Nonblocking Assignment)
always @(posedge clock)
begin
A=C;
B=A;
end
always @(posedge clock)
begin
B=A;
A=C;
end
always @(posedge clock)
begin B<=A; A<=C;
end
begin
B<=A; A<=C; end
clock
D
Q
A
D
Q
B
A
B
C
C
A
B
D
Q
A
clock
D
Q
B
After optimization one flip-flop may stay.

## Slide 61: Rules (for Verilog)
Always use blocking assignment in “always block” intended to create combinational logic
Always use nonblocking assignment in “always block” intended to create sequential logic
Do not mix blocking and nonblocking assignment in the same “always block”
Do not make assignments to the same variables in two different “always blocks”.

## Slide 62: Concept of Block
Sequential Block
Named Sequential Block
begin procedural statement; … procedural statement; end
begin: block_name variable declaration; parameter declaration; procedural statement; … procedural statement; end

## Slide 63: Parallel Block
always @(posedge a)
begin
fork
#20 b=0;// at time= 30,at time=120
#10 b=a;// at time=20, at time=110
#30 b=1’bz;// at time=40, at time=130
join
#5 b=1’bz;//at time=45,at time=135
end
endmodule
Parallel block is enclosed
between keyword fork and join.
The order of operators does not
matter (operators are executed in parallel).
Example:
initial
begin a=0; //executed at time=0
#10 a=1;// executed at time=10
#20 a=0;//executed at time=30
#70 a=1;//executed at time=100
#20 a=0;//executed at time=120
end

## Slide 64: If Statement
Keyword: if-else
if (expression) if(expression!=0)
if (<expression) true_statement;
if (<expression) true_statement;
else false statement;
if (<expression1>) true_statement1;
else if (<expression2>) true_statement2;
else if (<expression3>) true_statement3;

## Slide 65: If-else Statement, if Statement
module mux2_1(in0, in1,s, y);
input in0,in1,s;
output y;
reg y;
always @(in0,in1,s,)
if (s==1) y=in1;
else y = in0;
endmodule
Both descriptions correspond to 2:1 multiplexer.
module mux2_1(in0, in1,s, y);
input in0,in1,s;
output y;
reg y;
always @(in0,in1,s,)
begin
y=in0;
if (s==1 ) y=in1;
end
endmodule

## Slide 66: If-else statement, If-statement
always @(in0,in1,s,)
begin
if (s==1 ) y=in1;
y=in0;
end
The result y will always be in0.
always @(in0,in1,s,)
begin
if (s==1 ) y=in1;
end
A synthesized circuit has to implement functionality
y=sin1 +s y
This effect is called implied memory (latch)

## Slide 67: Equality Operators
Expression | Description | Possible Logical Value | 
a == b | a equal to b, result unknown if x or z in a or b | 0,1,x | Supported by synthesis
a != b | a not equal to b, result unknown if x or z in a or b | 0,1,x | Supported by synthesis
a === b | a equal to b, including x and z | 0,1 | Not supported by synthesis
a !== b | a not equal to b, including x and z | 0,1 | Not supported by synthesis

## Slide 68: Examples
//Type 1 statements
if(!lock) buffer = data;
if(enable) out = in;
//Type 2 statements
if (counter< MAX_number)
begin sum = sum+data;
counter = counter + 1;
end else
$display(“End of operation ");
//Type 3 statements
//Execute statements based on ALU control signal.
reg[1:0] alu_control;
…
if (alu_control == 0) y = x + z;
else if (alu_control == 1) y = x - z;
else if (alu_control == 2) y = x * z;
else $display("Invalid ALU control signal");

## Slide 69: Case Statement
The keywords case, endcase, and default are used in the case statement.
Case statement may yield a faster synthesized circuit, based on multiplexers, and is more readable.
case (selection-expression) alternative1: statement1; alternative2: statement2; alternative3: statement3; … default: default_statement; endcase

## Slide 70: Case Statement: Example
reg[1:0] op_code;
…
case (op_code)
2’b00: y = x + z;
2’b01: y=x - z;
2’b10: y=x * z;
default:$display("Invalid op_code");
endcase
In a non full case the synthesizer will infer a latch to retain the previous outputs for any cases that are not covered.
The best coding practice is to use full case statements only.
The good coding practice is to use default statement except full case (especially for simulation).

## Slide 71: Casex, Casez
casez treats all z values in the case alternatives or the case expression as don't cares. Instead z can also be represented by ? casex treats all x and z values in the case item or the case expression as don't cares.
Example
reg [3:0] encoding;
integer state;
casex (encoding) //logic value x represents a don't care bit.
4'b1xxx : next_state = 3;
4'bx1xx : next_state = 2;
4'bxx1x : next_state = 1;
4'bxxx1 : next_state = 0;
default : next_state = 0;
endcase
Input encoding = 4'b010z would cause next_state = 2 to be executed.

## Slide 72: Looping Statements (For Loop, Repeat Loop)
Looping statements in Verilog: while, for, repeat and forever. All looping statements can appear only inside an initial or always block.
Syntax of for statement:
for (index=first_expr; logical_expression; index=second_expr)
begin procedural-statements end
At the beginning of each iteration it checks logical expression.
If the value is false, the for loop stops execution.
For synthesis, the first_expr must be constant, the second_exp – incrementing or decrementing.
Syntax of repeat statement:
repeat (integer_expression) procedural statement
The repeat construct executes the loop a fixed number of times.

## Slide 73: Forever Loop, While Loop
Syntax of forever statement:
forever procedural-statement
The loop does not contain any expression and executes forever until the $finish task is encountered.
Syntax of while statement:
while (logical_expression) procedural statement
The while loop executes until the logical expression is not true.
If the loop is entered when the logical_expression is not true, the loop is not executed at all.

## Slide 74: Example 1. For Statement
module counter_one’s(A, count);
parameter n=32;
parameter logn=5;
input [n-1:0] A;
output reg [logn:0] count;
integer i;
always @(A)
begin count=0;
for (i=0; i<n; i=i+1)
count=count + A[i];
end
endmodule
module counter_one’s(A, count);
parameter n=32;
parameter logn=5;
input [n-1:0] A;
output reg [logn:0] count;
reg [n-1:0] ra;
always @(A)
begin count=0;
for (ra=A; ra !=0; ra=ra>>1)
count=count + ra[0];
end
endmodule
One’s counter
Another variant

## Slide 75: Example 3. Repeat Statement
module counter_one’s(A, count);
parameter n=32;
parameter logn=5;
input [n-1:0] A;
output reg [logn:0] count;
reg [n-1:0] ra;
always @(A)
begin count=0; ra=A;
repeat (n)
begin
count = count+ra[0];
ra=ra >>1;
end
endmodule

## Slide 76: Example 4. While Statement
module counter_one’s(A, count);
parameter n=32;
parameter logn=5;
input [n-1:0] A;
output reg [logn:0] count;
reg [n-1:0] ra;
always @(A)
begin count=0; ra=A;
while (ra)
begin if (ra[0] ==1) count=count+1;
else count=count;
ra=ra>>1;
end
endmodule

## Slide 77: Example 6: Forever Statement
Example 1: Clock generation
//Use forever loop instead of always block
reg clock;
initial begin clock = 1'b0;
forever #10 clock = ~clock; //Clock with period of 20 units
end
//Example 2: Synchronize two register values at every positive edge of //clock
reg clock;
reg x, y;
initial
forever @(posedge clock) x = y;

## Slide 78: Disable Statement
disable <name of the block>;
It immediately terminates execution of the named block; subsequent statements in the block are not executed.
It is a way to complete the block. Not used in for loops, and repeat. It is used to exit the loop, out of any named block. An example of exit from forever loop:
initial begin: block1
forever
begin
#10 a = a + 1;
if (a > 30)
disable block1;
end
end

## Slide 79: Generate Operator
Generate statement is a powerful construct for writing configurable, synthesizable RTL. It can be used to create multiple instantiations of modules and code, or conditionally instantiate blocks of code.
module gray_to_bin (gray, bin);
parameter size = 8;
output [size-1:0] bin;
input [size-1:0] gray;
genvar i;
generate for (i=0; i<size; i=i+1)
begin:bit
assign bin[i] = ^gray[size-1:i];
end
endgenerate
endmodule
There are two kinds of Verilog generate constructs.
Generate loop constructs allow a block of code to be instantiated multiple times, controlled by a variable index. Similar of a for loop statement.
Conditional generate constructs: if-generate and case-generate. This constructs select at most one block of code between multiple blocks.

## Slide 80: Port Connection Rules
Low level module inputs can be register variables and net.
In the low-module they are declared as net. Register and net outputs in the low-module are declared as a net in the top-module.
Bidirectional variables are declared as net.
Low level module
net
Output reg/net
Input net
reg/net
Inоut
net
net

## Slide 81: Port Connection Rules
Connection module port by order list
Connection module port by name - .PortName( NetName )
module adder_2bit (a,b,sum);
input[1:0] a,b;
output [2:0] sum;
wire co_1;
half_adder m1(a[0], b[0], co_1, sum[0]); //connection by order list
full_adder m2(.cin(co_1), .a(a[1]),.b(b[1]), .sum(sum[1]),.cout(sum[2])); //connection by name
end
endmodule

## Slide 82: Low-Level Modules
module half_adder (a,b,cout,sum);
input a,b;
output sum,cout;
assign sum =a^b;
assign cout=a&b;
endmodule
module full_adder(cin,a,b,sum,cout);
input cin,a,b;
output sum,cout;
assign {cout,sum} =a+b+cin;
endmodule

## Slide 83: Example
module mux_2_1(a,b,out,out_bar, sel);
input a,b,sel;
output out, out_bar;
reg out;
always@(a or b or sel);
begin
if (sel)
out = a; // procedural
else out =b; // assignment
end
assign out_bar =~out; //continuous assignment
endmodule
Procedural and continuous assignments can exist within a module.

## Slide 84: Overriding Module Parameters
Implicit Overriding
Low-level module description
module shift_reg(data, load, rin,clk,q); parameter n=16;
input [n-1:0] data;
input clk, load, rin;
output [n-1:0] q;
integer i;
always @(posedge clk )
if (load) q<=data;
else begin
q<={rin,q[n-1:1]};
endmodule
Top-level module description
module top (. . .);
. . .
shift_reg #(32) m1( data,load,
rin, clk,q);
. . .
endmodule

## Slide 85: Overriding Module Parameters (2)
Explicit Overriding
module top (. . .);
. . .
shift_reg m1( data,load, rin, clk,q);
defparam n=32;
. . .
endmodule
If the operator defparam is contained in a separate module, then the operator must be written as follows: defparam shift_reg.n = 32

## Slide 86: Simulation in Verilog
Response Analysis/Display
Circuit Under
Test in Verilog
Hardware Description
. . .
Test
data
generation
.
.
.
.
Verilog
Simulator
Testbench Written in Verilog
Simulation outputs is generated in the form of a waveform for visual inspection or data files for record or for machine readability.

## Slide 87: Test_Bench
Unit Description
Inputs
Test bench
Outputs
Verilog Simulator
Unit description
Test Bench
Graphical results of simulation
Simulation results as text
Simulation Engine
User Interface
Parser

## Slide 88: Writing Testbench
A testbench specifies a sequence of inputs to be applied by the simulator to Verilog-based design.
The testbench uses an initial block and delay statements and procedural statement.
Verilog has advanced “behavioral” commands to facilitate this:
  Delay for n units of time
  Full high-level constructs: if, while, sequential assignment.
  Input/output: file I/O, output to display, etc.

## Slide 89: Timing Control
Timing controls specify the simulation time. There are three methods for timing control: delay-based, event-based, and level-sensitive
Delay-Based Timing Control:
# delay_value
delay_value::=<integer>||<variable>||<expression>
Regular delay control:
The symbol ”# ” before begin means that block must be executed with the delay_value.
If “#...” precedes to the operator it means that this operator executes after the previous later on delay_value
#10 а=b;
#10; a=b;
#5; #5 a=b;
The stop of sequential block on 10 ns takes place.

## Slide 90: Intra-Assignment
Intra-assignment timing control can be used with blocking and nonblocking assignments.
Type | Assignment | Equivalent
Delay with assignment | #5 a=b; | #5; a=b;
Intra-assignment | a= #5 b; | temp = b; #5; a=temp;

## Slide 91: Examples
Example 1
  r_out = #10 inputA;
  This is the same as:
  temp = inputA;
  #10;
  r_out = temp;
Example 2
  q = @(posedge clk) d;
  This is the same as:
  temp = d;
  @(posedge clk);
  q = temp;
Important Notes:
  If a statement contains intra-assignment timing controls, its right hand side expression is evaluated and its value is assigned after the time specified by the delay control or after an event specified by event control.
Example 3
  a = repeat (5) @(ready) b & c;
  This is the same as:
  Temp = b & c;
  @(ready);
  @(ready);
  @(ready);
  @(ready);
  @(ready);
  a = temp;

## Slide 92: Event-Based Timing Control
The @ symbol is used to specify an event control.
@(clock) q = d; //q = d is executed whenever signal clock changes value
@(posedge clock) q = d; //q = d is executed whenever signal clock does
//a positive transition ( 0 to 1, x or z, x to 1, z to1) @(negedge clock) q = d; //q = d is executed whenever signal clock does
//a negative transition ( 1 to 0,x or z, x to 0, z to 0)
q = @(posedge clock) d; //d is evaluated immediately and assigned
// to q at the positive edge of clock

## Slide 93: Level Sensitive Timing Control
Event control waited for the change of a signal value or the triggering of an event.
Verilog also allows level-sensitive timing control, i.e. the ability to wait for a certain condition to be true before a statement or a block of statements is executed.
The keyword wait is used for level-sensitive constructs.
always
wait (count_enable);
#20 count = count + 1;

## Slide 94: Functions and Tasks
function function_name; input declarations; variable declarations; parameter declarations; procedural_statement; … endfunction
A function is a procedure used in an expression.
Keywords: function, endfunction
Syntax of function definition:
The function is called by writing function_name (list of expressions).
The expressions are evaluated and assigned to the function’s inputs in the order that they appear in the function definition.

## Slide 95: Functions: Example
Description in Verilog of comparator (<=) and multiplexor
module comp_min (a,b,outmin);
input[7:0] a,b;
output[7:0] outmin;
function[7:0] compare;
input[7:0] ina,inb;
begin
if(ina<=inb) compare =ina;
else compare =inb;
end
endfunction
assign outmin=compare(a,b);
endmodule

## Slide 96: Tasks
A task is a procedure called from another procedure.
Keyword: task, endtask
task task_name; input declarations; inout declarations; output declarations; variable declarations; parameter declarations; procedural_statement; … endtask

## Slide 97: Example
module operation (ina, inb, start,C,D,E);
input[15:0] ina, inb;
input start;
reg[15:0] A,B;
output C,D,E;
reg C,D,E;
parameter delay=10;
always@(posedge start)
begin A=ina; B=inb;
task reduction_oper (C,D,E,A,B);//invoke the task
//reduction
end

## Slide 98: Example (2)
//define task reduction_oper
task reduction_oper;
input [15:0] a,b; //inputs to the task
output c,d,e;
reg c,d,e;
begin # delay
c = &{A,B};
d = |{A,B};
e = ^{A,B};
end
endmodule

## Slide 99: Differences between Tasks and Functions
Functions | Tasks
A function can enable another function but not another task. | A task can enable other tasks and functions.
Functions always execute in 0 simulation time. | Tasks may execute in non-zero simulation time.
Functions must not contain any delay, event, or timing control statements. | Tasks may contain delay, event, or timing control statements.
Functions must have at least one input argument. They can have more than one input. | Tasks may have zero or more arguments of type input, output, or inout.
Functions always return a single value. They cannot have output or inout arguments. | Tasks do not return with a value, but can pass multiple values through output and inout arguments.

## Slide 100: Compiler directives
`define
`define gate_delay = 5
. . .
y= # `gate_delay a & b;
. . .
`define width=32
. . .
reg [`width-1:0] data;
. . .
2. `include
`include "path/file-to-be-included "
Including the entire contents of other Verilog source file.
3. `timescale
`timescale 100ns/1ns
Setting the reference time unit and time precision of simulation.
`ifdef, `else, `elsif, `endif
directives for conditional compilation

## Slide 101: System Tasks
$display is the main system task for displaying values of variables or strings or expressions. This is one of the most useful tasks in Verilog.
Usage: $display(p1, p2, p3,....., pn);
p1, p2, p3,..., pn can be quoted strings or variables or expressions.
The format of $display similar to printf in C.
A $display inserts a newline at the end of the string by default.
A $display without any arguments produces a newline.
$finish
Terminate the simulation.

## Slide 102: Format $display and $monitor
Format | Display
%d or %D | Display variable in decimal
%h or %H | Display variable in hexadecimal
%o or %O | Display variable in octal
%s or %S | Display string
%c or %C | ASCII character
%v or %V | Display strength
%t or %T | Display in current time format
%e or %E | Display real number in scientific format
%f or %F | Display real number in decimal format
%g or %G | Display real number in scientific or decimal format
%m or %M | Display hierarchical name (no argument required)

## Slide 103: $monitor
Verilog provides a mechanism to monitor a signal when its value changes. This facility is provided by the $monitor task.
Usage: $monitor (p1,p2,p3,....,pn);
The parameters p1, p2, ... , pn can be variables, signal names, or quoted strings.
A format similar to the $display task is used in the $monitor task.
$monitor continuously monitors the values of the variables or signals specified in the parameter list and displays all parameters in the list whenever the value of any one variable or signal changes. Unlike $display, $monitor needs to be invoked only once.

## Slide 104: Synthesis in Verilog
Hardware
Description
Verified Circuit in Verilog
Target Library
Verilog Synthesis
Timing files and other hardware details
A netlist of
gates and
flip-flops

## Slide 105: Synthesis Flow
RTL-Description
RTL-synthesis and optimization
Technology Mapping and Optimization
Optimized Gate-Level Representation
Design Constrainst
Technology Independed Library
Target Technology Library

## Slide 106: Verilog HDL Constructs for Logic Synthesis
Constructs | Keyword or Description | Notes
Ports | Input, output, inout | 
Parameters | parameter | 
signals and variables | wire, reg, tri, integer | Vectors and arrays are allowed
Events | @( ) | Named events are not supported
Functions and tasks | Functions, tasks | Timing constructs ignored
procedural | always, if-else, case, casex, casez | initial is not supported

## Slide 107: Verilog HDL Constructs for Logic Synthesis (2)
Constructs | Keyword or Description | Notes
Procedural blocks | begin – end named blocks | fork – join is not supported disable – for named blocks only
Loops | for | 
Loops | while, forever, repeat | 
instantiation | module instances, primitive gate instances | E.g. mymux m1(out, i0, i1, s); E.g., nand (out, a, b);
Data flow | assign | Delay information is ignored

## Slide 108: Optimization within DC
High Level Optimization (Architectural Optimization), Logic Level Optimization, Gate Level Optimization.
Three types of high-level optimizations: resource sharing, common subexpression sharing and implementation selection.
Resource sharing:
Determines whether operators listed in separate lines of code can be shared.
Determines whether it is a good idea to share them, i.e. does it improve timing.
Consider the effect of the RTL-description on the optimization, in particular, Resource sharing.

## Slide 109: Resource Sharing
. . .
y1 =a+b;
y2=c+d;
y3=e+f;
y4=g+h;
if (sel==2’b00) y=y1;
else if (sel==2’b01) y=y2;
else if (sel==2’b10) y=y3;
else y=y4;
. . .
Resource sharing is impossible because the arithmetic operations are outside the if statement. Design may be much larger than necessary.
b
a
00
01
10
11
d
c
f
e
h
g
y1
y2
y3
y4
y
sel

## Slide 110: Resource Sharing
case(sel)
2’b00: y=a+b;
2’b01: y=c+d;
2’b10: y=e+f;
2’b11: y=g+h;
endcase
if(sel==2’b00) y=а+b;
else if(sel==2’b01) y=c+d;
else if (sel==2’b10) y=e+f;
else y=g+h;
00
01
10
11
00
01
10
11
a
b
c
d
e
f
g
h
y
+
sel
Coding to Allow Resource Sharing
or
DC can select the smallest architecture that meets timing

## Slide 111: Resource Sharing (3)
Forced Resource sharing
case(sel)
2’b00: begin op1=a; op2=b; end
2’b01: begin op1=c; op2=d; end
2’b10: begin op1=e; op2=f; end
2’b11: begin op1=g; op2=h; end
endcase
y=op1+op2;
Since the arithmetic “resource” is being shared outside the if statement DC cannot “un-share”.
00
01
10
11
00
01
10
11
a
b
c
d
e
f
g
h
y
+
sel
op1
op2

## Slide 112: Coding to Allow Operator Reordering
SUM <= A*B + C*D + E + F + G
A,B – late arriving signals
SUM <= E + F + G + A*B + C*D
Operators are re-ordered to reduce critical path delays.
+
+


+
+
C
D
A
B
E
F
G
SUM


+
+
+
+
A
B
C
D
SUM
E
F
G

## Slide 113: Coding to Prevent Operator Reordering
SUM <= (A*B) + ( (C*D) + ((E+F) + G) )
C, D – late arriving signals.
Poor architecture, if C*D SUM is timing critical.
+
+


+
+
C
D
A
B
E
F
G
SUM

## Slide 114: Optimization of Arithmetic Expressions
Constant/Operand Folding
Y= A + 3*B – 3 + B – A + 8 = 3*B + 5
Common Sub-Expression Sharing
Тhe operands must be in the same order for each expression.
Parentheses can be used to help the tool recognize common sub-expressions.
Timing constraints should be specified for the design.

## Slide 115: Common Sub-Expression Sharing
1.Without Sharing
Z1 = A + B + C; Z2 = B + C + D; T = B + C; Z1 = A + T; Z2 = T + D;
Prize - one adder.
Parentheses can be used to help the tool recognize common sub-expressions.
2. With Sharing
+
+
A
B
C
Z1
+
+
D
Z2
+
+
B
C
A
Z1
+
Z2
D
T

## Slide 116: Implementation Selection
Multiple implementations for arithmetic operators, available in the Standard Library, allow DC to evaluate speed/area tradeoffs and choose the best – the smallest that meets timing.
Examples are Carry-Look-Ahead adders, Ripple-Carry adders, Booth multipliers, and Wallace Tree multipliers.
Each implementation is then optimized for the target technology library.

## Slide 117: Logic-level Optimization. Structuring
Logic-level optimizations are performed on GTECH netlist.
Consist of two processes: structuring and flattening.
Structuring (by default)
  The subexpressions that have been identified
  and factored out can then be shared between the equations.
  For example:
  f1= ab + ac + ad
  f2= ab + ac + ae
  After structuring:
  f1 = at0 + ad;
  f2 = at0 + ae;
  t0 = b+c ;
  Structuring is usually recommended
  for designs with regular structured logic.
a
b
c
d
e
f1
f2

## Slide 118: Logic-level Optimization. Flattening
Flattening
  Flattening tries to convert logic into two-level, Sum-of-Products representation. Flattening produces fast logic (by minimizing the levels of logic between the inputs and outputs) at the expense of the area increase.
  Flattening is recommended for designs containing unstructured or random logic.
e
а
b
c
d
f1
f2
t0

## Slide 119: Example
module selector(d4,d3,d2,d1,s2,s1,y);
input d4,d3,d2,d1,s3,s2,s1;
output reg y;
always @(d4,d3,d2,d1,s3,s2,s1)
begin
if (s1) y=d1;
else
if (s2) y=d2;
else
if (s3) y=d3
else y=d4;
end

## Slide 120: Structuring and Flattening
Structuring
Flattening
0
1
0
1
0
1
D4
D3
S1
S2
D2
D1
S1
Y
D4
D3
D2
D1
S3
S2
S1
Y

## Slide 121: Gate-Level Optimization
Gate-level optimizations work on the technology-independent netlist and map it to the library cells to produce a technology-specific gate-level netlist.
Mapping
  This process maps the cells from technology-independent netlist (GTECH) to the cells in library specified by the target_library variable.
  Mapping optimization tries to meet the following constraints:
Design rule constraints (DRCs) Highest priority
Timing constraints
Area constraints Lowest priority
Process of mapping takes many iterations.
The optimizations DC performs (or does not perform) depend on the constraints. Therefore, setting realistic constraints is one of the most important synthesis tasks.

## Slide 122: Library Elements
INVERTOR
NAND3
NAND2
NAND4
AOI21
AOI22
XOR

## Slide 123: Variants of Mapping

## Slide 124: Better Variant of Mapping

## Slide 125: Sequential Mapping and Optimization
The process by which DC maps to sequential cells from the technology library:
Tries to save speed and area by using more complex sequential cells (optimization).
1
0
D
C
data
enable
clk
clk
D
En
DFF_ ENBL

## Slide 126: Synthesis Flow
Load designs and
libraries
Apply design
constraints
RTL-Description
Start-up file
Constraints file
Synthesize
the design
Select appropriate design flow
Write out design
data

## Slide 127: Specifying an Area Constraint
dc_shell> read_verilog MY_DESIGN.v
dc_shell> current_design TOP_CHIP_or_BLOCK
dc_shell> link
dc_shell> set_max_area 245000
set_max_area 0

## Slide 128: Default Design Scenario
Current design
Reg1
Reg2
Reg3
Reg4
Clk
M
N
X
S
T
Circuit Y
Circuit X
Design Compiler assumes a “synchronously clocked”
environment. By default:
Input data arrives from a pos-edge clocked device
Output data goes to a pos-edge clocked device

## Slide 129: Create Clock Constraining Register-to-Register Paths
Clock Period = 2ns
create_clock -period 2 [get_ports Clk]
Reg2
Reg3
CLK
N
X
S
P
1 ns
1 ns
CLK
The unit of time is defined in the technology library. It is commonly 1 nano-second, as in the example above, but it may also be defined differently, for example: 0.1 nano-second, 10 pico-seconds, or 1 picosecond.
Assume that setup_time = 0.1
Treg-to-reg, max = P – Setup_Time (assuming 0 clock skew) = 2 – 0.1 = 1.9ns

## Slide 130: Modeling Clock Trees
Reg2
Reg3
CLK
TU
TT
Latency
Post-Layout Circuit
Uncertainty appearance of the signal Clock (TU) is treated as follows:
set_clock_uncertainty –setup TU [get_clocks CLK]
TU = clock skew + jitter + margin

## Slide 131: Pre/Post Layout Clock
Latency
Uncertainty
Transition
[ jitter 0.05 + skew 0.3 + margin 0.15 ]
reset_design
create_clock -p 5 -n MCLK Clk
set_clock_uncertainty -setup 0.5 MCLK
set_clock_transition 0.08 MCLK
set_clock_latency -source -max 4 MCLK
set_clock_latency -max 2 MCLK

## Slide 132: set_clock_uncertainty and Setup Timing
0.1
0.14
0
1
1.76
1.9
2
Max allowable delay Reg-to-Reg
Setup_time Reg3=0.1ns (lib setup)
set_clock_uncertainty –setup 0.14 [get_clocks CLK]
Max allowable delay Reg-to-Reg = 2- (0.14+0.1)=1.76 ns.

## Slide 133: Setup and Hold
Setup – the time before a clock edge before which the data should be stable on the D pin of a flip-flop.
Hold – time after a clock edge for which the data should be held stable.
Setup slack – data setup requierement – last arriving signal
Hold slack - earliest arriving signal - data stability requirement
Hold Slack
Setup Slack
Setup
Hold

## Slide 134: Modeling Latency or Insertion Delay
Origin of Clock
Source
Latency
Network
Latency
3ns
1ns
create_clock -period 10 [get_ports CLK]
set_clock_latency -source -max 3 [get_clocks CLK]
set_clock_latency -max 1 [get_clocks CLK] ;# pre layout
#set_propagated_clock [get_clocks CLK] ; # post layout

## Slide 135: Constraining Input Paths
TLOG_M
Clk
Design
Reg1
Reg2
Reg3
M
N
X
S
A
TCLK-to-Q
TINPUT_DELAY
TLOG_N,MAX
T INPUT_DELAY,MAX + T LOG_N,MAX + TSETUP +TU  P
T LOG_N,MAX = P – TINPUT_DELAY,MAX – TU – TSETUP
What is the maximum delay Tmax for the input path N in design?

## Slide 136: Example 1
Period =2
TU
0
1
1.76
1.9
2
Max delay Reg-to-Reg =1,76
TSETUP
TINPUT_DELAY
TLOG_N
0.6
Time
left for internal input logic,
1.76 - 0.6=1.16
Given ТINPUT_DELAY,MAX = 0,6 ns, Clock frequency = 500 MHz,
TU= 0.14 ns, TSETUP_REG2=0.1 ns. P = 2ns
Maximum delay for path N
T LOG_N,MAX = 2 – 0,6 – 0,14 – 0,1 = 1,16.
Command - set_input_delay
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty –setup 0.14 [get_clocks CLK]
set_input_delay –max 0.6 –clock CLK [get_ports A]

## Slide 137: Example 2
Given T LOG_N,MAX =1.2 ns.
P= 2,5 ns. F= 400 MHz. TSETUP = 0.1 ns
Necessary to write the time constraints so as to report DC the value of TLOG_N,MAX.
Compute TINPUT_DELAY = 2,5 – 1.2 – 0.14 – 0.1 = 1.06 ns.
create_clock -period 2.5 [get_ports CLK]
set_clock_uncertainty –setup 0.14 [get_clocks CLK]
set_input_delay –max 1.06 –clock CLK [get_ports A]

## Slide 138: Constraining Output Paths
TCLK-to-Q
TLOG_S
TLOG_T
Design
Reg2
Reg3
Reg4
N
X
S
T
B
TOUTPUT_DELAY,MAX=0.8
TOUTPUT_LOGIC=?
ТSETUP+TLOG T
Latest Data Arrival Time at Port B - TOUTPUT_DELAY,MAX
TOUTPUT_DELAY,MAX = TLOG_T + TSETUP_REG4
TOUTPUT_LOGIC = TCLK-to-Q + TLOG_S,
TOUTPUT_LOGIC + TOUTPUT_DELAY,MAX + TU  P
Command - set_output_delay

## Slide 139: Example 3
For given TSETUP_ REG4 =0,1. P=2 ns, TU = 0,3.
TOUTPUT_DELAY_MAX =T SETUP REG4 + TLOG_T = 0,1 +0,7 = 0,8.
DC calculates how much time (TOUTPUT_LOGIC (MAX)) is left to the internal output logic of the synthesized project.
T OUTPUT_LOGIC (MAX) = P - TU - T OUTPUT_DELAY_MAX = 2 - 0.3 - 0.8 = 0.9 ns.
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty –setup 0.3 [get_clocks CLK]
set_output_delay –max 0.8 –clock CLK [get_ports B]

## Slide 140: Timing Diagram for Example 3
TSETUP =0.1
TU =0.3
0
1
1.9
2
Max delay Reg-to-Reg
Period
0,9
0.7
TLOG_Т
Time left for internal output logic
0.3
1.2
TOUTPUT_DELAY_MAX
0.8

## Slide 141: Example 4
Design
Reg2
Reg3
Reg4
N
X
S
T
B
TOUTPUT_LOGIC(MAX)=0.7
TOUTPUT_DELAY_MAX = ?
Given maximal delay of internal designed output logic from CLK to the port B (TOUTPUT_LOGIC(MAX).
P=2 ns, TU = 0,3. TSETUP = 0.1, T OUTPUT_LOGIC(MAX) = 0,7.
In order to indicate this time DC, necessary determine TOUTPUT_DELAY_MAX.
TOUTPUT_DELAY_MAX = P – TU – TOUTPUT_LOGIC,MAX = 1 ns.

## Slide 142: Timing Constraints and Diagram for Example 4
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty –setup 0.3 [get_clocks CLK]
set_output_delay –max 1 –clock CLK [get_ports B]
TU =0.3
0
1
1.9
2
Max delay Reg-to-Reg
TSETUP =0.1
Period
0.7
0.9
TLOG_Т
TOUTPUT_LOGIC(MAX)
(given)
0.3
1.0
TOUTPUT_DELAY_MAX

## Slide 143: Constraining Combinational Paths
Design
Reg1
Reg4
Clk
M
T
Combina-tional
circuit
The syntax of virtual clock:
create_clock -name VCLK -period 2
Let the time of arrival to the input port A combinational circuit is TM = 0.4ns.
TT = 0.2ns, TSetup=0.1ns, P=2 ns

## Slide 144: Constraining a Purely Combinational Design
Design
Reg1
Reg4
Clk
M
T
Combina-tional
circuit
External launching circuitry
External capturing circuitry
A clock that is not connected to any port or pin within the current design
Serves as a reference for input or output delays
Create_clock -name VCLK -period 2

## Slide 145: Constraining a Purely Combinational Design (2)
Assume the time of arrival to the input port A combinational circuit is TM=0.4ns. TT = 0.2ns, TSetup=0.1ns, P=2 ns
create_clock –name VCLK –period 2
set_input_delay –clock VCLK –max 0.4 [get_ports A] set_output_delay –clock VCLK –max 0.3 [get_ports B]
Design
Reg1
Reg4
Clk
M
T
Combinational
circuit
A
B
TT =0.2
TSetup=0.1
Tinput=0.4
TCOMB,MAX = 2 – 0,4 – 0,3 = 1,3