## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Basic Combinational Circuits

## Slide 4: Multiplexers
The function of multiplexer (mux) is to connect data from one of n sources to its output. Two type inputs – data inputs and select (address) inputs.
The number of address inputs s=log2n.
If data inputs are m bits wide, mux has m bits output.
Multiplexer 2:1
Y = ~S·X0+S·X1
i0 MUX
i1
S
x1
x0
S
y
y
x0
x1
S
S X0 X1 | y
0 0 x | 0
0 1 x | 1
1 x 0 | 0
1 x 1 | 1

## Slide 5: Mux 2:1 ln Verilog
Verilog
module mux2(input [3:0] d0, d1, input s, output [3:0] y);
assign y = s ? d1 : d0;
endmodule
In SystemVerilog, internal signals are usually declared as logic.
System Verilog
module mux2(input logic [3:0] d0, d1, input logic s,
output logic [3:0] y);
assign y = s ? d1 : d0;
endmodule

## Slide 6: Simplified View of Multiplexer
in0
in1
in2
…
in2n-1
a0
a1
an-1
Y
n=4
Y=in0~a1~a0 +in1~a1 a0+
+in2a1~a0 +in3a1a0

## Slide 7: Multiplexers (2)
Multiplexer 4:1
in0
in1
in2
In3
a0
a1
u
v
w
x
nota0
nota1
y
y
00
01
10
11
in0
in1
in2
in3
a1
a0

## Slide 8: Multiplexers in Verilog.Gate Level Implementation
module multiplexer4_1 (y, in0, in1, in2, in3, a0, a1);
// port declarations
output y;
input in0, in1, in2, in3, a0, a1;
// internal wire declarations
wire nota0, nota1, u, v, w, x, y;
//create nota0 and nota1 signals
not (nota0, a0);
not (nota1, a1);
// 3-input and gates instantiations
and(u, in0, nota0, nota1);
and(v, in1, a0, nota1);
and(w, in2, nota0, a1);
and(x, in3, a0, a1);
//4-input or gate instantiation
or(y, u, v, w, x);
endmodule

## Slide 9: Logic Statement Implementation
module multiplexer4_1 (y, in0, in1, in2, in3, a0, a1);
output y;
input in0, in1, in2, in3, a0, a1;
assign y = (in0&~a0&~a1)|(in1&a0&~a1) |(in2&~a0&a1)|(in3&a0&a1);
endmodule

## Slide 10: Case Statement Implementation
module multiplexer4_1 (y, in0, in1, in2, in3, a0, a1);
output y;
input in0, in1, in2, in3, a0, a1;
reg y;
always @ (in0 or in1 or in2 or in3 or a0 or a1)
case ({a1, a0})
2’ b00: y = in0;
2’ b01: y = in1;
2’ b10: y = in2;
2’b11: y = in3;
default: $display (“Please check control bits”);
endcase
endmodule

## Slide 11: Conditional Operator Implementation
module multiplexer4_1 (y, in0, in1, in2, in3, a0, a1);
output y;
input in0, in1, in2, in3, a0, a1;
assign y = a0 ? (a1 ? in3 : in1) : (a1 ? in2 : in0);
endmodule
Nested conditional operators

## Slide 12: Example 2
  The implementation of given function
  using multiplexer 8:1.
x4
0 MUX
1
2
3
4
5
6
7
A0
A1
A2
“0”
“1”
Y
x3 x2 x1
x1 x2 x3 x4 | y | Cofactors
0 0 0 0 | 0 | I0 =x4
0 0 0 1 | 1 | 
0 0 1 0 | 0 | I1 =0
0 0 1 1 | 0 | 
0 1 0 0 | 1 | I2 =1
0 1 0 1 | 1 | 
0 1 1 0 | 1 | I3 = ~x4
0 1 1 1 | 0 | 
1 0 0 0 | 1 | I4 = ~x4
1 0 0 1 | 0 | 
1 0 1 0 | 1 | I5 = ~x4
1 0 1 1 | 0 | 
1 1 0 0 | 0 | I6 = x4
1 1 0 1 | 1 | 
1 1 1 0 | 1 | I7 = ~x4
1 1 1 1 | 0 | 
MUX 8:1

## Slide 13: Example 3
y= x1~x2 +x2~x3~x5 +~x1x3+~x1x4+x4x5
Definition cofactors of y function
Given function f(x1,x2,x3,x4,x5) is implemented using multipleplexer 8:1
y~x1~x2~x3= x4+x4x5=x4
y~x1~x2x3 =x4x5
y~x1x2~x3=~x5+x4+x4x5=~x5+x4
y~x1x2x3 =1
yx1~x2~x3 =1
yx1~x2x3 = 1
yx1x2~x3 =~x5+x4
yx1x2x3 =x4x5
y
0 MUX
1 8:1
2
3
4
5
6
7
A0
A1
A2
“1”
x3 x2 x1
x4
x5

## Slide 14: Pyramidal Structure of Multiplexers
Given function f(x1,x2…xk…xn).
Shannon’s extension by k variables:
F(x1,x2…xn) = ~x1·~x2…~xk·f(0,…,0,xk+1,…xn) +
+~x1·~x2…~xk-1·xk·f(0,…,0,1,xk+1…xn) +
~x1·~x2…xk-1~xk·f(0,…,1,0,xk+1,…xn) + … +
+ x1·x2…xk ·f(1,1,…1,xk+1,…xn) =
=F0·~x1·~x2…~xk +F1·~x1·~x2…xk +F2·~x1·~x2…xk + . . .+
+F2k-1·x1·x2…·xk
where F0=f(0,0,…0,xk+1 …xn) =f~x1…~xk ; F1=f(0,0,…1,xk+1,…xn)=
f~x1~x2…xk; F2 = f(0,0,…1,0,xk+1,…xn)=f~x1~x2…xk-1~xk; … F2k-1 = f(1,1,…1,xk+1,…xn)=fx1x2…xk

## Slide 15: Pyramidal Structure of Multiplexers (2)
{0,1}
{0,1}
{0,1}
Xn
Xn-1
Xk+1
0 MUX 0
1
2P-1
A0
A1
…
AP-1
0 MUX1
1
…
2P-1
A0
A1
…
AP-1
0 MUX 2k-1
1
…
2P-1
A0
A1
…
AP-1
0 MUX
1
…
2k-1
A0
A1
…
Ak-1
f(x1,x2…xn)
Xk
Xk-1
X1

## Slide 16: Example (1)
Implementation of given function using two-level scheme of multiplexers 4:1
i0 MUX
i1
i2 y
i3
a0
a1
Y
x1 x2 x3 x4 | y
0 0 0 0 | 1
0 0 0 1 | 1
0 0 1 0 | 0
0 0 1 1 | 0
0 1 0 0 | 1
0 1 0 1 | 1
0 1 1 0 | 1
0 1 1 1 | 0
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 1
1 0 1 1 | 0
1 1 0 0 | 0
1 1 0 1 | 0
1 1 1 0 | 1
1 1 1 1 | 0

## Slide 17: Example (2)

## Slide 18: Shannon Cofactors
  f(x1,x2, . . . xn) = ~xif~xi(x1,x2 . . .xi-1, xi+1 . . .xn) + xi fxi (x1,x2 . . .xi-1, xi+1 …xn)
  f~xi,fxi - cofactors of f by literals ~xi and xi.
  Cofactor (fx): the function that is obtained when substituting 1 for x in f.
  ROBDD is a compressed Shannon co-factoring tree:
    f = v·fv + ~v·f~v
    Leafs are constants “0” and “1”
    Each node is written as a triple: f = (v,g,h) where g=fv , h=f~v. v is a top variable of f.
    This triple is read as: f = if v then g else h = ite (v,g,h) = v·g+~v·h.
    a multiplexer can be put into compliance to each node.

## Slide 19: Cofactors
f=~vh+vg
f=(a+b)c
f=0 f=1 f=bc
f=c
MUX
f
v
h
g
0
1
v
h
g
0
1
x
x
a
b
c
0
1
0
1

## Slide 20: Example
a b c d | y
0 0 0 0 | 0
0 0 0 1 | 0
0 0 1 0 | 1
0 0 1 1 | 1
0 1 0 0 | 0
0 1 0 1 | 1
0 1 1 0 | 1
0 1 1 1 | 1
a b c d | y
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 0
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
Y = f(a,b,c,d)

## Slide 21: Example
b
c
a
b
b
c
c
a
1
0
c+bd
c+d
d
a
c
d
b
1
0
b
bd
c+bd
f=ab+~ac+b~cd
Two different orderings, the same function

## Slide 22: Implementation by 2:1 Multiplexers
MUX
b
1
0
1
MUX
d
0
1
MUX
f
a
0
1
MUX
c
1
0
1
0
0
MUX
c
1
0
1
a
c
d
b
1
0
b
bd
c+bd

## Slide 23: ITE Operator
Sets Subset Expression Equivalent
0000 0 0 0
0001 AND(f, g) fg ite(f, g, 0)
0010 f> g ~gf ite(f,~g, 0)
0011 f f f
0100 f< g ~fg ite(f, 0, g)
0101 g g g
0110 XOR(f, g) f  g ite(f,~g, g)
0111 OR(f, g) f + g ite(f, 1, g)
1000 NOR(f, g) ~(f + g) ite(f, 0,~g)
1001 XNOR(f, g) ~(fg) ite(f, g,~g)
1010 NOT(g) ~g ite(g, 0, 1)
1011 f  g f+ ~g ite(f, 1, ~g)
1100 NOT(f) ~f ite(f, 0, 1)
1101 f  g ~f+ g ite(f, g, 1)
1110 NAND(f, g) ~(fg) ite(f, ~g, 1)
1111 1 1 1
ITE operator
can implement
any two
variable logic
functions.
Example of set:
1011  00 1
01 0
10 1
11 1

## Slide 24: Decoders
The function of binary decoder is to convert binary input code to unary output code. The number of inputs is usually less than the number of outputs.
Binary (full) decoder: n inputs, 2n outputs (n-to-2n).
Inputs |  |  | Outputs |  |  | 
En | A1 | A0 | Y3 | Y2 | Y1 | Y0
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0
The input code word A1A0 represents an integer in range 0 – 3.
The output code word has Yi=1, if A1A0 is binary representation of i.

## Slide 25: Decoders (2x4)
In general case a decoder is multiple-input, multiple-output circuit, that converts coded input into coded output.
The input code generally has fewer bits than the output code.
There is one-to-one mapping from input code words to output code words.
A0
A1
En
Y0
Y1
Y2
Y3

## Slide 26: Decoders in Verilog
3’ b010: Yout = 8’ b 00000100;
3’ b011: Yout = 8’ b 00001000;
3’ b100: Yout = 8’ b 00010000;
3’ b101: Yout = 8’ b 00100000;
3’ b110: Yout = 8’ b 01000000;
3’ b111: Yout = 8’ b 10000000;
default: Yout = 8’ b 00000000;
endcase
end
endmodule
module decode
(input [2:0] A, En, output reg [7:0] Yout);
always @ (En or A)
begin
if (!En)
Yout = 8' b00000000;
else
case ( A )
3’ b000: Yout = 8’ b 00000001;
3’ b001: Yout = 8’ b 00000010;
DC
A0
A1
A2
En
y0
y1
y2
y3
y4
y5
y6
y7

## Slide 27: Decoder Description by Verilog using for statement
module dec4to16(a,en,y);
input [3:0] a;
input en;
output reg [0:15] y;
integer k;
always @(a or en)
for (k=0; k<=15; k=k+1)
if(a==k&&en==1)
y[k]=1;
else y[k]=0;
endmodule

## Slide 28: Decoder Description with Parameter and test_Bench
module decoder(in,en,out,out);
parameter n=5;
input en;
input [n-1:0] in;
output reg [2**n-1:0] out;
integer k;
always @(*)
for (k=0; k<2**n; k=k+1)
if ((in==k)&&(en==1))
out[k]=1; else out[k]=0;
endmodule
module test_bench;
parameter n=5;
reg en;
reg [n-1:0] in;
wire [2**n-1:0] out;
integer k;
decoder my_dec(in, en,out);
initial begin
en=0; #5 en=1;
for (k=0; k<2**n; k=k+1)
in = #5 k;
#80 $finish;
end
endmodule

## Slide 29: Decoder in SystemVerilog
module decoder3_8(input logic [2:0] a,
output logic [7:0] y);
always_comb
case(a)
3’b000: y = 8’b00000001;
3’b001: y = 8’b00000010;
3’b010: y = 8’b00000100;
3’b011: y = 8’b00001000;
3’b100: y = 8’b00010000;
3’b101: y = 8’b00100000;
3’b110: y = 8’b01000000;
3’b111: y = 8’b10000000;
default: y = 8’bxxxxxxxx;
endcase
endmodule
DC
A0
A1
A2
y0
y1
y2
y3
y4
y5
y6
y7

## Slide 30: Decoder in System Verilog
module test_bench;
parameter n=5;
reg en;
reg [n-1:0] in;
wire [2**n-1:0] out;
integer k;
decoder my_dec(in, en,out);
initial begin
en=0; #5 en=1;
for (k=0; k<2**n; k=k+1)
in = #5 k;
#80 $finish;
end
endmodule

## Slide 31: Boolean Functions Realization Using Decoders
x2 x1 x3 | f(x1x2x3)
0 0 0 | 1
0 0 1 | 1
0 1 0 | 0
0 1 1 | 0
1 0 0 | 1
1 0 1 | 0
1 1 0 | 1
1 1 1 | 0
DC
A0
A1
A2
y0
y1
y2
y3
y4
y5
y6
y7
f(x1x2x3)
x3
x2
x1
Minterms

## Slide 32: IC 74x138
Inputs | Outputs
~E1~E2 E3 C B A | ~y7~y6~y5~y4~y3~y2~y1~y0
1 x x x x x x 1 x x x x x x 0 x x x 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 1 0 0 0 1 0 1 1 0 0 1 1 0 0 0 0 1 1 0 1 0 0 1 1 1 0 0 0 1 1 1 1 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 0 1 1 1 1 1 1 1
A Y0
B Y1
C Y2
Y3
Y4
E1 Y5
E2 Y6
E3 Y7
1
2
3
4
5
6
15
14
13
12
11
10
9
7
Truth Table

## Slide 33: Demultiplexers
Multiplexer can be used to select one of 2n sources of data to transmit on a bus.
Demultiplexer can be used to route the bus data to one of 2n destinations (inverse function).
s0
s1
sn-1
Output 0
Output 1
.
.
.
Output 2n-1
N=4
Output 0 = Input~s0 ~s1
Output 1 = Input ~s1s0
Output 2 = Input s1~a0
Output 3 = Input s1 s0
Input

## Slide 34: Demultiplexer in Verilog
module demultiplexer1_to_4(out,in,s);
output reg[0:3]out;
input in;
input [1:0]s;
always @(s , in)
case (s) // Switch based on control signals
2'b00:out={in,3’bz};
2'b01:out={1’bz,in,2’bz};
2'b10:out={2’bz,in,1’bz};
2'b11:out={3’bz,in};
default:out =4’bz;
endcase
endmodule

## Slide 35: Encoders
The function of binary encoder is to convert input code (unary) to output code (binary) (2n-to-n). The number of inputs is usually more than the number of outputs.
Inputs – D0,D1, . . ., Di, . . .
Di&Dk=0; if Dk=1, yout = k.
If input signals are independent, then condition Di&Dk=0 is unrealizable. In this case the priority is assigned for each input.
Let priority grow with increasing the input number i.
Then priority encoder gives out the binary representation of i (Di=1) if (Dk=1): k<i.

## Slide 36: Priority Encoder 4-to-2
Design priority encoder 4-to-2
The priority encoder implements the following functions:
H3 = D3; H0 = ~D3·~D2·~D1·I0;
H2 = ~D3·D2; A1 = H3 + H2;
H1 = ~D3·~D2·D1; A0 = H3 + H1; G = D0 + D1 + D2 + D3;
G – Group Select;
D3
D2 A1
D1 A0
D0 G
A0
Priority
circuit
Encoder
H3
H2
H1
H0
D3
D2
D1
D0
A1
G
D0D1D2D3 | A1A0 G
x x x 1 | 1 1 1
x x 1 0 | 1 0 1
x 1 0 0 | 0 1 1
1 0 0 0 | 0 0 1
0 0 0 0 | 0 0 0
D3 - highest priority

## Slide 37: Priority Encoder 4-to-2
D3
D1
D0
G
A0
A1
D2
After minimization
A1=D3+D2; A0=D3 + ~D2D1;
G= A1+D1+D0;

## Slide 38: Priority Encoder 8-to-3 using for statement
module priority_encoder(data,Y, gs);
input [7:0] data;
output reg [2:0] Y;
output reg gs;
integer k;
always @(data)
begin
Y=3’ b0;
gs=0;
for (k=0; k<8; k=k+1)
if (data[k])
begin Y=k;
gs=1; end end
endmodule
Highest priority – data[7]
The iteration, that corresponds to the highest priority input that is equal to 1 will override any setting of Y establish during the previous iterations.

## Slide 39: Verilog Description of Encoder
module prior_encoder(data,y, gs);
input [15:0] data;
output reg [3:0] y;
integer k;
output reg gs;
always @(data)
begin
y=0;gs=0;
for(k=0; k<16; k=k+1)
if (data[k])
begin
y=k; gs=1;
end
end
endmodule
module test_bench;
reg [15:0] data;
wire [3:0] y;
wire gs;
prior_encoder encoder(data,y, gs);
initial begin
data=0;
#5 data =16'b1000_1100_0111_0010;
#5 data=16'b0011_0000_0101_0111;
#5 data=16'b0000_1000_0101_0111;
#5 data=16'b00111_0000_0101_0111;
#10 $finish;
end
endmodule

## Slide 40: Verilog-Description of EncoderUsing Case Statement
module stimulus;
reg [3:0] din;
wire [1:0] aout;
wire gs;
integer k;
coder mod(din, aout, gs);
initial begin
for (k=0;k<16; k-k+1)
din= #5 k;
#20 $finish;
end
endmodule
module coder (din, aout, gs);
input [3:0] din;
output [1:0] aout;
reg [1:0] aout;
output reg gs;
reg gs;
always @(din)
begin if (din==4’b0000)
begin gs=0; aout=2’b00; end
else begin gs=1;
casex (din)
4’b1???: aout =2’b11;
4’b01??: aout = 2’b10;
4’b001?: aout = 2’b01;
4’b0001: aout = 2’b00;
default: aout=2’b00;
endcase
end
end
endmodule //coder

## Slide 41: IC 74x148
Truth Table
EI
I7
I6
I5
I4
I3
I2
I1
I0
A2
A1
A0
GS
EO
Inputs | Outputs
~EI ~I0 ~I1 ~I2 ~I3 ~I4 ~I5 ~I6 ~I7 | ~A2 ~A1 ~A0 ~GS ~EO
1 x x x x x x x x 0 x x x x x x x 0 0 x x x x x x 0 1 0 x x x x x 0 1 1 0 x x x x 0 1 1 1 0 x x x 0 1 1 1 1 0 x x 0 1 1 1 1 1 0 x 0 1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 0 1 1 1 1 1 1 1 1 | 1 1 1 1 1 0 0 0 0 1 0 0 1 0 1 0 1 0 0 1 0 1 1 0 1 1 0 0 0 1 1 0 1 0 1 1 1 0 0 1 1 1 1 0 1 1 1 1 1 0

## Slide 42: 16-inputs Priority Encoder
A3
A2
A1
A0
RGS
EI
I7
I6
I5
I4
I3
I2
I1
I0
A2
A1
A0
GS
EO
~In7
~In6
~In5
~In4
~In3
~In2
~In1
~In0
EI
I7
I6
I5
I4
I3
I2
I1
I0
A2
A1
A0
GS
EO
~In15
~In14
~In13
~In12
~In11
~In10
~In9
~In8
Input ~In15 has highest priority.
If the first encoder has no active inputs, then EO =0.
Since EI=EO=0, the second encoder is activated

## Slide 43: Double Priority Encoder (2)
EI
I7
I6
I5
I4
I3
I2
I1
I0
A0
A1
A2
GS
EO
R0 1 1
R1 2 2
R2 3 3 R3 4 4
R4 5 5
R5 6 6
R6 7 7
R7 8 8
E1
E2
E3
A
B
C
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
EI
I7
I6
I5
I4
I3
I2
I1
I0
A0
A1
A2
GS
EO
1
2
3
4
5
6
7
8
1
2
3
1
2
3
1
2
3
A[2:0]
AVALID
B[2:0]
BVALID
1
1
2
2
3
3
4
4
5
5
6
6
7
7
8
8
R0-R7 - active low.
R0 has highest priority

## Slide 44: Priority Circuit (System Verilog)
module priority_circuit (input logic [3:0] a,
output logic [3:0] y);
always_comb
if (a[3]) y <= 4'b1000;
else if (a[2]) y <= 4'b0100;
else if (a[1]) y <= 4'b0010;
else if (a[0]) y <= 4'b0001;
else y <= 4'b0000;
endmodule
In Verilog and SystemVerilog, if statements must appear inside of always statement

## Slide 45: Full Adder
The function of the full adder is to add two binary digits and a carry that might be generated or propagated by the previous stage.
Inputs a b cin | Outputs s cout
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 0 1 0 0 1 1 0 0 1 0 1 1 1

## Slide 46: Full Adder (2)
S=a  b  c;
cout = a·b + a·cin + b·cin = a·b +cin(a+b); majority function
g= a·b; p=a+b or p=a^b; g= generation, p – propagation functions.
bcin
a
00
01
11
10
0
1
1
1
1
1
S
bcin
a
00
01
11
10
0
1
1
1
1
1
cout

## Slide 47: The Circuit of Full Adder
Cout=ab +cin(ab)
Standard approach – 6 gates
cin
a
b
s
cout

## Slide 48: Full Adder
cin
a
b
s
cout
g
p
g=ab
P=cin (ab)

## Slide 49: Full Adder
In SystemVerilog, internal signals are usually declared as logic.
module fulladder(input logic a, b, cin,
output logic s, cout);
logic p, g;
assign p =a ^ b;
assign g =a & b;
assign s = p ^ cin;
assign cout = g | (p & cin);
endmodule

## Slide 50: XOR and XNOR Gates
Equivalent symbols for XOR gates
Equivalent symbols for XNOR gates
a
b
f
f
a
b
a
a b | ab | ~(ab)
0 0 | 0 | 1
0 1 | 1 | 0
1 0 | 1 | 0
1 1 | 0 | 1

## Slide 51: Comparators
Comparator is the circuit whose function is to determine
which of two binary numbers A and B is equal (or large,
less . . .).
Comparator  
Given two binary numbers A = (an-1an-2 . . . a1a0) and
B = (bn-1bn-2 . . . b1b0).
F = (an-1==bn-1)(an-2==bn-2) . . . (a1==b1)(a0==b0).
XOR and XNOR can be considered as 1-bit comparators.

## Slide 52: Comparator /  (using XNOR)
Y
Y=
a3
b3
a2
b2
a1
b1
a0
b0

## Slide 53: Comparator  / (using XOR)
Y=
Y
a3
b3
a2
b2
a1
b1
a0
b0

## Slide 54: Verilog Description for n-bit Comparator
module compare (compout, a,b);
parameter size = 32;
output compout;
input [size-1:0] a;
input [size-1:0] b;
assign compout = (a==b);
endmodule //compare

## Slide 55: Comparator >,<,=
Determine functions YA>B, YA=B, YА<B
YA>B=(a3>b3)+(a3==b3)(a2>b2)+(a3==b3)(a2==b2)(a1>b1)+
+(a3==b3)(a2==b2)(a1=b1) (a0>b0) ;
YA=B = (a3 = =b3)(a2 = =b2)(a1= =b1)(a0 = =b0);
YА<B = ~YA>B  ~YA=B;
Fa>b=a~b
a | b | Fa>b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 56: A Four-bit Comparator Circuit
a3
b3
a2
b2
a1
b1
a0
b0
A==B
A<B
A>B

## Slide 57: IC 74x85
A3
A2 CMP
A1
A0
B3
B2
B1
B0
>
=
<
a3
a2
a1
a0
b3
b2
b1
b0
AGTBout
AEQBout
ALTBout
AGTBout = (A>B) + (A==B)AGTBin
ALTBout = (A<B) + (A==B)ALTBin
AEQBout =(A==B)AEQBin
AGTBin
AEQBin
ALTBin

## Slide 58: IC 74x85 Truth Table
Data Inputs | Extended Inputs | Outputs
A3,B3 A2,B2 A1,B1 A0,B0 | A>Bin A<B A=Bin | A>Bout A<Bout A=Bout
A3>B3 x x x | x x x | 1 0 0
A3<B3 x x x | x x x | 0 1 0
A3=B3 A2>B2 x x | x x x | 1 0 0
A3=B3 A2<B2 x x | x x x | 0 1 0
A3=B3 A2=B2 A1>B1 x | x x x | 1 0 0
A3=B3 A2=B2 A1<B1 x | x x x | 0 1 0
A3=B3 A2=B2 A1=B1 A0>B0 | x x x | 1 0 0
A3=B3 A2=B2 A1=B1 A0<B0 | x x x | 0 1 0
A3=B3 A2=B2 A1=B1 A0=B0 | 1 0 0 | 1 0 0
A3=B3 A2=B2 A1=B1 A0=B0 | 0 1 0 | 0 1 0
A3=B3 A2=B2 A1=B1 A0=B0 | 0 0 1 | 0 0 1
A3=B3 A2=B2 A1=B1 A0=B0 | 0 0 0 | 1 1 0

## Slide 59: 12-bit Comparator
Inputs: A>B – AGTBin; A<B – ALTBin; A=B – AEGBin;
Outputs: A>B – AGTBout; A<B – ALTBout; A=B – AEGBout;
A3
A2 CMP
A1
A0
B3
B2
B1
B0
>
=
<
A3
A2 CMP
A1
A0
B3
B2
B1
B0
>
=
<
A3
A2 CMP
A1
A0
B3
B2
B1
B0
>
=
<
>
=
<
a3
a2
a1
a0
b3
b2
b1
b0
a7
a6
a5
a4
b7
b6
b5
b4
a11
a10
a9
a8
b11
b10
b9
b8
>
=
<
>
=
<
A>B
A=B
A<B
Vcc

## Slide 60: Verilog Description
module comparator (a, b, agtbin, altbin, aeqbin, agtbout, altbout, aeqbout);
input [3:0] a,b;
input agtbin, altbin,aeqbin;
output agtbout, altbout, aeqbout;
reg agtbout, altbout, aeqbout;
always @ (a or b or agtbin or altbin or aeqbin)
if (a==b)
begin agtbout=agtbin; altbout=altbin; aeqbout=aeqbin; end
else if (a> b)
begin agtbout=1’b1; altbout=1’b0; aeqbout=1’b0; end
else if (a< b)
begin agtbout=1’b0; altbout=1’b1; aeqbout=1’b0; end
else
begin agtbout=1’bx; altbout=1’bx; aeqbout=1’bx; end
endmodule

## Slide 61: Tri-State Buffers
A tri-state buffer allows multiple sources to share a single party line, as long as only one device ”talks” at a time.
Noninverting, active-
high enable.
Noninverting, Inverting, active- Inverting, active-
active-low enable high enable low enable
A
En
Y
A
En
Y
A
En
Y
Y
Y
A
A
En=1
En=0
A
En
Y
En A | Y
0 0 | Hi-Z
0 1 | Hi-Z
1 0 | 0
1 1 | 1

## Slide 62: Tri-State Buffers (2)
To avoid fighting control logic must guarantee a dead time on the line in which no one drives.
S1S0
3
D
A
0
1
B
E
Dead time
0
Sdata
S0
S1
A
B
C
D
A
B
E
0
1
2
3

## Slide 63: Tri-State Buffers (3)
module tristate (en, a, y);
input a, en;
output y;
reg y;
always @ (a or en)
begin if (en)
y = a;
else y = 1’bz;
end
endmodule
Using continuous assignment and ternary conditional operator
module tristate (en, a, y);
input a, en;
output y;
assign y = en?a:1’bz;
endmodule

## Slide 64: SystemVerilog
module tristate(input logic [3:0] a,
input logic en,
output tri [3:0] y);
assign y = en ? a : 4'bz;
еndmodule
y is declared as tri rather than logic.
tri output from a module can be used as a logic input to another module.

## Slide 65: MUX 2:1 Based on Tri-State Buffers
Y=d0·S + d1·S
d0
d1
Y
S
SystemVerilog
module mux2(input logic [3:0] d0, d1,
input logic s, output tri [3:0] y);
tristate t0(d0, ~s, y);
tristate t1(d1, s, y);
endmodule
In SystemVerilog, expressions such as ~s are permitted in the port list for an instance. Arbitrarily complicated expressions are legal but discouraged because they make the code difficult to read.

## Slide 66: Verilog and SystemVerilog
Type of signal | Verilog | Type of signal | SystemVerilog
wire {0,1,x,z} | left hand of = in assign statement. One driver | logic, one driver | nearly all SystemVerilog signals
reg | left hand side of <= or = in an always block | Logic, one driver | Synonym a reg
tri | wire | tri | Multiple drivers
bit {0,1} | byte |  | 
SystemVerilog relaxes the rules on assign statements and hierarchical port instantiations so logic can be used outside always blocks where a wire traditionally would have been required.
The exception is that signals with multiple drivers (e.g.,a tristate bus) must be declared as a net.

## Slide 67: Example
D0
D1
D2
D3
D4
D5
D6
D7
E1
E2
A1
A2
A3
A4
A5
A6
A7
A8
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
E1
E2
A1
A2
A3
A4
A5
A6
A7
A8
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Microprocessor
Read
InSEL1
InSEL2
DB0
DB1
DB2
DB3
DB4
DB5
DB6
DB7
DB0
DB1
DB2
DB3
DB4
DB5
DB6
DB7
DB7
DB6
DB5
DB4
DB3
DB2
DB1
DB0
Data Bus[0:7]
.
.
.
User
Inputs
.
.
.
Input
Port 2
Input
Port 1

## Slide 68: Tri-states for Getting on a Bus
Bus
sb0
sb1
sb2
sb3
rb3
rb2
rb1
rb0
DC
Source address
DC
Dest. address

## Slide 69: Data Transfer on the Bus Using Multiplexer-Demultiplexer
Bus
MUX
DMX
En1
En2
src0
src1
src2
src3
dst3
dst2
dst1
dst0
srcsel
dstsel

## Slide 70: Bus Transceiver
Bus transceiver contains a pair of tri state buffers connected in opposite directions between each pair of pins.
A
B
En
Dir
En Dir | Operation
0 0 | Transfer data from src on B to dst on A
0 1 | Transfer data from src on A to dst on B
1 x | Transfer data on A and B independently

## Slide 71: Bus Transceiver in Verilog
Verilog module for 8-bit transceiver:
module transciever_8(En, Dir, A,B);
input En, Dir;
inout [7:0] A, B;
assign A = ~En&~Dir ? B: 8’bz;
assign B= ~En&Dir ? A: 8’bz;
endmodule

## Slide 72: Bidirectional Buses
IC1
IC3
IC2
Control
Unit
IC5
IC7
IC6
IC4
En
EN
Dir
AtoB
A0
A7
B0
B7
Bus A
Bus B

## Slide 73: Parity Circuit
Daisy-chain connection
Y=in1in2in3in4in5in6in7in8
T = (n-1), where  - one XOR-gate delay
odd
in1
in2
in3
in4
in5
in6
in7
in8

## Slide 74: Parity Circuits (2)
Tree structure
T = log2n  The tree structure is faster.
When inverting the output, parity circuit is obtained.
in1
in2
in3
in4
in5
in6
in7
in8
odd

## Slide 75: Parity Circuit in Verilog
module parity_using_function (
data_in , parity_out);
output parity_out ;
input [31:0] data_in;
wire parity_out ;
function parity;
input [31:0] data;
integer i;
begin parity = 0;
for (i = 0; i < 32; i = i + 1)
begin parity = parity ^ data[i];
end
end
endfunction
always @ (data_in)
begin
parity_out = parity(data_in); end
endmodule
module parity_using_reduction (data_in , parity_out );
output parity_out ;
input [31:0] data_in ;
assign parity_out = ^data_in; endmodule

## Slide 76: Propagation and Contamination Delay
Combinational logic is characterized by its propagation delay and contamination delay.
The propagation delay tpd is the maximum time from when an input changes until the output or outputs reach their final value.
The contamination delay tcd is the minimum time from when an input changes until any output starts to change its value (reaction time).
a
y
tcd
tpd
a
y

## Slide 77: Critical Path
a=10
b=1
c=0
d=1
n1
n2
y=10
delay
a
n1
n2
y
time
Critical Path
Short Path

## Slide 78: Short Path
The causes of delay in circuits include the time required to charge the capacitance in a circuit and the speed of light.
  tpd and tcd may be different for many reasons, including different
  rising and falling delays
  multiple inputs and outputs, some of which are faster than others
  circuits slowing down when hot and speeding up when cold
a=1
b=1
c=0
d=10
n1
n2
y=10
delay
d
y
time