## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Finite States Machines (FSM)

## Slide 4: Concepts of Abstract Automata
The abstract automaton (sequential machine or state machine) is given by means of the following five sets:
А = { X, Y, S,  , }, where Х = {X1, X2 . . . XM} – the input alphabet of the automata or a set of input symbols;
  Y = {Y1, Y2 . . . YN} – the output alphabet of the automata or a set of output symbols;
  S = {S0, S1 . . . SK-1} – the alphabet or set of internal states of automata;
   – next state (transition) function,  - output function.
  Finite-state machine (FSM) – if X, Y, S sets are finite (or counting).
  The automata functions in discrete points of time t = 0, 1, 2 . . .n

## Slide 5: Concepts of Abstract Automata (2)
In each point of time the automaton stays in one of states belonging to set S.
S0 – initial state of automaton (at the time t = 0).
Next state function  can be written as follows:
  St+1 = (St, Xt ) or : SX  S;
   - direct Cartesian products SX into S.
Output function  defines the output of automaton in each point of time.
There are two models of automaton – Mealy and Moore models. They differ in output function, which is defined in the following way:
  Yt =  (St , Xt) - for Mealy automaton, or : SXY.
  Yt =  (St) - for Moore automaton.
The state is a memory of automaton about the previous input actions (history of inputs).

## Slide 6: Concepts of Abstract Automata (3)
Abstract automaton has 1 input and 1 output.
Transforms input sequences into output sequences.
  Lengths of input and output words are identical
  Identical initial parts of input words correspond to identical initial parts of output words
Automaton example - serial adder.
To the input of the machine comes with the same name bits ai and bi of both terms A and B, the bit of sum Si is formed on the output. The serial adder is automaton – it should remember, if there was or there was no carry from i-1 the bit.

## Slide 7: Concepts of Abstract Automata (4)
X = {00, 01, 10, 11};
Y = {0,1};
S = {0,1};
0 – absence of carry, 1 – presence of carry.
A
X
{00,01,10,11}
Y
{0,1}
0
1
01/1
10/1
11/0
00/1
11/1
10/0
01/0
00/0
Mealy FSM
+ 0 1 1 0 1 1 1 0
1 0 1 0 0 1 0 1
10 0 0 1 0 0 1 1
S X | 00 | 01 | 10 | 11
0 | 0/0 | 0/1 | 0/1 | 1/0
1 | 0/1 | 1/0 | 1/0 | 1/1

## Slide 8: Serial Adder (Moore FSM)
S1/0
S0/0
S2/1
S3/1
00
11
01
10
01
10
00
11
00
11
11
01
10
01
10
00
Output | X S | 00 | 01 | 10 | 11
0 | S0 | S0 | S2 | S2 | S1
0 | S1 | S2 | S1 | S1 | S3
1 | S2 | S0 | S0 | S0 | S1
1 | S3 | S2 | S1 | S1 | S3

## Slide 9: Representation of FSM (2)
Moore FSM
Output | X S | X1 | X2 | . . . | XM
(S0) | S0 | (S0 ,X1) | (S0 ,X1) |  | (S0,XM)
(S1) | S1 | (S1 ,X1) | (S1, X2) |  | (S1,XM)
(SK-1) | SK-1 | (SK-1,X1) | (SK-1, X2) |  | (SK-1, XM)

## Slide 10: Representation of FSM
State Transition Table
Mealy FSM
S X | X1 | X2 | … | XM
S0 | (S0,X1)/(S0,X1) | (S0,X2)/(S0,X2) |  | (S0,XM)/(S0,XM)
S1 | (S1,X1)/(S1,X1) | (S1,X1)/(S1,X1) |  | (S1,XM)/(S1,XM)
… |  |  |  | 
SK-1 | (SK-1,X1)/(SK-1,X1) | (SK-1,X1)/(SK-1,X1) |  | (SK-1,X1)/(SK-1,X1)

## Slide 11: Representation of FSM. State Transition Graph (STG)
Mealy FSM
X = {X1, X 2, X3 }; Y = { Y1, Y2, Y3, Y4 };
S = {S0, S1, S2, S3, S4}
S3
X2/Y4
X1/Y2
X2/Y3
X1/Y1
X3/Y1
X2/Y2
X3/Y1
S0
S1
S33
S4
X2/Y4
X1/Y1
X3/Y3
X3/Y1
X1/Y2
X1/Y2
X2/Y4
X3/Y2
S2

## Slide 12: Moore FSM
X = {X1, X2}; Y = {Y1,Y2}; S = {S0,S1,S2}
X1
X2
S0/Y1
S1/Y2
S2/Y1
X2
X1
X1
X2

## Slide 13: Examples of FSM
Example 1
Design STG of detector of input sequence of zeros and ones. If a sequence from 4 ones is given to the input, “1” appears in the output in FSM. In all other cases, the output equals “0”.
X = {0, 1}; Y = {0, 1}.
The set of states, transition function and output function are defined at designing a graph.

## Slide 14: Example
S0 – the last input symbol was 0
S1 – got one 1
S2 – got two 1s
S3 - got three 1s (repeatedly)
1/1
0/0
0/0
0/0
0/0
1/0
1/0
1/0
S0
S1
S2
S3

## Slide 15: Example (2)
Develop state diagram of linear (sequential) adder.
The same bits of consecutive augends A and addend B
come to the input FSM serially: first, for example ai, then bi.
Input sequence: a0 b0 a1b1…ai bi …anbn
Output sequence: - c0 – c1 – c2 - … - cn
“-” means that output don’t care
S1
S0
S2
S3
S4
0/-
1/-
0/0
1/1
0/1
1/0
0/-
1/-
0/0
1/1
X = {0,1}; Y = {0,1}; S = {S0,S1,S2,S3,S4}.

## Slide 16: Extended Transition and Output Functions
Let А={X,Y, S, s0, , } – FSM
Let X - the alphabet (finite set of symbols)
X* - chain of input symbols (input words) from X.  - empty chain. =xi,x2,.. xpX* Y* - multitude of chain of input symbols
Extended transition and output functions of FSM are called *: SX* S and *: SX* Y* functions, defined as follows:
*(si , )=si; *(si ,xmxp)=*((si,xm),xp);
*(si,  )= ; *(si,xmxn)={*(si,xm), *((si,xm), xn)},
The extended output function is a reaction of FSM under the given input sequence.

## Slide 17: Incompletely specified FSM
Complete specified FSM - if the output function and transition function are completely defined.
  For any pair of “state – input symbol” the next state is defined
  For any pair of “state - input symbol” the output symbol is defined (Mealy FSM). For every state there is output signal (Moore FSM).
Otherwise FSM is called incomplete specified.
As a result:
Next state functions and output functions have “don’t care” values.
Don’t cares arise when some combinations are of no interest: they will not occur or their output will not observe.
For these, the next state or output functions may not be specified.
At the implementation level, only one of the possible next states and outputs in chosen (complete specification).

## Slide 18: Non-Determinate FSM
Non-determinism is associated with many transitions:
  From a given current state and under the same input conditions it is possible to go to different states and have different outputs.
S0
S1
S2
xi/0
xi/1

## Slide 19: Reaction and Equivalence of FSM
The state Si S is called reachable if (X*) *(S0, )=Si, and unreachable when (Si)  (X*)*(S0, ) Si.
Definition. Two FSMs А and В with identical input alphabets are called equivalent if after setting them into their initial states their reactions to any identical input sequences coincides.
Condition of equivalence is the following:
Input alphabets of FSM coincide XA = XB = X
Implemented mapping coincides:
(X*) A*(s0A, )= B*(s0B, )

## Slide 20: Direct Product of FSM
A and B FSMs are given.
A={X,YA, SA, A ,A) , B={X,YB, SB, B ,  B) .
Direct product АB is called the FSM, defined as follows:
AB = {X, YAYB,SA SB,(s0A,s0B), AB,AB}, where
(sASA)(sBSB)(xX) AB((sA,sB),x)=(A(sA,x), B(sB,x))
(sASA)(sBSB)(xX) AB((sA,sB),x)=(A(sA,x),B(sB,x))

## Slide 21: Product of FSM
А
B
YA
YB
X
AB
Direct product of FSM – two non-interacting FSMs, operating in the same common input.

## Slide 22: Equivalence of FSM (Production of FSM)
Moore theorem:
Two FSMs A = {X, YA, SA, A ,A} and B = {X, YB, SB, B ,B}
with identical input alphabets are equivalent only when for any reachable state (sA,sB) of FSM production АB, the following is carried out:(xX)A(sA,x)= B(sB,x).
For every state in A there is a corresponding equivalent state in B and vice versa.
Theorem: The equivalence partition is unique.

## Slide 23: Example
(a)
(б)
x2/1
q0
q1
q2
x1/1
x2/0
x1/0
x2/0
x1/1
s0
s1
x2/0
x1/1
x1/0
x2/1
FSM A
FSM B
Given FSMA and FSMB. Define direct product AB.

## Slide 24: Direct production of FSM: AxB
q0,s0
q1,s1
q2,s0
q0,s1
q1,s0
q2,s1
x1/(1,1)
x2/(0,0)
x2/(0,0)
x1/(1,0)
x2/(1,1)
x2/(0,1)
x1/(1,1)
x2/(1,0)
x1/(1,0)
x1/(0,0)
x2/(0,1)
x1/(0,1)
FSMs A and B are not equivalent

## Slide 25: FSM Equivalence Checking (Product of FSMs)
The FSMs are equivalent if for all inputs their outputs are identical on all reachable state pairs.
A
YA
YB
X
AB
B
If A = B then the output is always zero

## Slide 26: Interrelation between Mealy and Moore Models
Transformation of Moore FSM to Mealy FSM
FSM reaction to the input sequence  = X1X2X2X1X1X2
Si/Yj
Xs
Si
Sk
Xs/Yp
X2
S0 Y1
S1 Y2
S3 Y3
X1
X2
X1
X2
X1
X1
S2Y2
X2/Y2
S0
S1
S2
S3
X1/Y2
X1/Y3
X2/Y3
X2/Y3
X1/Y2
X1/Y1
X2/Y2
X2
Sk/Yp

## Slide 27: Transformation of Moore FSM to Mealy FSM
Moore FSM
X1 X2 X2 X1 X1 X2
S0 S1 S1 S1 S3 S2 S3
ω1= Y1 Y2 Y2 Y2 Y3 Y2 Y3
Mealy FSM
X1 X2 X2 X1 X1 X2
S0 S1 S1 S1 S3 S2 S3
ω2 = Y2 Y2 Y2 Y3 Y2 Y2

## Slide 28: Transformation of Mealy FSM to Moore FSM
In the shown fragment Si state is split into two states – Si1 and Si2. All the transitions from Si state must be saved for Si1 and Si2 states of equivalent FSM.
Xr
Sj
Yk
Si2Ym
Si1Yp
Xk
Xi
Xi
XS
Xk/Yp
Xr/Ym
Xj/Yk
XS/YP
Si
Sj
Xr
Sj
Yk
Si2Ym
Si1Yp
Xk
Xi
Xi
XS
Xk/Yp
Xr/Ym
Xj/Yk
XS/YP
Si
Sj

## Slide 29: Example
Transformation of Mealy FSM to Moore FSM
X1/Y2
S0
S1
S2
S3
X1/Y1
X2/Y2
X2/Y1
X2/Y4
X2/Y2
X1/Y1
X1/Y3
S22Y4
X2
S0 Y1
S12Y3
S3 Y2
S11Y2
S21Y1
S23Y2
X1
X2
X1
X2
X1
X1
X2
X1
X1
X2
X2
X2
X2

## Slide 30: Reaction of FSM
Reaction of both FSMs, being in their initial states, to the input sequence X1 X2 X1 X1 X2 X2 X2 X1.
Mealy:
X1 X2 X1 X1 X2 X2 X2 X1
S0 S0 S1 S2 S1 S2 S3 S0 S0 1 = Y1 Y2 Y1 Y3 Y4 Y2 Y1 Y1
Moore:
X1 X2 X1 X1 X2 X2 X2 X1
S0 S0 S11 S21 S12 S22 S3 S0 S0 2 = Y1 Y1 Y2 Y1 Y3 Y4 Y2 Y1 Y1
Reactions coincide (1=2).
The output sequence of Moore FSM is late on one clock from output sequence of Mealy FSM. The number of its states does not change, whereas at transition from Mealy FSM to Moore FSM, as a rule, increases.

## Slide 31: State Minimization: Completely Specified Machine
FSM may contain redundant states, i.e. states whose function can be accomplished by other states.
State minimization is the transformation of a given machine into an equivalent machine with no redundant states.
Minimization task is in partitioning of set of states into classes of equivalent states and replace of each class by one state.
Two states Si and Sj are 1-equivalent if and only if (XkX) (Si,Xk)=(Sj,Xk).
Two states Si and Sj are k-equivalent if *(Si,k)= *(Sj,k) for any kX*.
Two states Si and Sj are equivalent (or compatible) if *(Si, ) = *(Sj, ), for any X* ( Si  Sj).

## Slide 32: State Minimization
States Si and Sj are k-equivalent if and only if they are 1-equivalent and (XpX) (Si,Xp) and (Sj,Xp) are (k-1) -equivalent.
Two states, Sk and Sp of FSM are distinguishable if and only if there exists a finite input sequence which when applied to M causes different output sequences depending on whether M started in Sk or Sp.
States Si and Sj are said to be equivalent (Si  Sj) if no distinguishing sequence exists for Si and Sj.
If any states are k-equivalent so they belong to the same k-1 class of equivalency.

## Slide 33: Example
S0
S2
S1
S3
1/0
0/1
1/0
1/0
1/0
0/1
0/0
0/1
Given FSM
A1
B1
A1
A1
X S | 0 | 1
S0 | S1/1 | S2/0
S1 | S3/0 | S2/0
S2 | S1/1 | S0/0
S3 | S2/1 | S0/0
The states of FSM in serial are partitioned into 1-, 2- … k-,(k+1)
- classes of state equivalence.
Partitions: Po, P1,…, Pk+1. P0 = {S0,S1,S2,S3}; P1= {A1,B1}. A1={S0,S2,S3}; B1={S1}.

## Slide 34: Example (2)
A1
B1
P2={A2,B2,C2}; A2={S0,S2}; B2={S3}; C2={S1}.
A2
C2
A2
A2
B2
C2
A3
A3
B3
C3
B2
P3={A3,B3,C3}; A3={S0,S2}; B3={S3}; C3={S1}.
P2=P3=PFin; S0S2; replace S0 and S2 by S02
X S | 0 | 1
S0 | B1 | A1
S2 | B1 | A1
S3 | A1 | A1
S1 | - | -
X S | 0 | 1
S0 | B2 | A2
S2 | B2 | A2
S3 | A2 | A2
S1 | - | -

## Slide 35: Example (3)
S02
S1
S3
1/0
1/0
0/1
0/0
1/0
0/1
State diagram corresponding to reduced FSM

## Slide 36: Equivalence Checking
A0
A2
A1
A3
1/0
0/1
1/0
1/0
1/0
0/1
0/0
0/1
B0
B1
B2
1/0
1/0
0/1
0/0
1/0
0/1
Determine AB
FSM A – original FSM
FSM B – reduced FSM

## Slide 37: Production of FSM
FSMs are equivalent, since for any transitions under the action of the same inputs their outputs are identical
A0B0
0/(1,1)
A1B1
A2B0
1/(0,0)
A3B2
0/(1,1)
1/(0,0)
0/(1,1)
1/(0,0)
0/(1,1)
1/(0,0)

## Slide 38: Design of FSM
Understand the problem
Create formal definition as state diagram or state table
Simplify the design by state minimization
Make structural synthesis.