## Slide 1: Logic Design
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2: Course Overview
Boolean Functions
  3 lectures
Boolean Functions Minimization. Combinational Logic Design Principles
  4 lectures
Introduction to Verilog
  3 lectures
Basic Combinational Circuits
  4 lectures
Finite States Machines (FSM)
  3 lectures
Synthesis of Synchronous FSM
  5 lectures
Basic Sequential Circuits
  3 lectures
Problems of Synchronous Design
  3 lectures
Asynchronous FSM. Self-Timed Circuits
  3 lectures
Arithmetic Units
  4 lectures
Programmable Logical Integrated Circuits (PLDs)
  3 lectures
Memory Devices
  3 lectures
Notes: 2

## Slide 3: Basic Sequential Circuits of Synchronous FSM

## Slide 4: Registers
Register - a circuit that is used to store the data word.
n-bit register consists of n flip-flops or latches with common control .
D0
D1
D2
D3
CLK
CLR
Q0
Q1
Q2
Q3
Q0
Q1
Q2
Q3
CLK
CLR
D0
D1
D2
D3
D
D
D
D

## Slide 5: Verilog Description for a Positive-Edge Triggered D Flip-flops
module register(clk, data, reset, q);
input clk, reset;
input [3:0] data;
output reg [3:0] q;
always @(posedge clk or negedge reset)
if (!reset)
q<= 0;
else q<=data;
endmodule

## Slide 6: Edge-Triggered Register with Active-Low Clock-Enable Input
CLK
EN
D0
D1
D2
D3
D4
D5
D6
D7
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Truth Table
EN | D0 … D7 | CLK | Q0 …Q7
1 | x x … x | x | Q0last … Q7last
0 | D0 … D7 |  | D0 …D7
0 | x x ... x | 0 | Q0last … Q7last
0 | x x ... x | 1 | Q0last … Q7last

## Slide 7: Verilog Description of Register with Active-low Clock-Enable Input
module register(clk, data, en, q);
input clk,en;
input [7:0] data;
output reg [7:0] q;
always @(posedge clk )
if (!en)
q<= data;
else q<=q;
endmodule

## Slide 8: 16-bit Register with Clock-Enable and Output-Enable
CE
OE
D0
D1
D2
D3
D4
D5
D6
D7
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Q0
Q1
Q15
D0
D15
D
D
D
D1
C
OE
>
!i_Q0
!i_Q1
!i_Q15
>
> Clk
>
CE
En
En
En

## Slide 9: Description for 16-bit Register with Clock-Enable and Output-Enable
module reg_16(clk, clk_en, oe, reset, data,q);
input clk, clk_en, oe, reset;
input [0:15] data;
output [0:15] q;
reg [0:15] inter_q;
always @(posedge clk or negedge reset)
if(reset==0) inter_q<=16’b0;
else if (clk_en==1) inter_q<=data;
else inter_q<=inter_q;
assign q = (oe==0)? inter_q: 16’bz;
endmodule
module reg_16( input logic clk, clk_en, oe, reset, input logic [0:15] data, output logic [0:15] q);
logic[0:15] inter_q;
always_ ff(posedge clk, negedge reset)
if (!reset) inter_q<=0;
else if (clk_en) inter_q<=data;
assign q= !oe? inter_q:16’bz;
endmodule
SystemVerilog
Verilog

## Slide 10: 8-bit Latch (IC 74x373)
C
OE
D0
D1
D2
D3
D4
D5
D6
D7
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Q0
Q1
Q7
D0
D7
D
D
D
D1
C
OE
C
C
C
!i_Q0
!i_Q1
!i_Q7

## Slide 11: Verilog Module for 8-bit Latch
module Latch_8(clk, oe, data,q);
input clk, oe;
input [0:7] data;
output [0:7] q;
reg [0:7] i_q; //internal signal vector
always @(clk or data)
if(clk==1) i_q<=data;
else i_q<=i_q;
assign q = (oe==0)? i_q : 8’bz;
endmodule
module latch_8( input logic clk,oe, input logic [0:7] data,
output logic[0:7] q);
logic[0:7] i_q;
always_latch
if (clk) i_q <= data;
assign q=(oe==0)?i_q:8’bz;
endmodule
SystemVerilog
Verilog

## Slide 12: Counters
Classification of counters:
  Binary, based on shift registers, binary-coded decimal, with random numeration.
According to count direction:
  Up counters
  Down counters
  Up/Down counters
According to the way to form carry:
  Ripple (sequential) carry
  Parallel carry
According to FSM type:
  Asynchronous
  Synchronous.

## Slide 13: Asynchronous Counters
Input
Down count
Up count
J
C
K
“1”
“1”
“1”
“1”
Input
J
C
K
J
C
K
J
C
K
D
D
D
D
UP | DOWN
0000 | 0000
0001 | 1111
0010 | 1110
0011 | 1101
0100 | 1100
0101 | 1011
0110 | 1010
0111 | 1001
1000 | 1000
1001 | 0111
1010 | 0110
1011 | 0101
1100 | 0100
1101 | 0011
1110 | 0010
1111 | 0001

## Slide 14: Asynchronous Counters
The worst case - the carry propagates to all bits (from the lowest to the highest bit).
t  n, where  - time of FF switching.
Maximum frequency of input pulses is limited by possibilities of FF of the lowest bit as all the following bits are switched by lower frequencies.
Advantage:
  Simplicity of the circuit
Disadvantages:
  Relatively low performance
  Occurrence of false states because of delays of FF switching in transition processes.

## Slide 15: Asynchronous Modulo 8 Up-Down Counter
q2
Input
Down_Count
Up_Count
D
D
D
Reset
q0
q1
D flip-flops are used as a T flip-flops

## Slide 16: N-bit Binary Counter based on Adder
The counter consists of an n-bit adder and a register. On each cycle, the counter adds 1 to the value stored
in the register.
n
RG
“1”
CLK
Reset
n
+

## Slide 17: Parallel Up Counter Design
Design a circuit of 3-bit counter using T flip-flops.
Table of transitions of the counter
q2q1 q0 | t2 t1 t0
0 0 0 | 0 0 1
0 0 1 | 0 1 1
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 0 0 1
1 0 1 | 0 1 1
1 1 0 | 0 0 1
1 1 1 | 1 1 1
Transition | T
0  0 | 0
0  1 | 1
1  0 | 1
1  1 | 0
0
2
1
3
5
6
4
7

## Slide 18: Parallel Up Counter Design (2)
Define the excitation functions with the help of Karnaugh maps.
t0 = 1
t1 = q0
t2 = q1q0
00
01
11
10
0
1
1
1
q1q0
q2
q2
00
01
11
10
0
1
1
1
1
1
q1q0

## Slide 19: Parallel Counter Design (3)
F – frequency of clock signals. Counter – frequency divider.
Low bit (q0) - F/2, q1 – F/4, q2 – F/8.
T
C
T
C
T
C
q2
q1
q0
“1”
Clk
F
F/2
F/4
F/8
20
21
22
Reset
t0
t1
t2

## Slide 20: Timing Diagram of Counter
1
2
3
4
5
6
7
8
clock
q0
q1
q2

## Slide 21: Parallel Down Counter Design
Design a circuit of 3-bit counter using T flip-flops.
Table of transitions of the counter
q2q1 q0 | t2 t1 t0
0 0 0 | 1 1 1
1 1 1 | 0 0 1
1 1 0 | 0 1 1
1 0 1 | 0 0 1
1 0 0 | 1 1 1
0 1 1 | 0 0 1
0 1 0 | 0 1 1
0 0 1 | 0 0 1
Transition | T
0  0 | 0
0  1 | 1
1  0 | 1
1  1 | 0
0
6
7
5
3
2
4
1

## Slide 22: Parallel Down Counter Design (2)
Define the excitation functions with the help of Karnaugh maps.
t1 = ~q0
t2 = ~q1~q0
00
01
11
10
0
1
1
1
q1q0
q2
q2
00
01
11
10
0
1
1
1
1
q1q0
1
t0 = 1

## Slide 23: Down Counter Module 8
>
>
>
q0
q1
q2
t0
clk
J
K
J
K
J
K
t1
t2
“1”
reset

## Slide 24: 4-Bit Counter with Parallel Carry and Count Enable
CNTEN – Count Enable
J
C
K
J
C
K
J
C
K
J
C
K
CNTEN
CLOCK
20
21
23
22
reset

## Slide 25: Counter Description by Verilog (Behavioral)
Verilog
module count_en (q, cnten, reset, clock);
parameter size = 8;
input cnten, reset, clock;
output reg [size-1:0] q; always @(posedge clock or negedge reset)
if (!reset)
q< = 0;
else if(cnten)
q<=q+1;
endmodule
SystemVerilog
module count_en #(parameter n=8)
(input logic cnten, input logic reset,
input logic clk, output logic [n-1:0] q);
always_ff @(posedge clk or negedge reset)
if (!reset)
q< = 0;
else if(cnten)
q<=q+1;
endmodule

## Slide 26: Counter with Asynchronous Load
Parallel 3-bit counter operates in loading mode if Load =0. Loading is asynchronous.
~Load
D0
D1
D2
J
K
C
J
K
C
J
K
C
“1”
PRE
PRE
PRE
CLR
CLR
CLR
Clk

## Slide 27: Counter with Asynchronous Load in Verilog
module counter (q, data, load, clk);
parameter size = 8;
input load, clk;
input [size-1:0] data;
output reg [size-1:0] q;
always @(negedge clk or negedge load)
if (!load)
q <= data;
else q<=q+1;
endmodule

## Slide 28: IC 74x193
Up/Down Counter with Modulo 16
CPd
Load
D0
D1
D2
D3
Reset
Q0
Q1
Q2
Q3
CPu
TCu
TCd
R | ~Load | CPu | CPd | D0…D3 | Mode
1 | x | x | x | x | Asynch. reset
0 | 0 | x | x | D0…D3 | Asynch. Load
0 | 1 |  | 1 | x | Up count
0 | 1 | 1 |  | x | Down count

## Slide 29: IC 74x193 (2)
12-bit Up/Down counter (modulo 4096)
Load
CPd
Load
D0
D1
D2
D3
Reset
Q0
Q1
Q2
Q3
CPu
TCu
TCd
CPd
Load
D0
D1
D2
D3
Reset
Q0
Q1
Q2
Q3
CPu
TCu
TCd
CPd
Load
D0
D1
D2
D3
Reset
Q0
Q1
Q2
Q3
CPu
TCu
TCd
Reset

## Slide 30: Decoding Binary Counter States
The decoder outputs may contain “glitches” on state transitions where two or more counter bits change.
The counter outputs don’t change in exactly the same time.
Multiple signal paths in a decoder have different delays.
CPd
Load
D0
D1
D2
D3
Reset
Q0
Q1
Q2
Q3
CPu
TCu
TCd
20 Y0
21 Y1
22 Y2
Y3
Y4
Y5
Y6
Y7
“1”
Clock
E0
E1
E2
“1”
“0”

## Slide 31: A Modulo-8 Binary Counter and Decoder with Glitch-Free Outputs
Decoder outputs have been renamed to account for the 1-tick delay through the register
CPd
Load
D0
D1
D2
D3
Reset
Q0
Q1
Q2
Q3
CPu
TCu
TCd
20 Y0
21 Y1
22 Y2
Y3
Y4
Y5
Y6
Y7
“1”
Clock
E0
E1
E2
“1”
“0”
Clk
OE
D0 Q0
D1 Q1
D2 Q2
D3 Q3
D4 Q4
D5 Q5
D6 Q6
D7 Q7
S0
S1
S2
S3
S4
S5
S6
S7
RS7
RS6
RS5
RS4
RS3
RS2
RS1
RS0

## Slide 32: Shift Registers
D
C
D
C
D
C
D
C
SERIN
Clock
Output
Serial Input
SERIN = 0
Shift register is n-bit register the content of which can be shifted into several bit. Shift right register (by one bit)
Cycle | q1 q2 q3 q4
0 | 1 1 0 1
1 | 0 1 1 0
2 | 0 0 1 1
3 | 0 0 0 1
4 | 0 0 0 0
Cycle | q1 q2 q3 q4 | Output
0 | 1 1 0 1 | 
1 | 0 1 1 0 | 1
2 | 0 0 1 1 | 0
3 | 0 0 0 1 | 1
4 | 0 0 0 0 | 1
Serial Output

## Slide 33: Shift Left Register
Shift Left Register ( by one bit)
Serial input DL=1
Clock
DL
Input
D
C
D
C
D
C
D
C
Output
Cycle | q1 q2 q3 q4
0 | 1 0 1 0
1 | 0 1 0 1
2 | 1 0 1 1
3 | 0 1 1 1
4 | 1 1 1 1

## Slide 34: Shift Left and Shift Right Register
D
q1
D
q2
D1
q3
Shift Right
Shift Left
Clk
Rin
Lin
q3

## Slide 35: 4-bit Universal Shift Register (74x194)
S1
S0
RIN
D0
D1
D2
D3
LIN
CL
R
Q0
Q1
Q2
Q3
Truth Table
R | S1S0 | RIN | D3D2D1D0 | LIN | CLK | Q3Q2Q1Q0
0 1 1 1 1 1 1 | x x 0 0 0 1 0 1 1 0 1 0 1 1 | x x 0 1 x x x | x x x x x x x x x x x x x x x x x x x x x x x x D3D2D1D0 | x x x x 0 1 x | x       | 0 0 0 0 Qlast 0 Q3Q2Q1 1Q3Q2Q1 Q2Q1Q0 0 Q2Q1Q0 1 D3D2D1D0

## Slide 36: Verilog Description
module shift_reg(data,rin, lin, s,q,clock, reset);
input clock,reset, rin, lin;
input [1:0] s;
input [3:0] data;
output [3:0] q;
reg [3:0] q;
always @(posedge clock or negedge reset)
begin
if (!reset) q<=4’b0;
else
case(s)
2’b00: q<=q;
2’b01: q<={rin,q[3:1]};
2’b10: q<={q[2:0,lin};
2’b11: q<=data;
default: q<=4’b0;
endcase
end
endmodule

## Slide 37: Shift Operations
0
0
0
Logical shift right
Logical shift left
Arithmetical shift right
Arithmetical shift left

## Slide 38: Shift Operations (2)
Cyclic shift left
Cyclic shift right

## Slide 39: Logical Shift
a=1100_1010
0110_0101 logic shift right by 1 bit a <= a>>1;
1100_1010
0011_0010 logic shift right by 2 bit a <= a>>2;
1100_1010
0000_1100 logic shift right by 4 bit a <= a>>4;
a=1100_1010
1001_0100 logic shift left by 1 bit a <= a<<1;
1100_1010
0010_1000 logic shift left by 2 bit a <= a<<2;
1100_1010
1010_0000 logic shift left by 4 bit a <= a<<4;

## Slide 40: Arithmetical Shift to the Right
0101_1011_0100; arithmetical shift by 1 bit
0010_1101_1010;
1011_1100_0100;
11011_1100_010; a<={a[11],a[11:1]};
-10000111100
-01000011110
010110110100; arithmetical shift by3 bit
000010110110;
101111000100;
111101111000; a<={a[11],a[11],a[11],a[11:3]};
a <={3{a[11]},a[11:3]};

## Slide 41: Cyclical Shift
a=0101_1011_0100; cyclic shift right by 1 bit
0010_1101_1010; a<={a[0],a[11:1]};
cyclic shift right by 2 bits
a=101111000101; a<={a[1:0],a[11:2]};
011011110001;
0101_1011_0100; cyclic shift left by 1 bit
0010_1101_1010; a<={a[10:0],a[11]};
cyclic shift left by 4 bits
101111000101; a<={a[7:0],a[11:8]};
110001011011;

## Slide 42: Combinational Shifters
1
0
1
0
1
0
1
0
q3
q2
q1
q0
0
y3
y2
y1
y0
Shift
1
0
1
0
1
0
1
0
q3
q2
q1
q0
0
y3
y2
y1
y0
Shift
Shift Left by one bit
Shift Right by one bit

## Slide 43: Barrel Shifter
Barrel shifter – combinational logic circuit with n data inputs, n data outputs and [log2n] control inputs. The output word equals the input word, rotated by a number of bit positions specified by the control bits.
Barrel
Shifter
q3
q2
q1
q0
y3
y2
y1
y0
s1
s0
S1 S0 | y3 y2 y1 y0
0 0 | q3 q2 q1 q0
0 1 | q0 q3 q2 q1
1 0 | q1 q0 q3 q2
1 1 | q2 q1 q0 q3

## Slide 44: Barrel Shifter (2)
RG
q3
q2
q1
q0
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
y3
y2
y1
y0
d3
d2
d1
d0
S1 S0
M3
M2
M1
M0
module barrel_shifter(X,S,Y);
input [15:0] X;
input [3:0] S;
output [15:0] Y;
wire [15:0] T;
assign {T,Y} = {X,X} >>S;
endmodule
Verilog Description (16 bit)
1011
1101
1110
0111
1
0
1
1
1 1
0
1
1
1
1 0

## Slide 45: Combinational Shift
Logical Shift to the Left (barrel shifter)
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
y3
y2
y1
y0
S1 S0
MUX0
MUX1
MUX2
MUX3
x3
x2
x1
x0

## Slide 46: Combinational Shift
Logical Shift to the Right (Barrel shifter)
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
y3
y2
y1
y0
S1 S0
MUX0
MUX1
MUX2
MUX3
x3
x2
x1
x0

## Slide 47: Combinational Shift
Arithmetical Shift to the Right
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
y3
y2
y1
y0
MUX0
MUX1
MUX2
MUX3
X3 (Sign)
x2
x1
x0
S1
S0

## Slide 48: Counters Based on Shift Registers (Ring Counter)
D
C
D
C
D
C
D
C
Clock
Preset
q1
q2
q3
q4
S0
S1
S2
S3
“1”
“1”
“1”
“1”
 | q1q2q3q4
S0 S1 S2 S3 S0 | 1 0 0 0 0 1 0 0 0 0 1 0 0 0 0 1 1 0 0 0
For state decoding, additional circuits are not required

## Slide 49: Johnson’s Counter
Reset
D
C
D
C
D
C
D
C
Clock
q1
q2
q3
q4
~q4
S | q1q2q3q4
S0 | 0 0 0 0
S1 | 1 0 0 0
S2 | 1 1 0 0
S3 | 1 1 1 0
S4 | 1 1 1 1
S5 | 0 1 1 1
S6 | 0 0 1 1
S7 | 0 0 0 1

## Slide 50: State Decoding of Johnson’s Counter
Number of states of n-bit Johnson’s counter - 2n. To design a counter with odd number of states it is enough to add one gate.
S0 = ~q1~q4; S1 = q1~q2; S2 = q2~q3; S3 = q3~q4; S4 = q1q4; S5 = ~q1q2; S6 = ~q2q3; S7 = ~q3q4;
module Johnson_cnt(clk,reset,q);
parameter n=16;
input clk,reset;
output reg [n-1:0] q;
always @(posedge clk)
if(reset)
q<=0;
else q<={~q[0],q[n:1]};
else q<=q;
endmodule
Verilog Description

## Slide 51: Johnson’s Counter with State Decoding
~q4
D
C
D
C
D
C
D
C
Clock
q1
q2
q3
q4
Reset
S0
S1
S2
S3
S4
S5
S6
S7

## Slide 52: Polynomial Counters
Polynomial counters refer to the class of linear state machine (LSM), which are variants of FSMs.
FSM is called linear if its memory is realized on D flip-flops, and excitation functions and the output functions are linear.
LSM makes the base of coding theory.
LSM is often used as a transformer of one polynomial into another.
Used in devices of test diagnosis of digital units to solve mathematical tasks by Monte-Carlo method, as a generator of Galois fields, etc.

## Slide 53: Primitive Polynomials
A polynomial of degree n, that is not divisible by any polynomial of degree less than n but greater than 0, is called irreducible. Any polynomial f (x) that is not divisible by x is a divisor of the polynomial xi – 1 for some integer i. The smallest such positive number i is called the exponent to which the polynomial f (x) belongs. For any n and any prime p, there exists at least one irreducible polynomial of degree n belonging to the exponent pn - 1.
Polynomial d(x) with coefficients in GF(p) is a primitive polynomial if its degree is m and it has a root α in GF(pm) such that {0, 1, α, α2, α3, ..., αp^m−2} is the entire field GF(pm). d()=0;

## Slide 54: Example 2
Galois field GF(24) from 24 elements can be made as a field of polynomials above GF(2) by modulo 1 + x + x4.
Let  be the root of polynomial
1 + x + x4 with extension of Galois field and primitive element.
All 15 non-zero elements of the field are shown in the table.
d(x)=1+x+x4 d()=1+  +  4
1+  +  4=0;  4=1+ 
Representation of GF(24)
0= 1
1= 
2= 2
3= 3
4= 1 + 
5=  + 2
6= 2 + 3
7= 1 +  + 3
8= 1 + 2
9=  + 3
10= 1 +  + 2
11=  + 2 + 3
12= 1 +  + 2 + 3
13= 1 + 2 + 3
14= 1 + 3
15= 1 = 0
14= (1+ 2 + 3)  = 3 +1

## Slide 55: Galois Finite Fields
Finite field with P elements where P is prime, is the set of integers modulo P.
{0,1,2,3,4,5,6} modulo P field (P=7).
30=1; 40=1; 50=1; 20=1; 60=1;
31=3; 41=4; 51=5; 21=2; 61=6;
32=2; 42=2; 52=4; 22=4; 62=1
33=6; 43=1; 53=6; 23=1;
34=4; 54=3;
35=5; 55=1;
Operations on the field - addition and multipication by modulo 7.
Only 3 is a primitive element in modulo
7 field.
0`= | 1 |  |  | 
1`= |  |  |  | 
2`= |  |  | 2 | 
3`= |  |  |  | 3
4`= | 1+ |  | 2 | 
5`= |  | + |  | 3
6`= | 1 |  |  | 
Given d(x) =1+x2+x4;
d()=0;
4=1+ 2; 6=1
d(x) – is non primitive polynomial.
Number of non-zero elements equal 6 (6 = 1)

## Slide 56: Galois LFSR
LFSR circuit is a generator of a sequence of maximum length if a primitive polynomial is in the feedback loop.
This LFSR has 2n-1 states.
d(x) = 1+x +x4
The number of states 24-1 =15
LFSR-counter never goes in a loop through the state 0000. This state is a state of rest. The circuit generates all 2n -1 polynomials modulo the polynomial in the feedback circuit. d(x)= 1+x +x4
CLK
D
C
D
C
D
C
D
C
q0
q1
q2
q3
0
1
2
3
4

## Slide 57: LFSR with Polynomial d(x)=1+x2+x4
CLK
D
C
D
C
D
C
D
C
q0
q1
q2
q3
0
1
2
3
4
1000
0100
0010
0001
1010
0101
1000
The number of states - 6

## Slide 58: Fibonacci LFSR (n=4)
d(x) = 1 + x + x4
d() = 1 +  +  4 =0
4 =1 + 
D
C
D
C
D
C
q0
q1
q2
2
1
0
D
C
Clk
q3
3

## Slide 59: Circuit of Polynomial Counter (Galois LFSR)
The generator of Galois field with primitive polynomial n degree in feedback is the circuit having pn-1 states (if p=2, то 2n-1) .
Primitive polynomial and divider of polynomial x31-1 is d(x) = 1+x2+x5.
5 element corresponds to the one, shifted from the highest bit. The feedback substitutes it with equal element 1+2.
It follows from the fact that  is the root d(x) , i.e. 1+ 2 + 5 =0.
Hence 5 = 1+2.
D
C
D
C
D
C
D
C
D
C
CLK
0
1
2
3
4

## Slide 60: Sequence of States of Polynomial Counter
(q0 q1 q2 q3 q4)
S0 0 = 1 1 0 0 0 0
S1 1 =  0 1 0 0 0
S2 2 = 2 0 0 1 0 0
S3 3 = 3 0 0 0 1 0
S4 4 = 4 0 0 0 0 1
S5 5 = 1 + 2 1 0 1 0 0
S6 6 =  + 3 0 1 0 1 0
S7 7 = 2 + 4 0 0 1 0 1S8 8 = 1 + 2 + 3 1 0 1 1 0
. . .
S30 30 =  + 4 0 1 0 0 1
31 = 0 =1.

## Slide 61: Circuit of Polynomial Counter (Galois LFSR)
The generator of Galois field with primitive polynomial n degree in feedback is the circuit having pn-1 states (if p=2, то 2n-1).
Primitive polynomial and divider of polynomial x31-1 is d(x) = 1+x3+x5.
5 element corresponds to the one, shifted from the highest bit. The feedback substitutes it with equal element 1+3.
It follows from the fact that  is the root d(x) , i.e. 1+ 3 + 5 =0.
Hence 5 = 1+3.
D
C
D
C
D
C
D
C
D
C
CLK
0
1
2
3
4

## Slide 62: Sequence of States of Polynomial Counter
(q0 q1 q2 q3 q4)
S0 0 = 1 1 0 0 0 0
S1 1 =  0 1 0 0 0
S2 2 = 2 0 0 1 0 0
S3 3 = 3 0 0 0 1 0
S4 4 = 4 0 0 0 0 1
S5 5 = 1 + 3 1 0 0 1 0
S6 6 =  + 3 0 1 0 1 0
S7 7 = 2 + 4 0 0 1 0 1
S8 8 = 1 + 2 + 3 1 0 1 1 0
. . .
S30 30 =  + 4 0 1 0 0 1
31 = 0 =1.

## Slide 63: LFSR
Advantage:
Combinational circuit of LFSR is very simple.
Example: the polynomial counter based on 10-bit shift register with feedback polynomial d(x)=1+x7+ x10, has 1023 states
Combinational circuit – only one 2-input XOR gate.
Fibonacci LFSR, Galois LFSR are used.
Applications:
  as generator of pseudorandom numbers (meaning, after some time the same sequence returns).
The mathematics of a cyclic redundancy check (CRC), used to provide a quick check against transmission errors, are closely related to those of an LFSR.
  Uses in cryptography
  Uses as counters

## Slide 64: Fibonacci LFSR (n=5)
CLK
D
C
D
C
D
C
D
C
D
C
q0
q1
q2
q3
q4
d(x) = 1+x2+x5
Other example of LFSR circuit (maximum-length sequence generator)
d(x) = x**153 + x**152 + 1 is a maximum-length LFSR with 2**153 -1 states.

## Slide 65: Feedback Primitive Polynomials
N | Feedback polynomial | Period (2n -1)
2 | x2 + x +1 | 3
3 | x3 + x +1, x3 + x2 +1 | 7
4 | x4 + x3 +1, x4 + x +1 | 15
5 | x5 + x3 +1, x5 + x2 +1 | 31
6 | x6 + x5 +1, x6 + x +1 | 63
8 | x8+ x6 + x5 +x4 + 1 | 255
9 | x9 + x5 +1, x9 + x4 +1 | 511
10 | x10 + x7 +1 | 1023
11 | x11 + x9 +1, x11 + x2 +1 | 2047
12 | x12+ x11 + x10 +x4 + 1 | 4095
13 | x13+ x12 + x11 +x8 + 1 | 8191
N | Feedback polynomial | Period (2n -1)

## Slide 66: Feedback Primitive Polynomials
N | Feedback polynomial | Period (2n -1)
15 | x15+x14+1 | 32 767
17 | x17+x14+1 | 131 071
20 | x20+x17+1 | 1 048 575
21 | x21+x19+1 | 2 097 151
22 | x22+x21+1 | 4 194 303
23 | x23+x18+1 | 8 388 607
24 | x24+x23 +x22 +x17+1 | 16 777 215

## Slide 67: Fibonacci LFSR
module LFSR_Fib(clk, load, data,out);
input clk,load;
input [4:0] data;
output [4:0];
always @(posedge clk, negedge load)
if(load==0)
out<=data;
else out<={q[0]^q[2],q[4:1]};
endmodule
d(x) = 1+x2+x5

## Slide 68: 8-bit LFSRs
CLK
D
D
D
D
D
D
D
D
Galois LFSR
d(x) = 1 + x4 + x5 + x6 + x8. The number of states 255
Fibonacci LFSR
CLK
D
D
D
D
D
D
D
D
Galois LFSR is faster than Fibonacci
0
1
2
3
4
5
6
7

## Slide 69: LFSR in Verilog
module Fibonacci_LFSR(clk, load, en, q, data);
input clk, load, en;
input [7:0] data;
output reg [7:0] q;
always @(posedge clk or posedge load)
begin
if (load) q<=data; //can be anything except zero
else if (en)
q<={q[4]^q[3]^q[2]^q[0], q[7:1]};
end
endmodule

## Slide 70: LFSR in Verilog (2)
module Galois_LFSR(clk, load, en, q, data);
input clk, load, en;
input [0:7] data;
output reg [0:7] q;
always @(posedge clk or posedge load)
begin
if (load) q<=data; //can be anything except zero
else if (en)
q<={q[7],q[0:4], q[7]^q[4],q[7]^q[5],q[6]};
end
endmodule
d(x) = 1 + x5 + x6 + x8.The number of states 255

## Slide 71: LFSR in Verilog (3)
module Galois_LFSR(clk, load, en, q, data);
input clk, load, en;
input [0:7] data;
output reg [0:7] q;
always @(posedge clk or posedge load)
begin
if (load) q<=data; //can be anything except zero
else if (en)
q<={q[7],q[0:2], q[7]^q[3],q[7]^q[4],q[7]^q[5],q[6]};
end
endmodule
d(x) = 1 + x5 + x6 + x8.The number of states 255

## Slide 72: Fibonacci LFSR with Synchronous Load
q0
Clk
D
C
D
C
D
C
q1
D
C
q3
1
0
1
0
1
0
1
0
q2
Data (4bit)
Output
Load