## Slide 1: Static Timing Analysis
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2
CONFIDENTIAL INFORMATION
The information contained in this presentation is the confidential and proprietary information of Synopsys. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Synopsys without prior written authorization.
IMPORTANT NOTICE
In the event information in this presentation reflects Synopsys’ future plans, such plans are as of the date of this presentation and are subject to change. Synopsys is not obligated to update this presentation or develop the products with the features and functionality discussed in this presentation. Additionally, Synopsys’ services and products may only be offered and purchased pursuant to an authorized quote and purchase order or a mutually agreed upon written contract with Synopsys.

## Slide 3: Course Overview
STA Concepts
  1 lecture
Delay Modeling
  1 lecture
Interconnect Parasitics
  1 lecture
Delay Calculation
  1 lecture
Configuring the STA Environment
  1 lecture
Timing Checks
  1 lecture
Crosstalk and Noise
  1 lecture

## Slide 4: 2. Delay Modeling

## Slide 5: Path Delay: Basic Approach
b
a
c
d
e
y
t=1n
t=2n
t=0.5n
tdelay=3.5n

## Slide 6: Delay Dependencies
trise
CL
td
td ~ CL
td ~ trise
td
CL
trise
trise 10ps – 120ps
Cload 10fF – 50 fF

## Slide 7: Path Delay Calculation
b
a
c
d
e
y
t1=f(t2,c1)
t2d
t2e
tfy
t3=f(t2e,c3)
t2=f(t2d,t2c,c2)
C1
C2
C3
ttotal= f(t2a,t2b,t2c,C1,C2,C3)
t2a
t2b
t2c
Specific PVT

## Slide 8: Operating Conditions
Process: TT, FF, SS, etc.
Voltage: ∓10%
Temperature: -40 -1250C
P:SS
V:0.9
T:-40
P:TT
V:1.2
T:125
td ~ Process Variations
td ~ Voltage
td ~ Temperature
trise
CL
td

## Slide 9: Linear Delay Model
Slope Delay ()
  The transition time of the previous gate
Intrinsic Delay ()
  Delay of an element
Transition time ()
  Delay introduced by capacitive load on driving pin
Connect Delay ()
  Delay from transition of the driving pin to endpoint changing after the
Ttransition
B
A
D
C
Tconnect
Tslope
Tintrinsic

## Slide 10: Delay Calculation (Linear) Example
1.2 ns
Cwire= 2.6

## Slide 11: Nonlinear Delay Model
Transition time ()
  Delay introduced by capacitive load on driving pin (measured, not calculated)
Propagation delay ()
  Time from the 50 percent input pin voltage until the gate output just begins to switch (10 percent output voltage) (measured, not calculated)
Connect Delay ()
  Delay from transition of the driving pin (estimated interconnect delay)
Transition time and Propagation delay for each cell are measured beforehand and stored in form of lookup table
  Ttotal = Tpropagation + Ttransition + Tconnect

## Slide 12: Nonlinear Delay Calculation Example
net n1
Ctotal
G1
G2
G3
P
T
T
rise
fall
fall

## Slide 13: Two-dimensional Interpolation
Fall Propagation Delay
Output
Capacitance
Input
Transition
Time
x
y
z
0.20
0.34
0.56
0.72
1.23
10.2
30.8
58.7
99.9
110.1
151.6

## Slide 14: Non Linear Delay Model (NLDM)
cell
_
rise
or
cell
_
fall
table
output cap
Input slew
0
.
7
0
.
5
0
.
2
0
.
1
.
023
.
047
.
065
.
078
.
091
Linear Delay model:
Delay = Intrinsic Delay + Slope_factor * Load(Cap)
0.25 | 0.27 | 0.31 | 0.33 | 0.4
0.26 | 0.28 | 0.29 | 0.31 | 0.35
0.35 | 0.37 | 0.39 | 0.41 | 0.45
0.40 | 0.41 | 0.43 | 0.48 | 0.51
Input slew
Output cap
Delay/Power are measured as function of input slew and output cap

## Slide 15: Composite Current Source Model (CCS)
Network model
C1
C2
The driver model uses a time-varying current source.
The receiver model consists of 2 different capacitors. The first one is used as load up to the input delay threshold. A second capacitance value is used when the input waveform reaches the threshold value.
CCS models are frequently used in advanced technology nodes.

## Slide 16: Synopsys Liberty Format (.lib)
library (Digital_Std_Lib) {
  technology (cmos);
  delay_model : table_lookup;
  cell(AND2) {
  area : 2;
  pin(A) {
  direction : input;
  }
  pin(B) {
  direction : input;
  }
  pin(Z) {
  direction : output;
  function : "A*B";
      timing() {
        related_pin : “A" ;
        timing_type : "combinational" ;
        cell_rise(…) {
index_1("0.016, 0.032, 0.064”);
index_2("2, 4");
        values("1.0020, 1.1280, 3.547 “, \
        "1.0080, 1.1310, 3.847 “ );
        }
        }
      } /* end of pin */
  } /* end of cell */
} /* end of library*/
 |  | trise |  | 
 |  | 0.016 | 0.032 | 0.064
CL | 2 | 1.0020 | 1.1280 | 3.547
 | 4 | 1.0080 | 1.1310 | 1.1310
td
CL
trise
Lookup table
Notes: 16

## Slide 17: Cell Timing Data
cell (INVX1) {
pin (Y) {
timing () {
related_pin : "A";
timing_type : "combinational";
timing_sense : "negative_unate";
cell_rise ("del_1_7_7") {
index_1("0.016, 0.032, 0.064, 0.128, 0.256, 0.512, 1.024");
index_2("0.1, 0.25, 0.5, 1, 2, 4, 8");
values("0.016861, 0.0179019, 0.0195185, 0.0229259, 0.029658, 0.043145, 0.07712", \
"0.0239648, 0.0255491, 0.0279298, 0.0319930, 0.0387540, 0.0520896, 0.0790211", \
"0.0342118, 0.0366966, 0.0402223, 0.0462823, 0.0558327, 0.0705154, 0.0967339", \
"0.0491695, 0.0524727, 0.0576512, 0.0665647, 0.0810999, 0.1027237, 0.1342571", \
"0.0721332, 0.0765389, 0.0836775, 0.0960890, 0.1171612, 0.1497265, 0.1957640", \
"0.1111560, 0.1164417, 0.1252609, 0.1422002, 0.1712097, 0.2171862, 0.2847010", \
"0.1841131, 0.1901881, 0.2010298, 0.2194395, 0.2555983, 0.3182710, 0.4139452");
}
library(){
lu_table_template ("del_1_7_7") {
variable_1 : "input_net_transition";
index_1("1, 2, 3, 4, 5, 6, 7");
variable_2 : "total_output_net_capacitance";
index_2("1, 2, 3, 4, 5, 6, 7");
}

## Slide 18: Cell Types: Sequential Cells
Combinational
  Cell output changes with changes at input
Sequential
  Cell has memory and output depends on memory and input
B
A
C
Output
Data
Reset
Clock
Asynchronous input
Synchronous input
Flip Flop

## Slide 19: Timing Group Names
N | Parameter | Unit | Symbol | Figure | Definition
 | Rise transition time rise_transition | ns | tR |  | The time it takes a driving pin to make a transition from kVDD to (1-k)VDD value. Usually k=0.1 (also possible k=0.2, 0.3, etc)
 | Fall transition time fall_transition | ns | tF |  | The time it takes a driving pin to make a transition from (1‑k)VDD to kVDD value. Usually k=0.1 (also possible k=0.2, 0.3, etc)
 | Propagation delay low-to-high (rise) cell_rise | ns | tPLH (tPR) |  | Time difference between the input signal crossing a 0.5VDD and the output signal crossing its 0.5VDD when the output signal is changing from low to high
4. | Propagation delay high-to-low (Fall) cell_fall | ns | tPHL (tPF) |  | Time difference between the input signal crossing a 0.5VDD and the output signal crossing its 0.5VDD when the output signal is changing from high to low

## Slide 20: Combinational Timing Arc Syntax
Combinational timing arc between input A and output Y, with negative dependence, i.e. When A is rising Y is falling and vice-versa
cell (INVX1) {
pin (Y) {
timing () {
related_pin : "A";
timing_type : "combinational";
timing_sense : "negative_unate";
cell_rise ("del_1_7_7") {
index_1("0.016, 0.032, 0.064, 0.128, 0.256, 0.512, 1.024");
index_2("0.1, 0.25, 0.5, 1, 2, 4, 8");
values("0.0168610, 0.0179019, 0.0195185, 0.0229259, 0.0296588, 0.0431451, 0.0702328", \
"0.0239648, 0.0255491, 0.0279298, 0.0319930, 0.0387540, 0.0520896, 0.0790211", \
"0.0342118, 0.0366966, 0.0402223, 0.0462823, 0.0558327, 0.0705154, 0.0967339", \
"0.0491695, 0.0524727, 0.0576512, 0.0665647, 0.0810999, 0.1027237, 0.1342571", \
"0.0721332, 0.0765389, 0.0836775, 0.0960890, 0.1171612, 0.1497265, 0.1957640", \
"0.1111560, 0.1164417, 0.1252609, 0.1422002, 0.1712097, 0.2171862, 0.2847010", \
"0.1841131, 0.1901881, 0.2010298, 0.2194395, 0.2555983, 0.3182710, 0.4139452");
}

## Slide 21: Delay Analysis
Calculation of each timing arc’s value cell delay or a net delay
  Positive unate timing arc combines rise delays with rise delays and fall delays with fall delays
  Negative unate timing arc combines incoming rise delays with local fall delays and vice versa
  Non-unate timing arc combines local delay with the worst – case incoming delays logic functions whose output value change cannot be predicted
1
1
1
0

## Slide 22: Timing Constraints: Timing Types
N | Parameter | Unit | Symbol | Figure | Definition
1 | Setup time (only for flip-flops or latches) | ns | tSU |  | The minimum period in which the input data to a flip-flop or a latch must be stable before the active edge of the clock occurs
2.. | Hold time (only for flip-flops or latches) | ns | tH |  | The minimum period in which the input data to a flip-flop or a latch must remain stable after the active edge of the clock has occurred
3 | Removal time (only for asynchronous Set or Reset) | ns | tREM |  | The minimum time in which the asynchronous Set or Reset pin to a flip-flop or latch must remain enabled after the active edge of the clock has occurred
4 | Recovery time (only for asynchronous Set or Reset) | ns | tREC |  | The minimum time in which Set or Reset must be held stable after being deasserted before next active edge of the clock occurs
Setup/Hold, Recovery/Removal Constraints
removal_rising,
removal_falling
setup_rising
setup_falling
hold_rising
hold_falling
recovery_rising,
recovery_falling

## Slide 23: Hold Timing Example
pin(D) {
timing () {
timing_type : "hold_rising";
related_pin : "CLK";
rise_constraint ("vio_7_7_1") {
index_1("0.016, 0.032, 0.064, 0.128, 0.256, 0.512, 1.024");
index_2("0.016, 0.032, 0.064, 0.128, 0.256, 0.512, 1.024");
values("-0.011, -0.011, -0.014, -0.013, -0.003, 0.025, 0.097", \
"-0.011, -0.011, -0.015, -0.013, -0.003, 0.028, 0.097", \
...
"-0.015, -0.018, -0.033, -0.063, -0.100, -0.128, -0.228");
}
fall_constraint ("vio_7_7_1") {
...
}
}
}
lu_table_template ("vio_7_7_1") {
variable_1 : "related_pin_transition";
index_1("1, 2, 3, 4, 5, 6, 7");
variable_2 : "constrained_pin_transition";
index_2("1, 2, 3, 4, 5, 6, 7");
}