## Slide 1: Static Timing Analysis
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2
CONFIDENTIAL INFORMATION
The information contained in this presentation is the confidential and proprietary information of Synopsys. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Synopsys without prior written authorization.
IMPORTANT NOTICE
In the event information in this presentation reflects Synopsys’ future plans, such plans are as of the date of this presentation and are subject to change. Synopsys is not obligated to update this presentation or develop the products with the features and functionality discussed in this presentation. Additionally, Synopsys’ services and products may only be offered and purchased pursuant to an authorized quote and purchase order or a mutually agreed upon written contract with Synopsys.

## Slide 3: Course Overview
STA Concepts
  1 lecture
Delay Modeling
  1 lecture
Interconnect Parasitics
  1 lecture
Delay Calculation
  1 lecture
Configuring the STA Environment
  1 lecture
Timing Checks
  1 lecture
Crosstalk and Noise
  1 lecture

## Slide 4
Interconnect Parasitics

## Slide 5: Net
Net is a wire connecting pins of standard cells and blocks. It:
  Has only one driver
  Can drive a number of fanout cells or blocks
  Can travel on multiple metal layers of the chip
  Can be broken up into segments for equivalent electrical representation

## Slide 6: Interconnect Parasitics
Interconnect resistance - resistance between the output pin of a cell and the input pins of the fanout cells
Interconnect capacitance - is comprised of grounded and between neighboring signal routes
Interconnect inductance - arises due to current loops; effect of inductance can be ignored for low frequencies

## Slide 7: Overview
Cells
Input capacitances
Net parasitics
I1
I2
O2
O1
I1
I2
O2
O1
I1
I2
O2
O1

## Slide 8: RC Tree of Interconnect
Rtotal = Runit * L
Ctotal= Cunit * L
Distributed RC tree
H
L
Interconnect

## Slide 9: T - model
Rtotal is broken in two parts
Ctotal is connected between them
Ctotal

## Slide 10: - model
Ctotal is broken into two parts
Rtotal is connected between them
Rtotal

## Slide 11: N Section Representation
Breaking Rtotal and Ctotal into multiple sections increases accuracy
T model:
model:

## Slide 12: Elmore Delay
Elmore delays are used to calculate delay of RC trees, which
  Have single input node
  Do not have resistive loops
  Have capacitances only coupled to ground

## Slide 13: Elmore Delay Equation
Elmore delay equation is:
For example,
1
2
i-1
i
N

## Slide 14: Wire Load: Parasitic Effects
Parasitics are inevitable
Not known without layout
Delay and area will be incorrect/optimistic without estimation of parasitics
td
CL
trise
b
a
c
y
t2=f(t2d,t2c,c2)
C3
ttotal= f(t2a,t2b,t2c,C1,C2,C3)
t2a
t2b
t2c
b
a
c
y
t2=f(t2d,t2c,c2)
C3
ttotal= f(t2a,t2b,t2c,C1,C2,C3)
t2a
t2b
t2c
Delay > 0
Area >0

## Slide 15: Estimating Parasitic Devices
All parasitics depend on interconnect length
Generalization
R = length ∙ Runit length
C = length ∙ Cunit length
Area = length ∙ Areaunit length
The more the fanout (output connections) the larger the length
Length components
The larger the chip (the more gates it has) the more the length
length = f (gate count, fanout)

## Slide 16: Library: Wire Load Syntax
wire_load (name) {
  area : float ;
  capacitance : float ;
  resistance : float ;
  slope : float ;
{fanout_length (fanout, length) ;
...
}
}
wire_load_selection (name) {
{wire_load_from_area (min_area1,max_area1,wire_load_name1);
...}
}
default_wire_load : name ;
default_wire_load_selection : name ;
default_wire_load_area : float ;
default_wire_load_capacitance : float ;
default_wire_load_resistance : float ;
default_wire_load_mode : top | segmented | enclosed ;
Notes: If you define a wire_load_selection group in the library group, Design Compiler automatically selects a wire_load group for wire load estimation, based on the total cell area of the design.

## Slide 17: Library: Wire Load Example
wire_load (“8000”) {
capacitance : 0.024051;
  resistance : 1.860000e-03;
area : 0.010000;
slope : 30.285426;
fanout_length("1", "8.2750360");
fanout_length("2", "18.4914880");
fanout_length("3", "29.3531220");
}
default_wire_load : "8000";
default_wire_load_selection : "predcaps";
wire_load_selection (predcaps) {
wire_load_from_area (0.000000,200.000000, “4000");
wire_load_from_area (200.000000,8000.000000, "8000");
wire_load_from_area (8000.000000,16000.000000, "16000");
}
}

## Slide 18: Library: Wire Load Table
wire_load_table (name) {
  fanout_length(fanout, length);
  fanout_capacitance(fanout, capacitance);
  fanout_resistance(fanout, resistance);
  fanout_area(fanout, area);
  ...
}
Notes: It is practical to set the default_wire_load_mode to enclosed or segmented instead of top.
If the default_wire_load_mode is set to top, all nets in both the top design and subblocks
use the wire load model selected from the area of the top design. If the
default_wire_load_mode is set to enclosed, the nets fully enclosed within a design use
the wire load model selected from the area of that subdesign. If the
default_wire_load_mode is set to segmented, the nets partially enclosed within a design
use the wire load model selected from the area of that subdesign.

## Slide 19: Interconnect Trees: Best-case Tree
Assumed that:
  Load pin is physically adjacent to the driver
  None of the wire resistance is in the path to the destination pin
  Wire capacitance and pin capacitances act as load on the driver pin
Rdrive
Cout
C1
C1
C1
Rwire
Cwire

## Slide 20: Interconnect Trees: Balanced Tree
Assumed that:
  Each destination pin is on a separate portion of the interconnect
  Each path has equal portion of the total wire resistance and capacitance
Rdrive
Cout
C1
C1
C1

## Slide 21: Interconnect Trees: Worst-case Tree
Assumed that:
  All the destination pins are together at the far end of the wire
  Each destination pin sees the total wire resistance and the total wire capacitance
Rwire
Cwire
Rdrive
Cout
C1
C1
C1
Rwire
Cwire