## Slide 1: Static Timing Analysis
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2
CONFIDENTIAL INFORMATION
The information contained in this presentation is the confidential and proprietary information of Synopsys. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Synopsys without prior written authorization.
IMPORTANT NOTICE
In the event information in this presentation reflects Synopsys’ future plans, such plans are as of the date of this presentation and are subject to change. Synopsys is not obligated to update this presentation or develop the products with the features and functionality discussed in this presentation. Additionally, Synopsys’ services and products may only be offered and purchased pursuant to an authorized quote and purchase order or a mutually agreed upon written contract with Synopsys.

## Slide 3: Course Overview
STA Concepts
  1 lecture
Delay Modeling
  1 lecture
Interconnect Parasitics
  1 lecture
Delay Calculation
  1 lecture
Configuring the STA Environment
  1 lecture
Timing Checks
  1 lecture
Crosstalk and Noise
  1 lecture

## Slide 4
Configuring the STA Environment

## Slide 5: Getting Ready for STA Tool Usage
To identify all the timing issues in the gate level design, the following information is required:
  Clocks
  I/O timing characteristics
  False paths
  Multicycle paths
  Environment

## Slide 6: Setting Design Environment
To perform STA on this design, it is required to:
  Specify the clocks
  Set timing constraints for input and output paths
  Define driving circuitry
  Set output loads
Design Under Analysis (DUA)
Output load
Driving Circuitry
clock
IN0
IN1
INn
OUT0
OUT1
OUTn
clock

## Slide 7: Basic Clock Details
Clock Definition Components:
  Source
    Port of a design
  Period
    Time period of the clock (frequency)
  Duty cycle
    Positive and negative phase
  Edge times
    Rising edge and falling edge
  Variability
    Changes in frequency

## Slide 8: Clock Definition
create_clock -name CLK -period 10 [get_port CLKB]
T=10
CLK
0
5
10
15
Design
CLKB
CLK

## Slide 9: Clock Waveform
create_clock -period 10 \
-waveform {3 5 7 9 } [get_port CLKB]
T=10
CLKB
0
3
9
7
5
10
13
15
T=10
CLK
0
5
10
15
High duration
Low duration
Design
CLKB
CLK

## Slide 10: Clock Uncertainty
set_clock_uncertainty -setup 0.4 [get_clocks CLKB]
set_clock_uncertainty -hold 0.04 [get_clocks CLKB]
Setup uncertainty
Effective period
CLKB
Hold uncertainty
Uncertainty= clock skew + clock jitter

## Slide 11: Clock Skew Types
Global
  Clock difference between any pair of sequential elements of the whole design
Local
  Clock difference between any pair of sequential elements that have a datapath in between
Useful
  Can be used to fix timing violations
Notes: 11

## Slide 12: Clock Jitter
Ideal
Reference
T
T+ ∆T2
T+ ∆T1
T+ ∆T3
T+ ∆T4
Actual Waveform

## Slide 13: Clock Uncertainty Modeling Example
Setup = 2ns
0
5
10
D
Q
CLK
DFF
D
Q
CLK
DFF
D
Q
CLK
DFF
D
Q
CLK
DFF
Clock period: Tclk = 10ns
DFF Setup time: tsetup =2ns
Minimum delay for combinational logic
Clock uncertainty

## Slide 14: Inter-Clock Uncertainty
set_clock_uncertainty -from CLKA -to CLKB -hold 0.3
set_clock_uncertainty -from CLKA -to CLKB -setup 0.6
CLKA
D Q
CLKB
D Q
C1
CLK
CLK

## Slide 15: Modeling Clock Latency
Clock latency can be of two types:
  Source latency: the delay of clock signal from its source to designs input port (useful when clock generation circuitry is not part of the design)
  Network latency: average propagation delay of clock signal inside the design itself
CLK
D
Q
1ns
3ns
CLK
DESIGN
Network Latency
Source Latency
Origin of Clock

## Slide 16: Clock Latency
set_clock_latency 0.9 [get_clocks CLK]
set_clock_latency 0.8 –source [get_clocks CLK]
set_clock_latency 0.7 -source -min /
[get_clocks CLK]
set_clock_latency 0.3 -source -max /
[get_clocks CLK]

## Slide 17: Divided Clock (Generated)
create_clock -name CLK1 10 [get_pins SRC/CLK]
create_generated_clock -name CLK2 -source SRC/CLK -divide_by 2 \
[get_pins DIV/CLK]
CLK1
CLK2
Clock
source
CLK
CLK
Frequency divider
CLK1
CLK2
SRC
DIV
CLK

## Slide 18: Multiplied Clock (Generated)
create_clock -period 10 -waveform {0 5} [get_ports CLK1]
create_generated_clock -name CLK2 -source [get_ports CLK1] -multiply_by 2 [get_pins MULT/CLK]
CLK1
CLK2
0
10
20
0
10
15
5

## Slide 19: Gated Clock (Generated)
create_clock 10 [get_ports CLK1]
create_generated_clock -name CLKG -divide_by 1 -source CLK1 [get_pins G1/Z]
D Q
CLK
CLK1
Z
CLKG
G1

## Slide 20: Inverted Clock (Generated)
create_clock 10 [get_ports CLK1]
create_generated_clock -divide_by 1 -combinational -invert -source CLK1 \
[get_pins G1/Z]
Create an inverted generated clock:
  With respect to the source clock
  With the same period.

## Slide 21: Generated by Edges
create_clock 2 [get_ports CLK]
create_generated_clock -name CLK1 -edges {3 4 7} -source DCLK [get_pins G1/Z]
create_generated_clock -name CLK2 -edges {2 4 6} -source DCLK [get_pins G2/Z]
CLK
CLK1
D Q
CLK
QN
G2
CLK2
G1
1
2
3
4
5
6
7
8
9
10
CLK
CLK1
CLK2

## Slide 22: Latency of Generated Clock
Generated clock total latency is the sum of:
  Master clock source latency
  Generated clock source latency
  Generated clock network latency
D Q
CLK
Master clock
Generated clock
Generated clock
Source latency
Source latency
network latency
Clock source
Master clock definition
Generated clock definition

## Slide 23: Input Delay
set_input_delay -clock CLKA -max [expr TDFF + Tc] [get_ports IN]
IN
CLKA
First clock edge launches data
Design
tc
tDFF

## Slide 24: Output Delay
set_output_delay -clock CLK -max [exp tc + tsetup] [get_ports OUT]
CLK
Design
tsetup
out
tc

## Slide 25: Input Path with Virtual Clock
create_clock -name VCLK -period 10 -waveform {0 5}
set_input_delay -clock VCLK -max 3 [get_ports IN]
D Q
CK
Design
IN
CLK
D Q
CK
VSLK
t = 3
VCLK
0 5 10
CLKM
Data arrives
Data required
Setup check
3.1 9.5
0.1
Tsetup=0.5

## Slide 26: 3-cycle Setup Clock
create_clock -name CLK -period 10 [get_ports CLK]
set_multicycle_path 3 -setup -from [get_pins G1/Q] -to [get_pins G2/D]
D Q
CLK
G1
D Q
CLK
G2
3-cycle delay
CLK
C1
C2
CLK1
CLK2
Hold
check
1 cycle
Capture edge
Three cycles
to propagate
2 cycle
Capture edge
3 cycle
Capture edge

## Slide 27: 2-cycle Hold Check
set_multicycle_path 2 -hold -from [get_pins G1/Q] -to [get_pins G2/D]
Setup
lauch edge
Hold check moved to lauch edge
Setup multicycle = 3
Default hold check
Setup capture edge
Data is free change

## Slide 28: Half-Cycle Path
The design that has both negative and positive edge triggered flip-flops, can have half-cycle paths
Launch edge
Hold check
Setup check
0
6
12
Capture edge
C1
C2
D Q
D Q
CLK
CLK
C1
C2

## Slide 29: Slow to Fast Clock Domain
create_clock -name CLK1 -period 20 -waveform {0 10} [get_ports CLK1]
create_clock -name CLK2 -period 5 -waveform {0 2.5} [get_ports CLK2]
D Q
CLK
D Q
CLK
Divide by 4
CLK1
CLK2
Common base period
Launch clock
CLK1
Capture clock
CLK2
Hold check
Setup check
0
5
20

## Slide 30: Fast to Slow Clock Domain
create_clock -name CLK1 -period 5 -waveform {0 2.5} [get_ports CLK1]
create_clock -name CLK2 -period 20 -waveform {0 10} [get_ports CLK2]
D Q
CLK
D Q
CLK
CLK2
CLK1
Launch clock
CLK1
Capture clock
CLK2
Hold
Setup2
Setup1
Setup3
Setup4
0 5 10 15 20
Divide by 4

## Slide 31: Phase Shifted Multiple Clocks
create_clock -period 2.0 -waveform {0 1.0} [get_ports CLK1]
create_clock -period 2.0 -waveform {0.5 1.5} [get_ports CLK90]
D Q
CLK
D Q
CLK
CLK1
CLK1
CLK2
0.5 1.5 2.5 3.5
0 1.0 2.0 3.0 4.0
Setup
Hold
CLK90

## Slide 32: Path Groups
Path group is created of paths working with the same clock
Non-clocked paths are in default path group
The STA is performed on each path group separately

## Slide 33: Path Groups (2)
D Q
CK
CLK1
CLK2
CLK1 group
DEFAULT
CLK2 group
DEFAULT
D Q
CK

## Slide 34: Design Externals
The following attributes are required to be set:
  set_driving_cell
  set_input_transition
D Q
CLK
IN
OUT
Design
set_load

## Slide 35: Driving Cell
set_driving_cell -lib_cell INV -library test [get_ports IN]
set_input_transition 0.9 [get_ports IN]
D Q
CLK
IN
OUT
Design
0,9

## Slide 36: Capacitive Load
set_load 20 [all_outputs]
D Q
CLK
IN
OUT
Design
20
20

## Slide 37: Design Rule Checks
Rules for all ports and pins in the design to meet transition time and capacitance limits:
  Maximum transition
  Maximum capacitance
set_max_transition 0.3 [current_design]
set_max_capacitance 0.7 [current_design]

## Slide 38: Combinational Designs
Sometimes the design is a combinational circuit
No clock to constraint timing
Circuit under design
Combinational Logic

## Slide 39: Combinational Designs
Combinational circuit is put in the same clocked environment as the clocked one
An abstract clock called “Virtual clock” is defined for this environment
By setting correct clock period, input/output delays of the combinational logic can be controlled
D
Q
CLK
DFF
D
Q
CLK
DFF
Clock
Combinational Logic
Delayin=1ns
Delayout=3ns
Delaymax= Tclk– Delayin – Delayout=7ns

## Slide 40: Refining
set_case_analysis
  Constant value on a pin of a cell or input port
set_disable_timing
  Breaks a timing arc
set_false_path
  Specifies false path not real which implies that these paths are not checked in STA
set_multicycle_path
  Specifies multi-cycle paths

## Slide 41: Point-to-point Specification
set_max_delay 4 -to G1
set_max_delay 1 -from G1 -to G2
set_max_delay 3 -from G1 -through G2 -to G3
set_min_delay 3 -from [get_clocks CLK1] -to [get_clocks CLK2]