## Slide 1: Static Timing Analysis
Synopsys Armenia Educational Department
Sci.D.Professor Vazgen Melikyan

## Slide 2
CONFIDENTIAL INFORMATION
The information contained in this presentation is the confidential and proprietary information of Synopsys. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Synopsys without prior written authorization.
IMPORTANT NOTICE
In the event information in this presentation reflects Synopsys’ future plans, such plans are as of the date of this presentation and are subject to change. Synopsys is not obligated to update this presentation or develop the products with the features and functionality discussed in this presentation. Additionally, Synopsys’ services and products may only be offered and purchased pursuant to an authorized quote and purchase order or a mutually agreed upon written contract with Synopsys.

## Slide 3: Course Overview
STA Concepts
  1 lecture
Delay Modeling
  1 lecture
Interconnect Parasitics
  1 lecture
Delay Calculation
  1 lecture
Configuring the STA Environment
  1 lecture
Timing Checks
  1 lecture
Crosstalk and Noise
  1 lecture

## Slide 4
Timing Checks

## Slide 5: Timing Checks
Constraints set by sequential circuits:
  Setup
  Hold
Possible conditions:
  Best-case (Hold)
  Worst-case (Setup)

## Slide 6: Setup Timing Check
Data must be stable before the active edge of the clock
D Q
CLK
CLK
D
Unstable data
Setup time

## Slide 7: Launch and Capture Flip-flops
Setup is checked from first active edge (clock) of launch flip-flop to closest active edge of capture flip-flop
D Q
CLK
Logic
D Q
CLK
clock 1
clock 2
data 2
launch flip-flop
capture flip-flop
FF
FF

## Slide 8: Data and Clock Signals for Setup Timing Check
Setup condition
Tlaunch + TLFF + Tc < Tcapture + Tcycle - Tsetup
Tcycle
Tlaunch
CLK
Launch edge
LFF/CK
CFF/D
CFF/CK
Tcapture
Setup
Capture edge
D Q
CLK
D Q
CLK
Logic
CLK
data 2
launch flip-flop(LFF)
capture flip-flop(CFF)
FF
FF
Tlaunch
Tcapture
Tc
Tc
TLFF

## Slide 9: Hold Timing Check
Verifies that the data is held stable for a specified amount of time after the active edge of the clock
D Q
CLK
CLK
D
Hold time

## Slide 10: Data and Clock Signals for Hold Timing Check
Tcycle
Tlaunch
CLK
Launch edge
LFF/CK
CFF/D
CFF/CK
Tcapture
SetupTsetup
Capture edge
D Q
CLK
D Q
CLK
Logic
CLK
data 2
launch flip-flop(LFF)
capture flip-flop(CFF)
FF
FF
Tlaunch
Tcapture
Tc
Tc
TLFF
Hold condition
Tlaunch + TLFF + Tc > Tcapture + Thold

## Slide 11: Hold Checks and Setup Check Cycles
A hold timing check ensures that:
  Data from the subsequent launch edge must not be captured by the setup receiving edge
  Data from the setup launch edge must not be captured by the preceding receiving edge
Launch flip-flop clock
Capture flip-flop clock
Launch edge 1
Launch edge 2
Setup check 1
Capture edge 0
Capture edge 1
Hold check 1
Hold 0

## Slide 12: Removal Timing Check
Verifies that there is required amount of time between an active clock edge and the release of an asynchronous control signal
D Q
CLK
D Q
set
CLK
CLK
set
CLK
Earliest set can be removed
Active clock edge
set
Removal time

## Slide 13: Min Pulse Width Checks
The minimum pulse width refers to the shortest duration of a pulse (high or low state) that a clock signal must maintain to be reliably recognized and processed by the digital circuit.
Clock pulse width violations can cause the following problems:
Sequential devices (flip-flops and latches) might not capture data properly.
In some logic circuits, the entire pulse could disappear
Typically, the pulse width shrinks because of the difference in the rise and fall delays of the cells. These differences arise because of variation effects which are more dominant in lower tech nodes, i.e.:
Delay variation due to device aging. Rise and fall delays change at different rates, which causes min_pulse_width violation
parts of clock tree age differently because of clock gating which causes increased clock skew and reduced min pulse width.

## Slide 14: Min Pulse Width Checks
CLK in
CLK out
CLK in
td_rise=0.05ns td_fall=0.02ns
0.5ns
0.5ns
period=1ns,
Pulse Width H=0.5ns
Pulse Width L=0.5ns
0.05ns
0.02ns
0.47ns
0.05ns
0.53ns
CLK out
period=1ns,
Pulse Width H=0.47ns
Pulse Width L=0.53ns
To set a min_pulse_width_check constraint:
- Use set_min_pulse_width command (on clocks/cells/ pins/ports)
- Or specify the requirement in .lib file for the respective pin
To report min pulse width use:
- report_min_pulse_width
- report_constraint -min_pulse_width
D Q
CLK
Min_pulse_width of CLK pin is usually included in the .lib. If not specify with set_min_pulse_width command
In this example if min_pulse_width constraint on flipflop/CLK pin is i.e. 0.5ns (for both high and low) The actual pulse width for high (0.47ns) will be violating the min pulse width constraint.